## Slide 1: FELIX -- Phase 2
Lorne Levinson
ATLAS Israel Review, 22 August 2018

## Slide 2: FELIX Phase 1 Team
Michael Oberling
Alex Paramonov
Soo Ryu
Jinlong Zhang
Mikael Baymani
Markus Joos
Jörn Schumacher
Wainer Vandelli
Will Panduro
Israel Grayzman
Lorne Levinson
(Julia Narevicius)
Alex Roich
Hucheng Chen
Kai Chen
Francesco Lanni
Shaochun Tang
Weihao Wu
Andrea Borga
Henk Boterenbrood
Frans Schreuder
Jos Vermeulen
Anamika Aggarwal
Mark Dönszelmann
Frank Filthaut
Nikolina Ilic
Rene Habraken
Kevin Bauer
(Daniel Guest)
Serguei Kolos
Andrew Lankford
Gokhan Unel
Daniel Whiteson
Phase 2
Already joined:
Bologna
Wuppertal

## Slide 3: ATLAS DAQ Today
FE
FE
FE
FE
FE
Today
2015
2017
2019
2021
2023
2025
Run 4
Custom electronic
components
ROD
ROD
ROD
ROD
ROD
Custom
point-to-point links
ReadOut
Driver
HLTPU
HLTPU
HLTPU
HLTPU
HLTPU
HLTPU
HLTPU
HLTPU
HLTPU
HLTPU
HLTPU
HLTPU
HLTPU
HLTPU
HLTPU
HLTPU
HLTPU
HLTPU
HLTPU
HLTPU
Ethernet
PCs
(COTS)
High-Level Trigger Farm
~1500
servers
Run 2
Run 3
~100
servers
ROS
ROS
ROS
ROS
ROS
Point-to-point
S-links
ReadOut
System
100 kHz /
~200 GB/s
~2000
links
Frontend
Notes: Run2 event data
Custom FE electronics
Subdetector specific RODs
ROS first part in the chain with COTS hardware (PCIe)
goal

## Slide 4: Upgrade for Phase-I
2019
2015
2017
2019
2021
2023
2025
NSW
LAr
L1 Calo Tr.
FE
FE
FE
FE
FE
ROD
ROD
ROD
ROS
ROS
ROS
HLTPU
HLTPU
HLTPU
HLTPU
HLTPU
HLTPU
HLTPU
HLTPU
HLTPU
HLTPU
HLTPU
HLTPU
HLTPU
HLTPU
HLTPU
HLTPU
HLTPU
HLTPU
HLTPU
HLTPU
HPC Network
Custom electronic
components
including
FELIX cards
High-Level Trigger Farm
Data
Handler
Data
Handler
HPC Network
100 Gb Ethernet
Run 4
GBT links* or FULL mode links
PCs
PCs
(COTS)
Run 3
Run 2
* GBT: GigaBit Transceiver with Versatile Link
Notes: Goal: remove one layer of custom hardware
Number of subdetectors directly interfacing to felix
Industry standard networks

## Slide 5: Upgrade for HL-LHC
Run 4
FE
FE
FE
FE
FE
Data
Handler
Data
Handler
Data
Handler
Data
Handler
Data
Handler
HLTPU
HLTPU
HLTPU
HLTPU
HLTPU
HLTPU
HLTPU
HLTPU
HLTPU
HLTPU
HLTPU
HLTPU
HLTPU
HLTPU
HLTPU
HLTPU
HLTPU
HLTPU
HLTPU
HLTPU
HPC Network
GBT, LpGBT* or FULL mode links
2024
High-Level Trigger Farm
HPC Network
COTS network technology
2015
2017
2019
2021
2023
2025
~20,000 links
less than
10 TB/s
PCs
(COTS)
Run 3
Run 2
Custom electronic
components
including
FELIX cards
*LpGBT: Low power GBT
Notes:   Bandwidth and scalability will increase more for HL-LHC
  All subdetectors by 2024

## Slide 6: Phase 2 FELIX
Basic concept remains: aggregation, COTS network, software
All ATLAS detectors  more variety & more complex requirements
  Dedicated protocol for ITK
  Higher bandwidths
  Newer GBT: Tx/Rx: GBTx @4.8G/4.8G  10G/2.5G
  Many more links
  ITK has extra requirements to support efficient calibration
  New TTC/BUSY system (“LTI”) allows synchronization of commands stored in FELIX that configure FE ASICS with timing defined by the TTC system
Design depends on:
  Experience in Run 3
  Experience with the Phase 2 demonstrators (ITK) now starting
  Detailed requirements from the detectors (in progress)
  How industry progresses with:
    Processors
    PCIe  …
    Networks
    FPGAs

## Slide 7: Scope of the project effort
Capture of Phase 2 requirements from all the ATLAS detectors
FPGA hardware that fulfills our requirements (links, clocks, performance)
Firmware that implements the required functionality
Software for controlling, configuring, reading and routing data streams, including SCA (DCS) data streams
Interface to the new TTC system and its interaction with calibration sequences
Low level software: drivers, debugging tools, configuration GUI's, etc.
Performance studies and bench-marking to optimize the FW and SW
Network interface software and network studies to optimize networking
Does not include, but we work in close association with:
  Software ROD: requirements and interface with FELIX
  Backend support of GBT-SCA for DCS and detector front end configuration/calibration
Requirements for selection of the server PC and of the FPGA card manufacturer
User support of the detector groups in developing their FELIX-based DAQ
  JIRA tickets, User Workshops, documentation, hands-on participation in detector tests

## Slide 8: Current estimation of links
Detector | # FELIX boards | # down links | BW (Gb/s) | # up links | BW (Gb/s)
ITk Pixel | 224 | 1285 | 2.5 | 10596 | 5
ITk Strips | 76 | 1552 | 2.5 | 1824 | 10
LAr LASP | 36 | 100 | 2.5 | 770 | 10
LAr LDPB | 8 | 31 | 2.5 | 155 | 10
L0Calo | 8 | 16 | 2.5 | 120 | 10
NSW | 96 | 864 | 5 | 1440 | 5
NSW Trigger | 4 | 64 | 5 | 64 | 5 or 10
Global Trigger | 4 | 48 | 2.5 | 96 | 10
Tile | 8 | 160 | 10 | 160 | 10
TGC | 8 | 192 | 10 | 192 | 10
MDT | 64 | 1536 | 10 | 1536 | 10
RPC | 4 | 64 | 10 | 64 | 10
CTP | 1 | 12 | 10 | 12 | 10
MUCTPI | 1 | 4 | 10 | 4 | 10
LUCID uplink | 1 | 24 | 5 |  | 
ZDC uplink | 1 | 24 | 5 |  | 
AFP uplink | 1 | 12 | 5 |  | 
 | 545 | 5988 |  | 17033 | 
System will be much bigger, more complex, higher typical speeds:
Phase 1 total: 2,200 links
Phase 2 total: 18,000 links
×10
FELIX system was designed to be scalable.
Is it really scalable?

## Slide 9: Phase 1 FELIX PCIe FPGA card
BUSY output
TTC fiber input
multi-fiber
connector
(fiber ribbons to 2x4 “minipods” not shown)
BNL-712
$$ Most of the cost of FELIX is this board and its FPGA.
Open question if Phase 2 FELIX will remain a PCIe card

## Slide 10: ITK
On-going major effort required to understand ITK requirements … and map them to a FELIX-based TDAQ architecture
Demonstrators, finally in progress, will really help to converge understanding
Compared to NSW, ITK has much tighter integration with the trigger system:
  for calibration
  especially if ATLAS adopts a system with a two-level hardware trigger (baseline is one level)  low latency transmission of L0 regions of interest info back to the FE ASIC via the TTC path
ITK plans on using a data transmission protocol not used by the Phase 1 detectors
Added complexity due to need to put, readout, configuration, DCS, and trigger info on the same electrical link to/from the FE ASIC
FE chips so far need a pre-aggregation of five 1G links to one 5G link.

## Slide 11: Resources needed
We need already now to play a larger role in working with the Phase 2 demonstrators in order to understand their requirements
Firmware engineering expertise
To support the development, testing, bench-marking
  A full FELIX path from front end emulators thru’ the swROD needs to be working in Israel
    Software and Linux expertise to maintain and help operate
    The equipment

## Slide 12: Open issues
Currently the PC server is in the data path, i.e. all the data flows thru’ PC memory Need to investigate architectures with FPGA  network with the PC software only controlling
Solutions for the ITK pre-aggregation: Needs to be as close as possible to the detector. Does this mean an aggregation ASIC or rad tol FPGA
Understand the interaction and division of labour with the TTC LTI module (Local Trigger Interface) for a two-level trigger for calibration sequences

## Slide 13: End