## Slide 1: Remote alignment for HL-LHC link to the experimental beam pipe TA(X)S alignment ATLAS and CMS
Antje BEHRENS
Dirk MERGELKUHL
Joint meeting WP8-WP15 – CERN – 21.08.2018

## Slide 2: ATLAS TAS situation
ATLAS TAS, bars, shielding and cylinders

## Slide 3: Actual ATLAS TAS Alignment Concept
TAS alignment based on bars attached to TAS and traversing the JFC and JFS shielding
Bars are made of two parts
  1st part fix inside TX1STM
  2nd part removable in JFS and supports the targets
2nd part needs to be (dis-)mounted manually for opening/closing
Z-coordinates of 2 top points determine vertical alignment
X-coordinates of 2 side points determine radial alignment
Alignment in single configuration possible (experiment closed, shafts open, cherry-picker available to put bars and targets)
Regular manual intervention with constraints on configuration, planning, access, exposure

## Slide 4: Survey procedure for TAS (ATLAS)
Same survey procedure as since 2007 for TAS
  Fiducials on 2 vertical and 2 horizontal bars
  Access with nacelle for bar, target installation and adjustment
Measurement frequency: every YETS/EYETS/LS
Adjustment frequency
  ATLAS: YETS/EYETS/LS if difference to nominal > 0.5 mm
Measurement with laser tracker (AT40x) and high precision 1.5 inch targets

## Slide 5: RP Calculations
Situation outside ATLAS JFS shielding in LS6
Radiation dose next to TAXS bars < 10uSv/h
  Acceptable for installation and alignment
Reference: CERN-RP-2014-119-REPORTS-TN

## Slide 6: Movements ATLAS TAS in time
Largest adjustments have been after installation with up to 5.4 mm
Maximum adjustment after first beam up to 1.2 mm
Generally adjustments >= 0.5 mm in YETS or LS
Insertion problem for bars ‘’creates’’ offset of ~6 mm
Horizontal + = to LHC entre
Vertical + = to top
Horizontal + = to LHC entre
Vertical + = to top

## Slide 7: Movements of TX1STM shielding
Movements TX1STM-A+C in time (GLANCE) from ~20 measurements (2008-2017)
TX1STM is the shielding that supports the TAS
  Maximal movements for TX1STM-A
    In Xatl (m) : 0.0011 (radial)
    In Yatl (m) : 0.0024 (vertical)
    In Zatl (m) : 0.0040 (longitudinal)
  Maximal movements for TX1STM-C
    In Xatl (m) : 0.0012 (radial)
    In Yatl (m) : 0.0030 (vertical)
    In Zatl (m) : 0.0045 (longitudinal)
Vertical movement of ~1 mm included due to JFC1-3

## Slide 8: CMS TAS situation
CMS TAS, shielding, bars, retro targets

## Slide 9: Actual CMS TAS Alignment Concept
TAS alignment based on bars attached to TAS and traversing the FIN shielding (green)
Single parts of bars stay permanently
  1st fix part inside FIN
  Retro-targets are mounted as targets in 2009
Rotating shielding needs to be open for measurement
Z-coordinates of 2 top points determine vertical alignment
X-coordinates of 2 side points determine radial alignment
Manual intervention with constraints on configuration, planning, access, exposure

## Slide 10: Survey procedure for TAS (CMS)
Same survey procedure as since 2009 for actual TAS
  Fiducials on 2 vertical and 2 horizontal bars
Shorter bars and targets are permanently installed
Non-contact measurement (distance ~12.0 m)
Adjustment frequency: last adjustment in 2009!
For TAXS: Change of equipment to laser tracker and precision PLX1.5 inch targets (permanent, ceramic)

## Slide 11: Movements CMS TAS in time
Position of TAS targets wrt CMS coordinate system in time
  Vertical position: min -1.7mm
  Radial position: min -0.9mm
Vertical movement from last alignment 10.2009 to 12.2017 (8 years):
  1.1 mm for TAS 54
  0.5 mm for TAS 56
Chart: TAS 54 - Difference to nominal [mm]
| 12.10.09 | 20.01.10 | 13.12.10 | 19.12.11 | 10.02.12 | 26.02.13 | 05.03.15 | 12.01.16 | 13.12.16 | 11.12.17
Target 1 (radial) | -0.50167 | -0.445 | -0.445 | -0.865 | -0.375 | -1.035 | 0.42 | -0.175 | 0.145 | 0.42
Target 2 (radial) | -0.22356 | -0.18356 | -0.65356 | -0.80356 | -0.063556 | -0.86356 | 0.29644 | -0.16856 | 0.24644 | 0.38144
Target 3 (vertical) | -0.379 | -0.91233 | -0.91233 | -1.1923 | -0.76233 | -1.4523 | -1.5498 | -1.4523 | -1.5923 | -1.5823
Target 4 (vertical) | -0.429 | -1.2773 | -1.1023 | -1.4523 | -1.0923 | -1.5423 | -1.6623 | -1.6623 | -1.6423 | -1.7023
Chart: TAS 56 - Difference to nominal [mm]
| 09.10.09 | 20.01.10 | 14.12.10 | 19.12.11 | 10.02.12 | 21.03.13 | 05.03.15 | 13.01.16 | 13.12.16 | 18.12.17
Target 5 (radial) | -0.08 | 0.07 | -0.13333 | -0.17333 | -0.053333 | 0.62667 | -0.73583 | -1.1933 | -0.69333 | -0.92833
Target 6 (radial) | 0.21 | 0.14333 | -0.12667 | -0.26667 | -0.13667 | 0.47333 | -0.45917 | -0.69667 | -0.43667 | -0.61167
Target 7 (vertical) | 0.17 | 0.17333 | -0.13667 | 0.0033333 | -0.14667 | -0.46667 | -0.78667 | -0.62667 | -0.58667 | -0.61
Target 8 (vertical) | -0.15 | -0.035 | -0.11 | -0.43 | -0.27 | -0.85 | -0.7875 | -0.65 | -0.8 | -0.605

## Slide 12: ATLAS and CMS TAS
Measurement possible in long and short TS
Adjustment possible in long (short?) TS
Lessons from actual TAS
  Z-stoppers for both experiments
  Installation of shielding plugs for ATLAS
  Eventually rigid tubes instead of flexible bars
    => redundancy allows control of fiducialisation and installation of bars
  Best case for ATLAS: modified cylinders and shorter, rigid bars to reduce significantly the installation time

## Slide 13: Adjustment range of TAS and TAXS
Reduced adjustment range due to knowledge of actual shielding position
  Reduced tolerances for production and installation of shielding
  Adjustment range of +- 10.0 mm for ATLAS and CMS
  ATTENTION: Adjustment is sequentially for 2x2 directions!
New mechanical system still to be designed:
  Current priorities of WG8 on LS2 activities
  Design of mechanical system during / after LS2 by WG8

## Slide 14: Actual baseline for TAXS
Baseline for future TAXS alignment:
Same concept as so far (limited mechanical choice); 2x vertical, 2x horizontal
Permanent targets for laser tracker (non-magnetic) in CMS
TAXS get Z-stoppers => no alignment in beam direction
Demanded accuracy for adjustment 0.5 mm at 1 sigma (unchanged)
For ATLAS:
Alignment based on 4x long bars (2 parts) for ATLAS (points outside second layer of shielding called JFS)
  As so far but with more rigid bars and different connection system
For CMS:
Alignment based on 4x short, rigid bars for CMS (points outside first layer of shielding called FIN)

## Slide 15: Error budget for TAXS measurements
A) Target precision with support
B) Fiducialisation using mole (to be produced)
C) Cavern network up to UPS gallery
D) Low-beta system (UPS gallery to Q1, Q2, Q3)
E) Fiducialisation of low-beta magnets (warm)
Cold warm transition not considered!
Worst case (linear add 1 sigma):
A) 0.03 mm, B) 0.25 mm, C) 0.30 mm
D) 0.10 mm, E) 0.08 mm => Total = 0.76 mm

## Slide 16: CMS - VAX support and BP support @ 16m
Beam pipe support @ 16 m
3D model
VAX support
prototype
CMS Engineering and Integration Center
New VAX and beampipe support @ 16m
LS2:
  Installation of VAX support box without equipment
  Installation of new beampipe and beampipe support at 16m
LS3:
  Installation of VAX equipment, valve, bellows

## Slide 17
CMS Beam pipe supports
Forward support @16000
concept
New half shells inside Thin rotating shielding
VAX support
Pump and BP support @16m
A. Gaddi, CMS E&I center
CMS – LS2

## Slide 18: ATLAS and CMS - VAX alignment
Alignment of empty VAX support after installation
  CMS: LS2
  ATLAS: LS3
Installation of VAX equipment based on plug-in
No alignment of VAX equipment in cavern
No future alignment of VAX box foreseen due to increased valve diameter (current situation)
Final design of VAX support, beampipe support
Survey interfaces, fiducialisation and alignment still to be defined

## Slide 19: Thanks for your attention!

## Slide 20: BACK UP SLIDES

## Slide 21: Change of Targets
Advantages:
Different reflectors exist on the market (size, type)
Non-magnetic devices exist (ceramic)
Compatible with laser trackers available at CERN
Size and weight of target support could be reduced
Radiation hard up to 10 MGy (test crab cavities)
No access needed for measurement (if permanent)
Constraints:
Long-term maintenance could be necessary
  Cleaning from dirt, dust
  Protection?
Costs per prism ~1000-1500 EUR
  8 prisms per experiment needed (if permanent)
  Prisms available for temporary installation
  but access needed in this case! Exposure?
Prism supports need to be manufactured (design is available)