## Slide 1: Update on DQW HOMs
J. A. Mitchell
131st HL-LHC WP2 Meeting
CERN-Internal, 25th September 2018

## Slide 2
SPS Crab Test Stand
HOM Couplers (x3)
Tuner
FPC
DQW crab cavity (vertical)
Helium Vessel
Cold magnetic shielding
Field probe

## Slide 3
Ancillaries: Non-conformity
All HOM coupler ports are + 5 mm compared to design.
Reduces coupling to majority of HOMs
Does not present impedance issue for SPS test.

## Slide 4
Ancillaries: Field probe as fourth HOM coupler
The pick-up is designed extract 1 W at the fundamental mode frequency  Qe = 1.6 x 1010.
It is also a HOM coupler for the 1.75 GHz mode  cannot couple to this mode with HOM couplers.
The PU is made from Nb and Cu to avoid heating.

## Slide 5
Mode measurements
Transmission measurements using VNA in cryomodule cold test in M7 buncker.

## Slide 6
Mode measurements
Transmission measurements using VNA in cryomodule cold test in M7 buncker.
Deviations are hence:

## Slide 7
Modified impedance spectra
Impedance spectra:
  Frequencies and Qe values are known for a large number of modes.
  Simulated spectra altered for both cavities.
  Note, remembering to use the +5 mm simulation results!
For both cavities the 960 MHz mode has increased in frequency.
From BELOW to ABOVE the harmonic!
This shows it is feasible for the mode to be excited by the 24th harmonic at 25 ns bunch spacing.

## Slide 8
HOM power: effect of frequency and Qe shift
Using SPS HOM coupler and HL-LHC parameters:
However, the frequency and Qe of the modes can change.
Stochastically varying these two parameters, a worst-case power can be calculated.
13 times larger than 1 kW limit.
Due to mode at 960 MHz – coupler needs to be altered.

## Slide 9
Re-design
The coupler should be altered to:
  Improve ease of manufacture (not thoroughly detailed in this presentation).
  Reduce transverse impedance below threshold.
  Reduce maximum foreseeable HOM power to below 1 kW.
Assembly constraints…
Presented at HiLumi’17

## Slide 10
DQW HOMC V2
Impedance
Power
Highest power still a result of the 960 MHz mode.
If we vary this mode in frequency:

## Slide 11
Measurements with beam
Measurement aims:
  Validate we can predict HOM power accurately.
  Validate we have not ‘missed modes’ in simulation.
  Validate power increases with intensity (and bunch number) as expected.
A binomial distribution was initially used to represent the bunch profile.
H1
H2
H3

## Slide 12
Meas. with Beam: Single Bunch
27/08/2018: MD4
Cavity 1 - HOMC1
Cavity 2 - HOMC1
Analytic underestimates
Unforeseen power at 1.8 GHz

## Slide 13
Meas. with Beam: Single Bunch
High resolution narrow band scans also taken on high Zl modes.
Analytic under-represents power in all cases.
Large coupling difference seen between modes.
27/08/2018: MD4
Top HOM Coupler
Bottom HOM Coupler
580
704
960
1263
Mode [MHz]

## Slide 14
Meas. with Beam: Measured Profile
To evaluate whether the beam profile was the cause of the underestimation.
In the following crab cavity test (MD5) the bunch profile was measured during the coasts.
This time multiple bunches were used with a bunch spacing of ~ 525 ns.
05/09/2018: MD5
Courtesy of M. Schwarz

## Slide 15
Meas. with Beam: Measured Bunch Profile
Predicted is total power, not accounting for intra-coupler power flux.
There are still discrepancies between the measured and analytical.
This is under investigation:
  Cable transfer function, mechanical position of HOM couplers, calibrations, bellows etc…
05/09/2018: MD5

## Slide 16
Meas. with Beam: Power Distribution
Cavity 1
Cavity 2
H1
H2
H3
Measured power ratio for 4 high longitudinal impedance modes.

## Slide 17
Meas. with Beam: Multibunch
590 MHz
700 MHz
960 MHz
27/08/2018: MD3
Cavity 1
590 MHz mode is underestimated by > 10 dB.
Using measured profile could account for 5 dB.
Q or R/Q is underestimated.

## Slide 18
First HOMs
590 MHz mode is higher in power than predicted by > 10 dB
Decrease in damping:
  Transmission measurements on cavity show the difference between cavities.
  Test box measurements show a large deviation in the coupler’s ‘transfer function’.
  Tolerance on LHC couplers should be larger.
Notes: X-scale
Differences in coupling – under investigation

## Slide 19
Conclusions
LHC HOM Coupler in final stages.
  Files stored with CST models on EDMS.
HOM Power compared with single-bunch and multi-bunch.
  Under-represented by analytic bunch profile.
Notable Observations:
  960 MHz is dominant mode for power and > 95 % through top HOM coupler.
  590 MHz mode is 10 dB higher than expected.
  High frequency power not expected – being investigated.

## Slide 20: Update on DQW Multipoles
J. A. Mitchell
131st HL-LHC WP2 Meeting
CERN-Internal, 25th September 2018

## Slide 21
Simulations
WP2 Meeting, 22nd May 2018: Main comments
Does the b3 increase so much with the new ports?
Is the large increase in b4 realistic?

## Slide 22
Simulations
VT = 10 MV | re{b2} | im{b2} | re{b3} | im{b3} | re{b4} | im{b4}
Panofsky Wenzel @ 25 mm | -6 | 2 | -1494 | -56 | -830 | 135
PW @ 30 mm | -6 | 3 | -1491 | -19 | -466 | 629
LF @ 30 mm | -6 | 3 | -1505 | -32 | -575 | 498
Units: mTm/m(n-1)
K. Papke
Benchmarked with another person.
b3 is realistic and greater than specified 1000 mT/m2.
b4 needs investigation into radial convergence.

## Slide 23
Measurements
Azimuthal bead-pull measurements using metallic and dielectric needles.
We are able to measure the b1 and b3 components.
Working to evaluate to what accuracy we can measure them to.
Courtesy of Paul-Francois Gapais (see summer student report).