## Slide 1: Highlights of detector and instrumentation developments for INO project

## Slide 2: ICAL, e-ICAL and m-ICAL
Parameter | ICAL | e-ICAL | m-ICAL
No. of modules | 3 | 1 | 1
Module dimensions | 16.2m×16m×14.5m | 8m×8mx2m (90:1) | 4m×4mx1m (720:1)
Detector dimensions | 49m×16m×14.5m | 8m×8mx2m | 4m×4mx1m
No. of layers | 150 | 20 | 10
Iron plate thickness | 56mm | 56mm | 56mm
Gap for RPC trays | 40mm | 40mm | 45mm
Magnetic field | 1.3Tesla | 1.3Tesla | 1.3Tesla
RPC dimensions | 1,950mm×1,910mm×24mm | 1,950mm×1,910mm×24mm | 1,950mm×1,910mm×24mm
Readout strip pitch | 30mm | 30mm | 30mm
No. of RPCs/Road/Layer | 8 | 4 | 2
No. of Roads/Layer/Module | 8 | 4 | 1
No. of RPC units/Layer | 192 | 16 | 2
No. of RPC units | 28,800 (107,266m2) | 320 (1,192m2) (90:1) | 20 (74.5m2) (1440:1)
No. of readout strips | 3,686,400 | 40,960 (90:1) | 2,560 (1440:1)

## Slide 3: ICAL, e-ICAL and m-ICAL

## Slide 4: Bench marking of RPC detectors

## Slide 5: Glass spray painting robot

## Slide 6: Screen printing on electrodes

## Slide 7: Materials for gas gap fabrication
Schematic of an assembled gas volume
Edge spacer
Gas nozzle
Glass spacer

## Slide 8: Automatic RPC gap making

## Slide 9: Development of Pickup panels
Honeycomb panel
G-10 panel
Foam panel
Polypropylene as well
as PVC panels are
also developed.

## Slide 10: Closed loop gas system
About 200,000 litres (60 LPG cylinders) of gas will be circulating in the ICAL detector all the time.
Regenerate, Recycle and Reuse

## Slide 11: Development of Gas systems
ICAL detector holds about 200,000 litres of gas all the time.
Gas recycling system ensures that almost no gas is wasted.

## Slide 12: Functions of ICAL electronics
Signal pickup and analog front-end
Strip hit latch
Pulse shapers, timing units
Background noise rate monitor
Digital front-end and controller
Data network interface and architecture
Multilevel trigger system
Calibration and time stamping unit
Backend data concentrators
Event building, data storage systems
On-line data quality monitors
Slow control and monitoring
  Gas, magnet, power supplies
  Ambient parameters
  Safety and interlocks
Voice and video communications
Remote access to detector sub-systems and data

## Slide 13: Challenges of ICAL electronics
Large number of electronic data readout channels. This necessitates large scale integration and/or multiplexing of electronics.
Large dimensions of one unit of RPC. This has bearing on the way the signals from the detector are routed to the front-end electronic units.
Large dimensions of the ICAL detector. Disparate distances (i.e. delays of signals in cables) of RPCs from the backend requires elaborate calibration procedures for global signals.
Road structure for the mounting of RPCs. This necessarily imposes constraint that signals from both X & Y planes of the RPC unit, along with other service and power supply lines are brought out only from the transverse direction of the detector.
About 25cm gap is available between the face of the detector and the service trolleys. Any installations on the face of the detector have to be designed with this consideration.
About 40mm gap between iron layers is available for the RPC detector. Thickness of the RPC holding tray, thickness of tray sliding track, tolerances of the iron plate thickness, height of the on detector high voltage module, analog and digital front-end modules, routing of cables and all other service lines must fit in this gap.
Effect of fringe magnetic field on the performance.
Low power consumption per channel (25mW/channel → 100KW/detector)

## Slide 14: Design and fabrication of ICs
QFN-48
package
QFN-48
package
Fast preamplifiers
(Hybrid Micro Circuits)
Fast preamplifiers and comparators (ASICs)
Timing circuits (ASICs)
Analog
Digital
Mixed

## Slide 15: HMC preamps for ICAL test stands
Input & Output impedance: 50Ω
Nominal gain: 10
Rise time: ~1.2 ns
Bandwidth: 350MHz
Package: 22-pin DIP
Power Supply : ± 6V
Power Consumption:110mW
BMC1596
(Positive In – Positive Out)
BMC1597
(Positive In – Dual Out)
BMC1595
(Negative In – Negative Out)
BMC1598
(Negative In – Dual Out)
BMC1513
(Negative In – Negative Out)

## Slide 16: Voltage amplifier ASICs
SOIC-28
package
(11mmx18mm)
CLCC-44
package
(16mmx16mm)
0.35m SiGe BiCMOS process
An 8-channel AFE board using two, 4-channel preamplifier and one, 8-channel discriminator ASICs designed, fabricated and extensively tested on RPC test stands at BARC and TIFR.
Horizontal mounting in the RPC tray agreed upon for the Engineering Module as the board dimension couldn’t reduced below 200mm  45mm.
Small volume order for the ASIC chipset in QFN package and boards produced.
Chip packing options, board manufacturer development, automatic assembly lines and test equipment are being planned.
QFN-48
package
QFN-48
package

## Slide 17: Analog Front-End boards with NINO ASICs
17
Accepts inputs from 8 pickup strips of an SRPC.
8 differential drivers of unity gain.
One NINO chip with threshold control and other accessory circuits.

## Slide 18: ICAL’s TDC ASIC
Principle
  Two fine TDCs to measure start/stop distance to clock edge (T1, T2)
  Coarse TDC to count the number of clocks between start and stop (T3)
  TDC output = T3+T1-T2
Features and specifications
  UMC 130nm technology, QFN64 package, 3.2mm3.2mm in size
  Input clock: 10MHz (250MHz to DLL internally generated by PLL)
  16 hit channels, 1 trigger and 1 calibration channel
  Four paired time stamps: leading edge 65.5µs (125ps), pulse width 64ns (250ps)
  Readout buffers: 91 locations
  32-bit/hit, data on 4-and 11-line SPI bus.
  Self test features

## Slide 19: First module of ICAL’s DFE
Three boards
Altera Cyclone 4
HPTDC
Wiznet 5300

## Slide 20: DFE module – the workhorse
Unshaped, digitized, LVDS RPC signals from 128 strips (64x + 64y)
16 analog RPC signals, each signal is a summed or multiplexed output of 8 RPC amplified signals.
Global trigger
TDC calibration signals
TCP/IP connection to backend for command and data transfer.

## Slide 21: Soft-core processor
Event data acquisition
Monitoring data acquisition
Command interface
Remote system upgradation
HV control and Monitoring
Read/Write Hardware register access
Flash memory Access
TDC JTAG Access
Wiznet Network Interface
(EP4CE115F780)

## Slide 22: Test jig for DFE production QC

## Slide 23: Calibration module

## Slide 24: ICAL trigger scheme
Insitu trigger generation. Autonomous; shares data bus with readout system
For ICAL, trigger system is based only on topology of the event; no other measurement data is used
Huge bank of combinatorial circuits; Programmability is the game, FPGAs, ASICs are the players
Distributed
architecture

## Slide 25: Trigger criteria

## Slide 26: Trigger system for e-ICAL

## Slide 27: Back-end data concentrator hardware

## Slide 28: High voltage power supply
Output voltage adjustable in the range ± 0-6KV (to generate 0-12KV) with output current up to 2µA.
HV load regulation: better than 0.1% F.S
Output ripple/noise voltage: within 200 mV (p-p).
Adjustable HV Ramp rate 10-1000 Volts/ sec, HV on/off control, HV output read back facility.
HV load current read back facility with a resolution of 5 nA.
Required LV Input supply: 12V @200mA
Ambient fringe magnetic field: 500 gauss

## Slide 29: Status and future outlook
Development and characterisation of large area glass RPC detectors completed.
They are being produced in multiple industries now.
Prototype closed loop gas system is operational, working on the scalable design for the e-ICAL and ICAL.
Design of baseline ICAL detector electronics completed, reviewed.
Prototypes and limited quantities of various components and modules were produced, technologies and vendors identified.
Detectors and electronics are being used in many ICAL prototype detectors, including the m-ICAL which is currently under operation.
Useful experience gained and a number of problems were identified – useful when scaling up production for e-ICAL and ICAL.