## Slide 1: Test results from cryostats for SC Link without thermal shield and ECR
TCC Meeting, 13/09/2018
Amalia Ballarino, 13/09/2018

## Slide 2
With contributions to the WP6a from:
SCD (SC Link, design and assembly of test station, implementation of instrumentation, test program)
CRG (implementation of heaters, gas return lines and control system, participation in test campaign)
TF (operation of test station and contribution to data analysis
EN Design office for detailed execution drawings
Test results presented by P. Retz/G. Willering at WP6a meeting on 19/06/2018

## Slide 3: Background
When the length of the SC Links was significantly reduced (new underground configuration), we considered the possibility of using flexible cryostats with no active cooling. Rationale: reduced total integrated thermal load (W/m for a shorter length) and same enthalpy available (same mass flow rate and same THe).
Main advantage of passive cryostat: lower weight, much easier handling and smaller outer diameter of the SC Link cryostat; lower cost of the SC Link cryostats; simplified design of the DFH cryostats
Main disadvantage of passive cryostat higher static load.
We took the challenge of launching a procurement for 60 m long passive cryostats with target static heat load of 1.5 W/m.

## Slide 4: Industrial procurement
Procurement of six 60 m long semi-flexible cryostats from three companies: Nexans (D), Cryoworld (NL) and Criotec (I). From each company: three cryostats with active shield (4- walls) and three cryostats with passive shield (2-walls)
Cryostats all designed for hosting final multi-cable assembly and meeting heat load, max pressure and pressure drop requirements
Baseline today for WP6a: 4-walls cryostats

## Slide 5: Industrial procurement
A. Ballarino

## Slide 6: Handling of cryostats
Nexan’s cryostats. Delivery @ CERN

## Slide 7: Integration of dummy cable
To make representative pressure drop measurements
(and also: develop techniques for integration of cables,
learn about handling of SC Links)

## Slide 8: Test station in the SM-18
Length of SC Link: 60 m plus terminations

## Slide 9: Test Configuration 1

## Slide 10: Instrumentation
Cernox ribbon integrated with cable, spooled and transported to SM18

## Slide 11: Test configuration 2
3m
Bend NTS

## Slide 12: Mass flow rates up to 10 g/s

## Slide 13: Test performed

## Slide 14: Cryoworld

## Slide 15: Criotec Results
q calculated from sensors, positioned at ends, over 60m
Repeat test with additional sensors showed high heat-load at Return Box
In spite of the higher heat load, no problems with operation (RT all along the length on the outer vacuum pipeO
Images courtesy of Criotec

## Slide 16: Nexans Results
q based on 20m centre section sensors
Internal construction thought to be similar to Cryoworld
Mechanically very rigid; designed to wit stand high pressures

## Slide 17: Comparison with previous CERN SCLinks
CERN report 199308379 by N Delruelle et al
Performance as
rigid lines with shield

## Slide 18: Test results
Low heat load can be achieved
Pressure drop is not an issue (measured less than few mbar with mass flow rates of up to 10 g/s)
ECR has been discussed with CRG and drafted
Proposal: specify a heat load < 1.5 W/m for the Triplets (up to 2.5 W/m could be tolerated)
Cryogenic flow scheme already re-elaborated by CRG – and presented at the least WP6a meeting

## Slide 19: System performance with passive cryostats

## Slide 20: System performance with passive cryostats

## Slide 21
ECR Written
Discussed with CRG and VSC
Ready for being circulated
Change in baseline