## Slide 1: Beyond LHC: Future Circular Colliders Studies in Europe and China
F. Zimmermann, 20th RDMS CMS Meeting, Tashkent
incl. slides from M. Benedikt (CERN) and J. Gao, X. Lou (IHEP) gratefully acknowledging input from FCC coordination group,
global FCC design study team, CEPC/SPPC design study, and all other contributors
Geneva site
Qinhuangdao site
Work supported by the European Commission under the HORIZON 2020 projects EuroCirCol, grant agreement 654305; EASITrain, grant agreement no. 764879; ARIES, grant agreement 730871; and E-JADE, contract no. 645479
http://cern.ch/fcc

## Slide 2
Future Circular Collider study - scope
international FCC collaboration (CERN as host lab) to study:
pp-collider (FCC-hh)  long-term goal, defining infrastructure requirements
~100 km tunnel infrastructure in Geneva area, site specific
e+e- collider (FCC-ee), as potential first step
HE-LHC with FCC-hh technology
p-e (FCC-he) option, IP integration, e- from ERL
~16 T  100 TeV pp in 100 km
HE-LHC

## Slide 3
FCC-ee:
exploration of 10 to 100 TeV energy scale via couplings with precision measurements , ~20-50 fold improved precision on many EW quantities (equiv. to factor 5-7 in mass) (mZ, mW, mtop , sin2 weff , Rb , QED (mz) s (mz mW m), Higgs and top quark couplings)
machine design for highest luminosities at Z, WW, ZH and ttbar working points
FCC-hh:
highest center of mass energy for direct production up to 20 - 30 TeV
huge production rates for single and multiple production of SM bosons (H,W,Z) and quarks
machine design for 100 TeV c.m. energy & int. luminosity 20ab-1 within 25 years
HE-LHC:
doubling LHC collision energy with FCC-hh 16 T magnet technology
c.m. energy 27 TeV 14 TeV x 16 T/8.33T, target luminosity ≥ 4 x HL-LHC
machine design within constraints from LHC CE and based on HL-LHC and FCC technologies
FCC study: physics and performance targets

## Slide 4
FCC-ee basic design choices
follows footprint of FCC-hh, except around IPs
asymmetric IR layout and optics to limit synchrotron radiation towards the detector
2 IPs, large horizontal crossing angle 30 mrad, crab-waist optics
synchrotron radiation power 50 MW/beam at all beam energies
top-up injection scheme for high luminosity
requires booster synchrotron in collider tunnel
double ring e+ e- collider ~100 km

## Slide 5
parameter | Z | WW | H (ZH) | ttbar
beam energy [GeV] | 45 | 80 | 120 | 182.5
beam current [mA] | 1390 | 147 | 29 | 5.4
no. bunches/beam | 16640 | 2000 | 393 | 48
bunch intensity [1011] | 1.7 | 1.5 | 1.5 | 2.3
SR energy loss / turn [GeV] | 0.036 | 0.34 | 1.72 | 9.21
total RF voltage [GV] | 0.1 | 0.44 | 2.0 | 10.9
long. damping time [turns] | 1281 | 235 | 70 | 20
horizontal beta* [m] | 0.15 | 0.2 | 0.3 | 1
vertical beta* [mm] | 0.8 | 1 | 1 | 1.6
horiz. geometric emittance [nm] | 0.27 | 0.28 | 0.63 | 1.46
vert. geom. emittance [pm] | 1.0 | 1.7 | 1.3 | 2.9
bunch length with SR / BS [mm] | 3.5 / 12.1 | 3.0 / 6.0 | 3.3 / 5.3 | 2.0 / 2.5
luminosity per IP [1034 cm-2s-1] | >200 | >25 | >7 | >1.4
beam lifetime rad Bhabha / BS [min] | 68 / >200 | 49 / >1000 | 38 / 18 | 40 / 18
FCC-ee collider parameters: 4 modes

## Slide 6
ttbar 182.5 GeV
4 sextupoles (a – d) for local vertical chromaticity correction and crab waist, optimized for each working point.
Common arc lattice for all energies, 60 deg for Z, W and 90 deg for ZH, tt for maximum stability and luminosity
yellow boxes:
dipole magnets
asymmetric IR optics to suppress synchrotron radiation toward the IP, Ecritical <100 keV from 450 m from IP (e)
FCC-ee asymmetric crab waist IR optics
K. Oide

## Slide 7: CEPC CDR Baseline: 3 operation modes (no top running)
Higgs factory as first piority (fully partial double ring, with common SRF system for e+ and e- beams)
W and Z factories are incorporated by beam swithyard (W and Z factories are double ring, with
independent SRF system for e+ and e- beams)
Higgs factory baseline SR per beam 30 MW to Minimize AC power
economic CEPC baseline design as Higgs factory:
W, Z factories incorporated with the same SRF system hardware by using beam
switchyard to change from Higgs factory and W, Z factories
synchrotron radiation power per beam at Higgs energy is set to 30MW to minimize
AC power consumption
J. Gao

## Slide 8: CEPC CDR Parameters (September 2018)
 | Higgs | W | Z（3T） | Z（2T）
Number of IPs | 2 |  |  | 
Beam energy (GeV) | 120 | 80 | 45.5 | 
Circumference (km) | 100 |  |  | 
Synchrotron radiation loss/turn (GeV) | 1.73 | 0.34 | 0.036 | 
Crossing angle at IP (mrad) | 16.5×2 |  |  | 
Piwinski angle | 2.58 | 7.0 | 23.8 | 
Number of particles/bunch Ne (1010) | 15.0 | 12.0 | 8.0 | 
Bunch number (bunch spacing) | 242 (0.68s) | 1524 (0.21s) | 12000 (25ns+10%gap) | 
Beam current (mA) | 17.4 | 87.9 | 461.0 | 
Synchrotron radiation power /beam (MW) | 30 | 30 | 16.5 | 
Bending radius (km) | 10.7 |  |  | 
Momentum compact (10-5) | 1.11 |  |  | 
 function at IP x* / y* (m) | 0.36/0.0015 | 0.36/0.0015 | 0.2/0.0015 | 0.2/0.001
Emittance ex/ey (nm) | 1.21/0.0031 | 0.54/0.0016 | 0.18/0.004 | 0.18/0.0016
Beam size at IP sx /sy (m) | 20.9/0.068 | 13.9/0.049 | 6.0/0.078 | 6.0/0.04
Beam-beam parameters x/y | 0.031/0.109 | 0.013/0.106 | 0.0041/0.056 | 0.0041/0.072
RF voltage VRF (GV) | 2.17 | 0.47 | 0.10 | 
RF frequency f RF (MHz) (harmonic) | 650 (216816) |  |  | 
Natural bunch length z (mm) | 2.72 | 2.98 | 2.42 | 
Bunch length z (mm) | 3.26 | 5.9 | 8.5 | 
HOM power/cavity (2 cell) (kw) | 0.54 | 0.75 | 1.94 | 
Natural energy spread (%) | 0.1 | 0.066 | 0.038 | 
Energy acceptance requirement (%) | 1.35 | 0.4 | 0.23 | 
Energy acceptance by RF (%) | 2.06 | 1.47 | 1.7 | 
Photon number due to beamstrahlung | 0.1 | 0.05 | 0.023 | 
Lifetime _simulation (min) | 100 |  |  | 
Lifetime (hour) | 0.67 | 1.4 | 4.0 | 2.1
F (hour glass) | 0.89 | 0.94 | 0.99 | 
Luminosity/IP L (1034cm-2s-1) | 2.93 | 10.1 | 16.6 | 32.1

## Slide 9
lepton collider luminosities
total luminosity [1034 cm-2s-1]
ttbar
350-365 GeV

## Slide 10
FCC-ee physics operation model
working point | nominal luminosity/IP [1034 cm-2s-1] | total luminosity (2 IPs)/ yr half luminosity in first two years (Z) and first year (ttbar) to account for initial operation | physics goal | run time [years]
Z first 2 years | 100 | 26 ab-1/year | 150 ab-1 | 4
Z later | 200 | 48 ab-1/year |  | 
W | 25 | 6 ab-1/year | 10 ab-1 | 1 - 2
H | 7.0 | 1.7 ab-1/year | 5 ab-1 | 3
machine modification for RF installation & rearrangement: 1 year |  |  |  | 
top 1st year (350 GeV) | 0.8 | 0.2 ab-1/year | 0.2 ab-1 | 1
top later (365 GeV) | 1.4 | 0.34 ab-1/year | 1.5 ab-1 | 4
total program duration: 14 – 15 years - including machine modifications
phase 1 (Z, W, H): 8 – 9 years, phase 2 (top): 6 years

## Slide 11
FCC-ee luminosity projection

## Slide 12
three sets of RF cavities to cover all options for FCC-ee & booster:
high intensity (Z, FCC-hh): 400 MHz mono-cell cavities (4/cryom.)
higher energy (W, H, t): 400 MHz four-cell cavities (4/cryomodule)
ttbar machine complement: 800 MHz five-cell cavities (4/cryom.)
installation sequence comparable to LEP ( ≈ 30 CM/shutdown)
WP | Vrf [GV] | #bunches | Ibeam [mA]
Z | 0.1 | 16640 | 1390
W | 0.44 | 2000 | 147
H | 2.0 | 393 | 29
ttbar | 10.9 | 48 | 5.4
“Ampere-class” machine
“high-gradient” machine
FCC-ee RF staging scenario
O. Brunner

## Slide 13
5.5 x 24m2
400 MeV, 3 turns,
20 mA, 802 MHz
5-cell 800 MHz cavity, JLAB prototype for both FCC-ee (t-tbar) & FCC-eh
JLAB, Oct 25, 2017
F. Marhauser et al
31 MV/m
@ 2K
seamless 400 MHz single-cell cavity formed by spinning at INFN-LNL
CERN half-cells produced by Electro-Hydro-Forming (EHF) at Bmax
tooling fabricated and successfully tested with an aluminium cavity
Legnaro, Feb 2018
V. Palmieri † C. Pira
† We’re saddened by the sudden death of Vincenzo Palmieri this year
high strain rate technology using shockwaves in water from HV discharge.
EHF investigated for half-cells and seamless Nb&Cu cavities
J.-F. Croteau, EASITrain PhD Student
Regime of Eacc requirements
in LHeC, PERLE, FCC-ee
quench limit
FCC SRF cavity development (examples)
O. Brunner, E. Jensen

## Slide 14
CEPC SRF cavities - production at PAPS

## Slide 15
twin-dipole design with 2× power saving
16 MW (at 175 GeV), with Al busbars
first 1 m prototype
twin F/D quad design with 2× power saving; 25 MW (at 175 GeV), with Cu conductor
first 1 m prototype
low-power low-cost design for FCC-ee magnets
A. Milanese

## Slide 16
chambers feature lumped SR absorbers with NEG-pumps placed next to them.
construction of chamber prototypes in coming months and integration with twin magnets
Vacuum chamber cross section: 70 mm ID with ”winglets” in the plane of the orbit (SuperKEKB-like);
FCC-ee arc vacuum prototyping and integration
R. Kersevan, C. Garion

## Slide 17
SLC/SuperKEKB-like 6 GeV linac accelerating; 1 or 2 bunches with repetition rate of 100-200 Hz
same linac used for e+ production @ 4.46 GeV e+ beam emittances reduced in DR @ 1.54 GeV
injection @ 6 GeV into of Pre-Booster Ring (SPS or new ring) and acceleration to 20 GeV
injection to main Booster @ 20 GeV and interleaved filling of e+/e- (below 20 min for full filling) and continuous top-up
CEPC: 10 GeV linac, no prebooster
FCC-ee injector layout
S. Ogur, K. Oide, Y. Papaphilippou

## Slide 18
Beam energy (GeV) | 45.6 Z | 80 W | 120 ZH | 182.5 ttbar
RF (SR = 100) | 163 | 163 | 145 | 145
Collider cryo | 1 | 9 | 14 | 46
Collider magnets | 4 | 12 | 26 | 60
Booster RF & cryo | 3 | 4 | 6 | 8
Booster magnets | 0 | 1 | 2 | 5
Pre injector | 10 | 10 | 10 | 10
Physics detector | 8 | 8 | 8 | 8
Data center | 4 | 4 | 4 | 4
Cooling & ventilation | 30 | 31 | 31 | 37
General services | 36 | 36 | 36 | 36
Total | 259 | 278 | 282 | 359
FCC-ee el. power consumption [MW]

## Slide 19: CEPC Power for Higgs and Z
266MW
149MW
8x less luminosity than FCC-ee at ~60% the power
2.5x less luminosity than FCC-ee at ~equal power
J. Gao
CEPC power & comparing efficiency

## Slide 20
sketch of FCC-ee physics
EXPLORE 10-100 TeV energy scale (and beyond) with Precision Measurements
DISCOVER a violation of flavour conservation or universality & unitarity
DISCOVER dark matter as «invisible decay» of H or Z (or in LHC loopholes)
DISCOVER very weakly coupled particle in 5-100 GeV energy scale
such as: Right-Handed neutrinos, Dark Photons
ZH cross-section receives a Ecm -dependent correction from H
investigating now : the possibility of reaching 5 observation of Higgs self coupling at FCC-ee:
4 detectors + recast of running scenario
“First Look at the Physics Case of TLEP”, JHEP 1401 (2014) 164;
A. Blondel, ICHEP 2018

## Slide 21
parameter | FCC-hh |  | HE-LHC | HL-LHC | LHC
collision energy cms [TeV] | 100 |  | 27 | 14 | 14
dipole field [T] | 16 |  | 16 | 8.33 | 8.33
circumference [km] | 97.75 |  | 26.7 | 26.7 | 26.7
beam current [A] | 0.5 |  | 1.1 | 1.1 | 0.58
bunch intensity [1011] | 1 |  | 2.2 | 2.2 | 1.15
bunch spacing [ns] | 25 |  | 25 | 25 | 25
synchr. rad. power / ring [kW] | 2400 |  | 101 | 7.3 | 3.6
SR power / length [W/m/ap.] | 28.4 |  | 4.6 | 0.33 | 0.17
long. emit. damping time [h] | 0.54 |  | 1.8 | 12.9 | 12.9
beta* [m] | 1.1 | 0.3 | 0.45 | 0.15 (min.) | 0.55
normalized emittance [mm] | 2.2 |  | 2.5 | 2.5 | 3.75
peak luminosity [1034 cm-2s-1] | 5 | 30 | 16 | 5 (lev.) | 1
events/bunch crossing | 170 | 1000 | 460 | 132 | 27
stored energy/beam [GJ] | 8.4 |  | 1.3 | 0.7 | 0.36
FCC-hh collider parameters

## Slide 22
FCC-hh layout and optics
circumference 97.8 km
two high-luminosity experiments (A & G)
two other experiments (L & B) combined with injection upstream of experiments
two collimation insertions
  betatron cleaning (J)
  momentum cleaning (F)
Extraction/dump insertion (D)
RF insertion (H)
integrated optics for full ring established, beam dynamics studies confirm design goals

## Slide 23
phase 1 (initial):
b*=1.1 m, DQtot=0.01, tta=5 h
250 fb-1 / year
phase 2 (nominal):
b*=0.3 m, DQtot=0.03, tta=4 h
1 ab-1 / year
radiation damping: t~1 h
total integrated luminosity over 25 years of operation O(20) ab-1/experiment - consistent with physics goals
phase 2: Interplay of radiation damping,
luminosity burn-off, controlled transverse blow-up
transition via operation experience,
no HW modification
FCC-hh operation phases

## Slide 24
Baseline:
LHC @ 3.3 TeV
Alternative:
scSPS @ 1.3 TeV
Total of O(5.5 km) superconducting bends in transfer lines from LHC, at 7.2 T
O(6.5 km) normal-conducting bends from SPS, at 1.8 T
FCC-hh injector options
Current baseline: Injection energy 3.3 TeV LHC  Field-swing FCC-hh like LHC
Alternative options: Injection from SPSupgrade around 1.3 TeV
SPSupgrade could be based on fast-cycling SC magnets, 6-7T, ~ 1T/s ramp, cf. SIS 300 design
SPSupgrade would also be an ideal injector for HE LHC (as alternative to the 450 GeV SPS)

## Slide 25
Main development goal is wire performance increase:
Jc (16T, 4.2K) > 1500 A/mm2 50% increase wrt HL-LHC wire
Reduced coil & magnet cross-section
3150 mm2
~1.7 times less SC
~10% margin
HL-LHC
~10% margin
FCC ultimate
5400 mm2
after only one year development, prototype Nb3Sn wires from several new industrial FCC partners (Japan, Korea, Russia) already achieve HL-LHC performance
Conductor activities for FCC started in 2017:
Bochvar Institute (production at TVEL), Russia
KEK (Jastec and Furukawa), Japan
KAT, Korea
Columbus, Italy
University of Geneva, Switzerland
Technical University of Vienna, Austria
SPIN, Italy
University of Freiberg, Germany
  In addition, agreements under preparation:
  Bruker, Germany
  Luvata Pori, Finland
worldwide FCC Nb3Sn program

## Slide 26
short model magnets (1.5 m lengths) built from 2018 – 2022
Russian 16 T magnet program launched by BINP recently
16 T dipole design activities & options
M. Benedikt

## Slide 27
All coil parts, structural components and tooling are available at FNAL
Coil fabrication and the work with mechanical structure are in progress
First magnet test in September 2018
Iron Laminations
AL I-Clamps
Fillers
Axial Rods
End Plates
StSt Skin
15 T dipole demonstrator (US MDP)
A. Zlobin

## Slide 28
Coil fabrication
Winding of the first coil has been completed. Preparation for reaction on-going. All tooling for coil production ready
First ERMC coil winding
Coil Reaction Tool
Coil Impregnation Tool
Aluminum shell
Magnet yoke
Axial rods
Dummy coils
Magnet assembly
Components and tooling ready. Dummy assembly to characterize the structure behavior on-going.
16 T ERMC construction at CERN
D. Tommasini

## Slide 29
FCC 16 T magnet R&D schedule
total duration of magnet program: ~20 years
would follow HL-LHC Nb3Sn program with long models w industry from 2023/24
M. Benedikt, L. Bottura

## Slide 30
HE-LHC integration aspects
integration and design strategy:
development of optimized 16 T magnet, compatible with HE LHC requirements
new cryogenic layout to limit QRL dimension
  LHC tunnel diameter 3.8 m
  working hypothesis for HE LHC design:
  no major CE modifications on tunnel and caverns
  similar geometry and layout as LHC machine & experiments
  maximum magnet cryostat diameter 1200 mm
  maximum QRL diameter 830 mm
V. Mertens, M. Benedikt

## Slide 31
16 T dipole design evolution
Cosine-theta (baseline)
Block-type coils
Common-coils
2015 2017
800 mm 600 mm
Coil optimization and margin 18  14%
Inter-beam distance 250  204 mm
Stray-field < 0.1 T at cryostat
Half-sector cooling instead of full sector (as for LHC)
to limit cross section of cryogenic distribution line
higher heat load and integration limitations:
8 additional 1.8 K refrigeration units wrt. LHC
8 new higher-power 4.5 K cryoplants

## Slide 32
HE-LHC IR layout
triplet lengths:
LHC: 30.4 m
HL-LHC: 41. 8 m
HE-LHC: 56 m (13.5 TeV);
ca. 11 m
for crab cavities
L. van Riesen Haupt

## Slide 33
HE-LHC IR optics & triplet shielding
General optics design work ongoing for HE LHC with focus on: injection (energy), field quality, physical & dynamic aperture, protection
  collision optics
  with b*=0.25 m
l* = 23 m,
TAS 1.8 m long
(as for HL-LHC,
different radius)
rriplet quadrupole design with 2 cm inner tungsten shielding
for 10 ab-1 integral luminosity: 40 MGy peak dose (peak at Q3 can be reduced w addt’l shielding)
J. Abelleira
L. van Riesen Haupt

## Slide 34
Parameter | Unit | SPPC |  |  | FCC |  | 
 |  | PreCDR | “CDR” | “Ultimate” |  |  | 
Circumference | km | 54.4 | 100 | 100 | 100 |  | 
c.m. energy | TeV | 70.6 | 75 | 125-150 | 100 |  | 
dipole field | T | 20 | 12 | 20-24 | 16 |  | 
injection energy | TeV | 2.1 | 2.1 | 4.2 | 3.3 |  | 
#IPs |  | 2 | 2 | 2 | 2 |  | 
luminosity per IP | 1035 cm-2s-1 | 1.2 | 1.0 | - | 0.5 |  | 3.0
norm. emittance | mm | 4.1 | 2.4 | ? | 2.2 (0.44) |  | 
IP beta function | m | 0.75 | 0.75 | - | 1.1 |  | 0.3
beam current | A | 1.0 | 0.7 | - | 0.5 |  | 
bunch separation | ns | 25 | 25 | - | 25 (5) | 25 (5) | 
bunch population | 1011 | 2.0 | 1.5 | - | 1.0 (0.2) | 1.0 (0.2 | 
SR power /beam | MW | 2.1 | 1.1 | - | 2.5 |  | 
SR heat load/ap | W/m | 45 | 13 | - | 30 |  | 
SPPC main parameters
J. Tang

## Slide 35
SppC layout 2017
coexistence ee, pp, ep
two high-luminosity pp experiments
two other experiments for AA & ep
one (combined) collimation insertion
one RF insertion
extraction insertion
injection insertion
greenfield injector chain
circumference: 100 km
J. Gao
J. Gao, X. Lou, J. Tang

## Slide 36
p-Linac: proton superconducting linac
p-RCS: proton rapid cycling synchrotron
MSS: Medium-Stage Synchrotron
SS: Super Synchrotron
ion beams: dedicated linac (I-Linac) and RCS (I-RCS)
SppC injector chain
J. Gao

## Slide 37
Chinese 10-year R&D target
for SPPC collider
SppC: wire from Fe-based HTS*
*discovered at TIT/Japan in 2008

## Slide 38
In October 2016, A consortium for High-temperature superconducting materials, industrialization and applications was formed in China, with participation of major research and production institutions on HTS.
China is actually leading the development of Fe-HTS technology in the world; world-first 100-m Fe-HTS wire was made by CAS-Institute of Electrical Engineering in the last year .
SppC: China-Domestic Collaboration on HTS
J. Gao,
J. Tang,
Q. Xu

## Slide 39
SppC Design of 12-T Fe-based Dipole Magnet
Yoke OD
500mm
Table 1: Main parameters of the cables
Table 2: Main parameters of the strand
Cable | Hight | Width-i | Width-o | Ns | Strand | Filament | Insulation
IRONBASED1 | 8 | 1.5 | 1.5 | 20 | IRON-BASED | FE-BASED | 0.15
IRONBASED2 | 5.6 | 1.5 | 1.5 | 14 | IRON-BASED | FE-BASED | 0.15
IRONBASED3 | 5 | 1.5 | 1.5 | 12 | IRON-BASED | FE-BASED | 0.15
Strand | diam. | cu/sc | RRR | Tref | Bref | Jc@ BrTr | dJc/dB
IRON-BASED | 0.802 | 1 | 200 | 4.2 | 10 | 4000 | 111
One meter of such magnet requires iron-based HTS strand length of 6.08 km
C. Wang, E. Kong (USTC), Q. Xu et al.

## Slide 40
FCC-hh cryogenic beam vacuum system
FCC-hh beam-screen test set-up at ANKA/Germany:
beam tests since June 2017, for prototypes,
confirming vacuum design simulations
X-ray fan
2.5 GeV ANKA/KIT storage ring
synchrotron radiation (~ 30 W/m/beam (@16 T field) (cf. LHC <0.2W/m) ~ 5 MW total load in arcs
absorption of synchrotron radiation at higher temperature (> 1.8 K) for cryogenic efficiency
provision of beam vacuum, suppression of photo-electrons, electron cloud effect, impedance, etc.
ANKA e- photon spectrum
= FCC –hh spectrum

## Slide 41
FCC-hh cryoplants – energy efficiency
BS temperature choice through overall optimisation:
cryoplant power consumption
vacuum system performance
impedance and beam stability
100MW
200MW
300MW
optimum beam screen operation temperature 40 - 60 K
electrical power for beam screen cooling ~100 MW .
L. Tavian, P. Lebrun

## Slide 42
FCC implementation - footprint baseline
present baseline position established considering:
lowest risk for construction
fastest and cheapest construction
feasible positions for large span caverns (most challenging structures)
next step: review of surface site locations and machine layout
J. Osborne, J. Stanyard

## Slide 43
1)
2)
3)
4
1
2
3
4
5
6
CEPC Site Selections
1) Qinhuangdao, Hebei Province（Completed in 2014）
2) Huangling, Shanxi Province（Completed in 2017)
3) Shenshan, Guangdong Province(Completed in 2016)
4) Baoding (Xiong an), Hebei Province (Started in August 2017)
5) Huzhou, Zhejiang Province (Started in March 2018)
6) Chuangchun, Jilin Province (Started in May 2018)
J. Gao

## Slide 44
Item | Huangling | Shenshan | Funing
Project layout |  |  | 
Construction difficulty | Moderate | Relatively difficult | Relatively easy
Funing (100 km)
Huangling (100 km)
Shenshan (100 km)
X. Lou
Notes: Huangling: The site is mainly on the loess plateau. The buried depth of the tunnel and the depth of the shafts are quite different. The construction access layout is relatively simple.
Shen-Shan: The site is mainly the low mountain area. The buried depth of the tunnel and the depth of the shafts are large, and the construction access layout is relatively complicated.
Funing: The site is generally the low hilly areas; underground burial depth is not big; the construction site conditions are better; the construction access layout is relatively simple.

## Slide 45
FCC – tunnel integration in arcs
  FCC-ee FCC-hh
  5.5 m inner diameter
V. Mertens

## Slide 46
  6.0 m width, hosting 5 rings simulatenously
CEPC/SppC – tunnel integration in arcs
J. Gao

## Slide 47
4.5yrs
6.5yrs
Total construction duration 7 years
First sectors ready after 4.5 years
CE schedule studies

## Slide 48
schedule constrained by 16 T magnets & CE
→ earliest possible beam operation dates
FCC-ee: 2039
FCC-hh: 2043
HE-LHC: 2040 (with HL-LHC stop LS5 / 2034)
technical schedule for each of three options

## Slide 49
CEPC Schedule (ideal)
CEPC data-taking starts before the LHC program ends around 2035
earlier than the FCC(hh, ee)
possibly concurrent, but advantageous and complementary to ILC
design issues
R&D items
Pre-CDR
design, funding
R&D program
intl. collaboration
site study
seek approval, site decision
construction during 14th 5-
year plan
commissioning
Time of previous IHEP institutional review
X. Lou

## Slide 50
Global FCC Collaboration
30
Companies
32
Countries
124
Institutes
EC
H2020

## Slide 51
AIBU, Bolu,Turkey Ankara U., Turkey
Aristode U Thessaloniki, Greece
Athens U., Greece
Austrian Inst. of Tech., Vienna, Austria Basel U., Switzerland
Belgrade U., Serbia
Bern U., Switzerland
BINP, Novosibirsk, Russia
Birmingham U., UK
BUAP Universidad, Puebla, Mexico CASE (SUNY/BNL), USA
CBPF, Brazil
CEA Grenoble, France
CEA Saclay, France
CELLS/ALBA, Cerdanyola del Vallès, Spain
CIEMAT, Madrid,Spain
CINVESTAV, Mexico
CSIC, Madrid, Spain CSIL, Milan, Italy CNRS, Paris, France
CNR-SPIN, Genova, Italy
Cockcroft Institute, Daresbury, UK
Colima U., Mexico
UCPH Copenhagen, Denmark
CUNI, Prague, Czech Republic TU Darmstadt, Germany
TU Delft, Netherlands
TU Dortmund, Germany
DOE, Washington, USA
TU Dresden, Germany
Duke U, Durham, USA
EPFL, Lausanne, Switzerland UT Enschede, Netherlands ESS, Lund, Sweden ETHZ, Switzerland
FNAL, Batavia, USA Fraunhofer, Dortmund, Germany Genoa U., Genoa, Italy Geneva U., Switzerland
Giresun U., Turkey
Goethe U. Frankfurt, Germany
GSI, Darmstadt, Germany
GWNU, Gangneung, South Korea
Guanajuato U., Mexico
Hellenic Open U., Patra, Greece
HEPHY, Vienna, Austria
Houston U., USA
ICMAB-CSIC, Bellatera, Spain IFIC-CSIC, Paterna, Spain
IIT Kanpur, India IFAE, Bellaterra, Spain
IFJ PAN Krakow, Poland
INFN, Frascati/Rome, Italy
INP Minsk, Belarus
DESY, Hamburg, Germany
Iowa U., USA
IPM Tehran, Iran
Irvine UC, USA Isik U., Sile, Turkey
Istanbul U., Turkey
Istanbul Aydin U., Turkey
JAI, Oxford, UK
JINR Dubna, Russia
Jefferson LAB, Newport News, USA
FZ Jülich, Germany
KAIST, Yuseong gu, South Korea
KEK, Ibaraki, Japan
KIAS, Seoul, South Korea
King’s College London, UK KIT Karlsruhe, Germany
KU Leuven, Belgium KU, Seoul, South Korea
Korea U. Sejong, South Korea Lancaster U., UK
LAPP, Annecy, France
Liverpool U., UK Lund U., Sweden Malta U, Malta
MAX IV, Lund, Sweden
FCC Collaboration Status
123 collaboration members & CERN as host institute, April 2018

## Slide 52
Melbourne U, Australia MEPhI, Moscow, Russia Michigan U, Ann Arbor, USA
MINES ParisTech, Paris, France MISiS, Moscow, Russia MIT, Cambridge, USA
Naturhistorisches Museum, Vienna, Austria NIKHEF, Netherlands
Northern Illinois U., Dekalb, USA
NC PHEP Minsk, Belarus
Okan U., Istanbul, Turkey Oxford U., UK
Patras U, Greece
Piri Reis, Istanbul, Turkey
PSI, Villigen, Switzerland
Rostock U., Germany
RTU, Riga, Latvia
Santa Barbara UC, USA Sapienza/Rome, Italy
SFTC, Daresbury, UK
Siegen U., Germany
Silesia U., Katowice, Poland
SINP MSU, Moscow, Russia
Stanford U., USA Stuttgart U., Germany
FCC Collaboration Status
123 collaboration members & CERN as host institute, April 2018
Tel Aviv U., Israel
TOBB ETU, Ankara, Turkey
TU Bergakademie Freiberg, Germany
TU Tampere, Finland
TU Vienna, Austria
UAS TW, Austria ULUDAG, Turkey
UNICAL, Cosenza, Italy UNIMAN, Manchester, UK
UNIMI, Milan, Italy UNIROMA3, Rome, Italy
UPC, Barcelona, Spain URJC, Spain
USASK & CLS, Canada
UTOKYO, Tokyo, Japan Wigner RCP, Budapest, Hungary
Wroclaw UT, Poland Wirtschaftsuniversität Wien, Austria
Uzbekistan missing !?

## Slide 53
Scope:
FCC-hh collider
Optics Design (arc and IR)
Cryogenic beam vacuum system design including beam tests at ANKA
16 T dipole design, construction folder for demonstrator magnets
EU H2020 Design Study EuroCirCol
European Union Horizon 2020 program
Support for FCC-hh study
3 MEURO co-funding
Started June 2015, ends in May 2019
Notes: New slide from Davide.
Showing that conductor development is launched at international level, Russia, Japan, (Korea and Europe in preparation)
Underline importance of that development as main cost driver for the hadron collider machine.

## Slide 54
SC wires at low temperatures for magnets (Nb3Sn, MgB2, HTS)
Superconducting thin films for RF and beam screen (Nb3Sn, Tl)
Electrohydraulic forming for RF structures
Turbocompressor for Nelium refrigeration
Magnet cooling architectures
13 Beneficiaries
12 Partners
EASITrain Marie Curie Training Network
I-CUBE
European Advanced Superconductivity Innovation and Training Network
selected for funding by EC in May 2017, started 1 October 2017
Horizon 2020 program
Funding for 15 Early Stage Researchers over 3 years & training
J. Gutleber

## Slide 55
FCC Planning – CDR Production
CDR Concise summary volumes 1 (PH), 2 (hh), 4 (ee), 6 (HE):
  Completion of design work, coherent and consistent; contents for concise volumes by end June 2018
  Overall final editing July – August 2018; Proof reading and approval September – October
  “Print-ready” versions by November 2018
CDR long technical volumes 3, 5, 7:
  Collection of input (from status June 2018) during July – October 2018.
  Overall volume editing November 2018 – January 2019; Proof reading and approval February – March 2019
Cost study based on CDR status (June 2018), other documents for ESU, June - November 2018
M. Benedikt

## Slide 56: CEPC Accelerator from Pre-CDR to CDR
CEPC accelerator CDR completed in June 2018 (released on Spet. 2 2018)
  Executive Summary
  Introduction
  Machine Layout and Performance
  Operation Scenarios
  CEPC Collider
  CEPC Booster
  CEPC Linac
  Systems Common to the CEPC Linac, Booster
  and Collider
  8. Super Proton Proton Collider
  9. Conventional Facilities
  10. Environment, Health and Safety
  11. R&D Program
  12. Project Plan, Cost and Schedule
  Appendix 1: CEPC Parameter List
  Appendix 2: CEPC Technical Component List
  Appendix 3: CEPC Electric Power Requirement
  Appendix 4: Advanced Partial Double Ring
  Appendix 5: CEPC Injector Based on Plasma Wakefield Accelerator
  Appendix 6: Operation as a High Intensity -ray Source
  Appendix 7: Operation for e-p, e-A and Heavy Ion Collision
  Appendix 8: Opportunities for Polarization in the CEPC
  Appendix 9: International Review Report
March 2015
April 2017
Draft CDR for
Mini International
Review in Nov. 2017
CDR International Reviewed June 28-30, 2018, final CDR (accelerator) released on Sept. 2, 2018
J. Gao

## Slide 57
CEPC Path to Realization
Science & Technology is strongly supported by the present central government  it also is a “requirement” for local governments (difference seen in Beijing & Shanghai since 2016)
not difficult to find local support for the site
in March 2018 State Council announced “Implementation method to support China-initiated large international science projects and plans”
  science of matter, evolution of the universe, life science, earth, energy, …
  goal:
    up to 2020, 3-5 preparatory projects; 1-2 construction projects
    up to 2035, 6-10 preparatory projects; ? construction projects
  Ppossible competitors: 50 ideas collected, fusion reactor, space program, brain program, investigation of the Qinghai-Tibet Plateau, CEPC, …
CEPC/IHEP are working with MOST to be included in the roadmap planning, project selection, etc.
X. Lou

## Slide 58
FCC-hh detector – reference design
4 T, 10 m bore solenoid, 4 T forward solenoids, no shielding coil
14 GJ stored energy
rotational symmetry for tracking!
20 m diameter (~ ATLAS)
15 m shaft
~1 billion project
W. Riegler et al.
latest l* = 40 m

## Slide 59
sketch of FCC-hh physics
FCC-hh is a HUGE discovery machine (if nature …), but not only
- Highest center of mass energy → a big step in high mass reach!
ex: strongly coupled new particles up to >30 TeV
Excited quarks, Z’, W’, up to ~tens of TeV
Final word on natural Supersymmetry, extra Higgs etc.. reach up to 5-20 TeV ; Sensitivity to high energy phenomena in e.g. WW scattering
- HUGE production rates for single & multiple production of H,W,Z & quarks
-- Higgs precision tests using ratios to e.g. // /ZZ, ttH/ttZ @<% level
-- Precise determination of triple Higgs coupling (~3% level) and quartic Higgs coupling
-- detection of rare decays H V (V= ,,J/,,Z…)
-- search for invisibles (DM searches, RH neutrinos in W decays)
-- renewed interest for long lived (very weakly coupled) particles.
-- rich top and HF physics program
- Cleaner signals for high Pt physics
-- allows clean signals for channels presently difficult at LHC (e.g. H bb)
M. Magano et al., Physics at a 100 TeV pp collider: CERN Yellow Report (2017) no.3
H at the few percent level

## Slide 60
gHxx | FCC-ee | FCC-hh | FCC-eh
ZZ | 0.22 % | < 1% * | 
WW | 0.47% |  | 
H | 1.6% |  | 
 | 4.2% | <1% | 
Z | -- | 1% | 
ttH | 13% | 1% | 
bb | 0.7% |  | 0.5%
 | 0.8% |  | 
cc | 0.7% |  | 1.8%
gg | 1.0% |  | 
 | 8.6% | 1-2% | 
uu,dd | H ? | H ? | 
ss | H  ? | H  ? | 
ee | ee  H |  | 
HH | 40% | ~3-5% | 20%
inv, exo | <0.55% | 10-3 | 5%
HIGGS PHYSICS
hh, eh precisions assume
SM or ee measurements
Ffor FCC-hh : H ZZ to serve
as cross-normalization
(well measured at FCC-ee)
Higgs couplings gHxx precisions
for ttH, combination of
4% (model dependent)HL-LHC
with FCC-ee will lead to
ttH coupling to  3%...
model independent!
for gHHH investigating now : the possibility of reaching 5 observation at FCC-ee:
4 detectors
+ recast of running scenario
example synergy of FCC-ee/hh/eh

## Slide 61
how to go further – beyond FCC-hh?
muon collider* is back !
3 recent new ideas :
LEMMA m production by e+ annihilation
Gamma factory for e+ generation
full exploitation of FCC complex
*first proposed by Gersh Budker in 1969

## Slide 62
LHeC-class e+ source & e+ acceleration at 45 GeV
(circular/linear options)
e+ ring
100 KW target
m+
m-
isochronous rings
Positron Beam
key challenges
~1011 m / sec from e+e-gm+m-
key
R&D
1015 e+/sec, 100 kW class target, NON destructive process in e+ ring
key challenges
~1013-1014 m / sec
tertiary particle pgpgm:
fast cooling
(t=2ms)
by 106 (6D)
fast acceleration
mitigating m decay
background
from m decay
from US-MAP (2015) to LEMMA scheme (2017)
M. Antonelli, M. Boscolo, P. Raimondi et al.

## Slide 63
high photon energies,
high cross section
W. Krasny
FCC based Gamma Factory could provide >1017 e+/s
“Gamma Factory” based on “PSI”
Compton back scattering at LHC or FCC

## Slide 64
g factory proof-of-principle experiment in the LHC
Pb+81 beam lifetime 38 hours
(and first electrons in the LHC…)
“… this was a HUGE deal! One of the main scientiﬁc advances in the whole of physics this year!”
Dima Budker

## Slide 65
Cost-figure-of-merit versus power-figure-of-merit for future lepton colliders (Jean-Pierre Delahaye)
cost & power efficiency of future lepton colliders

## Slide 66
100 TeV m collider in C=100 km FCC tunnel with B=16 T → L>1034 cm-2s-1
Combining Gamma Factory, LEMMA,
FCC-ee and FCC-hh

## Slide 67
a few conclusions
FCC study develops high-performance energy frontier circular colliders for post-LHC era – input to ESU’19/20
parallel effort in China (CEPC/SppC) – Chinese decision could come within 2 to 5 years
worldwide R&D programs on key technologies: Nb3Sn superconductor, high-field magnets, highly-efficient SC RF
international FCC collaboration growing steadily, many R&D opportunities; all of the community invited to join
FCC concept supports attractive staged long-term strategy for particle physics: FCC-ee → FCC-hh → FCC-mm
highest-luminosity collisions up to very high energies; collider program extending well into the 22nd century

## Slide 68
PARIS
29 / 30 January, 2019
FCC CDR Presentation
Event

## Slide 69
Brussels
24-28 June, 2019
EuroCirCol Final Meeting
FCCWeek 2019
https://indico.cern.ch/event/727555