## Slide 1: Introduction to NSC3
High Performance Computing in High Energy Physics
Sep. 19- 21, 2018 @ CCNU, Wuhan

## Slide 2
华中师范大学
核科学计算中心
Chart: 
| April | August | September
Region 1 | 33.3 | 33.3 | 33.3
Experiments
Phenomenology
Theory
Lattice QCD
pQCD
计算平台至关重要
Lattice QCD(hep-lat)
HIC(nucl-th,hep-ph)
Detector simulation (nucl-exp)
Experimental Data analyses (nucl-exp)
……

## Slide 3
Computing resources not sufficient
for
Research
计算平台性能参数如下：
第一期(2008年)含双路服务器10台，每台含2块Intel至强E5-2620(2.0GHz，6核)CPU, 内存48GB；
第二期（2011年）含双路服务器32台，其中10台每台含2块Intel至强E5620(2.4GHz，4核)CPU,内存24GB；另外22台每台含2块Intel 至强X5650(2.66GHz，6核)CPU,内存16GB；
第三期（2012年）含双路服务器共55台，其中42台每台含2块Intel至强E5-2620(2.0GHz，6核)CPU, 内存48GB；另外13台每台含2块Intel至强E5410(2.33GHz，4核)CPU,内存16GB；
第四期（2014年）含双路服务器共12台，每台含2块Intel至强E5-2640(2.50GHz，6核)CPU, 内存48GB。
Old PC cluster（1216 cores, storage 480TB）
Peak performance： 0.044 PFlops/s

## Slide 4
S: Science
C3: Color 3 -> QCD
High Performance, Low Power Consumption
~100% utilized
N:
Nuclear
计算决定未来！
“道生一，一生二，二生三，三生万物” —- 《道德经》老子 600 BC

## Slide 5: Location of NSC3
North
NSC3

## Slide 6: Scenes back in 2014

## Slide 7: Support from CCNU

## Slide 8: computing room
机房外部

## Slide 9
North
Computer room
~160m2
layout of NSC3
Cooling pipes
& water filters
~ 32m2
Exhibition area ~160m2
Total area
~360 m2
Can be extended to install more racks
Battery room
~ 32m2
Low Voltage
Distribution
Room
~ 27 m2

## Slide 10
Layout of the computing room
可作为计算放置扩展区域
Capacity of 36 Racks
Fire extinguisher
2018：7 racks installed
Liquid Cooling Package
Electricity rack

## Slide 11
1000kVA
400kVA
UPS
Computing Nodes: 7/24 on
UPS: file server and login nodes
file servers & login nodes
computing
nodes
Two circles of
electricity power
A new
transformer

## Slide 12
Strategies of cooling | Cool each rack | Cool each two rows of racks | Cool the room
Layout |  |  | 
Cooling target | IT devices within a rack | IT devices with 1 or 2 rows of racks | whole computer room
Blow distance | 0.1~0.8m | 1.2~3m | 3~15m
Cooling efficiency | High | Medium | Low
Application | High Performance, Green computing | Cloud computing, mixed | Traditional computing room
Cooling strategies

## Slide 13
Temperature distribution
in a typical year of Wuhan
hours
Dry bulb temperature
There are 4516 hours yearly in Wuhan that T < 18℃
51% of the year free cooling is available

## Slide 14
Water Cooling

## Slide 15
Configurations of the GPU cluster
18 GPU nodes,
Maximally 8 nodes per rack
In one GPU node:
8 Volta 100 GPU cards
2 skylake-SP (12 cores)
256 GB DDR memory
2 HBA cards
In total:
144 GPUs
432(288) CPU cores
500 + 500 TB storage
GPU node interconnected
via EDR Infiniband

## Slide 16
8 Volta 100 NVLINK in one node

## Slide 17: LQCD Benchmarks
HISQ, 483x12

## Slide 18
June, 2018
NSC3
ranks 466 in Top500 list
and 268 in Green500 list
https://www.top500.org/list/2018/06/?page=5
https://www.top500.org/files/green500/green500_top_201806.xls
“Research” & “Academic” Institutes in China listed in Top 500

## Slide 19
Chart: PFlops/s
| 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025
Speed | 2 | 3 | 3 | 3 | 4 | 5 | 5 | 5
Plans for the near future
LQCD: QCD phase structure, Transport coefficients…
Hydro simulations
STAR/ALICE/LHCb data analyses
…
Programs to be determined by a committee
Domestic and international collaborations are welcome

## Slide 20
Thanks!