## Slide 1
Mini stave Thermal Finite Element Analysis
Boping Chen, Chunhui Chen, William Heidorn, Shuaiyan Kang, Soeren Prell, Roy Mckay, Jie Yu
JAN 18, 2019

## Slide 2: Mini stave with dummy PCB
Features: A 3-module long stave ~300 mm, design is similar to the normal 14-module stave
Two dummy PCBs glued on EOS card region
Seven resistors ( ~0.1 ohm) and five thermistors on each PCB
Resistors are used for simulating heat dissipation from chips on PCB
Objective: Do measurements using IR imaging and compare with FEA simulation

## Slide 3
What is Finite Element Analysis (FEA)?
FEA is a simulation method first developed in 19th century which is now widely used in civil engineering and aerospace. FEA gives the prediction of how a part behaves under given conditions. For example, it offers numerical approach to heat diffusion problems governed by complicated partial differential equations.
Mesh, consisting of minions of fine elements, is the fundamental of FEA simulation. Each element is calculated separately and then combined together to give final result of a model.

## Slide 4: Mini stave Model
One “meshed” EOS foam
Element size ~1mm3
U-bend foam and bus tape currently are not included

## Slide 5: Mini stave Model
EOS foam
L facing shell
PCB
X-Y view of the mini stave model (upper parts not shown)
Polyimide surface
Pipe foam
Cooling pipe
Parts are modeled individually then assembled together

## Slide 6
Mini stave surface temperature (master)
Ambient T at + 20C; surface to surface conductivity ;
pipe inner surface T at -35C; load on PCB resistors (in backup);

## Slide 7
Mini stave surface temperature (slave)

## Slide 8
Surface temperature across stave
Top PCB surface T
Top L shell surface T

## Slide 9
Next:
Compare the FEA simulation results with mini stave temperature measurement.

## Slide 10
Back up : Load for PCB resistors
For LHSS & LHSM side:
, each 0.169W(0.13V, 1.3A) 0.1W(0.1V, 1A)
For LHSS Only:
// ; // each 0.144W(0.12V,1.2A)