Calorimeter Slow Control
ECS Workshop
Thursday 29th November 2018
Frédéric Machefert
On behalf of the calorimeter upgrade group

---
Reminder of the LHCb calorimeters
1. The LHCb calorimeter system is based on the SPD/PS, ECAL and HCAL
2. Requirements :
  1. Energy/position measurements
  2. Particle id for g, electrons, hadrons
  3. Present L0 and futur LLT inputs
    1. almost no spill-over
    2. fast response
same electronics
same crates
Calibration
Power supply
Front-end Crates
Power Supply
Scintillating Pad Det (SPD)
Preshower (PS)
Scint. Pad + Fibres+ MAPMT
6016 cells each
ECAL
Shashlik (Pb-scint.)
6016 cells
HCAL
Tiles (Iron-scint.)
1488 cells

---
Reminder of the LHCb calorimeters
1. The LHCb calorimeter system is based on the SPD/PS, ECAL and HCAL
2. Requirements :
  1. Energy/position measurements
  2. Particle id for g, electrons, hadrons
  3. Present L0 and futur LLT inputs
    1. almost no spill-over
    2. fast response
same electronics
same crates
Calibration
Power supply
Front-end Crates
Power Supply
Scintillating Pad Det (SPD)
Preshower (PS)
Scint. Pad + Fibres+ MAPMT
6016 cells each
ECAL
Shashlik (Pb-scint.)
6016 cells
HCAL
Tiles (Iron-scint.)
1488 cells

---
Key points of the upgrade
1. New design of the Front-end electronics
  1. The calorimeter data will be sent @ 40 MHz to the upgraded-HLT / PC-farm
  2. Reduction of the PMT gain (factor 5 or 2.5) to reduce the integrated current
  3. The calorimeter will provide the necessary information to make the LLT decision
2. The SPD/PS system is removed
  1. Not so important after L0 disappears
  2. Particle identification is affected
  3. Easier calibration of the ECAL/better resolution

---
What will change ?
1. A fraction of the calorimeter system will not change :
  1. We will use the same crates
    1. Maraton PS will be kept (simply adaptation of the Voltage values)
    2. Turbine will be kept (unless replaced by another type)
  2. The CS source will be maintained
    1. Essentially no modifications
2. A fraction will be slightly modified (but affects the SC)
  1. HV/Calibration/Monitoring
    1. The Specs mezzanines will be replaced by GBT-SCA mezzanines
    2. The new GBT-SCA mezzanines receive the signals from a distribution board
3. A fraction is completely modified
  1. Front-end electronics crates are completely upgraded

---
Major developments
1. Mainly concerns the electronics
  1. New front-end electronics
    1. 278 FEB (including spares)
      1. Prototypes of the analog and digital parts have been designed
      2. FEB prototypes equipped with ICECAL have been tested intensively
        1. Firmware developments on the final version
        2. Integrate the final components (optical links, etc...)
    2. 21 Control boards (including spares)
      1. Prototype has been tested and firmware is being developped
      2. Final version reached
  2. Electronics for the HV control, monitoring and calibration
    1. Keep a large fraction of the present electronics
      1. Modify 2 mezzanine boards (control and ECS mezzanines)
    2. Design a GBT fanout (optical link → elinks)
  3. Firmware development (microcode) for the TELL40
    1. Event building and distribution of the events to the farm

---
Prototype of the Front-End Board
1. The Front-end board determines several quantities
  1. The Et for each calo cell based on the charges provided by the PMTs
  2. The max Et 2x2 cluster in the region corresponding to a FEB
  3. The position of this cluster
  4. The Et sum of the cells corresponding to a FEB
  5. The multiplicity
    1. Number of cells beyond a certain threshold (loaded by ECS) in the region corresponding to a FEB
2. The relevant quantity for the calculations is the Et = E sinθ
3. Obtained by properly tuning the HV of the PMT (→direct ADC Et measurement)
GBT-SCA

---
Control Board
Rear
Front
DC-DC converter
GBTx
VTRx
6U backplane connections
IGLOO2
FEBs delach. Info
ECS distribution to up to 16 GBT-SCA
GBT-SCA
3U backplane connections
Clock
TFC command

---
The ECAL regions and the crate corrrespondence

---
The Racks for the Calo - ECAL
L3B02
L3B03
L3B01
L3B04
Side C
L3B12
L3B13
L3B11
L3B14
Side A

---
ECAL C side

---
ECAL A side

---
HCAL C side

---
HCAL A side

---
Slow control for the DAQ
1. A rack is made of
  1. One or two crates
  2. A crate contains
    1. Up to 16 FEB
    2. One single 3CU board
  3. The FEB has ONLY DAQ fibres
  4. The SC fibres are connected to the 3CU
  5. Each board (3CU or FEB) is equipped with a GBT-SCA.
  6. A crate may have up to 17 GBT-SCA
  7. The GBT-X of the 3CU is ONLY used to access (e-links) up to 17 GBT-SCA
1. ECAL is made of 2 x 7 crates - HCAL is made of 2x 2 crates
2. One single bi-directional link per crate

---
3CU config
Protocol	Nr Channels	Nr devices per channel	Access pattern per device
I2C	1	1	366 reg 1 bytes (config – write/read) / GBT-X : part of the configuration burnt
JTAG	1	1 (chain)	FPGA config - write/read
SPI	-		NA
ADC	-		NA
DAC	-	-	NA
GPIO	-	-	NA
GPIO Interrupts	-	-	NA

---
FEB config
Protocol	Nr Channels	Nr devices per channel	Access pattern per device
I2C	1	4	4 x 366 reg 1 bytes (1463 bytes) (config – write/read)
JTAG	1	9	8 x FE-FPGA firmware loading (not at configuration) / 1 Trig Seq FPGA firmware loading (not at configuration)
SPI	17	1	8 x 45 reg of 2 bytes for FE / 8 x 16 reg of 2 bytes for ICECAL / 30 reg of 2 bytes Trig Seq
ADC	-	-	-
DAC	1	4	Config
GPIO	-	-	NA
GPIO Interrupts	-	-	NA

---
Yuri
Upgrade DCS
The High Voltage, Monitoring and Control systems of the Hadronic and Electromagnetic calorimeters are essentially slow control based, and therefore are independent on data taking.
 The “intelligent” components of the present CALO DCS based on SPECS bus are:
HV-LED boards (standalone);
integrator readout boards (INTEG) (HCAL PMT anode currents) (standalone);
LEDTSB boards (installed in the readout crates, 9U).
Thanks to their modular design, they do not need full replacement, but can be just modified for the Upgrade: the basic components (incl. motherboards) can be kept, while the communication mezzanines should be replaced by new ones, based on the GBT protocol.
Control mezzanines will also be replaced to new ones, based on IGLOO2, to enhance functionality.
Will need additional E-Link Distribution boards (GBTx based) - ELDM

---
Upgrade DCS
Each of the HV-LED, INTEG and LEDTSB have a SPECS and Control mezzanines
A HV-LED module is shown as an example.
Old SPECS slave mezzanine
To be replaced by a GBT-SCA based interface.
Old Control mezzanine based on ACTEL ProASICPLUS series FPGA. Same for HV-LED, INTEG and LEDTSB, but with different f/w
Will be also replaced, in order to be able to extend functionality, by a mezzanine based on Microsemi IGLOO2.

---
design considerations – ELDM board
ELDM board
GBTx based , optical line → several e-links
in functionality very much ressembles the existing CERN VLDB board
design is based on VLDB
will use VTRx
significantly simplified – we do not need on-board GBT-SCA, DC-DC converters can be replaced by linear regulators, etc...
two versions
standalone for HV-LED and Integrator readout
crate (9U) mounted – for LEDTSB
can adopt one PCB design for two versions
ELDM board

---
Control and SCA mezzanines
Microsemi M2GL010-1FGG484 can be used in the control mezzanines for HV-LED and INTEG boards; for LEDTSB (with more complicated f/w) M2GL025-1FGG484 will be used.
two versions of the control mezzanine
Also, two versions of the SCA mezzanine, for LEDTSB (I2C needed) and for HV-LED & INTEG (I2C not needed)
Communication protocol (s):
in the old (SPECS) version – Parallel Bus
with GBT: the Parallel Pus can be emulated with GPIO, but this looks a bit ugly
migration to SPI!
Also, for LEDTSB the I2C is used
new Control mezzanine
GBT-SCA mezz. HV & INTEG
GBT-SCA mezz.
LEDTSB

---
Inventory
	HV-LED	INTEG	LEDTSB
ECAL	34	-	8
HCAL	8	4	2
64 control mezzanines
46 “HV-LED” version (with M2GL010-1FGG484) + 6 spares
10 “LEDTSB” version (with M2GL025-1FGG484) + 2 spares
64 GBT-SCA mezzanines
56 + 8 spares
12 ELDM boards
6 “standalone” version +1 spare
4 “crate” version +1 spare
GBTx	12
GBT-SCA	64
VTRx	12

---
ECS – general considerations
the ECAL and HCAL remain the same – therefore the general structure of the HV and LED systems is expected to remain the same.
we would like to keep if possible the “top level” logics of the HV-LED system
it continuously reads out the DAC outputs with an ADC, compares with recipe values, corrects in case of a discrepancy
it performs automatic HV recipe updates between fills
of course with GBT-based read/write libraries

---
HV-LED boards
total of 42 boards
communication protocol: Parallel Bus SPI
each HV board contains 216 DAC channels: 200 for HV settings and 16 for LED flash magnitude settings (logically similar)
each channel: two registers 12 bits
DAC setting to write (or read back)
ADC reading of each DAC output
+ ~20 various control registers common for the whole board
total of 42×216×2 ~ 20k HW registers (16-bit)

---
Integrator Readout (INTEG) board
total of 4 boards
communication protocol: Parallel Bus SPI
each INTEG board has 13 measurement inputs
each input reads out up to 40 12-bit ADC readings
and has 1 register for measurement range settings (16-bit)
+ ~20 various control registers common for the whole board
total of 4×13×41 ~ 2200 HW registers

---
LEDTSB board
total of 10 boards
communication protocol: Parallel Bus SPI + I2C
each LEDTSB board control 64 LED timing channels.
each channel has a delay value (16 bit I2C + 16 bit SPI registers)
and a firing sequence (64 bits, SPI = 4 registers)
+ ~20 various control registers common for the whole board
total of 10×64×4 + 10×64×1 = 3200 registers SPI and 10×64×1 registers I2C

---
Definition of the registers of the FEB

---
First sketch of FEB panel

---
First sketch for a crate