## Slide 1: Direct Vlasov solvers – part II
Nicolas Mounet, CERN/BE-ABP-HSC
Acknowledgements: Sergey Arsenyev, Xavier Buffat, Giovanni Iadarola, Kevin Li, Elias Métral, Adrian Oeftiger, Giovanni Rumolo

## Slide 2: Direct Vlasov solvers
Part I
Introduction: collective effects
Motivation for Vlasov solvers
Vlasov equation historically, and in the context of accelerators
Transverse impedance and instabilities
Building of a simple Vlasov solver for impedance instabilities
Part II
Compact way to present the theory: Hamiltonians & Poisson brackets
Upgrade of part I theory to obtain Sacherer integral equation
Solving Sacherer equation – convergence
Benchmarks & examples of application of Vlasov solvers

## Slide 3: Introducing Hamiltonians
Some of the analytical work shown in part I can be made simpler by using Hamiltonians: the (conservative) system under study is governed by the Hamiltonian
Coordinates and momenta go in pair, and obey Hamilton’s equations: for example in the vertical plane
This does not introduce any additional physics, it just makes part of the derivation easier, more efficient and more elegant.
For more details on Hamiltonians, see W. Herr’s lecture in this CAS (14/11): https://indico.cern.ch/event/759124/contributions/3148186/attachments/1748350/2838297/ham1.pdf

## Slide 4: Vlasov equation with Hamiltonians
Going back to our simple Vlasov solver in 2D:
Vlasov equation then becomes … and this is completely general.
Going back to our simple Vlasov solver in 2D:
Vlasov equation then becomes … and this is completely general.
This is simply !
Reminder: Poisson brackets ( positions, momenta)
(see W. Herr’s CAS lecture on 14/11/2018)

## Slide 5: Perturbation
In any Vlasov solver using perturbation theory we look for a distribution function of the form
is the solution of the perturbed Hamiltonian
Stationary distribution for the Hamiltonian without impedance.
Perturbation of the stationary distribution, of first order
First order perturbation of the Hamiltonian, here from impedance.
Unperturbed Hamiltonian

## Slide 6: Linearized Vlasov equation using Poisson brackets
Second order
=0 since is solution of Vlasov eq. for
Only remaining terms
Isn’t that exactly what we did – somewhat more painfully – during part I?

## Slide 7: Linearized Vlasov equation using Poisson brackets
This is completely general for any Hamiltonian system within linear perturbation theory, up to the first order in the perturbation.
Poisson brackets are conserved within any canonical transformation of coordinates , i.e. any transformation for which there is:
  preservation of Hamilton’s equations,
  equivalently, symplecticity of the Jacobian : with
  Note that symplecticity entails

## Slide 8: Application to the derivation of part I
The transformation is symplectic:
and we get (see appendix)

## Slide 9: Hamiltonian of our simple Vlasov solver (part I)
For our simple Vlasov equation in part I we had
which corresponds to the Hamiltonian
For our simple Vlasov equation in part I we had
which corresponds to the Hamiltonian

## Slide 10: Application to our simple Vlasov solver (part I)
It’s slightly easier, and less prone to error, than what we did in Part I:
In coordinates, the linearized Vlasov equation
gives immediately
Reminder:

## Slide 11: Building a Vlasov solver: method outline
Outline of part I
New outline
Write Hamiltonian
Choose coordinates
Write stationary distribution
Introduce perturbation
Use equations of motion
Simplify and linearize Vlasov equation
Transform coordinates
Decompose perturbation
Reduce number of variables
Write impedance force
Final equation
Write stationary distribution
Introduce perturbation
Use equations of motion
Simplify and linearize Vlasov equation
Transform coordinates
Decompose perturbation
Reduce number of variables
Write impedance force
Final equation
Write stationary distribution
Introduce perturbation
Use equations of motion
Simplify and linearize Vlasov equation
Transform coordinates
Decompose perturbation
Reduce number of variables
Write impedance force
Final equation
Write Hamiltonian
Choose coordinates
Write stationary distribution
Write linearized Vlasov equation
Decompose perturbation
Reduce number of variables
Write impedance force
Final equation

## Slide 12: A more elaborate Vlasov solver
Let’s try to relieve some assumptions of the Vlasov solver of part I:
  Impedance is the only source of instability considered, and gives the EM force arising from the interaction of the beam with the resistive or geometric elements around it,
  only vertical plane, with position and “momentum” (using for convenience rather than )
  purely linear, uncoupled optics in transverse, within smooth approximation,
  no longitudinal motion, i.e. essentially rigid bunches in z,
  chromaticity ,
  Phase space distribution function is then
Let’s try to relieve some assumptions of the Vlasov solver of part I:
  Impedance is the only source of instability considered, and gives the EM force arising from the interaction of the beam with the resistive or geometric elements around it,
  only vertical plane, with position and “momentum” (using for convenience rather than )
  purely linear, uncoupled optics in transverse, within smooth approximation,
  no longitudinal motion, i.e. essentially rigid bunches in z,
  chromaticity ,
  Phase space distribution function is then
But we still neglect any effect from the transverse plane on the longitudinal motion.

## Slide 13: Hamiltonian
We add linear longitudinal motion (see A. W. Chao, Physics of Collective Beam Instabilities in High Energy Accelerators, John Wiley & Sons (1993), chap. 6):
remains as defined previously
and is still assumed to be an invariant, despite the coupling introduced by chromaticity approximation (typically done, e.g. in Chao’s book).
Synchrotron angular frequency
Hamiltonian
Slippage factor

## Slide 14: Transformation of coordinates
In transverse: ,
In longitudinal: , , ,
which is a canonical transformation (symplecticity checked in appendix). Then the Hamiltonian reads:
Hamiltonian
Coordinates

## Slide 15: Stationary distribution
The new unperturbed Hamiltonian
admits as stationary distribution
Hamiltonian
Coordinates
Stationary distribution

## Slide 16: Linearized Vlasov equation
with
We get:
Note: from our initial assumption that the transverse plane does not affect the longitudinal one, we have neglected , as in Chao’s book.
Hamiltonian
Coordinates
Stationary distribution
Linearized Vlasov eq.
Reminder:

## Slide 17: Writing the perturbation
We assume again a single mode of angular frequency , and we introduce for convenience (no need to be a canonical transform at this stage)
Then we decompose this mode using a Fourier series of the angle and another one for the angle :
Hamiltonian
Coordinates
Stationary distribution
Linearized Vlasov eq.
Perturbation decomp.
Additional phase factor (that we are allowed to put here without loss of generality) – will appear later to be very convenient
→ headtail phase factor

## Slide 18: Reducing the number of variables
Injecting the perturbation into Vlasov equation, we can simplify it even more:
Hamiltonian
Coordinates
Stationary distribution
Linearized Vlasov eq.
Perturbation decomp.
Reduction variables
Injecting the perturbation into Vlasov equation, we can simplify it even more:
As in part I, term by term identification leads to
and the assumption , gives
This is where we use this factor to simplify the term in brackets.

## Slide 19: Reducing the number of variables
Hamiltonian
Coordinates
Stationary distribution
Linearized Vlasov eq.
Perturbation decomp.
Reduction variables
Pushing further the computation gives:
Depends only on and
Depends only on
the ratio must be a constant.

## Slide 20: Reducing the number of variables
Hamiltonian
Coordinates
Stationary distribution
Linearized Vlasov eq.
Perturbation decomp.
Reduction variables
This gives the transverse shape of the perturbative distribution as in part I :
Putting the proportionality constant inside :
Only the and dependencies remain to be dealt with.

## Slide 21: Force from impedance
Hamiltonian
Coordinates
Stationary distribution
Linearized Vlasov eq.
Reduction variables
Impedance force
Compared to part I, one “simply” puts the additional longitudinal dependence:
and one can simplify this as in part I, using in addition:
Bessel function
Perturbation decomp.

## Slide 22: Force from impedance
Hamiltonian
Coordinates
Stationary distribution
Linearized Vlasov eq.
Reduction variables
Impedance force
In the end, defining the coherent tune of the mode , we get:
Perturbation decomp.

## Slide 23: Sacherer integral equation
Hamiltonian
Coordinates
Stationary distribution
Linearized Vlasov eq.
Reduction variables
Impedance force
Plugging everything back into Vlasov equation:
We can get rid of by integrating both sides with , and using again (here is any constant)
Final equation
Perturbation decomp.

## Slide 24: Sacherer integral equation
Hamiltonian
Coordinates
Stationary distribution
Linearized Vlasov eq.
Reduction variables
Impedance force
In the end, doing as in part I the approximation (smoothness of impedance and Bessel functions), we get the famous equation:
Final equation
Perturbation decomp.

## Slide 25: Solving Sacherer integral equation
They are various options to solve the integral equation:
Consider a simple and easy to solve longitudinal distribution , e.g. an airbag model (see A. Chao’s book).
Discretize as a superposition of airbag models (as in the NHTVS).
Integrate with and solve for (as in Laclare’s approach).
Decompose and over a basis of orthogonal polynomials such as Laguerre polynomials and compute the integrals involving Bessel functions analytically, as in MOSES and DELPHI:
, and constants to be adjusted

## Slide 26: Solving Sacherer integral equation
In the end one typically obtains an eigenvalue problem:
In the end one needs to diagonalize the matrix , which can be done numerically in many ways (e.g. Python, MATLAB®, Mathematica® , C, etc.)
The matrix being infinite in principle, the problem of truncation is the most important (and essentially the only) numerical issue: truncation sets the number of possible modes considered, and convergence has to be checked for each case.
Eigenvectors: e.g. Laclare’s , or coefficients of the decomposition over Laguerre polynomials, or coefficients of the discretization over airbag rings, etc.
Eigenvalue looked for: angular frequency shift of the mode
Kronecker delta:
Matrix, to be computed analytically

## Slide 27: Benchmarks
Vlasov solvers have been heavily benchmarked w.r.t. multi-particle simulations: here HEADTAIL (multi-particle simulation) vs. Laclare’s Vlasov approach, for LHC coupled-bunch instabilities vs. chromaticity

## Slide 28: Benchmarks
HEADTAIL vs MOSES (Vlasov solver), for the SPS transverse mode coupling instability:
From B. Salvant’s PhD thesis [EPFL no4585 (2010)]
Vlasov solvers and multi-particle compare very well, provided they are used in the same situation (and are well converged!)

## Slide 29: Applications – LEP TMCI with damper
Impedance model: two broad-band resonators (RF cavities + bellows), the rest is relatively small (<10%) [G. Sabbi, 1995].
experimental tune shifts and TMCI threshold (from simple formula) well reproduced,
TMCI threshold slightly less than 1mA.
Transverse feedback damper: several ideas and trials in LEP
reactive feedback (prevent mode 0 to shift down and couple with mode -1) → not more than 5-10 % increase in threshold, despite several attempts and models developed [Danilov-Perevedentsev 1993, Sabbi 1996, Brandt et al 1995],
resistive feedback, first found ineffective [Ruth 1983], tried at LEP but never used in operation.

## Slide 30: Applications – LEP TMCI with damper
Instability threshold vs. chromaticity Q’ and damper gain (up to 10 turns) with DELPHI Vlasov solver:
Resistive damper: one cannot do better than the ”natural” (i.e. without damper) TMCI threshold.
Reactive damper: one can do a little better than the ”natural” TMCI.
→ seems to match (qualitatively) LEP observations.

## Slide 31: Applications – LHC
Predicting the octupole instability threshold vs. chromaticity Q’ and damper gain, with DELPHI:
… and we can also plot the respective contributions of each machine elements (essentially collimators):

## Slide 32: Direct Vlasov solvers – summary part II
We have revisited the theory exposed in part I, introducing Hamiltonians and Poisson brackets to ease up the analytical work.
We have derived Sacherer integral equation within this framework, re-introducing the longitudinal plane.
We went through a few ways to solve Sacherer integral equation, and how to deal with the associated eigenvalue problem.
Finally we have shown benchmarks and applications of Vlasov solvers in CERN synchrotrons (LEP, SPS, LHC).

## Slide 33
Appendix

## Slide 34: Symplectic transformations
The transformation is symplectic:
, , ,
and we get

## Slide 35: Symplectic transformations
The transformation is symplectic:
, , ,
and we get