## Slide 1: Stopping Protons Analysis

## Slide 2: goal
To study stopping protons in the SuperFGD using data from the Aug/Sep test beam, analyzing where protons stop in the detector.
By considering the three types of MPPCs separately, build a distribution of the energy deposited in the last cell the proton reaches.
Use the shape of the distribution to check whether there is a saturation effect.

## Slide 3: MPPCs in the detector
MPPC III
MPPC I
15
23
0
47
Beam
24
X
Z
MPPC II

## Slide 4: Steps
dE/dx
Event Selection.
Treat MPPCs separately.
Obtain relative dE/dx from end point of each event.
Build histogram for energy deposited in the last cell.

## Slide 5: Data Sample
0.8 GeV/c Protons.
Magnet ON, 135 A.
Default HG, default LG (55, 55).
Proton trigger ON.

## Slide 6: 1. Energy deposition
Code by Sasha

## Slide 7: 2. Event selection
Need to consider different event scenarios.
Which to include, which to discard.

## Slide 8: No stop
Cut: No energy deposited in last layer (Z=47)

## Slide 9: meaningless events
Cut: Energy deposited at the peak > 250 p.e.

## Slide 10: Discontinuities
Cut: Before the peak, max number of allowed layers with ZERO deposited energy is 2.

## Slide 11: Scatterings, sometimes leaving the detector?
Cut: For the front (XY) view, stdDevX and stdDevY both < 1.0

## Slide 12: Multiple tracks
Eliminated by previous cut.

## Slide 13: First round of applied cuts
Energy deposited at the peak > 250 p.e.
No energy deposited in last layer (Z=47)
Before the peak, max number of allowed layers with ZERO deposited energy is 2.
For the front (XY) view, stdDevX and stdDevY both < 1.0
From 4525 Events → 1908 Events (42% left)

## Slide 17
Notes: Plots of the cell where protons stop (cell with max E) – Before cuts were made to remove events stopping at the very edges of the detector

## Slide 18: Events at the sides of the detector

## Slide 19: Events that may have escaped the detector
Low energy deposition

## Slide 20: Cuts to eliminate events
XatMax != 0 or 23
YatMax != 0 or 7
1908 events → 1199 events (37% lost)

## Slide 25: Next
Take a sample with 0.5 GeV/c protons to get more events stopping in the first half of the detector.
  → more statistics for MPPCII and MPPCIII
Do the ADC → p.e conversion outside the Stopping Proton code then test the code with the new branches.