## Slide 2: Handling and analysis of radiation data sets, the advantages of automated calculations and fast accessibility of radiation measurements
Kacper Bilko
(EN-EA-PE, Monitoring and Calculation Working Group)

## Slide 3: Dose detection and analysis (LHC BLMs)
MCWG’s analysis
Losses
Dose rate from CALS
LHC parameters
Other input
...
Accelerator operation leads to continuous slight losses, thus the radiation.
Ionising radiation is detected by Beam Loss Monitoring system.
Although it is not the primary purpose, can be used as distributed dosimetry system

## Slide 4: Dose detection and analysis (LHC BLMs)
MCWG’s analysis
Losses
Dose rate from CALS
LHC parameters
Other input
...
Accelerator operation leads to continuous slight losses, thus the radiation.
Ionising radiation is detected by Beam Loss Monitoring system.
Although it is not the primary purpose, can be used as distributed dosimetry system
Data from >3500 BLMs used 
HUNDREDS OF GB
of data to analyse

## Slide 5: Limitations in the past…
Every radiation request handled manually  slow, time-consuming
Slow access to CERN Accelerator Logging Service (CALS) via Timber Timber  processing (i.e. “excel”)  results
Usage of the non-offset corrected data
 BLM beam-not-present baseline contribution to the dose
Overestimations for low dose environments
(ARC sections)
So sluggish!
Download hourly integrated data via Timber (manually)
Summing
Providing the results
Took ages to obtain results

## Slide 6: Limitations in the past…
Every radiation request handled manually  slow, time-consuming
Slow access to CERN Accelerator Logging Service (CALS) via Timber Timber  processing (i.e. “excel”)  results
Usage of the non-offset corrected data
 BLM beam-not-present baseline contribution to the dose
Overestimations for low dose environment
(ARC sections)
So sluggish!
Download hourly integrated data via Timber (manually)
Summing
Providing the results
Took ages to obtain results
Manual, slow, time-consuming, inconsistent
Not efficient!
Reliable analysis impossible…
How to
improve it?
The only solution: AUTOMATION

## Slide 7: How to automate?
Technologies
Developed tools
Hardware
Automation
Physics
Ideas
Algorithms
Software

## Slide 8: Automation of the analysis
Data downloading
Data processing
Data analysis
BLM data from CALS
Offset correction
Integration
Data filtering
Beam modes contribution
Daily downloading
Data saved to the local database (DB) ensure rapid access,
  Online dashboard
  Daily PDF reports
  Annual doses for all BLMs with BM contribution
Dedicated
General
  Anomalies:
    Identification
    Monitoring
  User requests
Fully automated

## Slide 9: Data downloading
Download accelerator parameters
Save to local DB
Save to rapid and efficient local database  cross platform,
Download BLM data
LOSS_RS12 (dose rate averaged over ~ 84 s integration time)
From ~3600 BLMs
Intensities
Beam modes
Beam present flags
Different accelerator parameters (fill number, ...)
Easy access by all MCWG users  no need to store or download data on multiple workstations,
Not only automated,
But also parallelised
Daily basis

## Slide 10: Data processing
Data filtering
Offset correction
Save to local DB
Consider periods only when beam was in the LHC (interval)
Offsets, fill-by-fill doses, BM contributions, times are saved to DB
Integration
Each BLM separately,
Fill-by-fill basis,
Besides integration, calculate contribution of different beam modes,
Subtract beam-not-present baseline from the data.
34 188 296
BLM intervals in the DB

## Slide 11: Data processing
Data filtering
Offset correction
Save to local DB
Consider periods only when beam was in the LHC (interval)
Offsets, fill-by-fill doses, BM contributions, times are saved to DB
Integration
Each BLM separately,
Besides integration, calculate contribution of different beam modes,
Fill-by-fill basis,
Subtract beam-not-present baseline from the data.
No beam
Beam present

## Slide 12: Data processing
Data filtering
Offset correction
Save to local DB
Consider periods only when beam was in the LHC (interval)
Offsets, fill-by-fill doses, BM contributions, times are saved to DB
Integration
Each BLM separately,
Fill-by-fill basis,
Besides integration, calculate contribution of different beam modes,
Subtract beam-not-present baseline from the data.
100 328 374
BLM subintervals in the DB

## Slide 13: Data processing
Data filtering
Offset correction
Save to local DB
Consider periods only when beam was in the LHC (interval)
Offsets, fill-by-fill doses, BM contributions, times are saved to DB
Integration
Each BLM separately,
Fill-by-fill basis,
Besides integration, calculate contribution of different beam modes,
Subtract beam-not-present baseline from the data.
Not only automated,
But also parallelised
Daily basis

## Slide 14: Data analysis  results
Daily radiation reports
Online Monitoring Dashboard
Mission impossible without
full automation!!!

## Slide 15: Example: daily report - ARC 45, 2018
Anomalies
(“spikes”)
Baselines1
1 6 baselines for each ARC section

## Slide 16
Spikes exceed baseline
up to 3 orders of magnitude
Potentially dangerous
Identification
and monitoring is critical
Spikes identification algorithm
Dynamic behavior
Need of detailed analysis…

## Slide 17: Detailed spikes analysis
Detection of
evolution changes
Correlation with the accelerator parameters changes
Always comparing with
the corresponding baseline

## Slide 18: Current capabilities
Up-to-date radiation levels following the operation
Daily radiation reports
Online monitoring dashboard
Required human actions limited to minimum
 availability to handle more requests
Systematic approach
 results are reproducible and can be compared

## Slide 19: Future…
LHC BLMs based dose analysis – almost complete
Full automation of spikes and baseline analysis + implementation in the daily reports
Full automation of analysis for different radiation monitors
Full automation of radiation monitoring in Injector Chain and Transfer Lines
More sophisticated analysis
Machine Learning usage for detecting correlation between accelerator settings and dose distributions
Further development and maintenance

## Slide 20: Thank you for your attention!

## Slide 22: Backup slides

## Slide 23: ARC baseline analysis
Can be used to residual gas density estimations, spikes analysis and simulation scaling
Very low doses!  the highest baseline dose for pp operation 0.25 Gy/Run 2
Based on the multiple BLMs in each arc section

## Slide 24: Evolution of baseline doses over the integrated intensity for all beam modes (proton-proton operation only)

## Slide 25: Evolution of baseline doses over the integrated intensity for all beam modes (proton-proton operation only)