## Slide 1
RaToPUS: A Generic Radiation Tolerant Power Supply for Distributed I/O Tier Project
Lalit Patnaik
lalit.patnaik@cern.ch
R2E Annual meeting | 12 dec 2018

## Slide 2
Front-End Computer
VME/PICMG/PLC
master
Front-End Tier
Fieldbus Tier
Distributed I/O Tier
Fieldbus (WorldFIP/PROFINET/etc)
DIO3
slave
sensor
DIOn
slave
sensor
DIO2
slave
actuator
DIO1
slave
actuator
Objective
Design and test a generic PSU for Distributed I/O Tier (DIOT) crates
to be used under radiation environment by various CERN user groups.

## Slide 3
. . . . . . . .
. . . . . . . .
PSUs
Custom space
Each PSU: 3U x 170 mm x 8HP
Two PSUs in redundant/load-sharing mode
Accessible from front side
DIOT crate mockup
15” (38 cm)
19” (48.3 cm)
3U or 5.25” (13.3 cm)

## Slide 4
Target user groups in CERN
Beam instrumentation (BE-BI)
Magnet positioning (EN-SMM)
Machine protection (TE-MPE)
Electrical power converters (TE-EPC)
More …?
Assumptions
All PCBs in the crate (system and peripheral) have POL regulators for low voltage digital circuits (1-3.3V)
Power for high performance analog circuits (<10mV ripple + noise) is provided by dedicated linear regulators external to RaToPUS.

## Slide 5
Project schedule
Task | 2018 Q4 | 2019 Q1 | 2019 Q2 | 2019 Q3 | 2019 Q4 | 2020 Q1 | 2020 Q2 | 2020 Q3
Define specifications; Survey existing solutions |  |  |  |  |  |  |  | 
Design and simulation |  |  |  |  |  |  |  | 
Radiation effects training |  |  |  |  |  |  |  | 
Laboratory prototyping |  |  |  |  |  |  |  | 
Define test specifications and test plan |  |  |  |  |  |  |  | 
Non-radiation testing and improvements |  |  |  |  |  |  |  | 
Radiation testing and improvements |  |  |  |  |  |  |  | 
YEAR #1
YEAR #2

## Slide 6
Requirement specifications
Component design/selection
Spice
simulation
PCB design:
schematics, layout
Topology selection
PCB fabrication,
assembly, testing
Prototype vX.Y
User groups
Project workflow

## Slide 7
Parameter | Value
Input: , , | 230 Vac, 50 Hz
Outputs: , () , () | 12 V, 8.33 A (100 W) 5 V, 2 A (10 W)
Output voltage ripple + noise, | 100 mVpp for 12 V 20 mVpp for 5 V
TID | >500 Gy (1000 Gy?)
PCB dimensions | 100 mm x 160 mm x 37 mm
PSU dimensions (including packaging) | 3U x 170 mm x 8HP i.e. 133 mm x 170 mm x 40 mm
Switching frequency, | 250 kHz - 1 MHz
External monitoring/control | PMBus and PS_ON (for remote switching ON/OFF)
EMI specifications | EN55022 Class B
Thermal environment: Ambient temperature Fan tray available | 40⁰C Yes
Parameter | Value
 | 230 Vac, 50 Hz
 | 12 V, 8.33 A (100 W) 5 V, 2 A (10 W)
 | 100 mVpp for 12 V 20 mVpp for 5 V
TID | >500 Gy (1000 Gy?)
PCB dimensions | 100 mm x 160 mm x 37 mm
PSU dimensions (including packaging) | 3U x 170 mm x 8HP i.e. 133 mm x 170 mm x 40 mm
 | 250 kHz - 1 MHz
External monitoring/control | PMBus and PS_ON (for remote switching ON/OFF)
EMI specifications | EN55022 Class B
Thermal environment: Ambient temperature Fan tray available | 40⁰C Yes
Requirement specifications (tentative)
Notes: EN55022 Class B is the EMI specification for Pentair CPCIs power supply.

## Slide 8
Existing Rad-Tol PSU solutions at CERN
BE-BI-BL (25W)
TE-MPE-EP (40W)
TE-CRG-CI (100W)
  50 Hz Transformer Bridge Rectifier LDO
  50 Hz Transformer Bridge Rectifier DC/DC
7-15Vac
7-15Vac
10-20Vdc
10-20Vdc
Disadvantages
Large and costly transformer
Large heat dissipation in crate
No PFC Large EMI filter
  50 Hz Transformer Bridge/PFC Rectifier DC/DC
35Vac
48Vdc
TE-EPC-CCE (70W)
Advantages
Simple and robust design
No higher voltage switching
Notes: Traco TPP40 Series
Traco THM Series

## Slide 9
RaToPUS power architecture: Option-1
Large low-frequency transformer
MOSFETs switching at lower voltage
Large EMI filter?

## Slide 10
RaToPUS power architecture: Option-2
Small high-frequency transformer (part of isolated DC/DC converter)
MOSFETs switching at higher voltage
Small EMI filter

## Slide 11
Radiation hardness: Power stage components
Component | Options | Rad hardness (TID)
EMI Filter | Schurter FMLB-41 | ✓
Bridge rectifier diodes | Multicomp ABS8 | TBD
Power MOSFETs | Infineon IRLI540N Infineon IRHNJ67C30 Infineon IRFB4310 Vishay IRFL110 | TBD 1000 Gy† 300 Gy* 300 Gy*
Filter and DC link capacitors: Ceramic Aluminium electrolytic Tantalum electrolytic | TDK C Series -- -- | ✓
Filter inductor | Bourns SRP1038A Series | ✓
HF transformer | Coilcraft | ✓
LF transformer | Toroidal | ✓
*Tested by CERN †Tested by manufacturer
✓ Passive components are assumed to be rad hard by default
Notes: 600/700 V MOSFETs need to be rad tested by RADWG/R2E

## Slide 12
Radiation hardness: Other components
Component | Options | Rad hardness (TID)
Analog controllers for power stages: For DC-DC stage For PFC stage | FEAST ST1845 UCC28056 | 2 MGy* 1000 Gy† TBD
House-keeping bias (power supply for controllers): Extra flyback winding + diode on HF transformer | STPS10H100C Schottky | TBD
MOSFET gate drivers (+12V, -3V) | NCP5901 RHRPM4424 | TBD 1000 Gy†
Isolated voltage sensing | HCNR200 ACPL-C87B | 150 Gy* TBD
Isolated current sensing: Hall-effect sensors | ACS712 | TBD
PWM pulse isolation: High-speed optocouplers | FOD8012A | TBD
Temperature sensing: Solid-state sensors Thermocouple/RTD | LM45 PT100 | 1000 Gy* ✓
MCU/DSP/FPGA for PMBus implementation | TBD | TBD
*Tested by CERN †Tested by manufacturer
✓Passive components are assumed to be rad hard by default
Notes: There are dedicated PMBus chips, but they are not radiation qualified.
ARM Cortex M0 based MCU for PMBus implementation
There is a possibility to procure STMicro rad-hard components at lower price and even with plastic packages. E.g. Gate drivers. Note: For rad-hard, hundreds of pieces is considered a bulk order!
Look at CHARM test results for CAEN and Weiner power supplies. Some of those components can be used.

## Slide 13
Feasibility study: FEAST as controller for DC/DC stage
Typical configuration: Up to 10W
Modified configuration: Up to 100W
External MOSFETs of higher V and I rating
Larger LC filter on output side
9-12V HKB (house-keeping bias)
Delayed EN for bootstrap capacitor charging

## Slide 14
Feasibility study: FEAST as controller for DC/DC stage
Typical configuration: Up to 10W
Modified configuration: Up to 100W
Lab prototype
Loop stability issues
FEAST chip
External MOSFETs with heatsinks

## Slide 15
Feasibility study: FEAST as controller for DC/DC stage
Proposed
Solution
Vout
Vout
IL
IL
12V
12V
Spice simulation results: With R4 With C3ext
IL*
IL*
200us
400us
600us
200us
400us
600us

## Slide 16
https://wikis.cern.ch/display/DIOT/Rad-tol+power+supply
Future work and open questions
Can compensation network of FEAST be externally modified for stable operation with up to 100W load? Provisional answer: Yes
Can the switching frequency of FEAST be pushed under 1 MHz? (Typical 1-3 MHz)
Rad-hard isolated DC/DC converter: Design and implementation
Rad-hard PFC converter: Design and implementation
Can GaN/SiC FETs be reliably used in radiation environment?
Effect of switching high voltage MOSFETs (600/700V) under radiation?
  Threshold voltage
  Leakage current
  Single Event Effects/Burnout
Notes: Refer Pascal Oser and Sara Siconolfi’s work on SEB mitigation for Power MOSFETs