## Slide 2
Overview of the CERN Injector Chain
Radiation Environment and Equipment
Melanie Krawina, Rubén García Alía
EN – STI BMI
R2E annual meeting, December 2018

## Slide 3
Importance of the Injector reliability
R2E beyond LHC
The LHC injector system is becoming evermore critical for the availability of the LHC
Radiation levels are generally larger than in the LHC (i.e. warm machines), however the electronic systems less complex and sensitive to radiation (i.e. analogue systems)
The LHC injector upgrade (LIU) will include more complex system with state-of-the-art electronics, mostly based on COTS
Furthermore LS2 and Hi-Lumi upgrade will further increase the radiation levels in the injectors
A systematic Radiation Hardness Assurance approach needed for the injector chain to guarantee a successful after LS2 operation, as well as a dedicated environment evaluation related to LIU
FLUKA simulations, PS booster. Done by J. Saraiva

## Slide 4
  The LHC-IC work-package
Place within the R2E work-package structure
R2E Project
Lorem Ipsum is simply dummy text of the printing and typesetting industry. Lorem Ipsum has been the industry's standard dummy text ever since the 1500s.
B.1: CERN Facilities
B.2: RadMON Monitoring System
B.3: Optical Fibre Dosimetry
B.4: Shielding & Relocation
B. Infrastructure
A.1: Project Management
A.2: Radiation Working Group Support
A.3: Monitoring & Calculation Working Group Support
A.4: Materials Testing & External Facilities
A.5: LHC Injector Chain & Experimental Areas
A. Operations
C.1: Common Building Blocks
C.2: Vacuum
C.3: Beam Instrumentation
C.4: Quench Protection System
C.5: Power Converters
C. Developments
As introduced by R. García Alía yesterday

## Slide 5
Covers the LHC injector chain (LINAC4, PSB, PS, SPS) and the Experimental Areas (nTOF, AD, BDF test area …)
Description and objectives:
  Providing radiation maps and monitoring of radiation levels in strong collaboration with the MCWG (past: RP surveys for loss maps)
  FLUKA simulations for benchmarking and prediction of future scenarios in strong collaboration with the EN-STI BMI
  Developing a comprehensive inventory list of installed electronic systems and components
  Analyzing equipment failures and developing strategies to reduce them
  Support to equipment groups in the design, upgrade and qualification of electronic equipment to be installed in the accelerator tunnel or its vicinity
  Design and implementation of dedicated radiation shielding measures or optional relocation measures
  …
  The LHC-IC work-package
Overview and objectives
R2E Project

## Slide 6
  R2E requests for the IC
Over the last couple of months
LINAC4
  Possible R2E induced failures at preamplifiers close to the stripping foil (BE-BI), mitigation actions
PSB
  Upgrade of the BTV system, radiation maps needed (BE-BI)
  Benchmark of FLUKA radiation maps with OF sensors (EN-EA)
SPS
  LSS5 installation BTV system, radiation map and mitigation actions (BE-BI)
  LSS5 CV skid installation, mitigation action (EN-CV)
  LSS5 BCTW relocation, radiation map and mitigation action (BE-BI)
  LSS4/LSS6 gamma factory electronics. Radiation map
AD
  Upgrade of the BTV system, relocation of sensitive equipment
BDF test area
  Possible R2E induced failures in PLCs, mitigation actions (EN-STI)

## Slide 7
  Case Study: SPS LSS5 dump
R2E requests for SPS LSS5 dump area
SPS LSS5 – EXCX5 cavern, new beam dump region in Sextant 5 after relocation from LSS1
Historically low-radiation levels, different equipment stored here
New radiation environment due to beam
Three different requests for this area received for three different applications and different groups
All of them solved or ongoing activities, thanks to the collective effort of the whole R2E team
To highlight the efforts and describe the objectives of the LHC Injector Chain work package, region will be presented as case study.
Picture by W. Van den Broucke

## Slide 8
  Case Study: SPS LSS5 dump
R2E requests for SPS LSS5 dump area
Requests that will be highlighted:
BTV systems (BE-BI)
Beam dump cooling and ventilation (CV) skid (EN-CV)
BCTW system (BE-BI)
Picture by W. Van den Broucke

## Slide 9
  SPS LSS5 dump | BTV systems
Overview BTV system
Animation provided by S. Burger
Already explained by T. Lefevre yesterday, in a nutshell:
BI department provides operation parameters of the beam, key values: position, size, profile, length, Intensity …
BTV (Beam TV) system used, consisting of i) a luminescent beam screen/radiator that is inserted into the vacuum chamber ii) a detector (camera) that observes/detects emitted light.
Up to now based on analogue cameras (standard CCD) or ”radhard” solutions (tube based, ThermoFisher …) used at CERN -> Upgrade to digital COTS ones

## Slide 10
  SPS LSS5 dump | BTV systems
Problem statement
1.) BTV system
Upgrade from analogue CCD sensors to digital (higher performance, image rate, resolution …) – Digital more sensitive to SEU!
New camera will be purely commercial and no information regarding sensitivity to radiation
Qualification campaign of BASLER camera at CHARM conducted in 2016 (see EDMS 1736143)
  Key findings:
    TID: ~150 Gy lifetime limit
    SEU:
      SEU sensitive, power-cycle resets (ΦSEU = 1.5E9 HEH/cm2)
      total limit of ~5E11 HEH/cm2 over lifetime
  Target values camera for ECX5 :
    < 10Gy/y
    < 1E8 HEHeq/cm2/y
Pictures provided by S. Burger

## Slide 11
1.) BTV cameras – FLUKA studies
Different positions were tested during FLUKA study - Only reasonable location close to the cavern floor (beam approx. 6m above), on the side of the beam dump abutment
Mirror system will be installed to carry the image from the actual beam location to the sensor
  SPS LSS5 dump | BTV systems
Analysis
FLUKA simulations, LSS5. Done by D. Björkman Results scaled to 2E18 protons/year
Equipment
Equipment
FLUKA Side-view
FLUKA Top-view
TID: 0.01 < x < 10 Gy/y -> within target values
HEHeq fluence: 1E9 < x < 1E12 HEH/cm2/y -> bottleneck!
Additional full iron shielding surround the sensitive equipment of the camera itself -> reduction of HEHeq fluence to ~2.5E7 HEH/cm2/y
-> Prevention through shielding

## Slide 12
2.) CV skid
Cooling station close to the LSS5 beam dump, to minimize the volume of contaminated water
Will be installed at the floor, includes different electronics (purely COTS) with no qualification tests conducted, that will be subject to beam and dump radiation
Most critical components of the setup are Pressure Transmitters and Pressure Difference Transmitters (PT and PDT), other components analogue
Since no qualification tests have been conducted by the equipment group or us in the past, no reference values for the sensitivity known
FLUKA simulations conducted to analyze the radiation environment and see if there resulting levels are a thread for COTS equipment
Pictures by W. Van den Broucke
  SPS LSS5 dump | CV skid
Problem statement

## Slide 13
Analysis
Radiation environment highly critical for COTS systems. No qualification tests, therefore no information regarding sensitivity -> shielding actions probably not suitable since the levels would still be too high
ECA5 shielded area: lower levels than ECX5 but pose still a threat with 1E7 HEH/cm2/y. Also limitation with distance through cables/contaminated water
FLUKA simulations by J. Briz, Results scaled to 1.7E18 POT/y
FLUKA values (1m above ground)
  TID: 4 Gy/y
  1MeV Neq: 1.2E11 n/cm2/y
  HEHeq: 2E10 HEH/cm2/y
  SPS LSS5 dump | CV skid
General R2E levels for COTS
  TID: 10 Gy (lifetime)
  1MeV Neq: 1E12 n/cm2 (lifetime)
  HEHeq: 1E7 HEH/cm2/y

## Slide 14
  SPS LSS5 dump | CV skid
Analysis
Commercial rad-hard solutions (e.g Rosemount for NPP)
  Qualified for TID, no knowledge about behavior in mixed-field
  Niche market, therefore high costs due to certifications and R&D involved
  Price per unit: ~7000$
In-house development (proposed by S. Danzeca)
Standard pressure transmitter from CERN store (e.g SensorTechnics CTE7000)
Separation of i) piezo sensor and ii) sensitive electronics
  Electronics deported into BB5 (control cubicle)
  Piezo sensor stays with skid
-> Prevention through in-house development
Pictures by W. Van den Broucke

## Slide 15
Pictures by T. Levens
3.) BCTW
BCTW moved in LSS5 region, located down stream of the beam dump
BCTW for the SPS is a copy of the design developed for the LHC
Specific location at LSS5 chosen due i) aperture of the monitor ii) short cable distance to the rack and iii) historically low radiation levels
BCTW monitor rises concerns regarding degradation of materials (PTFE in cables, glues …) and residual activation of the monitor poses thread to personnel at interventions
Head Amplifier critical components given through i) op-amps (qualified up to 1kGy at OSI, see EDMS: 1738241) and ii) regulators.
Other BE/BI equipment installed in the same region: DC current transformer (DCCT), Fast Beam Current Transformer (FBCT) and Beam Gas Ionisation profile monitors (BGI) …
  SPS LSS5 dump | BCTW
Problem statement

## Slide 16
3.) BCTW
FLUKA values obtained for beam height:
  TID: ~ 10 kGy/y
  1MeV Neq: 9E12 n/cm2/y
  HEHeq: 6E12 HEH/cm2/y
FLUKA values obtained for 70cm below beam
  TID: ~ 1 kGy/y
  1MeV Neq: 2E12 n/cm2/y
  HEHeq: 6E11 HEH/cm2/y
In comparison with previous geometry (e.g larger dump aperture), dose levels increase in a factor of 10 for beam height, and a factor 3 for below the beam -> no low radiation levels anymore an highly critical for systems
-> Prevention through relocation from LSS5 to LSS3
  SPS LSS5 dump | BCTW
Analysis
FLUKA simulation by J. Briz, Results scaled to 1.7E18 protons/year

## Slide 17
Ongoing Tasks
Global goal: guaranteeing reliability of the LHC required for High-Luminosity project, by reducing/mitigating R2E issues in the Injector Chain
How?
Providing radiation maps and long-term monitoring of the radiation levels in the LHC injector chain (reach a monitoring and calculation level similar to LHC) – Strong collaboration with MCWG and EN-STI BMI
Development of a comprehensive inventory list of installed electronic systems and components, linked with dedicated qualification studies
Analyzing equipment failure, development of strategies of long- and short-term mitigation actions.
Support to the equipment groups in the design, upgrade and qualification of electronic equipment installed in LHC Injector Chain

## Slide 18
Melanie Krawina
CERN EN/STI-BMI
FLUKA Team - R2E Project
melanie.krawina@cern.ch
www.cern.ch
Special thanks to: Jose Briz, Luigi Esposito, Daniel Björkman, Stephane Brugger, Salvatore Danzeca, Elisa Guillermain, Tom Levens, Pierre Mondon, Willy Van Den Broucke, Francesco Cerutti

## Slide 19
List of references
Injector Chain Environment
J.P. de Carvalho Saraiva et al., Radiation Environments and their Impact at the CERN's Injector Chain, CERN-ACC-NOTE-2015-0042
J.P. de Carvalho Saraiva, Injector Chain Website
E. Guillermain et al., Study of the SPS radiation environment, Technical Note SPS-SI-EN-001
BTV
D. Björkman, SPS LSS5 – FLUKA calculation for the radiation environment und Updated Simulations
S. Burger, BTV SBDS Status and Plans
S. Burger, Irradiation test of Commercial (BASLER) digital cameras @ CHARM and CHARM EDMS report
S. Burger, BI projects involving camera
CV skid
J.Briz and L. Esposito, FLUKA simulations for Radiation Doses at LSS5 Dump Cooling Station
P. Mondon and W. Van den Broucke, Cooling station instrumentation SPS Beam Dump
BCTW
T. Levens, SPS BCTW R2E aspects
J. Briz and L. Esposito, LSS5 dump: Radiation Levels at BCTW.51932 location
T. Levens et al., SPS wall-current transformer (BCTW) relocation from LSS5 to LSS3, ENGINEERING CHANGE REQUEST SPS-BCTW-EC-0003