## Slide 1: LHC Interlocked BPM Renovation
07.11.2018 BI-TB meeting
Irene Degl’Innocenti, Jan Pospisil, Manfred Wendt, Andrea Boccardi, Michele Bozzolan
BE-BI-BP, CERN

## Slide 2: Outline
Introduction:
  LHC Interlock BPM system
  The current system limits
The proposed architecture:
  Front-end concept
  Digital acquisition chain options
Preliminary beam results
Doublet simulation
Carrier Upgrade
Status

## Slide 3: Introduction: LHC Interlock BPM system
BPM dedicated for machine protection purposes
  Beam dump protection
  Safe beam extraction
Real time, bunch-by-bunch, failsafe system on both beams
Beams
Dump
16 interlock BPM channels
2 planes
2 beams
2 locations
2x redundancy

## Slide 4: Introduction: Current System Limits
Wide Band Time Normalizer
Bunch-spacing of 25 ns required: No doublet bunches measurements
Intensity dependent offset
  Can generate false trigger
Sensitive to reflections  Historically switching sensitivity
  Problem resolved by adding absorptive filter.
  False trigger caused by fat pilots
  (wrong sensitivity settings).

## Slide 5: The Proposed Architecture
Time-multiplexing: single processing chain for both electrodes
Comb-filter: signal extension
Direct signal digitization
Processing in FPGA

## Slide 6: The Proposed Architecture: Front-end Concept
25 ns
Beam
25 ns
Stripline pick-up
Delay 12.5 ns
Delay 2 ns
Filter output
Electronics rack
Tunnel
LP filters
Image: Jan Pospisil

## Slide 7: The Proposed Architecture: Digital Acquisition Chain
LHC P5, USC55, BPMSY4L5 (Stripline)
1.24e11 Bunch Intensity
Acquired with 8 bit – 18 GHz scope

## Slide 8
Comb Filter
ADC Mezzanine
ADC
ADC
ADC
VFC board
FMC
FPGA
ADC sampling frequency bounded by FPGA transceivers max lane rate (6.5536 Gbps on VFC-HD).
Two mezzanines under test:
  Vadatech FMC225: 12 bits (8.8 ENOBS) up to 4 Gsps  operating @ 3.2 Gsps
  HTG-FMC-14ADC: 14 bits (9.6 ENOBS) up to 3 Gsps  operating @ 2.6 Gsps
The Proposed Architecture: Digital Acquisition Chain

## Slide 9
LHC P5, USC55, BPMSY4L5 (Stripline)
1.24e11 Bunch Intensity
Acquired with 8 bit – 18 GHz scope
The Proposed Architecture: Digital Acquisition Chain

## Slide 10: Beam Results : measurements set-up
Att
Att
Att
Comb Filter
50 Ω
ADC
VFC-HD
Memory
LHC P5, USC55
BPMSY4L5 Beam 2
Emulation of intensity and displacement
Decoupled from beam motion
ADC configurations:
  Vadatech 12bit @3.2 Gsps, beam asynchronous and beam synchronous;
  Vadatech 15bit @4 Gsps, decimated by 8, IQ modulation at 500 MHz
  HTG 14bit @2.6 Gsps

## Slide 11: Beam Results : position estimation algorithm
Signal power estimation by Root Mean Square (RMS) algorithm
  Best resolution results in simulation by now
  Further solutions are under study
Electrode signal power estimation and Delta/Sigma normalization to extract the displacement x:
A
B

## Slide 12: Beam Results: (1) Vadatech 12 bit @3.2 Gsps
40 – 12bit samples per electrode
Beam Asynchronous:
<20 um bunch-by-bunch offset variation due to the sampling time shift difference between the two electrodes
Beam Synchronous:
sampling clock generated from RF cavities 40 MHz, the offset variation is then fixed with a given beam energy
Comb-filter bunch response after digitization

## Slide 13: Beam Results : (2) Vadatech 15 bit IQ @4 Gsps 8-DDC
Decimate by 8 – Stopband response
DDC Block Diagram
NCO (500 MHz) + Digital Down Converting Filter (factor 8) embedded in the chip:
  NCO @ 500 MHz, decimation factor 8, IQ 15 bit
DDC filter too narrow, time response bigger than comb filter response

## Slide 14: Beam Results : (2) Vadatech 15 bit IQ @4 Gsps 8-DDC
Comb-filter bunch response after digitization
NCO (500 MHz) + Digital Down Converting Filter (factor 8) embedded in the chip:
  NCO @ 500 MHz, decimation factor 8, IQ 15 bit
DDC filter too narrow, time response bigger than comb filter response
Decimate by 8 – Stopband response

## Slide 15: Beam Results : (3) HTG 14 bit @2.6 Gsps
32.5 - 14bit samples per electrode
Beam asynchronous
DDC options under study
Higher frequency with VFC upgrade
Comb-filter bunch response after digitization

## Slide 16: Beam Results : Position Resolution Results
Chart: Intensity [cpb]
| 10000000000 | 13900000000 | 19500000000 | 27100000000 | 37900000000 | 52800000000 | 73700000000 | 103000000000 | 143000000000 | 200000000000
Simulation (12 bit ADC) | 167.174 | 122.614 | 87.317 | 63.36 | 44.945 | 32.126 | 22.986 | 16.314 | 11.83 | 8.523
Simulation (14 bit ADC) | 140.6248 | 93.7436 | 68.003 | 48.1595 | 35.7975 | 25.9695 | 19.3615 | 14.3709 | 11.3315 | 9.3615
M1a: LHC Beam Data (12 bit ADC) | 22.8121 | 204.5967 | 1405.3267
M2: LHC Beam Data (IQ) | 43.8923 | 127.165 | 333.3787
M3: LHC Beam Data (14 bit ADC) | 33.8633 | 74.2696 | 198.6765
ADC Full Scale Limit | 1 | 10000
Chart: Intensity [cpb]
| 10000000000 | 13900000000 | 19500000000 | 27100000000 | 37900000000 | 52800000000 | 73700000000 | 103000000000 | 143000000000 | 200000000000
Simulation (12 bit ADC) | 167.174 | 122.614 | 87.317 | 63.36 | 44.945 | 32.126 | 22.986 | 16.314 | 11.83 | 8.523
Simulation (14 bit ADC) | 140.6248 | 93.7436 | 68.003 | 48.1595 | 35.7975 | 25.9695 | 19.3615 | 14.3709 | 11.3315 | 9.3615
M1a: LHC Beam Data (12 bit ADC) | 22.8121 | 204.5967 | 1405.3267
M2: LHC Beam Data (IQ) | 43.8923 | 127.165 | 333.3787
M3: LHC Beam Data (14 bit ADC) | 33.8633 | 74.2696 | 198.6765
ADC Full Scale Limit | 1 | 10000
Intensity is scaled in order to cover the full ADC range with maximum intensity (2e11) and displacement (± 7.5 mm).

## Slide 17: Beam Results : Position Error Offset
Intensity is scaled in order to cover the full ADC range with maximum intensity (2e11) and displacement (± 7.5 mm).
Chart: Intensity [cpb]
| 62161145147.256279 | 19309422287.810314 | 6155388834.736743
Negative | 0 | -0.02714 | 0.010288
Center | 0 | -0.0012235 | -8.85e-05
Positive | 0 | 0.00266 | -0.0325
Mean value of Position Error for the ADC 14bit @2.6 Gsps
Intensity independent

## Slide 18: Doublet Simulation: Singlet vs. Doublet
A1+
A2-
A2+
A1-
A+
A-
25 ns
25 ns
One Singlet Bunch
One Doublet Bunch (two sub-bunches)
Signals are overlapped
Detection of free-overlap samples

## Slide 19: Doublet Simulation: Singlet vs. Doublet
A+
A-
25 ns
One Singlet Bunch
One Doublet Bunch (two sub-bunches)
25 ns
Signals are overlapped
Detection of free-overlap samples
RMS on one exact period
  4 time less samples than in the singlet case

## Slide 20: Doublet Simulation: Singlet vs. Doublet
One Singlet Bunch
One Doublet Bunch (two sub-bunches)
Signals are overlapped
Detection of free-overlap samples
RMS on one exact period
  4 time less samples than in the singlet case
  Half the resolution

## Slide 21: Carrier Upgrade: VFC-HS
Upgrade of VFC-HD:
  FMC+ connector
  Faster Xcvrs (10 Gbps)
Higher price
  3 kCHF vs. 1k2 kCHF
Schematics done, layout nearly done
https://www.ohwr.org/projects/vfc-hs

## Slide 22: Carrier Upgrade: iBPM Price/Resolution Variants
Carrier | Mezzanine | Sampling Speed [GSPS] | Chips | VME Cards | Expected Resolution [µm] *) | Est. Price [kCHF] | 
 |  |  |  |  |  | Per Channel | Total
VFC-HD | Vadatech FMC225 | 3.2 | 1x ADC 1x DAC | 20 | 200 | 8.4 | 168
VFC-HD | HTG 14ADC-16DAC | 2.6 | 1x ADC 1x DAC | 20 | 130 | 7.9 | 158
VFC-HS | HTG QUAD-14ADC | 3.0 | 2x ADC no DAC | 10 | 120 | 5.9 | 118 **)
16 channels + 4 spare = 20 channels total
CHF ~ USD
VFC-HD: 1.2 kCHF, VFC-HS: 3 kCHF (estimation)
*) Single bunch, I = 1e10
**) Plus VFC-HS development (~ 50 kCHF)

## Slide 23: Status
Analogue front-end:
  Balanced power combiner and PCB delay lines prototypes are finished.
  Still is to discuss the need of an anti-aliasing filter and an amplifier stage before the digitization.
Digital chain:
  To define system configuration (mezzanine + carrier).
  To define algorithm and firmware implementation.
Full system goal: fully functional prototype by the end LS2