## Slide 1: Cryogenic system configurations to cool superconducting radio frequency cavities at 2 K
07/22/2019
Dhananjay Ravikumar

## Slide 2
The Relativistic Heavy Ion Collider (RHIC)

## Slide 3: Upgrading the RHIC: eRHIC

## Slide 4: Designing a Quiet Helium Source: Problem description
Microphonics – What is it?
Sources
Around 4K
Fast (> 1Hz) pr change 0.01 – 0.05 mbar  detuning of ~20 Hz
At 2 K
Two phase flow
Pressure fluctuations
Cryogenic contribution

## Slide 5: Mitigating flow induced microphonics
SRF Cavity
4.5 K, 3 bar supply
2 K, saturated vapor

## Slide 6: Dual bath single temperature system
SRF Cavity
4.5 K, 3 bar supply
2 K, saturated vapor
2 K, saturated vapor

## Slide 7: Dual bath dual temperature system
4.5 K, 3 bar supply
2 K, saturated vapor
1.9 K, saturated vapor
SRF Cavity

## Slide 8: Quiet Helium Source (QHS)
Can completely suppress vapor generation if properly engineered
Liquid head needs to be calibrated depending on the inlet enthalpy
Liquid head is very sensitive to inlet enthalpy
When the supply is at 4.5 K, 3 bar, a head of 5m is required to completely suppress vapor
Workaround:
  Throttle the flow upstream of the subcooler,
  In the right range, J-T effect increases temperature.
  More heat can be transferred across the subcooler as a result.
  Other option would be to add a phase separator and supply saturated liquid at 4.5 K at point 1.
Manuscript submitted to Cryogenics

## Slide 9: Future work
Performing feasibility studies on heat exchanger sizes and approach
Incorporating the QHS design in eRHIC cryomodule designs
Performing experiments to test the QHS principle.