## Slide 1: PROPOSAL FOR A COST MODEL FOR THE X-FEL of the COMPACT LIGHT COLLABORATION
Evangelos Gazis
IASA @ Compact Light
Many Thanks to: R Rochow, J. Clarke, D. Schulte, W. Wuench

## Slide 2: CONTENTS
COMPACT LIGHT XFEL
OTHER XFEL SYSTEMS COST
COST of other systems breakdown
XFEL@DESY
ESS@LUND
COST MODEL for LARGE systems
COST MODEL PROPOSAL for XLS
======================================
TIME Schedule
RISK Analysis
Commissioning – Operation

## Slide 3
XLS Performance (Gerardo D’ Auria, XLS Kick-off meeting)
Parameter | Value | Unit
Minimum Wavelength | 0.1 | nm
Photons per pulse | >1012 | 
Pulse bandwidth | <<0.1 | %
Repetition rate | 100 to 1000 | Hz
Pulse duration | <1 to 50 | fs
Undulator Period | 10 | mm
K value | 1.13 | 
Electron Energy | 4.6 | GeV
Bunch Charge | <250 | pC
Normalised Emittance | <0.5 | mrad
Preliminary Parameters and Layout of XLS hard X-ray FEL facility

## Slide 4: Basic Parameters (D. Schulte et al, Trieste Meeting)
 | unit | CLIC_502 |  | CLIC_L |  | Swiss
Structures per RF unit |  | 12 | 16 | 12 | 16 | 4
Klystrons per RF unit |  | 2 | 2 | 2 | 2 | 1
Structure length | m | 0.23 | 0.23 | 0.48 | 0.48 | 1.98
a/lambda |  | 0.145 | 0.145 | 0.14 | 0.14 | 
Allowed gradient | MV/m | 100 |  | 80 |  | 
Operating gradient | MV/m | 77 | 67.5 | 59 | 51 | 27.5
Energy gain per RF unit | MV | 213 | 248 | 339 | 391 | 203
RF units needed |  | 27 | 23 | 17 | 15 | 26
Total klystrons |  | 54 | 46 | 34 | 30 | 26
Linac active length | m | 74 | 85 | 98 | 115 | 206
Cost estimate | a.u. | 76.2 | 71.5 | 63.4 | 64.5 | 
Preliminary estimates based on CLIC cost indicate:
cost of one RF unit CRF (no accelerating structures) is approximately the same as 4m (estimate 1) to 8m (estimate 2) of active length, used 6.67m
Needs to be reviewed
Assume cost of RF unit is 2 cost units (cu)
Thanks to Ph. Lebrun
and I. Syratchev

## Slide 5: COST of other systems Breakdown
TASK DISTRIBUTION
Electron Gun + Linac 27%
Accelerator sub-systems 9%
Undulator and photon 24%
Controls and operation 4%
Infrastructure 19%
Site and civil work 17%
COST M€
Project preparation 38.8
Project construction, capital investment 736.3
Project construction, personnel 250.1
Total construction cost 986.4
Beam commissioning 56.4
Total project construction cost 1,081.6
XFEL@DESY

## Slide 6: COST of other systems Breakdown
The European Spallation Source (ESS) will house the most powerful proton linac ever built.
    – Average beam power of 5 MW.
    – Peak beam power of 125 MW
    – Acceleration to 2 GeV
    – Peak proton beam current of 62.5 mA
    – Pulse length of 2.86 ms at a rate of 14 Hz (4% duty factor)
• 97% of the acceleration is provided by superconducting cavities
• The linac will require over 150 individual high power RF sources
    – with 80% of the RF power sources requiring over 1.1 MW of peak RF
    power
    – We expect to spend over 200 M€ on the RF system alone
ESS (Dave McGinnis/Accelerator Division)

## Slide 7: COST of other systems Breakdown
RF 37%
INSTRUMENTATION 6%
HIGH BETA 13%
MEDIUM BETA 6%
SPOKES 4%
FRONT END 7%
ACCELERATOR PHYSICS 2%
MANAGEMENT 1%
CRYOGENICS-VACUUM 16%
TEST STAND 2%
INSTALLATION 3%
ESS (Dave McGinnis/Accelerator Division)

## Slide 8: COST of other systems Breakdown
ESS (Dave McGinnis/Accelerator Division)

## Slide 9: COST of LARGE systems An example by V. Schiltsev
Total Project Cost = TPC
L = Length of the tunnel, E = cm Energy, P = total site AC power for the facility
α, β, γ = coefficients, but β varies with the accelerator technology

## Slide 10: A draft COST MODEL for XLS
Sub-Systems
RF-Gun
Injector
LINACS
Klystrons
Bunch Compressors
Magnets
Undulator
Controls & Operation
Rough Distribution %
      6
      9
      16
      25
      10
      5
      25
      4
WP Leaders should start providing rough estimation of the cost/item-system, to be frequently updated!

## Slide 11: A draft COST MODEL for XLS (thanks to Massimo Ferrario)
The yellow slots are missing costs PLUS any other missed item