## Slide 1: LINAC4 source tunnel and test stand
Alessandra Lombardi
Jean –Baptiste Lallement
Daniel Noll

## Slide 2: Source in the tunnel – same as the 2017-18 run
Performance achieved (at 160mA) :
  Current : 24 mA
  Emittance : 0.3 mm mrad rms /
  Useful Pulse length (5%flatness) : 600 µsec
  Pulse-to-pulse : 2%

## Slide 3: current

## Slide 4: emittance

## Slide 5: 600µsec good pulse length
Extensive pre-chopper and chopper tests to minimise the effect of neutralisation.
Final solution
  850µs from the source
  50µs chopper by the pre-chopper (min)
  200µs chopped by the chopper
after RFQ (before chopper)

## Slide 6
Chart: RF POWER 48kW– 5 hours 20 min – tuned 2 hours before stats
Pulse-to-pulse jitter (25 mA after the RFQ for 35 mA into the RFQ)
BCT at 45 keV
Sigma=3%
Filtering action of the RFQ is beneficial to pulse stability

## Slide 7
Chart: 
2. Pulse-to-pulse jitter correlation with RF stability
Current in the LEBT
Rf power
Running average over six hours

## Slide 8
Chart: Cesiation #2 (20 Sept to 5 Oct)
At ~41.3 kW RF power:
~0.05 mA/hour
~ 1.12 mA/day
Longer term drift (II)

## Slide 9: Solutions to long term drift
Automatic tuning
Continous cesiation
Achieve the desired current and stability in volume mode i.e. without the necessity of cesiation (this is within the reach, tests august 2018)

## Slide 10: To the test stand
Test stand is equipped with a delicate yet functional emittance meter and an rfq “mask”.
The volume mode source has been tested at the test stand for intensity in the RFQ acceptance

## Slide 11: Mask is a quick way to characterise a source

## Slide 12: Test stand plan – next 2 months
week | linac4 test stand | comments test stand | visitors test stand | tunnel | comments tunnell
8-12 october | cesiated,bore 8mm cusp free |  | Keio uni | cesiated ,bore 6.5 , cusp | reliability run
15-19 october | cesiated,bore 8mm cusp free |  | Ausburg | cesiated ,bore 6.5 , cusp | reliability run
22-26 otober | 21/10 :installation volume 7.5 mm cusp | regain performance |  | cesiated ,bore 6.5 , cusp | reliability run
29 october-2Nov | volume 7.5 mm cusp | emittance stability and mask |  | cesiated ,bore 6.5 , cusp | reliability run
5-9 Nov | volume 7.5 mm cusp | emittance stability and mask |  | cesiated ,bore 6.5 , cusp | reliability run
decision point : if the volume 7.5mm cusp gives at least 30mA in the mask and the stability is acceptable then we will follow the program below |  |  |  |  | 
12-16 Nov | clean and install the one from the tunnell with a bore 8.0 eletrode fitted |  |  | 12 Nov Install in tunnell volume 7.5 mm cusp | reliability run
19-23 Nov | volume ,bore 8.0 , cusp | emittance stability and mask |  | volume 7.5 mm cusp | reliability run
26-30 Nov | cesiated ,bore 8.0 , cusp | emittance stability and mask |  | volume 7.5 mm cusp | reliability run
3-7 Dec | volume ,bore 9.0 , cusp | emittance stability and mask |  | volume 7.5 mm cusp | reliability run
10-14 Dec | cesiated ,bore 9.0 , cusp | emittance stability and mask |  | volume 7.5 mm cusp | reliability run

## Slide 13: Upcoming review
We will present the reviewer with the two options for 25 mA (cesiate or non-cesiated)
We will present the plans for the continous cesiation and for autopilot
We will present the roadmap to 45mA out of the RFQ

## Slide 14: Spare RFQ
At the moment there are no firm plans for a full spare RFQ. Baseline plan is to buy the copper (done) and manufacture 1 section.
A working group (chaired by E. Mahner) is investigating whether we can increase the field in the RFQ to 50MV/m (presently 36MV/M). The answer should be there by the end of the year.
After the working group has finilised the report we can compare the advantage of a spare RFQ with increased acceptance vs an RFQ which is a copy of the existing one