## Slide 1: BI-BP future needs for rad-hard tunnel crates
12/10/2018 BI Technical Board
A. Boccardi, M. Barros Marin, M. Krupa, M. Wendt

## Slide 2: LHC arc BPM tunnel infrastructure
Infrastructure maintained for LHC BPM upgrade
Tunnel crate shared with BLMs
Cryostat feedthroughs (2 x 4 SMA)
SMA cables (2 x 4)
Optical fibres (2 x 2)

## Slide 3: Typical LHC arc installation
PSU
2 x BPM card
BLM PSU
BLM card
comms

## Slide 4: Unusual cases
Long cables

## Slide 5: Unusual cases
2 x 2 BPMs

## Slide 6: Unusual cases
Transfer lines

## Slide 7: LHC BPM card
Analogue electronics
100 mm
222 mm

## Slide 8: LHC BPM upgrade architecture
Maintain LHC fibres and cabling
Similar to LHC BPM interlock upgrade
Mixed analogue and digital installation in the tunnel crates:
  A passive analogue RF board for signal conditioning
  A digital board for signal digitising, pre-processing and transmission
Both boards installed as a single unit
Exact implementation details under discussion

## Slide 9: Digital board real estate
Not needed
Possibly needed
Needed
LHC BPM upgrade
160 mm
233 mm

## Slide 10: Maintain format of the digital board?
?
?
Might be possible but looks challenging

## Slide 11: RF analogue board real estate
LHC BPM upgrade
220 mm
256 mm
Needed
Distributed elements.
Board dimensions dictated by physics but compact designs could be investigated.

## Slide 12: Compact analogue RF board
63% size reduction required
Two options:
Very high ε dielectric
Multilayer design
Finding the right solution requires R&D

## Slide 13: LHC BPM upgrade preliminary spec
Real Estate:
  1 unit = 1 digital board + 1 passive analogue RF board
  Unit size: 3U might be possible. Is 4U an option?
  Typically 2 units per crate
Electrical:
  2 x < 50 W power consumption
  Passive cooling
  Independent power management per unit
  Backwards compatibility with FIP
  No “intelligent” backplane required:
    All communication: optical links
    BPM signals: RF SMA connectors
    Support of a BPM FE unit ID handling?
Mechanical:
  Fast and secure installation
  Simple, easy exchange of BPM FE units