## Slide 1
Gene Oleynik, Department Head, Data Movement and Storage
Hepix
10/11/2018
“Tape Carousel” Fermilab

## Slide 2: Outline
Tape Carousel –
Understand the end-point is to efficiently read data off of serial media to random-access media with minimal seeks
Context: Enstore and dCache HSM, not other possible solutions.
Description of relevant information on currently recall implementation
Issues
Potential solutions

## Slide 3: Relevant info on dCache and Enstore
dCache:
Request for files to dCache is load balanced across pools
dCache has finite tape store, restore as well as user request queues (pending and active limits)
User file read requests are queued and, if there, is a cache miss, they will immediately be read from tape subject to queue as well as other limitations
Enstore:
In order to prevent slow transfers to/from tape, Enstore has the concept of “discipline”. Only a configured amount of transfers to any given dCache pool node per Enstore ”library” can be active at any one time.

## Slide 4: Enstore info continued
Enstore ”libraries” are associations of tapes and drives. Requests are managed by a library manager.
Enstore movers manage tape drives and actual trasfers.
Library managers queue up read requests per tape
  Requests for files on a tape are ordered by their logical location
  Each request has a priority that increases with enqueue time.
  Read volume processing is ordered by the maximum priority of all enqueued read request for that volume.
Idle movers request work from their library manager
The library manager gives work (single file transfer) immediately to a requesting idle mover if it has work to do.

## Slide 5: ENSTORE Read queueing
OOO priorities reflect out of order receipt or disipline
VOL A
FILE 2 PRI 30
FILE 11 PRI 45
FILE 20 PRI 150
Queued PRI 150
VOL B
FILE 10 PRI 30
FILE 75 PRI 25
FILE 80 PRI 100
File 95 PRI 15
Queued PRI 100
VOL D
FILE 15 PRI 30
FILE 20 PRI 45 transferring
FILE 80 PRI 250
15 Skipped - discipline
In drive -processing

## Slide 6: Issues
When a batch of file requests for a tape are issued.
  Individual file requests will be spread across dCache pools
  Due to queueing and congestion, these requests will trickle into Enstore out of order.
  Since Enstore immediately starts processing the requests as they come in, they will be read out of order from the tape
Discipline limits the number of requests that can be active from a node. If the next logical ordered read is to a node that would violate discipline, it is skipped leading to out of order processing
The end result is inefficient access to the serial media – average overall rate of as low as 35% of rated drive speed (including overheads & mount times, disk and network rates)

## Slide 7: dCache queueing restores
Other pools can have files from same tape that are serviced out of order in time
Discipline ties up Active queue slots
Pool A Restore Queues
Active queue
1 transferring File 6 Tape A
2 discipline File 6 Tape C
3 transferring File 10 Tape B
4 discipline File 9 Tape A
…
Slot N max
Pending queue
Slot 1 File 80 tape A
Slot 2 File 20 tape B
Slot 3 File 2 tape B
Slot 4 File 1 tape B
…
Slot M max

## Slide 8: Potential solutions
Algorithmically delay the reads in the library manager (e.g. while requests are still coming in with some frequency).
  Issues: This in turn ties up dCache active restore slots; Parameters for algorithm will likely be experiment processing context dependent and hard to tune in general.
Eliminate discipline
  Issues: Discipline is used to help guarantee sufficient bandwidth between dCache and Enstore by eliminating disk or network bottlenecks. Slow transfers result in drives being occupied longer than necessary. Tradeoff?
Make dCache queuing tape content aware
  Issues: coupling of systems, difficult to achieve.
Buy more drives. High-luminosity rates could be very costly.

## Slide 9: Conclusion
Restating the obvious: Efficiently turning serialized access into high throughput random access is hard. Serial rates match disk rates OK. Seeks kills the efficiency - more than anything else besides mount overheads.
While this is WLCG focused, we have the same issues, to a higher degree, for the shared Fermilab “Public” dCache system used by the Neutrino experiments that we need to solve.
As outlined, We have a number of avenues we will be pursuing over the next couple of years.

## Slide 10: Collaborations / Partnerships / Members 28pt Bold