## Slide 1
Beam loss monitoring in SPS
- plans for LS2
Notes: Good morning.
For those of you who don’t know me yet, my name is Steen Jensen and I work in the BI software sections since a bit more than a year.
I will tell you about the LS2 changes foreseen for the SPS beam-loss interlocking

## Slide 2
Overview
BLM
BLM
BLM
BLM
BLM
BLM
BLM
BLM
Integrators
Multiplexer
Amplifier
ADC
BI_BLMADC #0
BLRSPS
ADC values per channel
(raw beam loss values)
BI_BLMDMP #1
ch0
ch1
ch2
ch3
ch4
ch5
ch6
ch7
SIS
BIS
CIBU
FEC
SPS
Steen Jensen, BE-BI-SW
Integrator gain
Channel selection
Amplifier gain
/8
BLM
BLM
BLM
BLM
Integrators
Multiplexer
Amplifier
ADC
ch32
ch33
ch34
ch35
ch36
ch37
ch38
ch39
BI_BLMADC #N, N <=4
Comparators
DAC1
/8
DAC8
…
…
…
/8
DAC1
DAC8
…
…
…
/8
DAC thresholds 1-16
Comparators
Set dump
Reset dump (general)
En-/disable dump
Reset watchdog timer
En-/disable dump channels
OR
Analogue integrated values
Analogue integrated values
Reset integrator
Reset dump (channels)
Start conversion
New version (v1) only
From BI_BLMDMP card in upstream FEC
Ch36 = Voltage of BLM power supply Ch37 = Current of BLM power supply
Ch38 = Unused
Ch39 = Unused
Maximum 36 BLM channels per FEC
BLM power supply
BLM ionization chambers in LHC
Disassemled BLM ionization chamber https://cds.cern.ch/record/930275/files/ab-2006-009.pdf
PostMortem
Notes: Here is an overview of the current beam-loss system in SPS.
The measuring device used for monitoring beam losses is an ionization chamber which gives an analogue output proportional to the radiation it receives.
This output is fed to the input of a VME hardware module which integrates and digitizes the signal so it can be read from the FESA class.
Another VME module – the BLMDMP - is connected to the BIS system and it allows us to dump the beam, either from the FESA class or in certain cases purely by hardware.

## Slide 3
Deployment
SPS overview, from https://cerncourier.com/protons-on-the-doorstep-of-the-lhc/
Transfer lines: LHC(TI2, TI8), AWAKE(TT40, TT41)
Active only on fast extractions
Single-shot => beam dump makes no sense => Prevents beam permit on following cycles, to be reset by operator.
Long Straight Sections (LSS)
Monitoring throughout cycle
Hardware based beam-dump in < 1ms
Arcs – the sections between LSS’s
Monitoring throughout cycle
Software based beam-dump in < 20ms
Software improvements possible
Notes: The BLM system is deployed in three different configurations:
…
In the following I focus on the configuration deployed in the Arcs

## Slide 4
Current Principle for Arc installations
CYCLE A
time
Cycle-losses
Steen Jensen, BE-BI-SW
Integration time, Δttick = 20ms
CYCLE B
Start Acquisition Measure @ tick Stop Acquisition
Cycle-losses
Response time up to 20ms
Only monitors integrated loss since cycle start
@Measure:
for ( all channels ) {
Acquire and store loss-value
if (loss-value > threshold) {
dump beam
}
}
@Stop acquisition:
for ( all channels ) {
Publish loss-values
}
@Start acquisition:
for ( all channels ) {
Reset & re-start hw integrator
}
Notes: The Arc installations work as follows:
Every 20ms the FESA class acquires the BLM value for each channel and determines if that value exceeds a predefined threshold.
If so, the beam is dumped.
Hence we are currently monitoring the integrated losses per cycle with a response time up to 20ms

## Slide 5
New functionalities for Arc (and LSS) installations
OP requests for the SPS BLM system:
Request: Reduce the integration time
  Solution: 5ms instead of 20ms (hardware access time reduced from ~12ms to ~2ms)
Request: Improve detection of fast losses
  Solution: 4 new interlocking running-sums:
    Veto-able per channel
    Adjustable threshold per channel
    Adjustable width per running-sum
    Sub-sets published every BP for visualization
    Timestamped max-values published end-cycle for diagnostic and trimming purposes
Additional functionality for RP (not interlocking)
  Ambient losses
    Measured from ejection to injection
  Fast extraction losses
    Measures losses in smallest possible time window covering the extraction
Notes: Op has requested an increase in mo

## Slide 6
New vs. Current Principles
CYCLE A
time
Cycle-losses
running-sum
Steen Jensen, BE-BI-SW
Post-LS2 principle
Δttick = 5ms
CYCLE B
Start Acquisition Measure @ tick
Fast extraction start
Fast extraction end Stop Acquisition
Cycle-losses
@Start acquisition:
for ( all channels ) {
Acquire & publish ambient loss
Reset & re-start hw integrator
}
@Measure:
For ( all channels ) {
Acquire and store loss-value
Process running-sum-1
Process running-sum-2
Process running-sum-3
Process running-sum-4
Process Cycle-running-sum
}
@Stop acquisition:
For ( all channels ) {
Publish max running-sums
Publish fast-extraction loss
Reset & re-start hw integrator
}
Ambient-losses
@Fast extraction start:
for ( all channels ) {
Register latest loss measurement as fast-extraction-start
}
@Fast extraction end:
for ( all channels ) {
Register latest loss measurement
Calculate/record difference from fast-extraction-start
}
“Process” means:
Calculate difference from loss X ticks ago
Compare difference to threshold
Dump beam if difference > threshold
Thresholds to be set by OP
Channels can be vetoed so they do not cause beam dumps
CYCLE A
time
Cycle-losses
Steen Jensen, BE-BI-SW
Current principle
Δttick = 20ms
CYCLE B
Start Acquisition Measure @ tick Stop Acquisition
Cycle-losses
@Measure:
for ( all channels ) {
Acquire and store loss-value
if (loss-value > threshold) {
dump beam
}
}
@Stop acquisition:
for ( all channels ) {
Publish loss-values
}
@Start acquisition:
for ( all channels ) {
Reset & re-start hw integrator
}

## Slide 7
Additional slides

## Slide 8
Deployment
Arcs
BLRSPS_BA1: 36 channels
BLRSPS_BA2 : 36 channels
BLRSPS_BA3 : 36 channels
BLRSPS_BA4 : 36 channels
BLRSPS_BA5 : 36 channels
BLRSPS_BA6 : 36 channels
BLRSPS_BA80 : 11 channels
LSS’s
BLRSPS_LSS: 12 channels
BLRSPS_LSS: 32 channels
BLRSPS_LSS: 8 channels
BLRSPS_LSS: 4 channels
BLRSPS_LSS: 14 channels
=>
297 channels
=>
297 channels
x
24 users
x
5 running-sums
=>
35.640 thresholds