## Slide 2: Simulation studies of the bunch length dependence on e-cloud build-up in circular drift tubes
Eric Wulff

## Slide 3
Outline
Goal
e-cloud simulation setup
SEY threshold
Heat load and current vs bunch length
Summary

## Slide 4
Outline
Goal
e-cloud simulation setup
SEY threshold
Heat load and current vs bunch length
Summary

## Slide 5
Goal
To study the dependence of bunch length on the heat load and current deposited on a circular drift tube of radius 40 mm

## Slide 6
Outline
Goal
e-cloud simulation setup
SEY threshold
Heat load and current vs bunch length
Summary

## Slide 7
e-cloud simulation setup
450 GeV beam energy
1.1 ×1011 p/bunch beam intensity
Standard 25 ns beam
No magnetic field
Uniform initial electron density
SEY scan: 1.0 - 1.8
Bunch length scan: 0.7 - 1.8 ns
Circular chamber with radius of 40mm

## Slide 8
Outline
Goal
e-cloud simulation setup
SEY threshold
Heat load and current vs bunch length
Summary

## Slide 9
SEY threshold
The SEY threshold is 1.4 for all simulated bunch lengths

## Slide 10
SEY threshold
The SEY threshold is 1.4 no matter which bunch length is used

## Slide 11
Outline
Goal
e-cloud simulation setup
SEY threshold
Heat load and current vs bunch length
Summary

## Slide 12
Current vs bunch length
The current is increasing linearly with the bunch length

## Slide 13
Heat load vs bunch length
For low SEYs the HL increases with growing bunch lengths
For high SEYs it decreases instead

## Slide 14
Outline
Goal
e-cloud simulation setup
SEY threshold
Heat load and current vs bunch length
Summary

## Slide 15
Summary
The SEY threshold is 1.4 for all bunch lengths in the range 0.7-1.8 ns according to simulations
The current is increasing linearly with the bunch length
For low SEYs the heat load increases with increasing bunch length
For high SEYs it decreases instead