## Slide 1: Status of ELENA C. Carli on behalf of the AD/ELENA team(s) ADUC, 30th October 2018
Recent Results from Commissioning (selection of a few highlights)
ELENA Commissioning Status
Summary and Outlook

## Slide 2: Recent Results from Commissioning Efforts for a new isolation transformer using oil as insulator
Last (repaired) isolation transfo using solid insulator and operated at 85 kV failed on Friday 21st September
Despite high priority by CERN groups for a transformer using oil, beam available only a few hours since
Oil tank for isolation transformer completed already on 26th September
Thanks a lot for the high priority and efforts by several groups and many people
Winding new secondary coil
Broken connector and new HV connection without connector
New support for secondary coils
1st mounting of transformer

## Slide 3: Recent Results from Commissioning Observation of the beam from the source on a ring pick-up
Observation of beam from source on first pick-up in ring
  Steering without kicker (flat-top shorter than beam pulse from source) up to first ring pick-up
  Higher deflection from septum and steering upstream
  No beam must hit pick-up plates (delicate!)
  Intensity fluctuations depend on source settings: probably caused by plasma fluctuations and may explain poor reproducibility observed
  Source optimisation easier with these observations
  Possibly, fluctuations may be reduced with longer rise times of the pulse
Pick-up sum signals showing (very likely intensity fluctuations, sometimes saturated)
Investigations by D. Gamba
Pick-up difference signals

## Slide 4: Recent Results from Commissioning Observation along the cycle
2 s/div
Peak signal of
pick-up sum signal
RF voltage
Intensity estimate from RF electronics
- Some signals along 2nd ramp and on the 100 keV plateau - Typical situation during the last weeks
- Significant efforts to reduce the loss and situation improving slowly
Bunched beam electron cooling
Real loss
Probably no loss, but systematic error with short bunches
- Measurements with a “scraper” at different times on the 35 MeV/c plateau
Clear emittance reduction observed
- Only limited amount of time spent on systematic optimization of electron cooling (lack of time)
=> Margin for further improvements?

## Slide 5: Recent Results from Commissioning Observation of antiproton beams at extraction
Bunches around extraction
  More than .5 107 antiprotons seen very reproducibly in ring prior to ejection and in line
  Possibly improved with better steering thanks to profile acquistions
  Bunch lengths a bit long with URF = 32 V programmed on harmonics h = 1
  Rms relative momentum spread of 0.68 10-3 from reconstruction about nominal (and possibly overestimated due to lower than expected RF voltage)
1 us/div
Transformer in LNE 50 line
Last time on a ring pick-up
Fast deflector
-0.6 0 0.6 ns
-0.6 0 0.6 keV
Reconstruction (“Tomography”) of longitudinal phase space density distribution from bunch shapes acquired during about one synchrotron oscillation

## Slide 6: Recent Results from Commissioning Observation of antiproton beams at extraction
Profiles in the GBAR line
  Acquisitions with second monitor LNE.BSGWA.5060 in GBAR line
  Beam sizes with voltages of first two quads of line set to zero
    bH =6 m gives rms emittance eH = 3.3 um (slightly overestimated without taking dispersion into account)
    bV = 20 m gives rms emittance eV = 1.25 um
Gaussian fit by hand with sH = 4.5 mm
Gaussian fit by hand with sV = 5 mm
Betatron functions along LNE50 line with settings to provide beam to GBAR and ring optics updated to quad settings used in practice

## Slide 7: Recent Results from Commissioning Observation of antiproton beams at extraction
Profiles in the GBAR line
  Acquisitions with second monitor LNE.BSGWA.5020 in GBAR line
  Beam sizes with voltages of first two quads of line set to zero
    bH = 6 m gives rms emittance eH = 4.1 um (slightly overestimated without taking dispersion into account)
    bV = 4 m gives rms emittance eV = 1.5 um
Gaussian fit by hand with sH = 5 mm
Gaussian fit by hand with sV = 2.5 mm

## Slide 8: ELENA Commissioning Status
Aims defined at the beginning of 2018:
  Continuation of Commissioning with electron cooler from April on
  Get Confidence that machine works properly
    Ideally demonstration of operational cycle to deliver 100 keV antiprotons
  First beams for GBAR
Achieved by and-October 2018:
  Deceleration of antiprotons to 100 keV so far with modest efficiency (very reproducible)
    Loss along 2nd ramp to 100 keV
    >20 % of injected beam extracted
  Clear emittance reduction in all three planes due to electron cooling (beneficial for deceleration)
  Operation for GBAR
    H- and antiproton bunches with about nominal intensities
    Emittance of antiproton bunches probably somewhat above nominal (factor <2 in transverse beam size)
Status, issues, plans:
  Less progress than expected at the beginning of the year, but evidence that conditions for experiments are improved
  Progress slowed down by unavailability of beam from the AD and from the source
  Open issues, studies to be done
    Estimate Injection matching, loss along second ramp, blow-up due to RF noise, still very limited observations with prototype profile monitor for transfer lines

## Slide 9: Summary and Outlook
Significant ELENA Commissioning progress over the year despite various delays
  Delay of restart due a vacuum leak of the cooler, unavailability of AD, issues with the ion source
  In practice, most progress made with antiprotons, only during dedicated AD shifts (change of commissioning strategy)
  Nominal antiproton cycle not (yet) available, single bunches (one per cycle) with characters “similar” to nominal bunches regularly sent to GBAR
Plans for LS2
  Installation of the transfer lines to the “old” experimental zone
  Upgrades of the ion source for reliable generation of 100 keV proton and H- beams
  Review of status and possible improvements (ring optics, applications, instrumentation …)
  Resume commissioning activities with beam from source in early summer 2020
    Test of ring and electron cooling with protons
    Commissioning of lines with H- (beam intensity and quality of measured profiles?)
Position of ELENA team on installation of lines to old experimental area
  Enough observations to be confident that ELENA can improve the conditions for the experiments despite a fully operational antiproton cycle not (yet) available
  Confidence in profile monitor availability thanks to a collaboration between Masaki Hori and BE/BI
  => Go on with the installation of the new lines (LS2 is the perfect moment for this activity)
  => Have 100 keV antiprotons for all experiments from 2021 on