## Slide 1: Tumor Therapy @ GSI
Gerhard Kraft
Biophysics Dep. GSI Darmstadt Germany
Motivation
Realisation

## Slide 2: Death in Germany (2007)
Cancer is the second most cause for death
https://de.wikipedia.org/wiki/Todesursache
live expectance : Men : 78 years / women: 83 Jahre
Statistisches Bundesamt (2012/14)
Motivation for ion beam therapy
cancer
cancer

## Slide 3
Motivation
Higher precision = better cure +less side effects ?

## Slide 4: Rational for particle therapy:
Physical advantages:
High dose at the end of range
small lateral scattering
Biological advantages
elevated relative biological effectiveness RBE in the tumor

## Slide 5: Technical problems
From a 1-dimensional monoenergetic beam
to a tumorconform treatment volume
possibilities for particle
beam shaping
Passive methods
absorber , collimators
Active methods:
Scanning , energy variation
IMRT
Particles

## Slide 6
Intense ion beam
Principle of beam scanning
Phatom of solid mater

## Slide 7: Active beam delivery: Principles of Beam scanning
O.Jaekel DKFZ
Notes: Evtl Animation

## Slide 8: Comparison of Treatment Plans
Heavy Ions (2 Fields)
IMRT (9 Fields)

## Slide 10: Advantages of Carbon
Higher precision => greater dose to tumor
=> smaller dose to normal tissue
Greater biological effectiveness
but restricted to the target volume
staying low in the normal tissue

## Slide 12
Dose distribution in nanometer scale

## Slide 13: Protons versus Carbon:
Survival
Carbon
Proton
Calculations : LEM IV Model
Experiment at HIT : same parameters
Protons and Carbon beams alternating
CHO cells
Normalized : same effect in the entrance
W.K.Weyrather et al.@ GSI

## Slide 14: Dose & RBE for protons, carbon, neon
in color: dose
RBE maximum

## Slide 15
Röntgenröhre
Bildverstärker
Patientenmaske
Strahlaustrittsfenster
Patientenmonitor
Patient
PET-Kamera
Patiententisch

## Slide 16: X-ray Imaging in Treatment Position

## Slide 17
Quality& beam control:
Ionisation- / multiwire Chambers
>10 000 measurements / sec
Patient fixation
In vivo beamcontrol with PET

## Slide 18: PET-control of treatment
projectile
target
[Enghardt et al. Rossendorf]

## Slide 19: Dose verification with PET
Treatment plan
Predicted b+-activity
Measured b+-activity
3D reconstruction by back projection
Positron emitter distribution neither proportional nor equivalent to the dose distribution
Comparison with expected positrion emitter distribution
[Enghardt et al. Rossendorf]

## Slide 20: Treatment of tumors close to the eye
39 patients
  High precision treatment using rasterscan
  precission spares critical structures
  Push button experiment
  correlates flashes with scan position
Patient signal
Patient signal
taking into account
reaction time
Light flashes are associated with
radiation effects in the retina
no evidence for direct stimulation of the optic nerves

## Slide 21
Carbon treatment of a recurrent chordoma in a 5 year old child
After 5 years 8 years 12 years
For comparison : IMRT treatment after 5 years
Sparing of bone sutures in children
No asymetric growth after particle RT
J.Debus et al.

## Slide 22: Absorbed dose along the spinal cord in a human phantom
Measurement direction
La Tessa ,Kaderka et al., Radiother Oncol , 2012
Beam
direction
Notes: 22

## Slide 23: Treatment plan: medulloblastoma
Intention to treat spinal cord and brain only

## Slide 24: Differential RBE in patients High RBE in the tumor, low RBE for the skin

## Slide 25: Tumor Control Rates: Chordomas
Schulz-Ertner, IJROBP 2007
Conventional RT
Protons
C-Ions
Better control because of:
higher target dose and better sparing of normal tissue : physical selectivity
greater biological effectiveness in the tumor : biological selectivity

## Slide 26: Summary Rational for Particle RT
Higher conformity to the target volume
Smaller scattering to normal tissue
Increased effectivenes for radioresitant tumors
But :
More complex beam delivery
sensitive to target motion

## Slide 27: Heidelberg Ion Beam Therapy (HIT)
Proposal 1998 – start 2003 – first patient 2009
Proton, Carbon, (Helium, Oxygen) @ 100 – 400 MeV/u
  GSI: hardware, Siemens: software, medical product
2 horizontal beams, 1 gantry, 1 research beam
>3500 patients treated
  ~700 / year
  up to 16h per day
  >300 days / year

## Slide 28: IGRT in der Partikeltherapie
Isocentric Rotation +/-100°
Roll max. +/-15°
Roboter zur - Positionierung - Bildsteuerung

## Slide 29: Ion beam therapies worldwide
MIT (2015)
HIT
(2009)
CNAO
(2012)
Med. Austron
(2016 )
SPHIC
(2012)
IMP-CAS
(2012)
HIMAC
(1994)
HIBMC
(2002)
GHMC
(2010)
SAGA-HIMAT
(2013)
i-ROCK
(2015)
KHIMA
(2018 geplant)
> 60 proton centers not shown, ~25 in the US
2 carbon centers in the US in planning stage

## Slide 30
GSI Darmstadt
oldest building at Darmstadt
900 years
DNA, dose and cell survival
2 km
Ion beam therapy
window

## Slide 31
Danke fürs
Zuhören

## Slide 33: Energy-Deposition in Micrometer-Scale
Zellkerne

## Slide 34: Comparison of treatment plans