## Slide 1
SpecMAT Spectroscopy of exotic nuclei
in a Magnetic Active Target
Riccardo Raabe
KU Leuven, Instituut voor Kern- en Stralingsfysica

## Slide 2: The active-target method
LOI I-119
Time-Projection Chamber (TPC) + gas is the target
  Full 3D track reconstruction
  High luminosity, keeping energy resolution
  Energy of stopped particles Particle identification
  Versatile: different gases, pressures, configurations ancillary detectors

## Slide 3: The active-target method
Time-Projection Chamber (TPC) + gas is the target
  Full 3D track reconstruction
  High luminosity, keeping energy resolution
  Energy of stopped particles Particle identification
  Versatile: different gases, pressures, configurations ancillary detectors
  SpecMAT:
  Magnetic field parallel to the beam direction
  Drift field parallel to magnetic field

## Slide 4: The active-target method
J. Diriken et al., PLB 736, 533 (2014) J. Diriken et al., PRC 91, 054321 (2015)
`
𝛾-ray detection
  CeBr3 scintillators: good efficiency and resolution
  Si photomultipliers

## Slide 5: Physics goals
stable nuclei
observed nuclei
unknown nuclei (predicted)
8
2
20
28
50
126
208Pb
78Ni
82
28
20
8
50
82
Changes in nuclear structure far from stability
  Shell evolution towards 78Ni
  Shape coexistence “west” of 208Pb

## Slide 6: Shell evolution towards 78Ni
K. Flanagan et al., PRL 103 (2009) 142501
  Migration of πf7/2, πf5/2 as νg9/2 is filled (tensor interaction)

## Slide 7: Shell evolution towards 78Ni
K. Flanagan et al., PRL 103 (2009) 142501
  Migration of πf7/2, πf5/2 as νg9/2 is filled (tensor interaction)
LOI I-191
Proposal P-495: 72,74,76Zn(d,3He) to directly measure the f7/2-f5/2 gap

## Slide 8: Shell evolution and shape coexistence
68Ni
Y Tsunoda, T Otsuka et al., PRC 89 (2014) 031301

## Slide 9: Shell evolution and shape coexistence
68Ni
Y Tsunoda, T Otsuka et al., PRC 89 (2014) 031301
T Otsuka and Y Tsunoda, JPG 43 (2016) 024009

## Slide 10: The n-deficient Pb region
B A Marsh et al., Nature Physics (2018)
Hg

## Slide 11: The n-deficient Pb region
  Transfer reactions in Hg
  185g,mHg (d,p), (p,d), (α,3He)
  Beam intensity ≈ 105 pps → feasible!
Data: NNDC, figure courtesy of Liam Gaffney Original figure in R. Julin et al., J. Phys. G 27 (2001) R109

## Slide 12: The n-deficient Pb region
  Transfer reactions in Hg
  185g,mHg (d,p) and (p,d)
  Beam intensity ≈ 105 pps → feasible!
Data: NNDC, figure courtesy of Liam Gaffney Original figure in R. Julin et al., J. Phys. G 27 (2001) R109
LOI I-195

## Slide 13: Study of the Pigmy Dipole Resonance
  Low-energy dipole strength
  First observation in 1961 𝛾 rays from neutron capture G.A. Bartholomew, Annu. Rev. Nucl. Sci. 11 (1961) 259
  First use of “pygmy resonance” (PDR) J.S. Brzosko et al., Can. J. Phys 47 (1969) 2849
  Description as a collective excitation Mohan et al., Phys. Rev. C 3 (1971) 1740 “Three-Fluid Hydrodynamical Model of Nuclei”: Neutron excess oscillates against the N=Z core
  Different experimental probes to investigate the isospin nature of these states
  Figure A. Bracco et al., Eur. Phys. J. A 51 (2015) 99 Data from K. Govaert et al., Phys. Rev. C 57 (1998) 2229 and J. Endres et al., Phys. Rev. C 85 (2012) 064331
isoscalar
isoscalar+
isovector

## Slide 14: Study of the Pigmy Dipole Resonance
  D. Vretenar et al., J. Phys. G 35 (2008) 014039
Core in phase +neutron skin
PDR
IVGDR

## Slide 15: Study of the Pigmy Dipole Resonance
  Isoscalar probe: (α,α’) inelastic scattering
  SpecMAT: 𝛾 rays from decay of bound states
  Cases: 90Sr, 194Hg, 146,148,150Gd ≈10 MeV/nucleon
LOI I-194

## Slide 16: Status
Design: O. Poleshchuk, KU Leuven
  GET Electronics (2048 channels): purchased and commissioned
  Pad plane and field cage designed in CERN (EP-DT-DD MPT) to be ordered shortly
  Chamber finalized and ordered
  Scintillators + SiPMs purchased, commissioning ongoing 48x48x48 mm3 Photopeak efficiency 8% at 1 MeV Nominal resolution 3.9% at 661 keV No degradation in 3-T magnetic field

## Slide 17: Status
Design: O. Poleshchuk, KU Leuven
  GET Electronics (2048 channels): purchased and commissioned
  Pad plane and field cage designed in CERN (EP-DT-DD MPT) to be ordered shortly
  Chamber finalized and ordered
  Scintillators + SiPMs purchased, commissioning ongoing 48x48x48 mm3 Photopeak efficiency 8% at 1 MeV Nominal resolution 3.9% at 661 keV No degradation in 3-T magnetic field

## Slide 18: Status
Design: O. Poleshchuk, KU Leuven
  GET Electronics (2048 channels): purchased and commissioned
  Pad plane and field cage designed in CERN (EP-DT-DD MPT) to be ordered shortly
  Chamber finalized and ordered
  Scintillators + SiPMs purchased, commissioning ongoing 48x48x48 mm3 Photopeak efficiency 8% at 1 MeV Nominal resolution 3.9% at 661 keV No degradation in 3-T magnetic field

## Slide 19: Status
Design: O. Poleshchuk, KU Leuven
  GET Electronics (2048 channels): purchased and commissioned
  Pad plane and field cage designed in CERN (EP-DT-DD MPT) to be ordered shortly
  Chamber finalized and ordered
  Scintillators + SiPMs purchased, commissioning ongoing 48x48x48 mm3 Photopeak efficiency 8% at 1 MeV Nominal resolution 3.9% at 661 keV No degradation in 3-T magnetic field
  Simulations for: electric field, mechanical stress, gas flow

## Slide 20: Status
Design: O. Poleshchuk, KU Leuven
  GET Electronics (2048 channels): purchased and commissioned
  Pad plane and field cage designed in CERN (EP-DT-DD MPT) to be ordered shortly
  Chamber finalized and ordered
  Scintillators + SiPMs purchased, commissioning ongoing 48x48x48 mm3 Photopeak efficiency 8% at 1 MeV Nominal resolution 3.9% at 661 keV No degradation in 3-T magnetic field

## Slide 21: Installation
  Installation through a platform and rails from the back of the ISS
  Cables (8m) running to the electronics racks outside the cage
  To be coordinated with the installation of the new ISS array

## Slide 22: Planning
  January – March 2019: characterisation of the full system
  Characterisation of the 𝛾-ray array
  Leak tests of the detector chamber
  Commissioning of the gas control system
  Tests of the electric field cage
  Characterisation of particle tracks
  2019 Move to CERN
  Safety clearance
  Installation

## Slide 23: Summary
  Thanks to the SpecMAT team!
  A. Arokja Raj, H. De Witte, O. Poleshchuk, J. Refsgaard, M. Renaud, J. Yang With us in the past: S. Ceruti, M. Babo, T. Marchi, C. Swartz
  The research leading to these results has received funding from the European Research Council under the European Union's Seventh Framework Programme (FP/2007-2013) / ERC Grant Agreement n. 617156