## Slide 1: PSB Beam Production Schemes with L4 C. Carli and B. Mikulec
Introduction
First Injections for Commissioning
First intermediate (and high) intensity beams with “slow” capture
Very low Intensity Beams
Intermediate Intensities – Injection into waiting buckets without painting
Longitudinal Painting for maximum Brightness (LHC) and Intensity (CNGS and ISOLDE)
Summary and Outlook

## Slide 2: Prerequisites
Linac4 successful commissioning including
  Pre-chopper and chopper
    to guarantee a min. of beam to head/tail dump of distributor
    no losses during switching between rings
    to allow the correct timing structure of the beam for injection into PSB RF buckets
  Linac4 beam characterisation in measurement lines
Synchronisation of Linac4 beam with injection systems (distributor, beam instrumentation, chicane bump, painting bump, PSB RF) has to be working
Adequate beam diagnostics has to be available (injection line and PSB rings)
Exhaustive hardware tests of newly installed equipment by equipment specialists (BI line)
Interlock for injection into the PSB functional
If necessary re-matching of the PSB injection line
Preparation of new magnetic cycle(s) in the PSB

## Slide 3: Introduction (1/2)
Aim of this presentation:
  Sketch schemes how beams could be generated in the PSB with Linac4 (approximately in the order they will be needed) during commissioning and operation
  Make sure that all schemes are compatible with installed hardware, synchronisation and control
  Proposals to be discussed/adapted with equipment specialists
Start with transfer of a beam at min. intensity (just enough to be detected by beam instrumentation) to avoid activation
  Losses have to be minimised due to increased activation with p lost at 160 instead of 50 MeV
Different phases of PSB re-commissioning with Linac4
  Re-commissioning to “nominal” performance (reproduce beams available with Linac2)
    Probably only injection of coasting beams and adiabatic capture (slower than now on plateau to minimise losses)
    Maybe injection of beams with large energy spread into waiting buckets on plateau for higher intensities
    Optimise transverse painting (hor.) and injection with offset (hor. and vert.)
  Commissioning to “ultimate” performance (profit from Linac4 to obtain better performance)
    Setting up of longitudinal painting first on plateau, then on ramp

## Slide 4: Introduction (2/2)
Linac4 intensity adjustments:
  At present: difficult to generate large transverse emittances by injecting one turn with large betatron oscillations and filamentation with “high” intensity Linac2 beam (M. Chanel)
    Coherent oscillations go on for several ms (can be explained by direct space charge) and are damped slowly (maybe by an impedance) yielding small emittances
    No such phenomenon with the “sieve” (reducing the Linac2 current density)
  Intensity variation pulse-by-pulse at source level not an option
  Reduction of Linac4 intensity by adjusting optics in LEBT and/or chopper line studied by Alessandra’s team
Beam head:
  In principle not required (see presentation of P. Baudrenghien http://indico.cern.ch/conferenceDisplay.py?confId=61654)
  Could be added easily (structure to be defined with RF experts) and is plotted in some cases
Versatility of PSB must be maintained with Linac4
  Providing from one cycle to the next beams with very different characteristics
  Intensities varying by more than three orders of magnitude (a few 109 to ~2×1013 per ring with Linac4)

## Slide 5: Current Beams from PSB
user | description | h (at ej.) | rings | intensity per ring | emittance (rms) x [mm mrad] (n.) y [mm mrad] (n.) z [eVs] at extraction | dp/p [10-3] | bunch length at extraction [ns] | energy [GeV]
LHC25A LHC25B | 25 ns LHC beam | 1 | 1,2,3,4 3+4 | nominal: 1.6E12 (optional 1/10, 1/5, 1/3, 1/2, 2/3) | 2.5 2.5 1.3 | 2.0 | 180 | 1.4
LHC50 | 50 ns LHC beam | 2+1 | 2,3,4 | 1.6E12 | 2.5 2.5 0.9 | 2.0 | 140 | 1.4
LHC75 | 75 ns LHC beam | 2+1 | 2,3,4 | 1.6-10.8E11 | 2.5 2.5 0.9 | 2.0 | 140 | 1.4
LHCPILOT | early LHC beam | 1 | 3 | 0.5E10 | 2.5 2.5 0.3 | 1.0 | 85 | 1.4
LHCPROBE | early LHC beam | 1 | 3 | 0.5-2.0E10 | <1 <1 0.2 | 1.0 | 75 | 1.4
LHCINDIV | single bunch physics beam | 1 | 1-4 | 2.0-12E10 | 2.5 2.5 0.3 | 1.0 | 80 | 1.4
* LHC50
Notes: For nominal LHC beam ~85% transmission through injector chain was assumed.

## Slide 6: Current Beams from PSB
user | description | h | rings | intensity per ring | emittance (rms) x [mm mrad] (n.) y [mm mrad] (n.) z [eVs] at extraction | dp/p [10-3] | Bunch length at extraction total, [ns] | energy [GeV]
SFTPRO | SPS fixed target | 2 | 1,2,3,4 | 3.5E12 | 6.0-8.0 5.0-6.0 1.6 | 2.7 | 180 | 1.4
CNGS | CNGS beam | 2 | 1,2,3,4 | 0.6-8.0E12 | varying varying 1.6 | 2.7 | 180 | 1.4
EASTA | PS East Hall | 1 | 3 | 2.0-3.0E11 | 3.0 1.0 1.1 | 2.0 | 150 | 1.4
EASTB | PS East Hall | 1 | 2,3 | 1.0E11 | 3.0 1.0 1.1 | 2.0 | 150 | 1.4
EASTC | PS East Hall | 1 | 3 | 4.5E11 | 3.0 1.0 1.1 | 2.0 | 150 | 1.4
AD | AD beam | 1 | 1,2,3,4 | 4.0E12 | 7.0-8.0 6.0 1.7 | 2.2 | 190 | 1.4
NORMHRS NORMGPS | ISOLDE HRS and GPS | 1 | 1,2,3,4 | up to 1E13 | <15.0 <9.0 2.3 | 2.7 | 230 | 1.0/1.4
STAGISO | ISOLDE staggered beam | 1 | 2,3,4 | depending on experiment | <5.0 <4.0 <1.6 | <2.0 | 230 | 1.0/1.4
TOF | nTOF beam | 1 | 1,2,3,4 | 9.0E12 | ~20 ~10 2.1 | 2.9 | 230 | 1.4

## Slide 7: First Injections for Commissioning (1/2)
Aim:
  Very first stage of PSB re-commissioning with Linac4
  Simple structure
  Intensity sufficient for diagnostics
Steps
  For matching and dispersion we rely as a first approximation on the measurement lines
    Start with 0 dispersion (at PSB injection) matching optics
  Steer beam through injection line & injection region
    PUs, BLMs, view screen close to foil position,…
  Beam structure to be provided by chopper: inject ~half a turn to create a beam structure visible with Booster pick-ups
  Quantify beam properties
  Closure of bumps (injection painting bump and chicane bump)
    Need multi-turn acquisition ability of at least a couple of PSB PUs
  Establish first injections and circulating beam
    Start with injection of coasting beam on a flat bottom
    Can we improve chicane bump closure (if required) by adjusting BS magnets individually?
  Continue with capture, later acceleration and extraction (no problems expected here)
Notes: ‘low’ intensity means already 2e11 p at 65 mA!

## Slide 8: First Injections for Commissioning (2/2)
Chopper pulse form (upper part) and beam structure (lower part) for first injections with Linac4
Probably beam head will not be needed (feed-forward)?
Just one beam slice (less than half a turn, i.e. <176 Linac4 bunches) injected for diagnostics (trajectory, closure of bumps…) with “low” intensity … until first circulating beam and capture
Next steps: injection in other ring/several rings, acceleration, extraction, increase intensity
Injection ring 3
just one beam
piece <0.5 ms
Beam head
(if necessary)
Distributor
switching beam
head to ring 3
> 20 ms LEBT
stabilization
> 20 ms source
switch off
Distributor
switching
ring 3 to tail dump
Chopper:
Beam:
Notes: ‘low’ intensity means already 2e11 p at 65 mA!

## Slide 9: Very Low Intensity Beams (1/2)
Simple calculation:
  One 40 ns chopper gap (=assumed min. chopper OFF time) lets 14 Linac4 bunches through
  At 65 mA one would only need 5-20 Linac4 bunches to produce the LHCPILOT and LHCPROBE beam (5 109 p / 5-23 109 p)
  A single PSB turn without chopping at 65 mA yields already 4 1011 particles.
At present: very low intensity obtained by heavy shaving (longitudinal, if not too small transverse emittances required – e.g. for LHCPILOT & LHC single bunch physics)
  Some losses and activation
Aim: Find schemes allowing to reduce losses using the chopper…. inject less particles
Linac4 Current | # Particles/Linac4 Bunch
65 mA | 1.15 109
40 mA | 0.70 109

## Slide 10: Very Low Intensity Beams (2/2)
Example to produce one low intensity bunch in each Booster Ring (in case some rings are not used, the Linac4 source pulse has to be shortened; trigger several distributor levels)
Injection without RF on plateau and “slow” capture after filamentation (say ~10 ms)
Several turns injected to obtain transverse emittances, longitudinal shaving (few particles lost) and blow-up to create longitudinal emittances.
No synchronization between Linac4 and PSB RF and between PSB rings required
Injection ring 4
1 to 10 pieces of
~40 ns per revolution
Beam head
(if necessary)
Distributor
switching beam
head to ring 4
Distributor
switching
ring 4 to ring 3
> 20 ms LEBT
stabilization
Injection ring 3
1 to 10 pieces of
~40 ns per revolution
> 20 ms source
switch off
Distributor
switching
ring 1 to tail dump
Injection ring 2 & 1
structure like rings 4 & 3
Distributor
switching
ring 3 to ring 2
Chopper:
Beam:
Notes: transv. emittances: falling painting bump ~120 turns (maybe injection on flat chicane bump; chicane bump falls after trigger; much slower than painting bump ~5 ms)
in addition inject with offset

## Slide 11: First intermediate (and high) intensity beams with “slow” capture
Inject 3 to 10 turns, Iav < 40mA (solid: reduced peak current, dotted: chopping to reduce Iav)
Injection on plateau (~x2 less tune spread than now) followed by filamentation and slow capture
Adjust working point
Maximum achievable intensity (losses and activation) compatible with CNGS??
No synchronization between Linac4 and PSB RF and between PSB rings required
Injection ring 3
3 to 10 turns
Distributor
switching beam
head to ring 3
>20 ms LEBT
stabilization &
beam head if needed
> 20 ms source
switch off
Distributor
switching
ring 1 to tail dump
Injection ring 2 and 1
structure see ring 3
Distributor
switching beam
head to ring 2/1
Chopper:
Beam:

## Slide 12: Intermediate Intensities – Injection into Waiting Buckets without Longitudinal Painting
This option could be envisaged
  If intensity too low for longitudinal painting to be practical
  If losses of adiabatic capture are too high for increased intensities
Description
  Waiting h1+h2 bucket for max. acceptance
  Possibly injection on ramp of 0.5 μs long beam pulse
  Increase natural energy spread of Linac4 beam (~120 keV 1σ) through detuning of debuncher (increase by ~factor of 3) – is this realistic?
Trev

## Slide 13: Intermediate Intensities – Injection into Waiting Buckets without Longitudinal Painting
Example to produce beam in each Booster Ring (if needed skip injection in unwanted rings)
Synchronization of Linac4 beam (not Linac4 RF) with Booster RF required
  Without synchronization of the four PSB rings: non-predictable and non-reproducible gaps at switching between rings
Injection ring 4
~0.5 ms/revolution
Beam head
(if necessary)
Distributor
switching beam
head to ring 4
Distributor
switching
ring 4 to ring 3
> 20 ms LEBT
stabilization
Injection ring 3
~0.5 ms/revolution
> 20 ms source
switch off
Distributor
switching
ring 1 to tail dump
Injection ring 2 & 1
structure like rings 4 & 3
Distributor
switching
ring 3 to ring 2
Chopper:
Beam:

## Slide 14: Longitudinal Painting for maximum Brightness (LHC) and Intensity (CNGS and ISOLDE) (1/4)
Recap of basic idea
  Saw-tooth shape energy offset (w.r.t PSB synch energy) variations of Linac4 beam
  Switch beam on and off if it is inside bucket (with margin)
  Inject into waiting accelerating bucket !!
Baseline: 20 turns minimum energy modulation period and 65 mA peak beam current
  One energy modulation period yields more intensity than nominal LHC (see later)
  Longer and/or several energy modulation periods for higher intensities
Longitudinal painting is baseline to fully profit from the increased PSB injection energy

## Slide 15: Longitudinal Painting for maximum Brightness (LHC) and Intensity (CNGS and ISOLDE) (2/4)
Longitudinal painting:
  Chopper pulse and energy modulation (dashed line)
  Beam structure (lower part)
one energy modulation period lasting 20 turns
(in this example)
> 20 ms LEBT
Stabilization
& beam head ?
Injection ring 4
One to five energy modulations
Small energy offset
Long Linac4 trains
Large energy offset
short Linac4 trains
Injection
ring 3
Injection
ring 2
Injection
ring 1
> 20 ms source
switch off

## Slide 16: Longitudinal Painting for maximum Brightness (LHC) and Intensity (CNGS and ISOLDE) (3/4)
Implications of acceleration
  Change of synchronous energy in filled ring to be compensated (same field for each ring during filling; adapt frequency)
    Worst (±154 keV) for longest injections
  Frequency change during injection into one ring (ramp)
Intensity for nominal LHC beam
  After one “nominal“ energy modulation period (20 turns) and peak current 65mA already 50% more intensity than required for nominal LHC beam (single batch PS transfer, 25ns)
  Energy modulation period likely to increase (Linac4 RF power and bandwidth restrictions)
  Reduction of Linac4 peak current with special Linac4 optics around the chopper (studied by Alessandra’s team)
  Variants of “nominal” painting scheme described before:
    Reduction of the average current by chopping (high frequency) additional short gaps into Linac4 pulse (sketch on next slide)
    Maybe easier to implement: injection every second turn … or even every third turn only (sketch on next slide)
  Watch out for multiple scattering in injection foil (emittance increase)

## Slide 17: Longitudinal Painting for maximum Brightness (LHC) and Intensity (CNGS and ISOLDE) (4/4)
Injection every second turn to halve intensity
Nominal (for single batch PS transfer) LHC intensity after one energy modulation period with 65mA peak beam current
Reduce “average” current during beam on by chopping additional short gaps
Injection into one ring with one energy modulation period
(lasting 26 turns in this example)
Chopper pulse and beam currents versus time
one energy modulation period lasting 26 turns in this example
Chopper pulse (upper images) and beam currents versus time

## Slide 18: PSB operation with pre-chopper only – emergency scenario (hopefully never applied)
Aim: Linac4 & PSB operation in case of 3 MeV chopper failure (delicate device)
Upgraded pre-chopper: can pulse multiple times to stop the beam (i) during switching PSB injection between rings and (ii) after completion of injection (source stop)
  Injection of coasting beams (no longitudinal painting, schemes to tailor distributions …)
  Linac4 (peak) beam current limited by Linac4 beam loading (<65 mA)
  Many partially deflected bunches during pre-chopper switching
  Will LEBT space charge compensation follow beam during pre-chopper pulsing?
Injection ring 3 just
one beam piece first ~20 ms
instable beam? (LEBT
space charge build-up)
Distributor
switching to ring 4
Source stabilization
no LEBT space
charge build-up?
> 20 ms source
switch off
Distributor
Switching to ring 3
Pre-chopper:
Beam:
Injection ring 4
Partially deflected
Linac4 bunches
Notes: Reaction time of pre-chopper: ~3 us; ~20-30 us for space charge compensation; fall time: ~2 us

## Slide 19: Summary and Outlook
Schemes to generate PSB beams at low energy with Linac4 have been sketched
  Various ideas exist for generating beams at low energy in the PSB
  Commissioning and all present operational beams covered by variants of schemes presented
  Flexibility exists; schemes can be adapted within certain limits, but need to keep margins for the “real” scenario
Next step: Discussion with work packages concerned to confirm feasibility & refine
    H- source: variable pulse length and operational limits
    Low level RF: implementation of chopping sequences and energy modulation
    Chopper: final optimisation of parameters
    Debunching: feasibility of different energy spreads for RF and Linac4 beam dynamics
    Interface and synchronization between Linac4 and PSB must be compatible with all cases (special attention on “0-turns” - leave out individual rings - and ring-specific triggers; high-level controls application)
    PSB H- injection

## Slide 20: Backup Slides

## Slide 21: Nominal Performance
Commissioning steps for first 3 months of 2015:
  Verify correct functioning of new distributor, septum, dumps and foil with available diagnostics
  Steer beam through injection chicane
  Verify closure of the injection bump and orbit
    For PUs need structure and sufficient signal  inject ~0.5 μs of beam into one ring
  Inject and capture first beams with small intensities
    Inject on plateau and slow adiabatic capture
  Minimise losses along cycle
  Increase gradually beam intensity and retune machine
  Reproduce each currently available beam in order of demand
Prerequisites:
  Working and sufficient diagnostics
  Adjust pulse length of Linac4 source
    R. Scrivens: possible, but affects intensity; 3 MeV tests should be pursued
  Need pre- and chopper functional (remove unuseable parts of source pulse; distributor gap)
  Need transverse painting to achieve larger transverse emittances for higher intensity beams or injection at large offsets with reduced source current; transverse blow-up?

## Slide 22: Ultimate Performance
Commissioning steps for “ultimate” performance (from ~April 2015):
  Maybe already during commissioning to “nominal” performance: injection into a waiting bucket for intermediate intensity beams (e.g. LHC50ns beam or LHC25ns at lower intensities)
    ~0.5 μs of beam with large energy spread
  Setting up of longitudinal painting
    First painting into buckets on a plateau, followed by painting on a ramp
    Minimise capture losses
Additional prerequisites:
  Increase energy spread with debuncher (dephasing?)
  Synchronisation of chopper and last PIMS modules with PSB RF
  Synchronisation differing between individual PSB rings

## Slide 23: 3 MeV Chopper
Remarks:
  3 MeV chopper characteristics (M. Paoluzzi)
  For the following considerations we assume to use the CERN driver with min OFF-time (i.e. when beam passes) of 40 ns.
 | Commercial Driver (FID) | CERN Driver
τon | 4.3 ns | 5.1 ns
τoff | 4.5 ns | 4.9 ns
Max. pulse duration | 1 μs | 50 μs
Min. ON time | 25 ns | 
Min. OFF time | 45 ns | ~30 ns tbc.
Pulse repetition rate | 15 MHz | 5 MHz
Notes: Commercial driver: 1 partially deflected bunch; CERN driver: 2 partially deflected bunches.