## Slide 1: Forward Detectors Report
A. Sbrizzi

## Slide 2: Integration of ZDC and ALFA in Athena (A. Dell’Acqua)
World volume increased to include the forward region when:
  SimFlags.ForwardDetectors.set_On()
ALFA activated in the G4 simulation (see Tom’stalk):
  DetFlags.ALFA_setOn()
Eta/Phi filters must be switched off to shoot particles in the forward detectors
  SimFlags.EventFilter.set_Off()
ZDC not yet there (12/10)

## Slide 3: Integration of Beam Transport Code in Athena (A. Dell’Acqua)
Currently, only G4 transport is available
  Rectilinear propagation (good for neutrals, not for charged particles)
Scheme proposed by A.Dell’Acqua
  Use G4 tracking to the end of the ATLAS cavern
  FP(N)Track will kick in and transport particles to the front face of the detector where accurate G4 simulation can be restarted
  This scheme is “technically” simpler than the original one proposed by ALFA and its implementation will start immediately since it is independent from the detectors being activated in the simulation (12/10)
Discuss the possibility to use the FLUKA simulation of the ATLAS-TRT region (R. Bruce) as the non-pp collision group (D.Berge, W.Kozanecki)

## Slide 4: Neutron transport (E. Carquin)
Edson is now taking care of FNTracker
  Mark Baker is no longer available
  D.Macina (LHC staff) is providing precious help for accelerator settings
First version of FNTracker has been obtained adapting FPTracker, which is valid for protons (see Tom’s talk), to handle neutral particles
Simple scheme to simulate particle decays has been added by Edson
  First trigger efficiencies based on the number of transported particles crossing the ZDC volume (no full simulation yet) are available
For the future
  Discuss the possibility to merge the two programs

## Slide 5: ZDC simulation (S. Mohapatra)
The first svn version created by A.Dell’Acqua will we updated by Soumya with the new features he developed (12/10)
Added two flags to simulation
  G4AtlasApps.SimFlags.ZdcPixelStatus=True/False
  G4AtlasApps.SimFlags.ZdcStripStatus=True/False
Final container adapted to be identical to real data
  Only done for strips, easily ported to pixels
Number/energy of photons in the strips/pixels are returned
  Both high and low gain channels are simulated
CPU Time
  The simulation of 7 TeV neutrons takes 10 min/event
  Ready to investigate other solutions if this turns to be an issue