## Slide 1
Powerlink: status and developments
Mattia Rizzi

## Slide 2
Industrial Ethernet Fieldbus
  ProfiNET (Siemens)
  EtherCAT
  Ethernet/IP
Open Standard
  No patents (royalties)
  No mandatory subscriptions
  No mandatory sell
Powerlink – What is?

## Slide 3
Fieldbus – What it does?
Transfer (physical) process data across a network
  Logical link between application and data produced/consumed by remote devices
Synchronization
Cycled vs event-driven
Fieldbus
Master node (PLC)
Position sensor
Motor
Operator Control panel
1 byte
(position setpoint)
2 bytes: encoder
1 byte: current
position setpoint
Control law
actual position
current intensity
Motor
Position sensor

## Slide 4
Powerlink network
Cycle based (down to sub-ms)
Master to slave polling requests and answers (broadcast)
Slave can directly use data produced by other slaves
Syncronous and asynchronus time-slots in each cycle
  isochronic cycles for time-critical data
  asynchronous for less time-critical data
Star or daisy-chain topology allowed
Master can configure slaves
  Only truly required data in isochronic cycles
Rad-tol slaves compliant with CiA-401: generic I/O module
  Up to 4 RPDOs
Fieldbus
Master node (PLC)
Position sensor
Motor
Operator Control panel
1 byte
(position setpoint)
2 bytes: encoder
1 byte: current
Monitor

## Slide 5
Powerlink stack
Open source implementation available (openPOWERLINK)
Run on a number of devices
  PLC
  Computer (userland and kernel)
  Embedded devices
    Userland runs in a ARM
    Kernel runs in a soft-processor for real-time perfomances
openPOWERLINK not designed for low-memory embedded device
  Running userland & kernel stack require >300 kB of memory (code and data)
  Code of Master and Slave implementation is mixed together
Goal: run it on a SmartFusion 2 FPGA

## Slide 6
SmartFusion 2
FLASH based FPGA, with fabric SRAM and DFFs
ARM core + ECC SRAM (64 kB) + eNVM (flash memory for code)

## Slide 7
Results at CHARM using ARM Cortex-M3
openPOWERLINK memory footprint reduced to 170 kB (143 kB of code, 27 kB of data)
Processor clocked at 100 MHz
Data memory protected by ECC
Tested in G0 position for one week (about 25 Gy TID)
  Multiple self-resets due to internal PLL loss-of-lock
  Freezed several times (one every 10 hours), power cycle required, no useful debug messages
  No increased power consumption detected
Cortex-M3 is not TMRed
AHB interconnect is not TMR
eNVM is OK under radiation, but it is connected to AHB interconnect!

## Slide 8
Soft-core based SoC
RISC-V softprocessor with TMR
ECC (SEC-DED) instruction memory up to 92 kB
ECC (SEC-DED) data memory up to 32 kB ought to be enough for anybody
Application loaded from eNVM memory and stored inside both memories (integrity check/cryptographic signature)
RISC-V
RISC-V
RISC-V
CPU
ECC
DPRAM
WB Slave & Scrubber
SecureROM
Instruction mem
ECC
DPRAM
WB Slave & Scrubber
Data memory
Ethernet MAC
UART (debug)
Watchdog
WISHBONE
interconnect
AHB
eNVM

## Slide 9
Logic utilization
Partial TMR of RISC-V running at 50 MHz, 32 kB + 32 kB of ECC SRAM, Ethernet MAC
Fmax: 60 MHz
DFFs and LUTs with MS2050 SF2: 30% (15k LUTs, 13k DFFs)
RISC-V
RISC-V
RISC-V
CPU
ECC
DPRAM
WB Slave & Scrubber
SecureROM
Instruction mem
ECC
DPRAM
WB Slave & Scrubber
Data memory
Ethernet MAC
UART (debug)
Watchdog
WISHBONE
interconnect

## Slide 10
Results at CHARM using RISC-V SoC
Partial TMR of RISC-V running at 50 MHz
ECC instruction and data memory: 8 kB + 8 kB
RISC-V running a checksum of data memory
ECC single error & double error stats
  SEU Cross-section: 2.44E-14
RISC-V
RISC-V
RISC-V
CPU
ECC
DPRAM
WB Slave & Scrubber
SecureROM
Instruction mem
ECC
DPRAM
WB Slave & Scrubber
Data memory
UART (debug)
Watchdog
WISHBONE
interconnect

## Slide 11
Things to do
True TMR of RISC-V, keeping 50 MHz
Optimize SRAM utilization
Fix Ethernet MAC bugs and improve it for rad-tol
Optimize Powerlink stack: 50 kB of code
Test low-latency Industrial Ethernet PHY (Texas Instruments DP83822) under radiation