## Slide 1
BE-CO Generic Infrastructure
Distributed I/O Tier and Fieldbus project
GREG DANILUK | EVA GOUSIOU
RADWG | 29 NOV 2018

## Slide 2
Custom Electronics Architecture
Front-End Computer
(VME/PICMG/PLC)
master
Front-End Tier
Fieldbus Tier
Distributed I/O Tier
Fieldbus (WorldFIP/PROFINET/etc)
DIO3
slave
sensor
DIOn
slave
sensor
DIO2
slave
actuator
DIO1
slave
actuator

## Slide 3
Custom electronics architecture
Front-End Computer
(VME/PICMG/PLC)
master
Front-End Tier
Fieldbus Tier
Distributed I/O Tier
Fieldbus (WorldFIP/PROFINET/etc)
DIO3
slave
sensor
DIOn
slave
sensor
DIO2
slave
actuator
DIO1
slave
actuator

## Slide 4
Rad-tol Communication Technologies
performance
GBTx/LpGBTx
500 Gy

## Slide 5
DIOT today
Power Converters
Beam Instrumentation
Cryogenics
Machine Protection
Beam Transfer
Magnets Positioning

## Slide 6
Future DIOT Recipe
+
=
Modular hw kit
Designed in collab
Maintained by BE-CO
App-specific parts
Designed by eq. groups
Power Converters
Magnets Positioning
Beam Instrumentation
Machine Protection
Beam Transfer
More robust designs
Benefit from existing developments
Re-use between equipment groups
Notes: Modular hw kit designed by CO in collab with eq. groups
Mainenance by CO

## Slide 7
Power
supply
Common hardware kit for DIOT
WorldFIP FMC
POWERLINK FMC
White Rabbit FMC
Industrial Ethernet FMC
Radiation-tolerant System Board
System Board
LpGBTx FMC
Notes: Here is the kit.
A 3U crate with passive backplane and rad-tol power supplies

## Slide 8
3U Chassis & Backplane
Low cost crate
9-slots backplane with RTM space
Off-the-shelf CompactPCI-Serial backplane
  Fully passive
  Star-topology differential lanes from System to Peripheral
Robust AirMax connector
  Used in transportation applications
  18 and 26 diff pair variants
Hosts Power Board, System Board & App-specific peripheral Boards
Power
supply
Notes:   No PCIe in radiation
  Robust connector used in transportation

## Slide 9
Rad-tol Power Supply
Lalit (FELL) dedicated to this task (BE-CO, R2E, TE-EPC colab)
Gathering requirements and drafting specs
  +12V, +5V, 100W
  Redundancy
  PMBus monitoring interface
  Standard PSU connector FCI 51939-667
First lab prototype using FEAST chips as controller of switched supply

## Slide 10
Rad-tol System Board
FPGA for
  application-specific logic
  crate monitoring and diagnostics
FMC for fieldbus
Backplane connector:
communication with
peripheral boards

## Slide 11
Rad-tol System Board
v1.0: modified C-GEFE with nanoFIP FMC

## Slide 12
Template Peripheral Board
I/O board based on WIC requirements
  24V generation (TRACO)
  16 opto-coupled current loop inputs (HCNR200)
  16 opto-coupled relay driving outputs (HCNR200)
EDA-0829

## Slide 13
Proof of Concept
WorlldFIP master
DIOT crate
Perip Board
Sys Board
WIC sensors/actuators
Notes: Off-the shelf non-rad-tol supplies in the demo crate

## Slide 14
Resources & Collabs
HL-LHC WP 18
  Rad-tol power supply design
  Crate diagnostics
  Rad-tol System board
  Reliability Studies
EN-SMM, TE-MPE, BE-BI
R2E task force
  POWERLINK implementation

## Slide 15
Timeline
Iterative process with eq. groups to define modular hw kit
Proof of concept
Building blocks available for eq. groups
Deployments in eq. groups
Sep 2018
2019-2020
LS3
2016
First POWERLINK tests in CHARM