## Slide 1: SPS experience for LHC ion run
R. Alemany, T. Argyropoulos, H. Bartosik, T. Bohl, M. Carla’, H. Damerau, V. Kain, G. Kotzian, K. Li, G. Papotti, A. Saa Hernandez, M. Schwarz, E. Shaposhnikova, F. Velotti
SPS & PS operators
LIU beam performance meeting, 13 December 2018

## Slide 2: SPS cycles and beams used
First half of the 2018 run with 4 bunch (100 ns) scheme
  Cycle prepared for 12 injections – LHC took only 9 injections due to abort gap settings
  Similar transmission in Q26 (2018) as in Q20 (2016)
Second half with 3 bunch (75 ns) scheme
  Cycle with up to 14 injections
  Scraping had been requested by LHC

## Slide 3: Intensity evolution LHC Pb-Pb run 2018
648 bunches in LHC
733 bunches in LHC

## Slide 4: Intensity evolution LHC Pb-Pb run 2018
1.6e11
648 bunches in LHC
733 bunches in LHC

## Slide 5: Integrated luminosity in LHC
~39 × (2015)
HL-LHC goal: 2.85 nb-1 (in ALICE, ATLAS, CMS)
2015
2015

## Slide 6: Pb-ion performance over the last years
100 ns spacing
100 ns spacing
75 ns
spacing
100 ns
spacing
100 ns
spacing
LIU goal (2.35e11)
slip stacking

## Slide 7: Issues with longitudinal stability
Significant reduction of intensity and bunch length along the SPS batch at end of flat bottom
  leads to instability of the shortest (and less intense) bunches
Transition crossing
  Adjustments are done using many knobs (2 main: transition timing and radial beam displacement)
  Instability and emittance blow-up during transition crossing lead to better beam stability later on
  Will be improved after LS2 due to LLRF (phase discriminator) upgrade
But … bunches crossing transition without significant blow-up become unstable later
Had to run with relaxed BQM settings
  bunch length tolerance 2.2 ns, …
  No particular issue from LHC side!

## Slide 8: Observations during slip-stacking MD
Radial displacement at intermediate flat portion (20 mm) didn’t lead to BCT losses
  maybe we can displace only one beam and simplify slip-stacking?
Instability is often starting at the plateau
  reduction in the synchrotron frequency spread?
Slip-stacking of unstable beam will be difficult and not reproducible
  Need to find mitigation measures for beam stabilisation before and during slip-stacking
Beam becoming unstable on flat portion
Beam stable after blow-up at transition

## Slide 9: Possible stabilisation of the ion beam
800 MHz RF system was finally applied during one MD after deployment for ions
  relative phase was not specifically calibrated for ion operation
  no effect on beam was observed
  can be used only after transition crossing (too late?)
  if used during slip-stacking – need separate control of each cavity (as 200 MHz) – not available
Controlled emittance blow-up
  very difficult in a single RF system due to small frequency spread
  In double RF can be done only after transition crossing (too late?)
  large bunch-by bunch variation in bunch length (> 50%) and then in synchrotron frequency shift
Feasibility of controlled blow-up needs to be studied during LS2 in simulations for realistic bunch-by-bunch particle distribution and SPS impedance model
  before transition crossing in a single RF
  after transition in double RF with phase noise or phase modulation of 800 MHz

## Slide 10: Summary & Outlook
Very successful ion run for the SPS and all injectors
  High intensity beam delivered by Linac3/LEIR and PS
  No particular issue related to 75 ns beam
  Q26 re-deployed with no big difference wrt. Q20 (Q26 required to avoid bunch rotation after slip stacking in the future!)
  Reached expected total intensity in LHC (67% of LIU intensity) with 3 bunch 75 ns scheme
  Longitudinal instabilities encountered after transition crossing (as with Q20)
  MDs devoted to tune scans and tests in view of slip stacking (data analysis ongoing)
  Test of 6 bunch scheme successful – option for slip stacking commisioning (low bunch intensity)
Outlook: slip stacking
  Reaching LIU goal requires slip stacking (in first run after LS2)
  Achieving longitudinal stability of ion bunches is big challenge, but pre-requisite to slip stacking
  Simulation studies during LS2 for achieving longitudinal stability and optimizing slip stacking manipulations
  Will need commitment of all people involved to make it operational in first year after LS2