## Slide 2: Trident Automated system tool for collecting and analyzing hardware performance counters
Servesh Muralidharan & David Smith
IT-DI-WLCG, UP Team
CERN
Mar 2019

## Slide 3: Introduction
Proposed Solution: Trident
  Continuous performance analysis
  System perspective
  Node level measurements
  Non-virtualized environment
  Low overhead and lightweight
  Utilizes hardware counters to measure Core, Memory and IO metrics
  Presents it in a HEP-human readable form
Existing tools
  Execution and profiling are separate steps
  Focus more on HPC Applications
    Fine grained analysis
    Architecture specific optimizations
Typical HEP Applications (As it is today!!!)
  A cluster of several hundred algorithms
  Complex framework interconnecting these algorithms
  Linear instruction spread (no hotspots)
  Non existence of classical numerical loops
  Average runtime of several hours

## Slide 4: Trident Architecture
Hardware Detection
Events
Collector
Configurator
Storage
Plugin
Plugin
Plugin
Detects the events supported by the node
Extensible event files for future architectures
Configures metrics based on these events
These metrics are sampled at preconfigured rate
Stored temporarily in local disk
Plugins perform transformations to the data
Simple low overhead online analysis
Data exported to centralized storage for offline analysis

## Slide 5: Trident - Core Performance Analysis
Instruction Per Cycle (IPC)
  Denotes ratio of parallel instructions executed
  Modern processors like Intel Haswell EP can do 4 IPC
Top down characterization
  Identifies the resources dominated by workload
  Front-End – fetch and decode program code
  Back-End – monitor and execution of uOP once the dependent data operands availability
  Retiring – Completion of the uOP
  Bad speculation – uOPs that are cancelled before retirement due to branch misprediction
Execution Unit Port Utilization
  Determines how many cycles the port was busy
  Identifies broadly the pressure from different types of uOPs
  INT & FP operations, address calculation, etc.,
Source: https://software.intel.com/en-us/vtune-amplifier-help-tuning-applications-using-a-top-down-microarchitecture-analysis-method
Source: https://arstechnica.com/gadgets/2013/05/a-look-at-haswell/2/
Intel Haswell EP

## Slide 6
Further info: https://www.anandtech.com/show/3851/everything-you-always-wanted-to-know-about-sdram-memory-but-were-afraid-to-ask/5
Memory bandwidth usage
  Amount of data read and written to main memory
Memory transaction classification
  Memory transaction occurs through pages from memory bank
  Page-Hit
    Memory bank in open state
    Lowest access latency (Open)
    Sequential memory access usually have high page hits
  Page-Empty
    Memory bank is idle and needs to be activated
    Moderate access latency (Usually 2x of page hit)
    Random memory access usually have high page empty counts
  Page-Miss
    Memory to be accessed requires closing of a page in the same bank
    Worst access latency (Usually 3x of page hit)
Trident - Memory Performance Analysis
Source: https://www.researchgate.net/figure/Example-of-a-typical-TLM-trace-with-DRAM-related-phases_fig4_282806593
Source: https://www.researchgate.net/figure/Multi-banked-SDRAM-architecture_fig1_221341164

## Slide 7
Data recorded form ProcFS
Transfer Rate Analysis
  Amount of data read and written to storage
  Limited by interface and type of memory
  Sustained Vs Bursts
Operation Rate Analysis
  Amount of operations performed
  Limited by controller for fast memory
  Limited by disk head for HDDs
  Random Vs Sequential accesses
Trident - IO Performance Analysis

## Slide 8
Test System
  2x Intel(R) Xeon(R) E5-2630 v3@2.40GHz /
  64GB DDR4-2133 RAM
  Centos 7 (3.10.0-957.5.1.el7.x86_64)
  Non-HT, 8 physical cores per socket
Workloads
  Standard Benchmarks – Repeated five times
    Extracted from Domenico Giordano’s Cloud Benchmark Suite
    HEPSPEC06 Benchmark Suite
      450.soplex,471.omnetpp,447.dealII,473.astar,444.namd,453.povray,483.xalancbmk
    SPEC17 Benchmark Suite
      508.namd_r,510.parset_r,511.povray_r,520.omnetpp_r,523.xalancbmk_r,526.blender_r,531.deepsjeng_r,541.leela_r
  HEP Workload Based Benchmarks - Pre & Post wait time of 60 seconds
    ATLAS – MC Simulation, MC Digitization & Reco, Derivation production
    CMS – Gen+Sim, Digi+Trigger+PileupSimualtion, Reco+Analysis data creation – Streaming Inputs
    LHCb – Generation + Simulation (DG Cloud Benchmark Suite)
    ALICE – Generation + Simulation (DG Cloud Benchmark Suite)
Experiment setup

## Slide 9
HS06

## Slide 10
SPEC2017

## Slide 11
ATLAS – MC Simulation

## Slide 12
ATLAS – MC Digi + Reco

## Slide 13
ATLAS – Derivation Production

## Slide 14
CMS – Generation + Simulation

## Slide 15
CMS – Digitization + Trigger + Pileup Simulation

## Slide 16
CMS – Reconstruction + Analysis Data Creation

## Slide 17
LHCb – Gen+Sim

## Slide 18
ALICE – Gen+Sim

## Slide 19: Domenico.G & Eva.S - Further Analysis