## Slide 1: Layout of DFH and current leads: status of on-going optimization studies: Work in progress
Jerome F., Yann L., Samer Y.
WP6a Integration weekly meeting #1

## Slide 2: Context
Each IP1 and IP5 sides equipped with 2 cold powering chains of cryostats
Triplet insertion : DFHx – SC Link (DSH) – DFX
Matching sections : DFHm – SC Link - DFM
Status:
Some preliminary designs to identify key challenges
Iterations on-going wp6a-wp6b to reach common proposal toward the end of the year
Next step:
Propose & iterate through WP15 with other services
D1
CP
Q3
Q2b
Q2a
Q1
IP
Power converters
DSHx
DFHx
DFX
D2
≈45m
DFHM
DFM
DSHm
≈80m
≈50m
≈8m
Service tunnel
Transverse tunnel
LHC tunnel
LHC tunnel
MBXF
D1
DFX
DSHx
MgB2
NbTi
Superfluid @ 1.9K
Liquid He @ 4.5 K
Gaseous He @ 4.5 K
Jumper D1
Jumper DFX
Splice
DFHx
DSHx
Beam
2 x 13 kA
8 x 0.6 kA
Jumper DFM
D2
Jumper D2
MBCRD
MBRD
DSHm
DFM
DFHm
DSHm
HTS
MgB2

## Slide 3: Specifications & design guidelines
Design objective:
  Ensure critical requirements
  Find a compromise between non critical requirements
Study:
  2 DFHx Units solution
  Boundary conditions:
    Power racks accessible from transport side
    Access to ESS, Crowbar racks from footbridge
    CL racks layout:
      1 for 2x18kA / 1 for 4x2kA type
    Integration : civil engineering
Work in progress
DFHx2
DFHx2
DFHx1
DFHx1
Transport
Transport
OptionA
OptionB
Courtesy S. Yammine
Courtesy S. Yammine
Current leads racks
Discon. Box
PC racks
Service racks
Courtesy S.Maridor
Courtesy S.Maridor

## Slide 4: Specifications & design guidelines
DFHx2
DFHx2
DFHx1
DFHx1
Transport
Transport
OptionA
OptionB
Courtesy S. Yammine
Courtesy S. Yammine
Work in progress
Current leads racks
Discon. Box
PC racks
Service racks
 | Option A | Option B
Energy recuperation | Recuperate all magnet energy for 18 kA | Partial dissipation in warm cables (longer cables)
Warm connections | Length minimised (bus-bars or WCCs) | Use of WCCs (even though significantly reduced with baseline)
HTS cable length | Several lengths from 6 to 14 m. Needs further development to reach 14 m. | One length of ≈ 6 m.
Services integration (HTS flexibles, water& power lines) | Crossing at ground level Nested integration | Independent routing and access
Installation | Mixed sequence CL-PC | Independent CL-PC assembly sequcence
Access for maintenance on current leads | Difficult access with lifting tool Difficult replacement operation | Access from transport side Flexible extraction through transport paths
CL assembly spares: | 6 types: 2 x 18 kA [6m ; 10m] 4 x 2 kA [6m,10m,12m,14m] | 2 types: 1 x 18kA, about 6m long HTS cable 1 x 2kA, about 6m long HTS cable