## Slide 1
Thermal analysis and testing of the electronical package for the new High Granularity Calorimeter (HGCAL) for the CMS detector
Trainee: GOMES, Ricardo
Supervisor: MOCCIA, Stefano
EP-CMX-EI

## Slide 2: Context
What is the CMS?
12/12/2018
1/14
CMS detector – 3D model
CMS detector – cavern photo
For the High Luminosity operation of the LHC, CMS will replace the endcap calorimeters with a new High Granularity Calorimeter.

## Slide 3: Context
12/12/2018
2/14
High Luminosity & High Granularity Calorimeter
HGCAL Slice drawing
HGCAL 3D Model
Initial focus will be on the Electromagnetic (CE-E)

## Slide 4: Context
12/12/2018
3/14
Cassette Layout?
Schematic Layout of a CE-E Cassette
Hexaboard layers
Outer edge of a CE-E cassette – 3D model
Hexaboard
Silicon Sensor
Glue
Cu and CU/W base plate
Exploded diagram of a motherboard and three silicon modules on a cooling plate (at -30˚ C)
First analysis will be focused on a small section of the cassette composed by three modules (Silicon sensor, CU-W baseplate, Hexaboard), the cooling plate, motherboard and lead steel cover.

## Slide 5: Internship objectives
12/12/2018
4/14
Thermal analysis of the Hexaboard-Motherboard (HB-MB) package
Proposal to improve the Thermal performance of the HB-MB configuration
Experimental setup and analysis to validate results
Thermal-mechanical model of the full cassette
Understand and propose new design solutions based on the obtained results

## Slide 6: MB-HB Baseline
12/12/2018
5/14
Detailed 3D model of the Hexaboard
Detailed 3D model of the Motherboard
Most recent models and heat loads provided by P. Rubinov (HGCAL Electronics Coordinator);
Detailed electronic components with pin connections to the boards;
Detailed plastic connectors between both boards;
P. Rubinov also provided the heat loads of each one of the electronic components
Max. Allowable operating temperature for the chips is 60° C.
A simplified model shall be made (necessary for the thermal analysis)
491 mm
189 mm

## Slide 7: MB-HB Model
12/12/2018
6/14
Electronic components cannot be moved due to motherboard design;
Each electronic component is considered to be a silicon block with a specific internal heat generation;
Motherboard- 3D model
Hexaboard – 3D Model
Motherboard components and specs
Hexaboard components and specs
eConD
eConD
DCDC conv
HGCROC
LDO
CLK_MUX
SCA
lpGBT
VTRX+OM
Connector

## Slide 8: MB-HB Model
12/12/2018
7/14
Partial CE-E Cassette - 3D simplified model
Cover
HexaBoard
MotherBoard
Materials and layers of the cassette
Cross section through the thickness of a cassette
Equivalent Thermal Contact Conductance (TCC) is going to be considered to simplify the model (no errors are introduced);
Posts connect the copper layer to the lead-steel cover;
No contact between the posts and the HB-MB;

## Slide 9: Major assumptions
12/12/2018
8/14
Simplified model using equivalent Thermal Contact Conduction (TCC);
Cooling plate at -30 ˚C;
Vacuum between Hexaboard and Motherboard (no difference by adding static air);
Perfect connection between the posts, copper plate and the lead-steel cover;
Perfect connection between each electronic components and the boards;
Only conduction is considered (neither convection or radiation)
Adiabatic system;
Steady-state;

## Slide 10: Baseline results
12/12/2018
9/14
Baseline Model temperature - Motherboard
Baseline Model temperature – PCB of Hexaboard
Baseline Model temperature – Silicon layer
Results:
eConT is the hottest electronic componet: 26.2 ˚C;
Maximum temperature reached by the sillicon layer is -27.8 ˚C;
PCB does not contribute to the heat dissipation (as expected);
eConT
The eConT temperature ΔT with respect to the cooling plate is about 56 ˚C.
This would represent a problem for the foreseen testing period with cooling plate at 15 ˚C

## Slide 11: Importance of the cover
12/12/2018
10/14
Without lead-steel cover temperatures will rise umpredictably;
Almost no heat transfer through the plastic connectors;
Good contact must be ensured between
the posts, lead-steel cover and the cooling plate
Motherboard temperature – Standard model with no lead-steel cover

## Slide 12: Most promising solution
12/12/2018
11/14
Possible solution could be the application of a thermal pad (10 W/m K) on eConT to the Hexaboard;
Robustness of this solution to be evaluated;
eConT decreases to -4˚C and Max. Temp. is reached by eConD: 6 ˚C
Motherboard temperature considering a thermal pad
Silicon temperature considering a thermal pad
Results:
Hottest electronic component is now eConD at 6.8 ˚C;
Local increase of the temperature on the silicon layer to -27.0 ˚C;
Lead-Steel cover has an extreme importance on the cooling of the motherboard;
 | Baseline | Thermal pad on eConT
eConT | 26.2 ˚C | -4.2 ˚C
eConD | 15.3 ˚C | 6.8 ˚C

## Slide 13: Summary
12/12/2018
12/14
Lead-Steel cover has a significant impact on the motherboard cooling;
High heat generation on several electronic components, specially on eConT – hottest component;
The use of a thermal pad seems to be a promissing solution (allowing thermal testing at room temperature);
Convection has no influence on the results;
Given the harsh environment (i.e. radiation, cooling cycles) degradation of the thermal pad material must be considered;

## Slide 14: Challenges for 2019
Improve the thermal contact modeling of the different considered parts (electronic components; cover; cooling plate and posts)
Collaborative work with the cassete and electronic design engineers to optimize the thermal performance of the HB-MB package;
Validate the obtained results (with experimental tests);
Expand the thermal-mechanical analysis to the all cassette;
12/12/2018
13/14

## Slide 15: Questions?
12/12/2018
14/14
References
[1] CMS Collaboration, “The Phase 2 Upgrade of the CMS endcap calorimeter”, Technical design report, 9 April 2018, ISBN 978-92-9083-459-5