## Slide 1: Particle Sources
Dr. Scott Lawrie
Ion Source Section Leader
ISIS Pulsed Spallation Neutron & Muon Facility
Rutherford Appleton Laboratory

## Slide 2: Many Many Particle Sources
Electron
Proton
Light Ion
Heavy Ion
Negative Ion
High Charge State
Radioactive
Spin-Polarised
Neutral
Muon
Exotic
Technique
Filament
Photocathode
Arc Plasma
Laser
Microwave
RF
Cyclotron-Resonance
Duopigatron
Duoplasmatron
…
Species
1+
4+
34+

## Slide 3: Fermi-Stats. & Work Function
EFermi
Fermi level, EFermi is kinetic energy of electron in highest occupied state
Work-function, φwork is energy input to release an electron from the surface (basis of photoelectric effect)
Higher temperature, T smears out the Fermi level
Some electrons may cross work-function and escape
Integrating the number of available released electrons gives current density, J
To get a lot of current, need high T and a material with a high A and low φwork
φwork
Richardson-Dushmann equation

## Slide 4: Child-Langmuir Law
Want the released particles to go somewhere
Apply potential difference to accelerate into a beam
E-field of already-emitted particles shields the cathode from the accelerating E-field: space-charge-limited flow
Cannot accelerate an arbitrarily high number of particles
Can calculate the extractable current density:
Kinetic energy
Poisson eqn.
Continuity eqn.
V
d
J
where:

## Slide 5: Child-Langmuir Law (cont’d.)
Substitute:
Then:
Integration gives:
So:
Rearrange and integrate again:
Bound. cond.:
So:
But from the previous slide:
Therefore:
This Child-Langmuir “V3/2” Law says that the extractable current density of a particle source depends ONLY on the voltage and electrode gap

## Slide 6: Child-Langmuir Law (cont’d.)
Total extracted current, I from an area, A is thus:
where:
This P is the perveance: depends only on source geometry
Real measured beam perveance always lower than this
Assumes infinite, thin, plane electrodes (usually not true)
Assumes particles starting with zero velocity
V3/2 law only holds if particle source can deliver the current
I [mA]
V [kV]
Space- charge limited
Production limited

## Slide 7: Perveance Measurement
Ideal Child-Langmuir perveance = 1.96 mA kV-3/2
Measured perveance = 1.7 mA kV-3/2

## Slide 8: Emittance
y [mm]
y’ [mrad]
Quality of beam just as important as quantity
  Emittance affects machine luminosity and beam-loss
  Want beam emittance < machine acceptance
Particles occupy 6-dimensional phase space
Practical measurements use position-angle (‘trace’) space
Emittance scan can tell immediately how a beam is focused
Also shows up important aberrations (not just pure ellipses)
z
y

## Slide 9: Emittance Ellipses
What is the best fit ellipse?
For real, non-elliptical data sets, calculate 4.RMS emittance statistically:
Ellipse defined by:
where:
are the Twiss parameters
Units usually given in [π mm mrad], but varies
Do we use RMS or 4.RMS?
and Pitfalls
What units? Watch out for π!

## Slide 10: High Voltage Considerations
Particle sources have very low beam energy:
Magnetic focusing
Magnetic deflection
RF acceleration
Relativistic
Ample space
High space-charge
Dirty vacuum
Sensitive diagnostics
HV is the only option, BUT:
Must protect insulator triple junctions
Must avoid points in E-field regions
Must ensure proper cable terminations

## Slide 11: Timing in Pulsed Sources
Usually only need beam a fraction of the time
However, more difficult to make pulsed power supplies
Duty Factor = Pulse Length x Repetition Rate
e.g. ISIS: 200 µs x 50 Hz = 1% Duty Factor
Different D.F.% but same total integrated charge

## Slide 12: Reliability and Stability
Seven week log

## Slide 13: Summary of Fundamentals
Electrons released from hot surfaces
Lower work-function materials release more electrons
Space-charge limit to amount of extractable current
Extraction systems described by their perveance
Particle beams described by their emittance
Many ways to define emittance and its units: be careful
Must consider high voltage engineering requirements
Usually need specialist pulsed power supplies
Reliability dominates all other performance goals
Now we can move onto real particle sources…

## Slide 14: Thermionic Electron Gun
W dispenser cathode with impregnated BaO:CaO:Al2O3

## Slide 15: Photocathode Electron Guns
Photo- cathode
Anode
Electron Beam
Laser Beam
Material | Type | (Egap + EAff) * or ϕwork [eV] | λ [nm] | Q.E. $
W | Metal | 4.5 | 375 | 10-6
W:Th | Metal | 2.6 | 477 | 10-5
Cs | Metal | 1.81 | 685 | 10-3
LaB6 | Ceramic | 2.6 | 477 | 10-6
GaAs:Cs | Semi-cond. | 2.3 | 532 | ~0.10 &
Cs2Te | Semi-cond. | 3.5 | 350 | 0.12
K2CsSb | Semi-cond. | 2.1 | 590 | 0.29
* In semi-conductors, the equivalent to work function ϕwork is (band-gap + electron affinity)
$ Q.E. = Quantum efficiency = Electrons/Photon
& Vacuum-dependent
Use low work function cathode
Raise temperature
Fire laser onto it
Accelerate e-beam
Bunch timing set by laser pulses

## Slide 16: DC Photocathode Gun
ALICE @ DL
350 kV DC, 80 pC bunch, GaAs:Cs

## Slide 17: RF Photocathode Gun
FERMI2 @ Trieste
3 GHz RF
50 Hz laser
Q.E. ~3x10-5
500 pC bunch
5.1 MeV beam

## Slide 18: Superconducting RF Gun
SRF2 @ ELBE
Cs2Te cathode
1.3 GHz CW RF
13 MHz UV laser
200 pC bunch
4.5 MeV beam
Main issue with all photoinjectors using Cs2Te cathodes is the need to replace the cathode after ~100 hours

## Slide 19: Most are Plasma-Based Sources
Electron
Proton
Light Ion
Heavy Ion
Negative Ion
High Charge State
Radioactive
Spin-Polarised
Neutral
Muon
Exotic
Technique
Filament
Photocathode
Arc Plasma
Laser
Microwave
RF
Cyclotron-Resonance
Duopigatron
Duoplasmatron
…
Species
1+
4+
34+

## Slide 20: Plasma Parameters
Air
Intergalactic
Interstellar Gas
1 eV ≈ 11,600 K
10-2 10-1 100 101 102 103 104 105
Plasma Temperature [eV]
1024
1022
1020
1018
1016
1014
1012
1010
108
106
Plasma Density [particles per m3]
Solar Wind
Van Allen Belts
Iono-sphere
Solar Corona
Ion sources
Sun Centre
Fusion Reactor

## Slide 21: Plasma Fundamentals
Maxwell-Boltzmann temperature-dependent velocity:
with
Debye length is distance charge perturbations can exist:
Electrons react to perturbations at the plasma frequency:

## Slide 22: Plasma Fundamentals
Particle collision frequency depends on cross-section:
With a mean free path between collisions:
Electron impact ionisation examples:
  e– + He0  He1+ + 2e– then e– + He1+  He2+ + 2e–
  e– + H2  H2* then e– + H2*  H– + H0
To ionise efficiently, need plasma confinement, usually in the form of magnetic fields

## Slide 23: Plasma Fundamentals
Charged particles confined transversely in a uniform B-field
If particles also have and B-field is increasing into screen, get longitudinal magnetic mirror confinement with:
Mirror both ends  magnetic bottle
Also ExB, gradB, curvature & diffusion drifts
Electrons
Ions
Larmor frequency:
Larmor radius:
Loss cone
Loss cone
(a.k.a. cyclotron)

## Slide 24: Plasma Confinement Techniques
Solenoid bottle
(often combined with hexapole cusp)
Multicusp ‘bucket’ of dipoles in checkerboard pattern
Dipole magnet, parallel cathodes and anode ‘window’

## Slide 25: The Typical Ion Source
Plasma
Confinement Magnet
Confinement Magnet
Plasma chamber
Power Feed
Gas Feed
Emission Aperture
Extraction Electrodes
Particle Beam
Every ion source basically consists of two parts:
Ion production inside a plasma
Beam extraction from the plasma

## Slide 26: No ‘Typical’ Ion Sources!
‘ELISE’ ITER Demonstration H– Source
ISIS H– Source

## Slide 27: Beam Extraction
Particle dynamics at emission aperture defines the beam performance throughout entire accelerator: crucial!
Plasma meniscus is notional ‘boundary’ where beam originates
Meniscus sets beam current, emittance and focussing. Shape varied by plasma density, extraction voltage and electrode geometry
Under-dense plasma: beam cross-over & aberrations
Perveance match: parallel beam
Over-dense plasma: very divergent beam
Meniscus

## Slide 28: Space Charge
50mA proton beam, 5mm initial radius, drifting 1m
10 keV beam
1 MeV beam
100 keV beam
CONCLUSION: Need to focus and accelerate low energy beams hard

## Slide 29: Space Charge Compensation
Space charge increases beam size
Beam ionises residual gas and traps electrons in beam potential: Space charge compensation. Takes ~50 µs, depending on vacuum pressure.

## Slide 30: Summary of Fundamentals (2)
Most ion sources involve plasma
Lots of parameters to describe a plasma
Plasmas confined with various topology magnetic fields
After plasma is the beam extraction region
Plasma meniscus defines initial beam focussing
Space charge affects low energy, high mass beams
Often attempt deliberate space charge compensation
Now we can move onto real examples of ion sources…

## Slide 31: Proton Sources
plasmatron
Duo
CERN Linac2 1956
300 mA protons
150 µs, 1 Hz
Cathode filament
Intermediate electrode
Steel yoke
Solenoid
Extraction electrode
Anode
Expansion cup

## Slide 32: Proton Sources
2.45 GHz ECR
SILHI @ CEA, INFN, ESS…
120 mA protons
All duty factors up to 100%
Electron Cyclotron Resonance (ECR)
RF cavity immersed in axial solenoid field
Select RF frequency to match Larmor frequency
Electrons gain energy
Increases ionisation rate
Electrons
E-field

## Slide 33: High Charge State Sources
Hexapole transverse confinement
Higher frequency  stronger B
Superconducting magnets
Large and very expensive!
SECRAL & VENUS 28 GHz ECRs
High currents of Bi20+, Pb34+…

## Slide 34: High Charge State Sources
EBIS @ RHIC
10 A electron gun
5 T, 1.9 m ion trap
Au32+, U39+…
10 µs, 5 Hz pulses
Superconducting Solenoid
Electron Gun
Drift tubes
High power electron beam ionises gas
Ions trapped and undergo step-wise ionisation
Remove trapping voltage to release ions
Electron Beam Ion Source

## Slide 35: Charge Breeders
Soon in USA:
FRIB
Impact protons onto target
Radioactive ions emerge
Further ionisation in plasma
Extract and (quickly!) accelerate and analyse
Study very exotic nuclei
ISOLDE @ CERN
107 132Sn per second
(Isotope Separation On-Line)
& ISOL

## Slide 36: Negative Ion Sources
Cyclotron
H+
H–
+4 MV
+2 MV
+0 MV
0 MeV H–
8 MeV H+
Tandem
50 MW H–
H0
Tokamak
H–
H+
Synchrotron

## Slide 37: H– Ion Production Methods
Volume Production (H– beams 0 mA)
Surface Production
(H– beams 0 mA)
efast + H2
eslow + H2*
Low φwork metals release electrons
Alternatively, energetic atoms hitting surface can take a free electron, creating H–
= H2* + eslow
= H– + H0

## Slide 38: Caesium: a Blessing and a Curse
Good Points | Bad Points
Allows copious H– production Reduces co-extracted e– current Allows high current plasma arc Stabilises plasma Nothing else as effective | Increases rate of HV sparking Makes vacuum vessel messy Highly explosive AND toxic Hard to work with and expensive Reduces ion source lifetime
Moral:
Only use ‘JUST ENOUGH’
caesium for acceptable ion source performance!

## Slide 39: ISIS Penning Surface H– Source
Machined molybdenum, ceramic, stainless & copper
High temperature and magnetic & electric fields
Microscope alignment of extraction electrode
Hydrogen & caesium feeds into the vacuum
Welded 1/8” air & water cooling pipes
Bolts torqued for good thermal contact
> 2 kW of power damages components
Lasts 3-4 weeks  have 10 ready to go
55 mA H– at 250 µs, 50 Hz
Wear after 35 days

## Slide 40: ISIS RF Volume H– Source

## Slide 41: Final Thoughts
Accelerator designers always want more from the particle source!
More current
Lower emittance
Higher charge states
Longer lifetime
More stability
Squarer pulse shape
Higher duty factor
More Gaussian Profile
Better vacuum
Very active & exciting career, always in need of more minds
Quicker start-up

## Slide 42: Thank you for listening!
Feel free to contact me if you’re interested in this subject.
Please email homework answers to me by 22/03/2019.
scott.lawrie@stfc.ac.uk
Notes: Questions?

## Slide 43: Homework Questions
Use the ideal gas law to calculate the particle number density inside a room-temperature vacuum vessel at a (somewhat poor) pressure of 10-4 mbar. Assuming = 6x10-19 m-2, calculate the mean free path. If the vessel is 0.5 m long, is the pressure high enough to be collisional?
You want to make an electron gun which can operate at 1 kHz, with an extracted charge of 500 pC/bunch. Your photocathode has Q.E. = 1x10-4. What power laser would you need if it operated at a wavelength of 532 nm?
You want to make an H– ion source with an output beam current of 40 mA at 45 kV extraction voltage operating at 50 Hz for the scSPS project.
  Discuss whether you would use caesium in this ion source.
  What are the benefits and drawbacks of altering the geometry terms A and d2 to reach a suitable perveance?
  Write a list and brief justification of the physics simulations you would need to perform to design this ion source.