## Slide 1: Linear Colliders
1: Introduction, Overview, Scaling, ILC/CLIC
2: Subsystems: source, DR, BC, main linac
3: Subsystems: linac, wakefields, RF, alignment
4: Parameters, NC/SC, CLIC
Linear Colliders
4 lectures

## Slide 2: Preface
Complex topic --- but: DON’T PANIC!
Approach:
  Explain the fundamental layout of a linear collider and the specific designs based on SuperConducting (SC) and normal conducting (NC) technology
  I will not go much into technical details
  Try to avoid formulae as much as possible
Goal: You understand
  Basic principles
  Some driving forces and limitations in linear collider design
  The basic building blocks of CLIC
Ask questions at any time! Any comment is useful! (e-mail: tecker@cern.ch)

## Slide 3: Linear Colliders Lecture 1: Introduction and Overview
Path to higher energy
Cost scaling
Luminosity
Generic LC layout
ILC / CLIC

## Slide 4: Path to higher energy
History:
  Energy constantly increasing with time
  Hadron Colliders at the energy frontier
  Lepton Colliders for precision physics
LHC has found the Higgs with mH = 126 GeV/c2
A future Lepton Collider would complement LHC physics

## Slide 5: Lepton vs. Hadron Collisions
e+
e-
Hadron Collider (p, ions):
  Composite nature of protons
  Can only use pt conservation
  Huge QCD background
Lepton Collider:
  Elementary particles
  Well defined initial state
  Beam polarization
  produces particles democratically
  Momentum conservation eases decay product analysis
LEP event: Z0 → 3 jets
LHC: H → ZZ → 4µ
ALICE: Ion event
p
p

## Slide 6: TeV e+e- physics
Higgs physics
  LHC has discovered the Higgs particle
  LC explore its properties in detail
Supersymmetry
  LC will complement the LHC particle spectrum
Extra spatial dimensions
New strong interactions
. . . => a lot of new territory to discover beyond the standard model
“Physics at the CLIC Multi-TeV Linear Collider” CERN-2004-005
“CLIC Conceptual Design Report– Vol.2” http://lcd.web.cern.ch/LCD/CDR/CDR.html
“ILC Technical Design Report – Vol.2 – Physics at the ILC” www.linearcollider.org/ILC/Publications/Technical-Design-Report
The CLIC potential for new physics CERN-2018-009-M

## Slide 7: The next lepton collider
Larger lepton storage ring? LEP-3?? (LEP L = 27 km, Ecm= 200 GeV)
Remember: Synchrotron radiation
  Emitted power: scales with E 4 !!
  Energy loss/turn: must be replaced by the RF system !!
RF costs: €RF ∝ U0 ∝ E4/ρ
Linear costs (magnets, tunnel, etc.) : €lin ∝ ρ
=> Optimum when: €lin ∝ €RF ⇒ ρ ∝ E2
Increase radius quadratically with energy => The size and the optimized cost scale as E2 as well as the energy loss per turn (was already 3% at LEP)
P
=
2
3
r
e
c
m
o
c
2
(
)
3
E
4
ρ
2
U
0
=
4
3
π
r
e
m
0
c
2
(
)
3
E
4
ρ

## Slide 8: The solution: a Linear Collider
NO bending magnets ⇒ NO synchrotron radiation
but: A lot of accelerating structures !!!
Cost scaling linear with E
e+
e-
source
damping ring
main linac
beam delivery
Storage rings:
  accelerate + collide every turn
  ‘re-use’ RF + ‘re-use’ particles
=> efficient
Linear Collider:
  one-pass acceleration + collision => need
  high gradient
  small beam size σ and emittance
  to reach high luminosity L (event rate)
much less limited by beam-beam effect

## Slide 9: Luminosity: LC vs Storage Ring
Collider luminosity L (cm-2 s-1) is approximately given by where: nb = bunches / train N = particles per bunch frep = repetition frequency σx,y = transverse beam size at IP HD = beam-beam enhancement factor (linear collider: typical value ~2)
LHC ring frep = 11 kHz
LC frep = few-100 Hz (power limited)
⇒ factor ~100-1000 in L already lost for the LC!
Must push very hard on beam cross-section at collision:
factor of 106 gain! needed to obtain high luminosity of a few 1034 cm-2s-1
LEP: σxσy ≈ 130×6 µm2
LC: σxσy ≈ (60-550) × (1-5) nm2

## Slide 10: Luminosity: RF power
Introduce centre-of-mass Energy Ecm
ηRF is RF to beam power efficiency
Luminosity is proportional to the RF power and efficiency for a given Ecm
Some numbers: Ecm = 500 GeV N = 1010 nb = 100 frep = 100 Hz
Need to include efficiencies: RF→beam: range 20-60% Wall plug→RF: range 28-40%
AC power: a few hundred MW to accelerate beams for a high luminosity
this limits the practically achievable energy and luminosity

## Slide 11: Luminosity: IP effects
choice of technology (NC vs SC):
  efficiency
  available power
Strong focusing needed for small beam size
  optical aberrations
  stability issues and tolerances
Beam-Beam effects:
  strong self focusing (pinch effect) ⇒ increases Luminosity
  beamstrahlung ⇒ photon emission
    dilutes Luminosity spectrum
    creates detector background

## Slide 12: Beam-Beam effects: pinch
Strong electromagnetic field of the opposing bunch:
  deflects the particles “beam-beam kick”
  focuses the bunches “pinch effect”
  Luminosity enhancement factor HD
Ey (MV/cm)
y/sy

## Slide 13: Collision Simulation
beams strongly focused during collision ⇒ Luminosity!
large divergence after collision ⇒ beam extraction difficult
D.Schulte

## Slide 14: Beamstrahlung
“synchrotron radiation” in the field of the opposing bunch
smears out luminosity spectrum
creates e+e- pairs background in detector
quantified by Disruption parameter

## Slide 15: Beamstrahlung: energy loss
RMS relative energy loss beamstrahlung energy loss
we want
  σx and σy small for high luminosity
  (σx+ σy) large for small δBS (=> better luminosity spectrum)
use flat beams with σx ≫ σy
Can increase luminosity by small σy
and minimise δBS by big σx

## Slide 16: Limit on beam size: Hour-glass effect
β-function at the interaction point follows
Luminosity has to be calculated in slices
desirable to have σz ≤ βy ⇒ short bunch length for high luminosity
σz=βy
σz=3βy
N.Walker

## Slide 17: Luminosity: more scaling …
substitute into
we get
now use
then
~1 (hour glass effect)

## Slide 18: The ‘final’ scaling for LC
we want high RF-beam conversion efficiency ηRF
need high RF power PRF
small normalised vertical emittance εn,y
strong focusing at IP (small βy and hence small σz)
could also allow higher beamstrahlung δBS if willing to live with the consequences (Luminosity spread and background)
  Above result is for the low beamstrahlung regime where δBS ~ few %
  Slightly different result for high beamstrahlung regime

## Slide 19: Generic Linear Collider
C.Pagani
Electron Gun Deliver stable beam current
Damping Ring Reduce transverse phase space (emittance) so smaller transverse IP size achievable
Bunch Compressor Reduce σz to eliminate hourglass effect at IP
Positron Target Use electrons to pair-produce positrons
Main Linac Accelerate beam to IP energy without spoiling DR emittance
Final Focus Demagnify and collide beams
Collimation System Clean off-energy and off-orbit particles
will see the different elements in the following…

## Slide 20: The real designs: JLC/NLC
NLC (Next Linear Collider)
JLC (Japanese Linear Collider):
  500 – 1000 GeV
  Normal conducting RF
  11.4 GHz
  65 MV/m gradient
not followed up any more
technology decision in Aug 2004 for superconducting technology

## Slide 21: The real designs: TESLA -> ILC
TESLA:
  Superconducting cavities
  1.3 GHz
  35 MV/m gradient
  500 – 800 GeV
ILC (Internat. Linear Collider):
  Superconducting cavities
  31.5 MV/m gradient
  500 GeV
  Upgrade to 1000 GeV possible
~31 km total length (500 GeV)

## Slide 22: ILC - Global Design Effort - LCC
ILC Reference / Technical Design Reports 2007 / 2013
Linear Collider Collaboration (LCC) continues ILC design effort until project approval
Web site: www.linearcollider.org
Japan has expressed interest in hosting ILC, evaluation by government
preferred candidate site selected: Kitakami (north Japan)
First stage of 2x125 GeV as Higgs-Factory

## Slide 23
RF Service Tunnel
Beam Tunnel
Concrete
Shield-Wall
Two 250 Gev linacs arranged to produce nearly head on e+e- collisions
  Single IR with 14 mrad crossing angle
Centralized injector
  Circular 6.5 km / 3.2 km damping rings
  Undulator-based positron source
Dual tunnel configuration 11x5.5m
  3.5m shield wall reduction being investigated
ILC Schematic
Slide 23

## Slide 24
The core technology for the ILC is 1.3GHz superconducting RF cavity intensely developed in the
TESLA collaboration, and recommended for the ILC by the ITRP on 2004 August.
The cavities are installed in a long cryostat cooled at 2K, and operated at gradient 31.5MV/m.
14560 cavities
1680 modules
ILC Super-conducting technology
Slide 24

## Slide 25: ILC Main Linac RF Unit
560 RF units each one composed of:
1 Bouncer type modulator
1 Multibeam klystron (10 MW, 1.6 ms)
3 Cryostats (9+8+9 = 26 cavities)
1 Quadrupole at the center
Total of 1680 cryomodules and 14 560 SC RF cavities
Slide 25

## Slide 26: ILC Main Linac RF distribution
downstream
upstream
shaft
CTO
surface rf power cluster building
service tunnel eliminated
underground heat load greatly reduced
accelerator tunnel
TE01 waveguide
surface
~1.06 km
~1.06 km
Either many small klystrons in the tunnel
or few clusters of higher power klystrons
O(10TW) instantaneous power

## Slide 27: CLIC – overall layout – 3 TeV
Slide 27
CLIC (Compact Linear Collider): only multi-TeV design 3 TeV, 100 MV/m, warm technology, 12 GHz, two beam scheme

## Slide 28: CLIC two beam scheme
Transfer lines
Main Beam
Drive Beam
CLIC TUNNEL
CROSS-SECTION
High charge Drive Beam (low energy)
Low charge Main Beam (high collision energy)
=> Simple tunnel, no active elements
=> Modular, easy energy upgrade in stages 380 GeV => ~1.5 TeV => 3 TeV
Main beam – 1 A, 156 ns
from 9 GeV to 1.5 TeV
Drive beam - 101 A, 240 ns
from 2.4 GeV to 240 MeV
5.6 m diameter

## Slide 30: CLIC two-beam scheme
RF Power per structure ~ 65MW
No of structures ~140,000
Total instantaneous power ~ 9.1 PW
RF power is produced by drive beam
Drive beam: 100 A current, 2.4 GeV
Main beam: 1 A, 1500 GeV

## Slide 31: First LC: SLC
T.Raubenheimer

## Slide 32: Parameter comparison
 | SLC | TESLA | ILC | J/NLC | CLIC
Technology | NC | Supercond. | Supercond. | NC | NC
Gradient [MeV/m] | 20 | 25 | 31.5 | 50 | 100
CMS Energy E [GeV] | 92 | 500-800 | 500-1000 | 500-1000 | 500-3000
RF frequency f [GHz] | 2.8 | 1.3 | 1.3 | 11.4 | 12.0
Luminosity L [1033 cm-2s-1] | 0.003 | 34 | 20 | 20 | 23
Beam power Pbeam [MW] | 0.035 | 11.3 | 10.8 | 6.9 | 4.9
Grid power PAC [MW] |  | 140 | 230 | 195 | 270
Bunch length σz* [mm] | ~1 | 0.3 | 0.3 | 0.11 | 0.07
Vert. emittance γεy [10-8m] | 300 | 3 | 4 | 4 | 2.5
Vert. beta function βy* [mm] | ~1.5 | 0.4 | 0.4 | 0.11 | 0.1
Vert. beam size σy* [nm] | 650 | 5 | 5.7 | 3 | 2.3
Parameters (except SLC) at 500 GeV

## Slide 33: Documentation about ILC/CLIC
Linear Collider Collaboration http://linearcollider.org
General documentation about the ILC: http://linearcollider.org/ILC
General documentation about the CLIC study: http://cern.ch/clic-study / http://clic.cern
Int. Linear Collider Workshop 2018 http://www.uta.edu/physics/lcws18
CLIC Workshop 2019 (most actual info) http://indico.cern.ch/event/753671
International school for Linear Colliders: http://linearcollider.org/school
CLIC detector and physics study: http://cern.ch/clicdp
CLIC conceptual design report: http://clic-study.web.cern.ch/content/conceptual-design-report
CLIC scheme description: http://preprints.cern.ch/yellowrep/2000/2000-008/p1.pdf
CERN Bulletin article: http://cdsweb.cern.ch/journal/article?issue=28/2009&name=CERNBulletin&category=News%20Articles&number=1&ln=en
CLIC Test Facility: CTF3 http://clic-study.web.cern.ch/content/ctf3-0
CERN Academic Trainings: CLIC technological challenges http://indico.cern.ch/conferenceDisplay.py?confId=a057972 CLIC (2018) http://indico.cern.ch/event/668147
CLIC project meetings http://indico.cern.ch/category/3589/
CLIC notes http://cdsweb.cern.ch/collection/CLIC%20Notes