## Slide 1: Experience with e-cooler at ELENA and requirements for optimisation of future applications D. Gamba on behalf of the AD/ELENA teams BE-ABP/BE-BI Joint Meeting 10th Jan 2019
ELENA layout and beam status at the end of the run (9 Nov 2018)
Hints about e-cooling performance
Desiderata for future optimisation
Conclusions
Experience with e-cooler at ELENA BE-ABP/BE-BI Joint Meeting 10th Jan 2019

## Slide 2: ELENA Overview and Layout
Deceleration of antiprotons from 5.3 MeV to 100 keV to improve efficiency of experiments
Circumference 30.4 m (1/6 the size of the AD)
  Fits in available space in AD hall and allows installing all equipment without particular efforts
  Lowest average field (beam rigidity over average radius) Br/R = 94 G (smaller than for AD 115 G)
High sensitivity magnetic pick-up for Schottky diagnostic
(intensity) and LLRF
Extraction towards existing experiments
(with fast electrostatic deflector)
Wideband RF cavity
Scraper to measure
emittances
(destructive)
Electron Cooler and
compensation solenoids
Extraction towards new exp. zone
Injection with
magnetic septum (≈300 mrad)
and kicker (84 mrad)
Quadrupoles
Line from H- and proton
source for commissioning
Experience with e-cooler at ELENA BE-ABP/BE-BI Joint Meeting 10th Jan 2019

## Slide 3: Status End of Run 2018
2 s/div
Magnetic cycle
Position pick-up sum signal,
proportional also to intensity
Intensity estimate from LLRF
Almost nominal cycle:
  Injection 100 MeV/c
  Deceleration to 35 MeV/c (h = 1)
  De-bunching and e-cooling
  Deceleration to 13.7 MeV/c (h=4)
  De-bunching and e-cooling
  Re-bunching (with e-cooler on) on h=4 and extraction to experiment
    GBAR only user so far.
If we trust LLRF intensity estimate we have about 50% deceleration efficiency
Still quite some losses at the end of second ramp
  Still to be understood…
Bunched beam e-cooling
e-cooling
Most “difficult” losses
(Almost) Ready and looking forward to send beam to all other AD experiments after LS2!
Experience with e-cooler at ELENA BE-ABP/BE-BI Joint Meeting 10th Jan 2019

## Slide 4: Important Facts: beam time
E-cooler studies (so far) only possible with pbars
  Unavailability of p beam from source; limited attempts with H-
AD cycle length ~110 s; MD shift of 8 h
  About 33 shots/hour; 260 shots/MD shift
  Typically 2/3 MDs per week ≈ 10% of time
  Unfortunate year for AD (about 62% availability = 4400h)
    i.e. about 15000 shots (upper boundary) for ELENA MDs in 2018
Courtesy T. Eriksson (link)
Experience with e-cooler at ELENA BE-ABP/BE-BI Joint Meeting 10th Jan 2019

## Slide 5: Important Facts: Beam Instrumentation
Scraper measurement
  Destructive
  Integrated in control system
Courtesy P. Grandemange (link)
Schottky diagnostic (LPU or TPU)
  Non-destructive
  Not fully integrated in CO
Also available:
2 BPMs in e-cooler section, but only used to measure ions (no tests with e-, isn’t it?)
Recombination Monitor only for e- beam optimisation with H- and p (not exploited)
Experience with e-cooler at ELENA BE-ABP/BE-BI Joint Meeting 10th Jan 2019

## Slide 6: E-cooler in action - 35 MeV/c plateau
E-cooler off
E-cooler on
~half profile measured with “scraper”
Clear transverse and longitudinal emittances reduction observed
Only limited amount of time on systematic optimization of cooling (lack of time)
  Some optimisation with orbit bumps/angles in e-cooler
  Surely(?) margin for improvements
Schottky signal
Courtesy G.Tranquille
Experience with e-cooler at ELENA BE-ABP/BE-BI Joint Meeting 10th Jan 2019

## Slide 7: Some details by J.Hunt
Schottky signal @h=10
Cumulative Distribution Functions from Left/Right scrapings
Analysis of Schottky signal
Longit. cooling time of the order of 1 s
  Momentum spread ~2.5e-4 compatible with expectations
Clear reduction of transverse beam size
Some drift of mean energy
  e- beam energy drift?
No sizable variation of beam mean transverse position
Re-bunching
De-bunching (unclear time)
Experience with e-cooler at ELENA BE-ABP/BE-BI Joint Meeting 10th Jan 2019

## Slide 8: Cooling time
from: ELENA Design Report (CERN-2014-002)
k = 0.16(?)
LC = Coulomb logarithm ≈ 10 typically
Q = -1; A = 1 for ELENA
j = e- current density
r.m.s. ion/electron “angular” spread
Putting everything together, to be expected cooling time of τ < 1 s
  Compatible with observations.
Experience with e-cooler at ELENA BE-ABP/BE-BI Joint Meeting 10th Jan 2019
Notes: \eta_c = \frac{L_{cool}}{L_{ring}} \approx 0.023
r_e &= 2.8 \times 10^{-15}\\
r_p &= 1.54 \times 10^{-18}
\gamma &\approx 1 \\
\beta_\gamma &\approx 0.038 - 0.015
N_e = \frac{j}{\beta_\gamma\,c\,e}= \frac{I_{e_{beam}}}{\beta_\gamma\,c\,e\, r_{e_{beam}}^2 \pi}
j &= N_e \beta_\gamma\,c\,e \\
N_e &\approx 1.4 \times 10^{12} [m^{-3}]
BetaTwiss = 2 m; emittance = 4 um
\Theta_{\parallel} &\approx \Delta p_{ion} / p_{ion} \approx 2\times10^{-3}\\
\Theta_{\bot} &\approx \sqrt{\epsilon \gamma_{Twiss}} \approx \sqrt{\epsilon /\beta_{Twiss}} \approx 1.4\times10^{-3}\\

## Slide 9: Transverse performance by J.Hunt
still, about x2 worst than design values (0.3/0.2 μm)
Great emit. improvement
Experience with e-cooler at ELENA BE-ABP/BE-BI Joint Meeting 10th Jan 2019

## Slide 10: Desiderata: looking at LEIR
from: A.Saa Hernandez (indico)
Each scan contains about 260 points = 1 ELENA pbar MD shift
Only destructive emittance measurement in ELENA
Experience with e-cooler at ELENA BE-ABP/BE-BI Joint Meeting 10th Jan 2019

## Slide 11: Scan using a single cycle?
We can profit of space-charge effect on e- beam energy distribution:
To the right, a quick test at LEIR
  Requires new tooling/flexibility of ELENA control system
from: J. Resta-López et al 2015 JINST 10 P05012 (link)
e- energy offset
wrt transverse position
time
frequency
Ion beam intensity
Hor. ion offset bump in the cooler
Best alignment?
Experience with e-cooler at ELENA BE-ABP/BE-BI Joint Meeting 10th Jan 2019

## Slide 12: Overcome scraper limitation
Use of available recombination monitor
  Only for H-/p operation
  Still to be exploited
  How to translate information to pbar operations?
Use of Transverse Resonant Schottky Pickup to estimate emittances
  Previous attempts in AD not successful (?)
Installation of dedicate IPM
  Proposal available (e.g. EDMS #1754985)
  Impact on vacuum and beam dynamics still to be fully evaluated (?)
  No short term plans (?)
beam
MCP
E
CO2
Experience with e-cooler at ELENA BE-ABP/BE-BI Joint Meeting 10th Jan 2019

## Slide 13: Conclusions
2018 a very fruitful year for ELENA commissioning
  Many sub-systems (RF, BI, e-cooler) (almost) fully commissioned
  Nominal beam performance (almost) established
E-cooling is doing what it has promised
  Emittance reductions of ~80% down to ~0.5 μm (nominal ~0.3 μm)
  Results obtained with limited-empirical studies “by hand”
Could not fully profit of the H-/p source => being fixed
  Use of p beam envisaged for e-cooling studies (higher rep rate)
After LS2 all pbars will need to go through ELENA
  More pbar “shots” available, eventually for parasitic observations
  Hopefully, more time for well-thought, systematic measurements
Still, limited emittance-measurement capabilities
  We probably need to discuss what are the options (e.g. IPM?)
Thanks for your attention, comments and questions …

## Slide 14: Backup

## Slide 15: Cooling time
from: Beam Cooling Techniques – I. Meshkov (indico)

## Slide 16
Some interesting slides from A.Saa Hernandez (indico):
Overview of 2018 MD studies in LEIR

## Slide 17
revolution frequency
time
harmonic 100
h=101
h=103
h=104
h=105
h=102
injection
reduce dp/p with cooling
drag ion beam
However:
same emittance blow-up for different final momentum
Can we capture at a higher momentum?
We do indeed accelerate the ion beam
And could afterwards capture and ramp with minor modifications (adjust RF at capture and correct ramp)
Electron
Cooler
Longitudinal
Schottky
Linac3 could not inject at a higher energy, so we would need to accelerate the ions without RF during the (no-longer) flat bottom by means of the Ecooler

## Slide 18: And if we cool a bunched beam?
At capture, losses and a emittance blow-up associated to SC and IBS always observed
What if we extend cooling time to after RF capture?
  Beam damped in all 3 planes
  By adjusting the electron cooler gun voltage, we drag ion beam to a frequency which has an offset with the RF frequency, creating hollow/flat distributions
h
h

## Slide 19: Heating processes: dominated by IBS or Space Charge?
Similar nature: Coulomb force
IBS: particle collisions as they perform betatron and synchrotron oscillations  redistribution of momenta within the bunch  increase emittances
Space charge: derived from the E-field generated by the distribution of charged particles, creates tune shift and can excite resonance  increase emittances
What happens here?
Depends on intensity? On WP? On resonance excitation? Does it cause losses?
Simulations ongoing for both IBS and space charge, separately. Qualitative agreements found, we needed to get lots of data for further understanding

## Slide 20: Equilibrium emittance vs Intensity vs Qy
For IBS dominated regime e ~ In (with n ~ 0.6 for ions of Ti22+, Kr36+, Xe54+, Au79+, U92+ measured at GSI)…
but then emittance blow up and losses should be similar for all tunes and we had already observed that was not the case
Look further: emittance dependence on WP, above a threshold intensity!
 Space charge dominates for certain tunes and intensities (ongoing studies)

## Slide 21: Can we compensate this resonance?
Sextupole settings found that compensate losses up to 90%
when crossing the resonance dynamically
Yes, if excited by the magnetic errors, it should be possible by means of a pair of skew sextupoles with a phase advance 3DQy = 90◦  Only XSF41 and XSF42 available, with 3DQy = 133◦
do a dynamic resonance crossing as a function of the current in the sextupoles and measure losses
Measurements for beams with low and high intensity, compensating on flat bottom and during ramp. Studies also for static (nominal) WP.

## Slide 22: Tune Scan: compensated vs. uncompensated
cycle evolution for different Qy
No compensation of resonance at Qy=2.66
With compensation of resonance at Qy=2.66 using skew sextupoles
Qx = 2.75
Qx = 2.66
1D vertical scan