## Slide 1
Simulation of electron guns
for electron cooler
Alexander Pikin, Hannes Pahl, Adriana Rossi, Gerard Tranquille

## Slide 2
Model:
Uniform magnetic field 2 kGs< B<3 kGs
Electron energy Eel=60.0 keV
Electron current range: 0.1 A < Ie < 5.0 A
Accelerating gap to 60 kV has width 60 mm.
The electron transverse energy was measured in the same magnetic field after acceleration in uniform magnetic and electrostatic fields at fixed electron energy of 60 keV.
Requirements:
Magnetic field on the cathode: 2.4 kGs
Cathode diameter: 25 mm
Nominal operating electron current is Iel =3.5 A.
Electron beam energy Eel=60 keV (110 MeV for protons)
The electron beam will expand in interaction region with magnetic field 600 Gs

## Slide 3
Cathode
Wehnelt electrode
Anode
Drift tube
Range of measurements
Model

## Slide 4
1. Convex cathode with flat electrodes:
Perveance = 2.93 A/V1.5
Kilpatrick safety factor (3.5 A and 11.2 kV) =4.54
Electric field strength distribution in the cathode-anode gap of electron gun with convex cathode for electron current Iel=3.5 A and anode voltage Uan 11.25 kV
Geometry of the gun:

## Slide 5
Electron trajectories in uniform magnetic field B=2.4 kGs from electron gun with convex cathode.
Iel=3.5 A, Uan=11254 V, Efinal=60 keV.
Chart: Radial profile of the emission current density from the gun with convex cathode 25 mm for I_el=3.5 A, U_an=18.6 kV,
Chart: Dependence of maximum electron transverse energy on magnetic field for electron gun with convex cathode.
| 2 | 2.0499999999999998 | 2.1 | 2.15 | 2.2000000000000002 | 2.25 | 2.2999999999999998 | 2.35 | 2.4 | 2.4500000000000002 | 2.5 | 2.5499999999999998 | 2.6 | 2.65 | 2.7 | 2.75 | 2.8 | 2.85 | 2.9 | 2.95 | 3
0.1 | 0.96592 | 0.63781 | 0.81071 | 0.67331 | 0.90327 | 0.86313 | 0.59184 | 0.93588 | 0.81223 | 0.66643 | 0.84193 | 0.76487 | 0.7693 | 0.77376 | 0.78447 | 0.82481 | 0.75806 | 0.80871 | 0.83611 | 0.77722 | 0.8263
0.5 | 2.0698 | 1.9215 | 1.5365 | 1.4025 | 1.6026 | 1.6979 | 1.5682 | 1.2994 | 1.4763 | 1.6461 | 1.7299 | 1.6575 | 1.4567 | 1.4417 | 1.5374 | 1.5807 | 1.5095 | 1.4706 | 1.5427 | 1.623 | 1.6363
1 | 3.218 | 1.6457 | 2.408 | 2.6791 | 2.0296 | 2.3721 | 1.8444 | 2.284 | 2.7448 | 1.8392 | 2.3206 | 2.4512 | 1.9123 | 2.3425 | 2.2659 | 2.0671 | 2.2915 | 2.1874 | 2.2204 | 2.3185 | 2.0693
2 | 4.7112 | 3.6797 | 5.082 | 3.6553 | 3.2367 | 2.9359 | 3.9373 | 3.3775 | 3.9104 | 3.4825 | 3.2941 | 3.0066 | 3.9728 | 3.0554 | 3.9068 | 3.1028 | 3.3682 | 2.9085 | 3.5995 | 3.2226 | 3.6013
3 | 6.4471 | 5.1437 | 7.1387 | 3.2658 | 4.436 | 3.1287 | 6.2952 | 4.3886 | 5.254 | 4.9039 | 3.4024 | 4.089 | 3.6973 | 5.428 | 4.0173 | 5.1113 | 4.0714 | 3.9841 | 3.8062 | 4.4824 | 4.606
3.5 | 4.3038 | 7.7824 | 7.0094 | 5.2446 | 7.72 | 4.1554 | 4.3637 | 3.7508 | 5.7032 | 6.1035 | 4.7744 | 6.1022 | 4.3732 | 4.2008 | 4.0834 | 5.2281 | 5.4914 | 4.6524 | 5.4932 | 4.3076 | 4.2934
4 | 4.0944 | 4.9272 | 3.9917 | 9.3673 | 6.837 | 6.1686 | 7.8224 | 4.5376 | 4.3434 | 4.2798 | 5.6518 | 7.0639 | 5.1798 | 6.489 | 5.2802 | 4.2032 | 4.6345 | 4.3846 | 6.4489 | 5.2278 | 5.6463
5 | 7.1955 | 10.6109 | 9.6816 | 4.7622 | 5.0543 | 4.7704 | 8.9709 | 9.1477 | 6.7759 | 8.2572 | 7.0354 | 4.8468 | 5.0269 | 4.6059 | 7.5372 | 7.7656 | 6.2569 | 7.1464 | 6.2112 | 4.8793 | 5.2023

## Slide 6
2. Concave cathode
Geometry of the gun:
Electric field strength distribution in the cathode-anode gap of electron gun with concave cathode for electron current Iel=3.5 A and anode voltage 11.25 kV
Perveance = 1.38E6 A/V1.5
Kilpatrick safety factor (Iel=3.5 A and Uan =18.6 kV) = 4.22

## Slide 7
Electron trajectories in uniform magnetic field B=2.4 kGs from electron gun with concave cathode.
Iel=3.5 A, Uan=18605 V, Efinal=60 keV.
Chart: Radial distribution of the emission current density from the gun with concave cathode 25 mm for I_el=3.5 A, Uan=18.6 kV,
Chart: DEpendence of maximu transverse electron energy on magnetic field for electron gun with concave cathode
| 2 | 2.0499999999999998 | 2.1 | 2.15 | 2.2000000000000002 | 2.25 | 2.2999999999999998 | 2.35 | 2.4 | 2.4500000000000002 | 2.5 | 2.5499999999999998 | 2.6 | 2.65 | 2.7 | 2.75 | 2.8 | 2.85 | 2.9 | 2.95 | 3
0.1 | 0.37242 | 0.33743 | 0.33691 | 0.31011 | 0.30109 | 0.28143 | 0.24792 | 0.25942 | 0.25861 | 0.24659 | 0.25001 | 0.27105 | 0.29041 | 0.29889 | 0.29895 | 0.29705 | 0.28903 | 0.28537 | 0.28091 | 0.28225 | 0.28753
0.5 | 1.5136 | 0.8043 | 0.60422 | 0.94246 | 0.56395 | 0.80421 | 0.59907 | 0.77805 | 0.80781 | 0.50745 | 0.88072 | 0.67512 | 0.63084 | 0.80379 | 0.62258 | 0.7081 | 0.69034 | 0.66182 | 0.72657 | 0.63751 | 0.72923
1.0 | 1.7761 | 1.2993 | 1.3017 | 1.2874 | 1.4832 | 1.0487 | 1.2361 | 0.8418 | 1.2798 | 0.84703 | 1.4434 | 0.7865 | 1.2971 | 0.78878 | 1.277 | 0.89567 | 1.2317 | 0.90121 | 1.1482 | 0.94547 | 1.1375
2.0 | 2.6345 | 1.9923 | 3.842 | 1.0462 | 2.0806 | 1.3565 | 1.8173 | 2.9837 | 1.5953 | 1.9605 | 1.9122 | 1.0635 | 1.9772 | 1.4666 | 1.8765 | 2.2932 | 1.3516 | 1.8591 | 1.4851 | 1.4869 | 1.8625
3.0 | 2.6734 | 1.3427 | 2.2331 | 1.3428 | 3.2715 | 4.9874 | 2.3465 | 3.3923 | 3.6653 | 1.2286 | 1.7042 | 2.1682 | 1.6401 | 2.9784 | 3.4681 | 2.1536 | 2.414 | 2.4164 | 1.3449 | 2.162 | 2.2956
3.5 | 5.3302 | 7.5563 | 3.4405 | 1.4057 | 2.2716 | 1.2165 | 2.9363 | 5.4555 | 3.599 | 2.9755 | 4.0386 | 2.7125 | 1.3559 | 2.2279 | 2.1633 | 2.0995 | 3.6371 | 3.586 | 2.3738 | 2.6563 | 2.549
4.0 | 5.5561 | 4.0028 | 6.7855 | 7.3978 | 2.3491 | 1.4991 | 2.2983 | 1.5252 | 3.3553 | 5.3977 | 4.1041 | 3.19 | 4.1837 | 3.1327 | 1.36 | 2.1475 | 2.4662 | 2.2198 | 3.3502 | 4.1384 | 3.0048
5.0 | 1.653 | 3.4093 | 6.2888 | 7.3475 | 5.1851 | 6.5956 | 8.656 | 5.5516 | 1.485 | 2.0449 | 1.8582 | 2.1697 | 4.0535 | 5.9723 | 5.048 | 3.9009 | 4.5438 | 3.8893 | 2.0265 | 1.8857 | 2.9266

## Slide 8
3. Flat cathode and flat electrodes
Geometry of the gun:
Perveance = 2.613E6 A/V1.5
Kilpatrick safety factor (Iel=3.5 A and Uan =12.15 kV) = 4.98
Electric field strength distribution in the cathode-anode gap of electron gun with flat cathode for electron current Iel=3.5 A and anode voltage 12.15 kV

## Slide 9
Electron trajectories from electron gun with flat cathode (Rsph=25 mm) in uniform magnetic field 2.4 kGs for electron current Iel= 3.5 A, and final energy Eel=60 keV
Chart: Radial distribution of the emission current density from the electron gun with flat cathode 25 mm for I_el=3.5 A, Uan=12.15 kV,
Chart: Dependence of maximum transverse electron energy on value of uniform magnetic field for flat cathode 25mm for different electron currents
| 2 | 2.0499999999999998 | 2.1 | 2.15 | 2.2000000000000002 | 2.25 | 2.2999999999999998 | 2.35 | 2.4 | 2.4500000000000002 | 2.5 | 2.5499999999999998 | 2.6 | 2.65 | 2.7 | 2.75 | 2.8 | 2.85 | 2.9 | 2.95 | 3
0.1 | 0.027863 | 0.012687 | 0.0040434 | 0.011728 | 0.02326 | 0.014817 | 0.020129 | 0.025306 | 0.019789 | 0.0071348 | 0.0063864 | 0.0056762 | 0.0020705 | 0.0029962 | 0.0030881 | 0.0013675 | 0.0030377 | 0.0048391 | 0.0032668 | 0.0014511 | 0.0021961
0.5 | 0.22733 | 0.12943 | 0.038873 | 0.018778 | 0.060921 | 0.019355 | 0.029303 | 0.071402 | 0.07334 | 0.031462 | 0.017237 | 0.045773 | 0.031524 | 0.01095 | 0.01766 | 0.024404 | 0.01126 | 0.0086188 | 0.023744 | 0.023457 | 0.0091406
1 | 0.45802 | 0.30516 | 0.11704 | 0.28256 | 0.043136 | 0.17074 | 0.04462 | 0.075052 | 0.15331 | 0.028588 | 0.19684 | 0.041904 | 0.072245 | 0.062624 | 0.019292 | 0.080881 | 0.024988 | 0.059606 | 0.022298 | 0.041204 | 0.053801
2 | 0.16877 | 1.64 | 0.52307 | 0.32585 | 0.32895 | 0.52368 | 0.17619 | 0.46592 | 0.58227 | 0.075035 | 0.29615 | 0.17463 | 0.22162 | 0.13505 | 0.37138 | 0.11234 | 0.24254 | 0.10402 | 0.095844 | 0.05666 | 0.11943
3 | 2.4442 | 1.3663 | 0.57014 | 0.68859 | 2.0295 | 1.1394 | 0.69825 | 1.4781 | 0.58868 | 0.12456 | 0.20233 | 0.45706 | 0.67384 | 0.2217 | 0.76372 | 0.57439 | 0.17144 | 0.35311 | 0.15574 | 0.19606 | 0.13884
3.5 | 2.4017 | 0.86238 | 2.4715 | 1.4164 | 0.57729 | 0.47829 | 1.6548 | 1.6612 | 0.6274 | 1.1987 | 1.1429 | 0.25857 | 0.23741 | 0.33696 | 0.6165 | 0.53807 | 0.37397 | 0.8592 | 0.59658 | 0.25823 | 0.32852
4 | 3.811 | 5.8817 | 1.6236 | 1.4163 | 2.4236 | 1.3622 | 0.52996 | 0.47353 | 1.6652 | 2.109 | 0.88993 | 1.0909 | 1.4298 | 0.5292 | 0.19049 | 0.24501 | 0.51667 | 0.78943 | 0.40189 | 0.70338 | 0.8718
5 | 4.2989 | 3.6415 | 1.3521 | 4.2978 | 6.2242 | 2.7194 | 1.3838 | 2.4566 | 1.6072 | 0.95613 | 0.42455 | 0.85703 | 1.9783 | 2.3568 | 1.0695 | 1.5396 | 1.6099 | 0.76576 | 0.19429 | 0.26967 | 0.53378

## Slide 10
Comparison of electron guns with different geometry with fixed electron current
Chart: Dependence of maximum transverse electron energy on magnetic field for electron guns with different cathode geometries. I_el=0.1 A, E_el=60 keV
| 2 | 2.0499999999999998 | 2.1 | 2.15 | 2.2000000000000002 | 2.25 | 2.2999999999999998 | 2.35 | 2.4 | 2.4500000000000002 | 2.5 | 2.5499999999999998 | 2.6 | 2.65 | 2.7 | 2.75 | 2.8 | 2.85 | 2.9 | 2.95 | 3
Convex | 0.96592 | 0.63781 | 0.81071 | 0.67331 | 0.90327 | 0.86313 | 0.59184 | 0.93588 | 0.81223 | 0.66643 | 0.84193 | 0.76487 | 0.7693 | 0.77376 | 0.78447 | 0.82481 | 0.75806 | 0.80871 | 0.83611 | 0.77722 | 0.8263
Concave | 0.37242 | 0.33743 | 0.33691 | 0.31011 | 0.30109 | 0.28143 | 0.24792 | 0.25942 | 0.25861 | 0.24659 | 0.25001 | 0.27105 | 0.29041 | 0.29889 | 0.29895 | 0.29705 | 0.28903 | 0.28537 | 0.28091 | 0.28225 | 0.28753
Flat | 0.036934 | 0.0080621 | 0.0028896 | 0.012851 | 0.012404 | 0.0091924 | 0.01468 | 0.023407 | 0.016502 | 0.0039493 | 0.0028776 | 0.0030682 | 0.0021764 | 0.0013088 | 0.0030666 | 0.0033524 | 0.00088033 | 0.00091387 | 0.0025671 | 0.0032728 | 0.0017323

## Slide 11
Chart: Dependence of maximum transverse electron energy on magnetic field for electron guns with different cathode geometries. I_el=3.5 A, E_el=60 keV
| 2 | 2.0499999999999998 | 2.1 | 2.15 | 2.2000000000000002 | 2.25 | 2.2999999999999998 | 2.35 | 2.4 | 2.4500000000000002 | 2.5 | 2.5499999999999998 | 2.6 | 2.65 | 2.7 | 2.75 | 2.8 | 2.85 | 2.9 | 2.95 | 3
Convex | 4.3038 | 7.7824 | 7.0094 | 5.2446 | 7.72 | 4.1554 | 4.3637 | 3.7508 | 5.7032 | 6.1035 | 4.7744 | 6.1022 | 4.3732 | 4.2008 | 4.0834 | 5.2281 | 5.4914 | 4.6524 | 5.4932 | 4.3076 | 4.2934
Concave | 5.3302 | 7.5563 | 3.4405 | 1.4057 | 2.2716 | 1.2165 | 2.9363 | 5.4555 | 3.599 | 2.9755 | 4.0386 | 2.7125 | 1.3559 | 2.2279 | 2.1633 | 2.0995 | 3.6371 | 3.586 | 2.3738 | 2.6563 | 2.549
Flat | 2.9111 | 1.4411 | 0.13463 | 0.40299 | 0.91842 | 1.1127 | 0.24154 | 0.77052 | 1.2542 | 0.4142 | 0.16359 | 0.30269 | 0.25199 | 0.25495 | 0.10495 | 0.33204 | 0.61134 | 0.20218 | 0.22106 | 0.24873 | 0.080876

## Slide 12
Chart: Dependence of maximum transverse electron energy on magnetic field for electron guns with different cathode geometries. I_el=5.0 A, E_el=60 keV
| 2 | 2.0499999999999998 | 2.1 | 2.15 | 2.2000000000000002 | 2.25 | 2.2999999999999998 | 2.35 | 2.4 | 2.4500000000000002 | 2.5 | 2.5499999999999998 | 2.6 | 2.65 | 2.7 | 2.75 | 2.8 | 2.85 | 2.9 | 2.95 | 3
Convex | 7.1955 | 10.6109 | 9.6816 | 4.7622 | 5.0543 | 4.7704 | 8.9709 | 9.1477 | 6.7759 | 8.2572 | 7.0354 | 4.8468 | 5.0269 | 4.6059 | 7.5372 | 7.7656 | 6.2569 | 7.1464 | 6.2112 | 4.8793 | 5.2023
Concave | 1.653 | 3.4093 | 6.2888 | 7.3475 | 5.1851 | 6.5956 | 8.656 | 5.5516 | 1.485 | 2.0449 | 1.8582 | 2.1697 | 4.0535 | 5.9723 | 5.048 | 3.9009 | 4.5438 | 3.8893 | 2.0265 | 1.8857 | 2.9266
Flat | 0.9333 | 3.4103 | 3.7306 | 1.2889 | 1.4129 | 3.1486 | 1.6465 | 0.29965 | 0.28229 | 0.62812 | 0.95583 | 0.97645 | 0.49132 | 0.94609 | 1.3969 | 0.72281 | 0.22372 | 0.32611 | 0.28595 | 0.25176 | 0.27155

## Slide 13
Chart: Dependence of maximum electron transverse energy on the magnetic field for electron gun with concave cathode and different accelerating gaps, I_el=4.0 A.
| 2 | 2.0499999999999998 | 2.1 | 2.15 | 2.2000000000000002 | 2.25 | 2.2999999999999998 | 2.35 | 2.4 | 2.4500000000000002 | 2.5 | 2.5499999999999998 | 2.6 | 2.65 | 2.7 | 2.75 | 2.8 | 2.85 | 2.9 | 2.95 | 3
40 mm | 3.9645 | 12.6265 | 12.8979 | 3.2488 | 6.3979 | 4.8943 | 3.07 | 5.5713 | 4.3708 | 3.8448 | 9.9808 | 6.5881 | 3.5347 | 5.3881 | 2.9621 | 2.6146 | 4.8676 | 3.1767 | 4.3408 | 5.9682 | 4.8731
60 mm | 7.4758 | 5.471 | 9.1478 | 9.3085 | 3.4103 | 2.1842 | 3.4876 | 2.3431 | 4.2715 | 7.4685 | 5.279 | 4.8375 | 5.3484 | 4.2439 | 1.897 | 3.3703 | 3.3264 | 3.3669 | 4.3419 | 6.027 | 4.2999
Comparison of the transverse electron energy for the gun with concave cathode for two different accelerating gaps: 40 mm and 60 mm.

## Slide 14
7 geometries of gun with flat cathode and flat electrodes has been tested:
2
3
4
5
6
1
7

## Slide 15
Performance comparison of electron guns with flat cathodes and different geometries with current 3.5 A
Chart: Dependence of maximum transverse electron energy on uniform magnetic field for electron guns 25 mm diameter cathode with different curvature radii. I_el=3.5 A.
| 2 | 2.0499999999999998 | 2.1 | 2.15 | 2.2000000000000002 | 2.25 | 2.2999999999999998 | 2.35 | 2.4 | 2.4500000000000002 | 2.5 | 2.5499999999999998 | 2.6 | 2.65 | 2.7 | 2.75 | 2.8 | 2.85 | 2.9 | 2.95 | 3
Flat_1 | 2.4017 | 0.86238 | 2.4715 | 1.4164 | 0.57729 | 0.47829 | 1.6548 | 1.6612 | 0.6274 | 1.1987 | 1.1429 | 0.25857 | 0.23741 | 0.33696 | 0.6165 | 0.53807 | 0.37397 | 0.8592 | 0.59658 | 0.25823 | 0.32852
Flat_2 | 0.67342 | 2.5247 | 3.4279 | 1.6087 | 0.23989 | 1.5605 | 2.4374 | 1.2367 | 0.51493 | 1.2876 | 1.2683 | 0.52733 | 0.17452 | 0.52176 | 0.92733 | 0.61225 | 0.28136 | 0.6588 | 0.7379 | 0.24467 | 0.14162
Flat_3 | 4.4768 | 0.91539 | 0.8356 | 1.4703 | 1.4544 | 0.7425 | 0.60482 | 2.0762 | 1.3905 | 0.41776 | 0.82082 | 0.63485 | 0.34931 | 0.19728 | 0.34897 | 0.84731 | 0.56307 | 0.35232 | 0.7158 | 0.3251 | 0.092563
Flat_4 | 0.43428 | 1.5673 | 2.8746 | 1.9404 | 0.29468 | 1.2204 | 2.2855 | 1.2447 | 0.30959 | 0.87195 | 1.0326 | 0.614 | 0.18239 | 0.40777 | 0.93611 | 0.65878 | 0.20671 | 0.46734 | 0.57551 | 0.2553 | 0.085942
Flat_5 | 0.51975 | 1.5581 | 3.8755 | 0.35435 | 1.6136 | 2.5903 | 1.3684 | 0.24188 | 0.86651 | 1.377 | 0.96807 | 0.30385 | 0.62112 | 1.2178 | 0.67468 | 0.15846 | 0.42594 | 0.71156 | 0.47182 | 0.14382
Flat_6 | 0.43428 | 1.5673 | 2.8746 | 1.9404 | 0.29468 | 1.2204 | 2.2855 | 1.2447 | 0.30959 | 0.87195 | 1.0326 | 0.614 | 0.18239 | 0.40777 | 0.93611 | 0.65878 | 0.20671 | 0.46734 | 0.57551 | 0.2553 | 0.085942
Flat_7 | 3.9321 | 2.2729 | 0.27833 | 0.7899 | 1.4656 | 1.6925 | 0.52178 | 1.2504 | 1.8656 | 0.74635 | 0.33179 | 0.55726 | 0.44425 | 0.48363 | 0.21751 | 0.61321 | 0.95286 | 0.44093 | 0.40448 | 0.51674 | 0.15946
Fit | 4.3951 | 4.2077 | 4.0283 | 3.8566 | 3.6922 | 3.5348 | 3.3841 | 3.2398 | 3.1017 | 2.9695 | 2.8429 | 2.7217 | 2.6057 | 2.4946 | 2.3882 | 2.2864 | 2.1889 | 2.0956 | 2.0063 | 1.9208 | 1.8389 | 1.7605 | 1.6854 | 1.6136 | 1.5448 | 1.4789 | 1.4159 | 1.3555 | 1.2977 | 1.2424 | 1.1894 | 1.1387 | 1.0902 | 1.0437 | 0.99922 | 0.95662 | 0.91584 | 0.8768 | 0.83942 | 0.80363 | 0.76937 | 0.73658 | 0.70517 | 0.67511 | 0.64633 | 0.61878 | 0.5924 | 0.56714 | 0.54297 | 0.51982 | 0.49766
Chart: Radial distribution of the emission current density from the el. gun with flat cathodes 25 mm for I_el=3.5 A and different electrodes

## Slide 16
Flat cathode + flat electrodes, Version 7- effect of control electrode negative bias: effect and price.
Chart: Radial distribution of the emission current density from the el. gun with flat cathode 25 mm (Flat7) with different bias of control electrode for I_el=3.5 A
Similar:
Chart: Dependence of maximum electron transverse energy on magnetic field for gun with flat cathode V7 with I_el=3.5 A, for different Wehnelt bias voltages.
| 0.5 | 0.55000000000000004 | 0.6 | 0.65 | 0.7 | 0.75 | 0.8 | 0.85 | 0.9 | 0.95 | 1 | 1.05 | 1.1000000000000001 | 1.1499999999999999 | 1.2 | 1.25 | 1.3 | 1.35 | 1.4 | 1.45 | 1.5 | 1.55 | 1.6 | 1.65 | 1.7 | 1.75 | 1.8 | 1.85 | 1.9 | 1.95 | 2 | 2.0499999999999998 | 2.1 | 2.15 | 2.2000000000000002 | 2.25 | 2.2999999999999998 | 2.35 | 2.4 | 2.4500000000000002 | 2.5 | 2.5499999999999998 | 2.6 | 2.65 | 2.7 | 2.75 | 2.8 | 2.85 | 2.9 | 2.95 | 3
-500 | 507.126 | 173.9006 | 82.4253 | 74.362 | 137.3193 | 270.6347 | 125.0463 | 11.4724 | 111.9787 | 93.854 | 20.1228 | 8.0844 | 19.2188 | 32.9477 | 15.0859 | 4.349 | 4.431 | 11.7471 | 10.9692 | 6.7788 | 1.0895 | 7.5595 | 13.6622 | 5.3175 | 1.1107 | 4.7547 | 4.0496 | 2.1771 | 1.3023 | 1.54 | 4.6834 | 3.5611 | 1.0335 | 0.99944 | 2.1057 | 1.3195 | 1.187 | 0.49864 | 1.9354 | 2.0658 | 0.79709 | 0.45605 | 0.79894 | 0.72852 | 0.56697 | 0.48628 | 0.61571 | 1.164 | 0.71973 | 0.27468 | 0.35972
-300 | 437.5994 | 146.6091 | 87.8224 | 116.5658 | 251.2734 | 236.369 | 25.9851 | 83.0695 | 131.3592 | 45.9209 | 18.7714 | 20.0889 | 50.2976 | 25.8011 | 5.8162 | 6.7498 | 14.7676 | 12.6979 | 9.8655 | 2.4426 | 10.5446 | 18.4578 | 7.4517 | 2.7537 | 8.4063 | 5.9493 | 3.2561 | 1.3722 | 3.877 | 6.7688 | 2.8602 | 0.86917 | 2.1316 | 3.651 | 2.0437 | 1.0928 | 1.931 | 3.7325 | 1.5003 | 0.74869 | 0.77768 | 1.5182 | 0.9029 | 0.97104 | 0.96084 | 1.9266 | 1.2343 | 0.5259 | 0.67363 | 0.71081 | 0.63261
-200 | 397.1228 | 89.1216 | 60.6419 | 105.1158 | 244.1904 | 184.9969 | 5.5146 | 133.6329 | 108.6706 | 23.5752 | 19.7861 | 26.3063 | 42.9535 | 20.227 | 6.4009 | 16.7424 | 16.6905 | 8.1205 | 4.244 | 3.4285 | 9.0068 | 17.5093 | 2.5029 | 9.7111 | 11.6691 | 2.8152 | 0.99202 | 1.3903 | 1.6972 | 4.5806 | 2.6795 | 2.8055 | 6.1638 | 2.4969 | 0.66281 | 1.3306 | 0.91536 | 1.4512 | 1.1747 | 1.3739 | 2.7918 | 1.7621 | 0.6692 | 0.9969 | 0.47329 | 0.42441 | 0.75899 | 0.56688 | 1.4813 | 1.2058 | 0.64918
-100 | 360.2779 | 64.0629 | 71.4121 | 120.5967 | 198.2065 | 80.4415 | 15.2689 | 128.4324 | 76.1475 | 13.5446 | 19.9716 | 33.6503 | 23.4735 | 2.6964 | 4.6521 | 12.6027 | 11.4905 | 3.1783 | 2.0671 | 7.0316 | 9.7265 | 3.9985 | 1.3407 | 9.524 | 5.3893 | 0.41276 | 1.7495 | 1.9866 | 1.4866 | 0.74785 | 0.402 | 2.6567 | 2.6796 | 0.40079 | 1.3022 | 1.4952 | 0.45948 | 0.12542 | 0.30126 | 0.69737 | 0.83106 | 0.31891 | 0.64859 | 0.79282 | 0.16712 | 0.10804 | 0.14713 | 0.21983 | 0.29943 | 0.14851 | 0.34496
0 | 362.29 | 137.5387 | 63.7564 | 88.2082 | 126.442 | 151.8148 | 172.3826 | 176.9738 | 142.6914 | 75.8577 | 19.1043 | 6.598 | 41.9733 | 82.8928 | 100.0577 | 89.7533 | 62.9968 | 12.1954 | 16.3295 | 35.3058 | 50.9393 | 30.5612 | 9.6945 | 1.9268 | 3.7835 | 7.6109 | 8.9748 | 8.5373 | 7.9007 | 6.9928 | 6.4526 | 4.9468 | 2.377 | 1.3433 | 4.0209 | 10.2956 | 15.1874 | 13.808 | 7.1595 | 1.693 | 1.4369 | 5.0137 | 7.8185 | 7.4265 | 5.0164 | 2.7339 | 1.3475 | 0.75917 | 0.93264 | 2.7321 | 3.6436

## Slide 17
Chart: Dependence of maximum transverse eelctron energy on magnetic field for electron gun with flat cathode V7, I_el=0.1A, e_el=3.0 keV.
| 0.3 | 0.35 | 0.4 | 0.45 | 0.5 | 0.55000000000000004 | 0.6 | 0.65 | 0.7 | 0.75 | 0.8 | 0.85 | 0.9 | 0.95 | 1 | 1.05 | 1.1000000000000001 | 1.1499999999999999 | 1.2 | 1.25 | 1.3 | 1.35 | 1.4 | 1.45 | 1.5 | 1.55 | 1.6 | 1.65 | 1.7 | 1.75 | 1.8 | 1.85 | 1.9 | 1.95 | 2 | 2.0499999999999998 | 2.1 | 2.15 | 2.2000000000000002 | 2.25 | 2.2999999999999998 | 2.35 | 2.4 | 2.4500000000000002 | 2.5 | 2.5499999999999998 | 2.6 | 2.65 | 2.7 | 2.75 | 2.8 | 2.85 | 2.9 | 2.95 | 3
0.1 | 0.73797 | 0.19266 | 0.14903 | 0.45818 | 0.19506 | 0.17151 | 0.16932 | 0.025992 | 0.051272 | 0.033863 | 0.014346 | 0.040974 | 0.014833 | 0.010303 | 0.017431 | 0.0063628 | 0.010188 | 0.0094407 | 0.0050597 | 0.0082859 | 0.0061244 | 0.0051106 | 0.0061004 | 0.0045061 | 0.0047404 | 0.0046774 | 0.003808 | 0.0039477 | 0.003565 | 0.0033796 | 0.0033242 | 0.0029711 | 0.0028874 | 0.0028571 | 0.0026505 | 0.0025251 | 0.0024175 | 0.0023425 | 0.0022717 | 0.0022403 | 0.0021121 | 0.0020855 | 0.00197 | 0.0018846 | 0.0018597 | 0.0017534 | 0.0017387 | 0.001659 | 0.0016258 | 0.0015983 | 0.0015705 | 0.0014666 | 0.0014733 | 0.0014512 | 0.0013832
Chart: Dependence of maximum transverse energy on magnetic field for electron gun with flat cathode V7. I_el=2.5 A, E_el=27 keV
| 2 | 2.0499999999999998 | 2.1 | 2.15 | 2.2000000000000002 | 2.25 | 2.2999999999999998 | 2.35 | 2.4 | 2.4500000000000002 | 2.5 | 2.5499999999999998 | 2.6 | 2.65 | 2.7 | 2.75 | 2.8 | 2.85 | 2.9 | 2.95 | 3
2.5 | 0.59216 | 0.43319 | 0.63454 | 0.68256 | 0.27119 | 0.1947 | 0.14305 | 0.14469 | 0.16128 | 0.29915 | 0.34737 | 0.21547 | 0.18815 | 0.10621 | 0.061639 | 0.072692 | 0.11462 | 0.18513 | 0.15291 | 0.14729 | 0.10667
Simulated maximum electron beam temperature for special regimes 0.1 A and 3 keV) and (2.5 A and 27 keV):

## Slide 18
Electron trajectories for gun with flat electrodes (Version 1) at Iel =3.5 A

## Slide 19
Schematic design of the cooler gun side version with open side flange:

## Slide 20
Axial magnetic field distribution of the gun solenoid: L=800 mm, ID=315 mm
Chart: Z, mm
Pancake structure of coils
Conductor: 6.35x6.35 mm, water channel 3.5 mm
For 2.4 kGs I=120 A, U=160 V,
Power consumption approx. 20 kWatt
Water consumption: 16 L/min,
Water pressure approx. 0.3 Bar,
Water temperature rise 200

## Slide 21
Conclusion:
Out of three simulated electron gun geometries the electron gun with flat cathode and flat electrodes provides the smallest transverse electron energy in all tested ranges of the electron current (0.1-5.0 A) and magnetic field (2.0 – 3.0 kGs). The convex electron gun has the largest perveance and the most uniform distribution of the electron current density across the beam. The electron guns with concave and flat cathodes have some elevation of the current density on the periphery.
Electrostatically all gun geometries are spark-safe for the anode voltage holdoff: at 3.5 A the Kilpatrick safety factor is larger than 3.9 for all guns.
The pattern of minima and maxima of the transverse energy as a function of the magnetic field depends on the accelerating gap: it can move with varying the gap.
Of all tested concepts the lowest transverse energy provides electron gun with flat cathode and flat electrodes. It is easy and safe to control the emission density distribution on the cathode by changing the Wehnelt bias.
For different geometries of guns with flat cathode the transvers energy variations as a function of the magnetic field for a fixed electron current stay within the same “corridor”. Analysis of different gun geometries with flat cathode and flat electrodes demonstrated that with small variations of transverse energy these guns generate beams with different radial distribution of current density depending on the shape of the Wehnelt electrode.
With electron current I00 mA and the beam energy of 3 keV the transverse electron energy remains lower than 1 eV up to magnetic field of 300 Gs.