## Slide 1: ELENA – Status and Plans for LS2 C. Carli on behalf of the AD/ELENA team(s) GBAR Meeting, 28th November 2018
Recent Results from Commissioning (selection of a few highlights)
ELENA Commissioning Status
Summary and Outlook

## Slide 2: Recent Results from Commissioning Observation of the beam from the source on a ring pick-up
Observation of beam from source on first pick-up in ring
  Steering without kicker (flat-top shorter than beam pulse from source) up to first ring pick-up
  Higher deflection from septum and steering upstream
  No beam must hit pick-up plates (delicate!)
  Intensity fluctuations depend on source settings: probably caused by plasma fluctuations and may explain poor reproducibility observed
  Source optimisation easier with these observations
  Possibly, fluctuations may be reduced with longer rise times of the pulse
Pick-up sum signals showing (very likely intensity fluctuations, sometimes saturated)
Investigations by D. Gamba
Pick-up difference signals

## Slide 3: Recent Results from Commissioning Efforts for a new isolation transformer using oil as insulator
Last (repaired) isolation transfo using solid insulator and operated at 85 kV failed on Friday 21st September
Despite high priority by CERN groups for a transformer using oil, beam available only a few hours since
Oil tank for isolation transformer completed already on 26th September
Thanks a lot for the high priority and efforts by several groups and many people
Winding new secondary coil
Broken connector and new HV connection without connector
New support for secondary coils
1st mounting of transformer

## Slide 4: Recent Results from Commissioning Observation along the cycle – typical situation during last weeks
Some signals along 2nd ramp and on the 100 keV plateau (1st ramp not seen!)
Typical situation end of October, beginning of November
  Only harmonic h=1 available
  Significant loss towards the end of the 2nd ramp
  Many efforts throughout the year resulted in slow improvements
  Clear effect of
2 s/div
Peak signal of
pick-up sum signal
RF voltage
Intensity estimate from RF electronics
Bunched beam electron cooling (increases pick-up peak signal)
Real loss
Probably no loss, but systematic error with short bunches

## Slide 5: Recent Results from Commissioning Electron cooling at intermediate 35 MeV/c plateau
- RF switched off
- No bunches, but “Schottky noise” generated by beam acquired by pick-ups
- Spectral noise density (power) proportional to beam distribution
=> Clear signs of longitudinal electron cooling
- Scraper is an aperture moved into the beam - Gives information on beam size and “emittance”
- Measurements with a “scraper” at different times on the 35 MeV/c plateau
- Clear emittance reduction observed - Only limited amount of time spent on systematic optimization of electron cooling (lack of time)
=> Margin for further improvements?
Without cooling
Cooling
Time (15 s)
Frequency (50 kHz) or rel. momentum offset (7.5 10-3 )
Bunched
beam

## Slide 6: Recent Results from Commissioning Observation of antiproton beams at extraction with harmonics h=1
Bunches around extraction
  More than .5 107 antiprotons seen very reproducibly in ring prior to ejection and in line
  Possibly improved with better steering thanks to profile acquisitions
  Bunch lengths a bit long with URF = 32 V programmed on harmonics h = 1
  Rms relative momentum spread of 0.68 10-3 from reconstruction about nominal (and possibly overestimated due to lower than expected RF voltage)
1 us/div
Transformer in LNE 50 line
Last time on a ring pick-up
Fast deflector
-0.6 0 0.6 ns
-0.6 0 0.6 keV
Reconstruction (“Tomography”) of longitudinal phase space density distribution from bunch shapes acquired during about one synchrotron oscillation

## Slide 7: Recent Results from Commissioning Observation of antiproton beams at extraction with h=1
Profiles in the GBAR line
  Acquisitions with second monitor LNE.BSGWA.5060 in GBAR line
  Beam sizes with voltages of first two quads of line set to zero
    bH =6 m gives rms emittance eH = 3.3 um (slightly overestimated without taking dispersion into account)
    bV = 20 m gives rms emittance eV = 1.25 um
Gaussian fit by hand with sH = 4.5 mm
Gaussian fit by hand with sV = 5 mm
Betatron functions along LNE50 line with settings to provide beam to GBAR and ring optics updated to quad settings used in practice

## Slide 8: Recent Results from Commissioning Observation of antiproton beams at extraction with h=1
Profiles in the GBAR line
  Acquisitions with second monitor LNE.BSGWA.5020 in GBAR line
  Beam sizes with voltages of first two quads of line set to zero
    bH = 6 m gives rms emittance eH = 4.1 um (slightly overestimated without taking dispersion into account)
    bV = 4 m gives rms emittance eV = 1.5 um
Gaussian fit by hand with sH = 5 mm
Gaussian fit by hand with sV = 2.5 mm

## Slide 9: Recent Results from Commissioning Observation from the very last day with beam in 2018
Higher harmonics h=2 and h=4 finally possible after upgrade of RF control
  Main motivation losses after re-bunching with >1 107 antiprotons with short bunches
  Of interest for observation along 2nd ramp (increased efficiency not expected)
  Whole cycle with beam combining two acquisitions (2nd with slightly higher intensity)
    Improved efficiency (close to 50%)
2 s/div
Peak signal of
pick-up sum signal
Intensity estimate from RF electronics
Bunched beam electron cooling (increases pick-up peak signal)
Probably real loss – 2nd ramp not priority during last weeks
Cycle

## Slide 10: Recent Results from Commissioning Observation from the very last day with beam in 2018
From sum signal of electro-static pick-ups (10 % uncertainty of calibration)
  3.7 107 antiprotons injected (consistent with data from AD running very well
  Four bunches, each with 0.43 107 antiprotons at extraction
  => Efficiency about 46 %
Total intensity estimated by “beam current transformer” in line about 1 107 antiprotons
  Real loss or acquisition problem?
100 ns/div
20 mV/div
100 ns/div
20 mV/div
One out of four bunches at extraction
Injected bunch
Position pick-up sum signals
1 us/div

## Slide 11: Recent Results from Commissioning Observation from the very last day with beam in 2018
100 ns/div
20 mV/div
Tomoscope acquisition – one of four bunches just before extraction about nominal beam characteristics
Measurement of the tunes (working point) along the second ramp Some significant variations – better control with improved procedures to generate functions for power converters?
1 us/div
-0.4 0 t us 0.4
-0.4 0 DE us 0.4
500 ms/div
.40 q .45
qH
qV

## Slide 12: ELENA Commissioning Status
Aims defined at the beginning of 2018:
  Continuation of Commissioning with electron cooler from April on
  Get Confidence that machine works properly
    Ideally demonstration of operational cycle to deliver 100 keV antiprotons
  First beams for GBAR
Achieved at the end of beam time in 2018:
  Reproducible deceleration of pbars to 100 keV
    Loss along 2nd ramp to 100 keV an issue (now >45 % of injected beam at extraction)
    About nominal characteristics in longitudinal phase space (intensities to be confirmed)
    Probably still larger than nominal emittances
  Clear observations of electron cooling (beneficial for deceleration)
  Close to having demonstrated nominal cycle
    Despite long periods without beam and technical problems with source
  Operation for GBAR
    H- and antiproton bunches with about nominal intensities
    Transverse emittance somewhat above nominal (factor <2 in transverse beam size)

## Slide 13: ELENA Commissioning Status
Open issues, improvements, next steps
  Efficiency and intensity at 100 keV
    Re-optimization of whole cycle (e.g. first ramp, which was not priority recently, cooling …)
  Injection matching and steering in AD to ELENA lines
    Started before 2nd failure of AD cooler, Potential to reduce losses along 1st ramp
  Profile monitors!
  Upgrades and studies of source
  Cycle generation (procedures and software to generate reference function for power converters) and cycle control
    Improved control of working point and “closed orbit”
    Integration of electron cooler compensation integrated to “closed orbit” manipulations?
  Further thorough studies on electron cooling
    Limited so far due to lack of time
Installation and Commissioning of transfer lines to old experimental area
  Main objective for LS2
  Relies on observation of H- with the profile monitors and availability of all hadware

## Slide 14: Summary and Outlook
Significant ELENA Commissioning progress over the year despite various delays
  Delay of restart due a vacuum leak of the cooler, unavailability of AD, issues with the ion source
  In practice, most progress made with antiprotons, only during dedicated AD shifts (change of commissioning strategy)
  Confidence that ELENA improves to conditions for all experiments
  Availability of a machine cycle similar to nominal one (intensities and efficiency to be confirmed and slighly large transverse emittances)
  Operation for GBAR with H- and antiproton beams (about nominal intensity for one bunch, but larger emittances)
Plans for LS2
  Installation of the transfer lines to the “old” experimental zone
  Upgrades of the ion source for reliable generation of 100 keV proton and H- beams
  Review of status and possible improvements (ring optics, applications, instrumentation …)
  Possibly test periods in 2019 for tests of the source (already in spring)
  Resume commissioning activities with beam from source in early summer 2020
    Test of ring and electron cooling with protons
    Commissioning of lines with H- (beam intensity and quality of measured profiles?)
100 keV antiprotons for all experiments from 2021 on