## Slide 1: Linac radiation dose and shielding Simulation by Joao Espadanal summary by Bruno M. implementation Jean-Yves Roussé

## Slide 2: linac radiation
Motivation:
  early failures of linac equipments (radiation-linked?)
  estimates of dose to linac/vacuum pump/coils very high (10-20 Mgy/year)
Simulation
  Initiated by Claudia Ahdida
  Large work by Joao Espadanal and Vlasilis Vachoudis
=> complete note available.
  Dose rates at all locations around the linac
  Comparison with in-situ measurements
  Simulation of many shielding configurations
  Calculation of activation and dose rate.

## Slide 3: Model

## Slide 4: Results (summary)
Dose in lower coil:
6 E(-03) Gy/pulse = 15.6 MGy/year
(1 year = 100 days of 24h)
Dose in Linac equipment
( ~50 cm above target)
1.2 MGy /year
Dose in vacuum equipment
(50-75 cm below target, 50 cm off-axis)
2.2 – 1.3 MGy/year

## Slide 5: Comparison calculation/dosimeters
Passive dosimeters in the Linac bunker
(Georgi Gorini, Federico Ravotti)
Dosimeters installed 10 Nov 2017
removed 6 June 2018
- Measured dose:
- Charge delivered by the LINAC
during this period (Tymek) : 30 C
Dose calculated by Joao for 30C delivered charge:
1200 -1400 Gy
Excellent agreement !

## Slide 6: Shielding options
Close shielding: cylinder around
the target vacuum chamber, 2 cm thick
=> Dose on coils: SS: 60%, Pb: 35%, W: 20%
(thicker plate does not improve much)
Top shielding: cylinder + 2 cm SS plate
=> Dose on linac : ~50%
Bottom shielding: cylinder + 2cm SS plate
=> Dose on vacuum equipment ~ 40%
Box-like SS shielding improves on the sides at large distance
Proposal: Pb cylinder + 2-3 cm thick SS box,
should reduce doses to less than 40%

## Slide 7: Activation in case of lead shielding?
Joao simulated the dose from activation one day after 12h continuous running , with and without lead shielding
average in z for
x = [-10; 10 ] cm and y = [-10; 10] cm
around x, y target
No change seen from lead shielding (even slight decrease, probably due to shielding itself…)
Recent news (yesterday): the simulation might have not included photonuclear reactions for lead!
Being discussed with RP.