## Slide 1: DFM – Concepts & pre-design Meeting objective : get feedback on conceptual approach, pre-design
Y.Leclercq, A. Kolehmainen

## Slide 2: Context
Each IP1 and IP5 sides equipped with 2 cold powering chains of cryostats
Triplet insertion : DFHx – SC Link (DSH) – DFX
Matching sections : DFHm – SC Link - DFM
DFM basic functions:
Electrical interface between SC Link and D2 (MBRD – 13 kA + 4 Correctors MCBRD)
Supply cryogenics to the DSHm SCLink
MBXF
D1
DFX
DSHx
MgB2
NbTi
Jumper D1
Jumper DFX
Splice
Beam
Jumper DFM
D2
Jumper D2
MBCRD
MBRD
DSHm
DFM
2 x 18 kA
2 x 13 kA
3 x 7 kA
12 x 2 kA
DFHx1
DFHx2
2 x 13 kA
8 x 0.6 kA
DFHm
HTS
MgB2
PT
PT
PT
PT
PT
PT
PT
LHC tunnel
UR: Service tunnel
D1
CP
Q3
Q2b
Q2a
Q1
IP
Power converters
DSHx
DFHx1
DFX
DFHx2
D2
≈45m
DFHM
DFM
DSHm
≈80m
≈50m
≈8m
Service tunnel
Transverse tunnel
LHC tunnel


Ghe <17K
Ghe <17K
Ghe @4.5K
Lhe @4.5K
SFHe @1.9K
SFHe @1.9K
Ghe @4.5K
Lhe @4.5K
UL: Transverse tunnel
Superfluid @ 1.9K
Liquid He @ 4.5 K
Gaseous He
Heater
Vacuum barrier
HTS
MgB2
NbTi
Warm cable
Splice

## Slide 3: Conceptual specifications
From IP
93.25m
≈140m
DFM
DSHm
D2
CC
CC
≈45 m
≈1.5 m
R≈1.9 m
Courtesy Amalia, 8th HL-LHC col.
DFM
Ghe mass flow
D2
Cold mass
Saturated liquid bath
@ 1.3 bara
Superfluid helium @1.9K
Plug
NbTi
NbTi D2 leads
MgB2
NbTi/NbTi splices
NbTi/MgB2 splices
CS : LHE inlet
From C
SD : GHE return
To D
EhEh’2
WP6a meeting : 28 August 2018
Cryogenic layout
Integration: & installation
  DFM located in the LHC tunnel about 45m from the shaft: fixed
Electrical layout :
  Number and material of leads : fixed (extra cables & NbTi leads geometry to clarify)
  D2-DFM Splices location : fixed
Cryogenic layout
  Common helium volume with SCLink / splices immersed: fixed
  Generated mass flow from liquid helium vaporisation: fixed
  Thermal contractions approach for DFM: in progress
Vacuum layout EDMS2048016
  Separated insulation vacuum with SCLink & D2-DFM link: fixed

## Slide 4: DFM functional specifications
Electrical
  Ensure continuity between DSHm and D2 leads 10 leads ? (15 leads) ?
  Ensure integrity of cables (transport, installation, thermal cycles) Rmin=1.25m / Fmax=400N
  Provide volume, access and protection for splices NbTi-NbTi TBC
  Ensure instrumentation acquisition (V-taps) TBC
Cryogenic
  Ensure max splices temperature < 5.5 K / Max Rsplice
  Ensure immersion of splices nominal ≈100 mm over splices +/-50 mm TBC
  Ensure GHE supply to SCLink : Nominal 2 g/s / design 3g/s
  Adapt to cryogenic layout One jumper, 1 inlet CS, 1 outlet Sd, 1 TS E’hFh2
  Ensure instrumentation acquisition TBC
  Ensure no condensation on external surfaces TBDesigned
  Budget static heat loads 20 W
  Budget dynamic heat loads 1.5 W
  Integrate thermal contractions layout scenario TBD
  Ensure circuits leak tightness 1.10-9 mbar.l.s-1 tbc
  For saturated LHe volume, a constant increasing slope shall be granted between coldest point and liquid-gas interface
  Autonomy nominal supply 5 minutes
Mechanical
  Design pressure for the vacuum vessels PS=1.49 bara
  Design pressure for the DFH helium vessels PS= PS(DSHx) + 0.5 bar
  Allowable accesses to splices (cut-open) 4 TBC
  Cables fixed points characteristics @ splice level / F max ??? TBC
Insulation vacuum
  Independent insulation vacuum with SCLink see Indico733790
  Share insulation vacuum with Current leads 1.10-5mbar
  Present pumping and instrumentation interfaces //
Integration
  Fit in LHC tunnel
  Interface with SCLink (cryostat & cables), current leads (mechanical & HTS): Dimensions TBC
Installation
  Compatible with SCLink transport configuration after testing TBD
  Interface with SCLink geometry (cryostat & cables distribution and orientation) Pitch: 0.8m
  Compatible with allowed manufacturing processes Welding
  Compatible with D2-DFM link TBD
Maintenance
  Allow required access to NbTi-NbTi splices TBD
  Allow access for inspections and replacement Safety devices, instrumentation
Safety & rules
  Strategy toward DFM liquid Protect SCLink+DFM
  Design, manufacture and test to Norms PED 2014-68-EU & CERN rules
  Design safe scenario for pressure relief devices ISO 21013-3
DFM

## Slide 5: Design guidelines
Ensure DFM installation & integration
Ensure MgB2 & NbTi cables integrity
Ensure splices immersion and gaseous mass flow to SCLink
Ensure increasing slope in saturated bath
Ensure instrumentation routing
Ensure safety aspects
Ensure maintenance

## Slide 6: Preliminary design (functional)
Insulation vacuum layout
Electrical layout
Cryogenic layout
  Cryogenic lines/jumper
  Cryogenic services (heater, gauges, instrumentation)
D2-DFM link
D2 jumper
DSHm
DFM
D2
QXL
A-A
B-B
Superfluid @ 1.9K
Liquid He @ 4.5 K
Gaseous He
Heater
Vacuum barrier
HTS
MgB2
NbTi
Warm cable
Splice
D2-DFM link
Plug
DFM
DSHm
SD
CS
E’HFH2
A-A
SD
CS
E’HFH2
B-B
P relief device
Instru. wire
Level gauge
Heater

## Slide 7: Preliminary design
Integration
  D2-DFM link: LHC stand alone type
  Physical position:
    Respect transport area
    Access for splices  above D2
Mechanical layout
  DFM fixed to D2
  DSHm fixed to DFM ?
  NbTi-NbTi splices fixed to he vessel
  Future discussions:
    SCLink interface: Inner pipe fixed to outer pipe ?
Superfluid @ 1.9K
Liquid He @ 4.5 K
Gaseous He
Heater
Vacuum barrier
HTS
MgB2
NbTi
Warm cable
Splice
D2-DFM link
Plug
DFM
DSHm
20 bar
DSHm Weight
D2DFM link routed along the wall
Courtesy E.Chaudet
Transport area
Cryo-lines
D2 &
beam
≈ 1m
R=1.9m

## Slide 8: Proposal Assembly sequence
Initial configuration:
  D2 installed
  D2-DFM link installed
  Plug toward D2-DFM link connected
SCLink installation
  Same configuration as DFX:
    MgB2-NbTi splices are located in a rigid protective sleeve
    Only NbTi leads are apparent
  Insertion straight
  Lower protective sleeve
  Close vacuum vessel
  Splice NbTi-NbTi
  Slide sleeve back & weld
Rigid protective sleeve
NbTi leads
MgB2-NbTi leads
MgB2 leads
Flexible
Rigid
SCLink outer jacket