## Slide 1: Landau damping in the longitudinal plane
T. Argyropoulos, I. Karpov, E. Shaposhnikova (CERN)
24.09.2019
With input from T. Bohl, H. Damerau, J. E. Muller, J. Repond, M. Schwarz. H. Timko
ICFA mini-Workshop on "Mitigation of Coherent Beam Instabilities in particle accelerators" MCBI 2019,
Zermatt, Switzerland

## Slide 2: Outline
Introduction
Single bunch
  Sacherer and Hofmann-Pedersen approaches
  Loss of Landau Damping in LHC
  Van-Kampen modes
  Lebedev’ equation
Landau damping in double RF system
Multi-bunch beam
  Stability diagrams in single and double RF
  Bunch-by-bunch Landau damping
Conclusion

## Slide 3: Introduction
Landau damping is lost when coherent bunch frequency moves outside incoherent frequency band modified by beam-induced voltage
In longitudinal plane, Landau damping of coherent modes is achieved by synchrotron frequency spread ∆ωs, which can be increased by
  increasing bucket filling factor
  → minimum RF voltage for a given emittance (limited by particle losses)
  increasing bunch emittance
    → controlled emittance blow-up, limited by available RF voltage (H. Timko’ talk)
  applying higher harmonic RF system (active or passive)
    (see also talks by M. Venturini and N. Yamamoto this afternoon)

## Slide 4: Sacherer’ formalism
General equation (F. Sacherer, 1971) for perturbation
  Coherent frequencies ωc are obtained for spread ∆ωs = 0 using effective impedance Zeff
Stability diagrams obtained for “synthetic kernel” assuming rigid bunch motion and replacing wake field by local interaction.
  → No LD for distribution function with μ ≤ 1 for η ImZ/n < 0 (space charge above transition)
The stability limit for μ =2 is replaced by semi-circle with radius ∆ωc/ ∆ωs = 0.25 (pessimistic)
  → Popular criterion for loss of Landau damping:
  dependence on particle distribution is removed
  (sinusoidal modes used for calculation of ∆ωc )
Analytical solutions for ∆ωc exist for some distribution functions (Gaussian, binominal with μ = 1/2, 1) → consistent approach when used together with the exact [∆ωc/ ∆ωs]stab

## Slide 5: Hofmann-Pedersen formalism
Self-consistent analytical solution for ωsc and ∆ωs in case of μ = 1/2 (“parabolic” line density) and ImZ/n=const
  rigid bunch motion (also)
  coherent frequency calculation: spread ∆ωs is included
  → non-zero threshold for η ImZ/n <0
Threshold for loss of LD
with F = π4/30 for short bunches agrees with Sacherer’ criterion for m=1 and μ = 1/2 with [∆ωc/ ∆ωs]stab = 2/3 → F = π2/4 (~ 30% higher)

## Slide 6: Longitudinal beam stability in CERN LHC
Beam 1: controlled blow-up: ε ~ E1/2
Beam 2: emittance blow-up didn’t work
→ instability during acceleration ramp
ramp
Measured average bunch length during cycle
D. Boussard, D. Brandt and L. Vos (1999) “Is a longitudinal feedback system required for LHC?
From Sacherer criterion ∆ωc < ∆ωs /4 (shift < spread/4)
at 7 TeV with ImZ/n = 0.28 Ohm, 4σ =1 ns, V=16 MV:
Nth = 2.4x1011 → no dedicated wideband feedback,
natural Landau damping is sufficient
To avoid LLD during ramp, emittance ε ~ E1/2
→ controlled emittance blow-up keeps τ = const
Significantly lower single-bunch stability threshold was measured: scaled to 7 TeV for 4σ =1 ns, V=16 MV,
Nth = 2.0x1011 for 3 times smaller ImZ/n = 0.09 Ohm

## Slide 7: Landau damping in LHC
(ImZ/n) = 0.09 Ohm
Similar results in simulations
for full Z
BLonD simulations using full LHC impedance model and μ = 2 agree with measurements
(PhD thesis J. E. Muller, 2016)
LHC impedance model
Measured & simulated
LHC threshold intensity
Nth ~ ε5/2
Fit of measured profiles with μ = 2
12 MV
450 GeV
6.5 TeV
For μ =2: F=1/3 (instead of 1/2)
λ(t) = λ0(1 - 4t2/τ2)2.5

## Slide 8: Landau damping in LHC
→ Expected scaling with energy, voltage and bunch length works in LHC with
ξth = (5.0±0.5)10-5 (ns)5V
on flat bottom, flat top and during cycle
Measurements in LHC
= ξ
ε ~ E1/2
(PhD thesis J. E. Muller, 2016)

## Slide 9: Comparison of loss of LD thresholds for LHC
Expected from Sacherer’ criterion scaling with energy, voltage and bunch length seems to work, but
→ The thresholds predicted from Sacherer’ stability diagrams (and Hofmann-Pedersen approach) are 3 – 4 times higher than measured/simulated thresholds.
The discrepancy cannot be explained either by
by different particle distribution: thresholds for different distributions are similar for the same FWHM bunch length (semi-analytical calculations of I. Karpov using Hofmann-Pedersen approach, also seen in simulations by J. E. Muller)
by “missing “ impedance due to good agreement between measurements and simulations

## Slide 10: Loss of Landau damping in the CERN SPS
Sacherer’ criterion for ImZ/n = const
predicts a factor 10 higher impedance thresholds at injection (26 GeV/c, 2 MV) than on flat top (450 GeV/c)
Measurements: similar thresholds ~1x1011
(optics Q26)
→ Due to initial particle distribution (rotated bunches) and/or change of effective impedance during the ramp
(factor two reduction in bunch length)?
Good agreement between measurements and simulations (with rotated bunches and full SPS impedance model).
Cycle time [s]
Measurements of a single bunch in single RF system
Calculations

## Slide 11: Landau damping: Van-Kampen modes
Method (A. Burov, 2010): find Van-Kampen modes solving Vlasov equation for perturbation f(J,ψ,t) of stationary distribution function F(J) expanded (Oide & Yokoya, 1990) as
Without mode coupling the matrix equation (in action J) is
where
and
Continuous spectrum - singular modes from incoherent band. Discrete modes - coherent solutions described by regular eigenfunctions → their existence outside incoherent band serve as criterion for loss of LD
Mode below threshold
Trivial solution J=0
Loss of LD
Incoherent frequencies
The effect of PWD is relatively small (< 10%)
2

## Slide 12: Lebedev’ approach
Matrix equation (A. N. Lebedev, 1967) in variables with
where and normalisation
Finally,
where is a solution of equation
where

## Slide 13: Sacherer’ stability diagram as a low-frequency limit
In a single RF, for short bunches
For Bessel function Jm can be replaced by
or
Then, for uncoupled modes m, eigenfunction Is solution of
Lebedev’ equation for mode m → Sacherer’ stability diagram with synthetic kernel used for m > 0
This equation is valid for low frequency impedances with f < 1/(π𝜏) (𝜏 - bunch length)
Consistent coherent frequency can be obtained neglecting synchrotron frequency spread
with effective impedance

## Slide 14: Van-Kampen modes vs Lebedev’ approach
Loss of Landau damping in LHC: comparison of calculations and measurements
Solution for ImZ/n = const doesn’t converge → physical impedance model should be used.
For LHC, the results strongly depend on cut-off frequency for ImZ/n = const or resonant frequency of the broad-band impedance model- study ongoing.
Good agreement with measurements for μ=2 and b-b impedance: fres= 5 GHz, Q = 1, ImZ/n = 0.076 Ohm, fcut = 20 GHz
→ Numerical code solving Lebedev’ matrix equation (I. Karpov, 2019) gives the same thresholds as Van-Kampen modes (slightly longer computation time) for the same impedance model (with or not PWD).
A. N. Lebedev
N. G. van Kampen

## Slide 15: Landau damping in double RF system
Synchrotron frequency distribution
400
Voltage in 2 RF systems: V = V1sinφ +V2 sin(nφ + Φ2)
with nV2/V1 < 1
For maximum change in ωs(0): Φ2 = φ2 – n φs
Above transition:
φ2 = 0 - BLM (Bunch-Lengthening Mode)
φ2 = π - BSM (Bunch-Shortening Mode)
BLM: “flat” bunches, increased bucket size, larger spread for the same V1/V2 = n, but region with ω’s(J) =0 for any ratio V2 /V1 (V. Balbekov, S. Ivanov, 1987)
and high sensitivity to error in Φ2
→ only BSM works for LHC beam in the CERN SPS (n=4)
The same (BSM) from studies in PS (H. Damerau et al.)
Lower is n, point ω’s(J) = 0 is further away from bunch center
→ For short bunches, ∆ωs is significantly increased
(by ~ 10/φb2) with optimum n ~ 5/φ (φb = h ω0 𝜏/2)
400 MHz RF

## Slide 16: Double RF system: single bunch stability
Thresholds from Van-Kampen modes
and simulations for ImZ/n = const
(inductive impedance above transition)
In simulations the criterion for LLD needs to be chosen (0.8)
This was also the case for Van Kampen modes
Oscillation amplitude normalised to the kick amplitude
→ For n=2, long bunches are more stable in BSM.
Different behaviour below transition (simulations O. Boine - Frankenheim, T. Shukla, PRST AB, 2005)?
T. Argyropoulous, PhD thesis, 2015

## Slide 17: Landau damping in BS-mode for n > 2
BS-mode with n=4 and V2/V1=n,
V1=0.6 MV @100 MHz , SPS @26 GeV/c
Threshold from particle simulations
(T. Argyropoulos, PhD thesis, 2015)
Synchrotron frequency distribution
in BS-mode for various n
→ Flat portion in ω’s(J) appears for n>2
Stability in BSM can be improved by phase shift, also in BLM (T. Argyropoulos, A. Burov, E.S., IPAC’12)

## Slide 18: Landau damping for multi-bunch beam
Stability diagram for
For narrow band impedance with ωr, only one resonant harmonic kr = ωr /ω0 = lM + n can be kept (M - number of equidistant bunches) in Lebedev’ equation:
stable
unstable
From stability diagram
(V. Balbekov, S. Ivanov, 1987):
with
→ Beam is stable if vertical line 1/Rsh is inside stability region

## Slide 19: Landau damping for multi-bunch beam: stability diagrams in single and double RF
μ= 2: Rth in double RF system (BLM) is higher than in single RF
Note that all modes m are excited simultaneously in the BL-mode (not in BS-mode) since
μ= 1: Rth in double RF system is decreasing with emittance
Stability diagrams (m=1) for μ =1,2 in 1RF & 2RF (BLM) for various φmax
The instability threshold
→ Strong depends on ω’s/F’
Distributions with non-zero function F’
at the edge are more unstable (μ < 1)

## Slide 20: Multi-bunch threshold
The FWHM bunch length is important
Lebedev’ equation allows analysis of beam stability with both narrow and broad-band impedances
This approach was used for narrow-band resonator and ImZ/n = const (M. Blaskiewicz, “Landau damping with high frequency impedance”, 2009)
In single RF system the threshold (no acceleration)
Threshold Rsh for coupled-bunch instabilities in FCC-hh at 50 TeV for nominal intensity Nb=1011, V = 38 MV, γt =99.3 (I. Karpov, E.S., IPAC’19)
where

## Slide 21: Stabilisation of LHC proton beam in CERN SPS
The LHC beam in SPS is stabilised by the 4th harmonic RF system (~ factor 4 in Nth). → Extra stability margin for the LHC beam by optimising the 800 MHz voltage program (J. Repond, PhD thesis, 2019). Ratio V4/V1 = 0.1 was used in the past for the whole cycle.
V800 = 0.25 V200
Optimum V800/V200
ratio during SPS cycle
Increasing V800 helps to improve beam stability thresholds, …
→ higher bunch intensities were stabilized at the end of 2018
but only towards the end of the ramp,
where the threshold is minimum
SPS @450 GeV

## Slide 22: Bunch-by-bunch synchrotron frequency spread
Coupled-bunch instability can also be stabilisied by bunch-by-bunch spread ∆ωs > shift ∆ωc:
spread in bunch population
{∆N/N}rms > Im{∆ωc}/Re{∆ωc}
low-frequency voltage-modulation
ωs0 ~ V1/2
from RF cavities at (h+1) or residual beam loading (from fractional ring filling) – ESRF storage ring (O. Naumann, J. Jacob, 1997)
CERN SPS simulations: LHC beam is globally more stable with fundamental impedance reduced (by feedback) than removed (J. Repond, M. Schwarz)
SPS, Q26, Nb = 3x1010 ppb, 16% RF AM
E. Vogel, T. Bohl and U. Wehrle, PRST 8 (2005)
Effect of main RF Amplitude Modulation

## Slide 23: Summary
In longitudinal plane, the simplified analytical criteria are often used for scaling of the loss of Landau damping threshold with beam and machine parameters.
Sacherer stability diagram in longitudinal plane is justified only for low-frequency impedances and in other cases should be used with caution.
More complete formalisms (Van-Kampen modes and Lebedev equation) together with particle simulations are available for accurate threshold estimations, also based on realistic impedance model.
Dependence of thresholds on particle distribution can be reduced by using the FWHM bunch lengths.
Landau damping can be significantly increased by additional, higher harmonic RF system, but its limitations in BLM and, for n > 2, in BSM should be taken into account for the choice of the beam and RF parameters.

## Slide 24: Summary
In longitudinal plane, the simplified analytical criteria are often used for scaling of the loss of Landau damping threshold with beam and machine parameters.
Sacherer stability diagram in longitudinal plane is justified only for low-frequency impedances and in other cases should be used with caution.
More complete formalisms (Van-Kampen modes and Lebedev equation) together with particle simulations are available for accurate threshold estimations, also based on realistic impedance model.
Dependence of thresholds on particle distribution can be reduced by using the FWHM bunch lengths.
Landau damping can be significantly increased by additional, higher harmonic RF system, but its limitations in BLM and, for n > 2, in BSM should be taken into account for the choice of the beam and RF parameters.
Thank you for your attention!

## Slide 25: Spare slides

## Slide 26: Thresholds for different distribution functions
Distribution function
Again full-width half-maximum bunch length is a good parameter for stability evaluation
The same full-width half-maximum bunch length
I. Karpov

## Slide 27: Threshold of loss of Landau damping for different particle distributions
Threshold of LLD for different particle distributions with 0.8 ns FWHM @4.0 TeV
Threshold of LLD for different particle distributions with 1 eVs emittance @4.0 TeV
J. E. Muller

## Slide 28: Synchrotron frequency distribution and phase between 2 RF systems in BS-mode
Very good agreement between measurements and simulations (with SPS impedance model):
single bunches are unstable in BS-mode with V2/V1=4
can be stabilised by significant phase shift of 800 MHz RF system
(T. Argyropoulos et al., IPAC’12)

## Slide 29: Damping of coupled-bunch instability with higher harmonic RF system in CERN PS
10 & 40 MHz in BL-mode
10 & 40 MHz in BS-mode
First successful tests at flat top energy in CERN PS, (H. Damerau et al., 2017)
Bunch mode spectrum

## Slide 30
Thresholds for different feedback models
1x72 bunches, V200/V800 = 10MV/1MV, Q20, full SPS impedance model
Model feedback of 200 MHz by
  Reduction of Rshunt by 26dB (continuous)
  Impedance reduction factor (data points)
  No 200 MHz TWC (dashed)
Reducing the shunt impedance yields similar threshold as without the 200 MHz TWCs
No threshold was found when using the impedance reduction factor , even though it has more ‘residual’ impedance around 200 MHz
M. Schwarz, 2019