## Slide 2: MCBI for CERN LHC Injectors Upgrade (LIU) and High Luminosity LHC (HL-LHC)
Giovanni Rumolo, CERN, Genève, Switzerland
ICFA Mini-Workshop on Mitigation of Coherent Beam Instabilities in Particle Accelerators – MCBI 2019
23 – 27 September 2019, Zermatt (Switzerland)
Acknowledgements: D. Amorim, S. Antipov, G. Arduini, M. Barnes, H. Bartosik, M. Beck, N. Biancacci, R. Bruce, O. Brüning, X. Buffat, M. Carlà, P. Costa Pinto, H. Damerau, R. Di Maria, B. Goddard, A. Huschauer, V. Kain, E. Koukovini-Platia, G. Iadarola, A. Lasheen, K. Li, M. Meddahi, L. Mether, E. Métral, B. Mikulec, N. Nasresfahani, Y. Papaphilippou, T. Pieloni, S. Redaelli, J. Repond, A. Romano, L. Rossi, B. Salvant, M. Schenk, E. Shaposhnikova, M. Taborelli, H. Timkó, R. Tomás, C. Vollinger, C. Zannini

## Slide 3
Why upgrades and what are the upgrades for LHC and its injector chain?
Present intensity limitations and future performance of the LHC injectors
  Where do we need mitigation of coherent beam instabilities?
  How far we can go with the upgrades
Mitigation of beam instabilities for HL-LHC

## Slide 4
Why upgrades and what are the upgrades for LHC and its injector chain?
Present intensity limitations and future performance of the LHC injectors
  Where do we need mitigation of coherent beam instabilities?
  How far we can go with the upgrades
Mitigation of beam instabilities for HL-LHC

## Slide 5: Goals of upgrades in a nutshell (HL-LHC)
The High Luminosity LHC (HL-LHC) upgrade
Aims at 3000 (4000) fb-1 total integrated luminosity over HL-LHC run (2026 – 2037)
Based on operation at levelled luminosity of 5 (7.5) x1034 cm-2s-1 by lowering b*
 | Nb (x 1011 p/b) | ex,y, (mm) | Bunch spacing | Bunches
HL-LHC beam | 2.3 | 2.1 | 25 ns | 4x72 per injection
Beam properties @LHC injection
Notes: Both the consideration of energy deposition by collision debris in the interaction region magnets, and the necessity to limit the peak pile-up in the experimental detector, impose an a priori limitation upon peak luminosity. The consequence is that HL-LHC operation will have to rely on luminosity levelling.

## Slide 6: Goals of upgrades in a nutshell (LIU)
The High Luminosity LHC (HL-LHC) upgrade
Aims at 3000 (4000) fb-1 total integrated luminosity over HL-LHC run (2026 – 2037)
Based on operation at levelled luminosity of 5 (7.5) x1034 cm-2s-1 by lowering b*
The LHC Injectors Upgrade (LIU)
Aims at matching the beam parameters at LHC injection with HL-LHC target
Needs to deploy means to overcome performance limitations in all injectors!
 | Nb (x 1011 p/b) | ex,y, (mm) | Bunch spacing | Bunches
HL-LHC target | 2.3 | 2.1 | 25 ns | 4x72 per injection
Present | 1.3 | 2.7 | 25 ns | 4x72 per injection
Beam properties @LHC injection
Notes: Invest on improved shielding, ventilation, etc to make accesses possible when needed

## Slide 7: A view on LHC Injectors and LIU
Linac4
160 MeV H- charge exchange injection
Acceleration to 2 GeV with new main power supply and new RF systems
Main RF system (200 MHz) upgrade
Longitudinal impedance reduction & anti-ecloud coating
New beam dump and protection devices
Acceleration of H- to 160 MeV
Nominal 40 mA within 0.4 mm
2 GeV injection
New RF equipment including broad-band feedback
Notes: PSB
  Connection to Linac4  New H- charge exchange injection at 160 MeV from Linac4 to double brightness of LHC beams
  Acceleration to 2 GeV
    New main power supply POPS-B
    Replacement of C02-C04-C16 RF systems by Finemet based RF system
PS
  New injection at 2 GeV for protons to mitigate space charge
  RF improvements to improve beam quality and increase longitudinal coupled bunch instability threshold
    Impedance reduction of the RF systems
    Installation of new Finemet RF system as longitudinal feedback
  Operational deployment of transverse feedback system
SPS
  200 MHz RF system upgrade
    Rearrangement of cavities and power upgrade
    New LLRF including slip stacking capability
  Electron cloud mitigation and impedance reduction to increase intensity reach
    a-C coating of QFs + one full arc
    QF-type flange shielding and HOM damping in 200 MHz cavities
  New beam dump system in LSS5 and new design of protection devices to comply with the target HL-LHC beam parameter values

## Slide 8: A view on LHC and HL-LHC

## Slide 9
Why upgrades and what are the upgrades for LHC and its injector chain?
Present intensity limitations and future performance of the LHC injectors
  Where do we need mitigation of coherent beam instabilities?
  How far we can go with the upgrades
Mitigation of beam instabilities for HL-LHC

## Slide 10: Present performance limitations
PSB injection: Brightness limited by efficiency of multi-turn injection process and space charge effects
PS and SPS injection: Brightness limited by space charge – DQ<0.31 (PS) and 0.21 (SPS), to limit beam degradation
PS cycle: Bunch intensity limited by longitudinal coupled bunch dipolar instability
SPS cycle: Bunch intensity limited by RF power, longitudinal coupled bunch instability
 | Nb (x 1011 p/b) | ex,y, (mm)
HL-LHC target | 2.3 | 2.1
Present | 1.3 | 2.7

## Slide 11: Present performance limitations
PSB injection: Brightness limited by efficiency of multi-turn injection process and space charge effects
PS and SPS injection: Brightness limited by space charge – DQ<0.31 (PS) and 0.21 (SPS), to limit beam degradation
PS cycle: Bunch intensity limited by longitudinal coupled bunch dipolar instability
SPS cycle: Bunch intensity limited by RF power, longitudinal coupled bunch instability
 | Nb (x 1011 p/b) | ex,y, (mm)
HL-LHC target | 2.3 | 2.1
Present | 1.3 | 2.7

## Slide 12: Lifting the brightness limitations
Halve the slope of the PSB brightness line
  160 MeV H- charge exchange injection from Linac4 replacing 50 MeV multiturn injection from Linac2 (demonstrated in simulations)
Reduce space charge at PS injection to accommodate same tune spread as current LHC beam (DQy=-0.31)
  Increase of PS injection energy from 1.4 GeV to 2 GeV
  Increase of longitudinal emittance (compatibly with other constraints) at transfer in order to gain from decreasing lmax and increasing d=(dp/p0)
Concerning beam stability:
  PSB H instability due to extraction kicker not expected to be an issue  Eirini’s talk
  Larger longitudinal emittance beneficial to beam stability

## Slide 13: Lifting the PS intensity limitation
Instability
Bunch current limited around 1.6e11 p/b at extraction
Above 1.6e11 p/b longitudinal coupled bunch instabilities appear on the ramp and at flat top for nominal longitudinal emittance
  Dipolar oscillation, caused by 10 MHz RF system impedance (as found also in simulations)

## Slide 14: Mitigation of the PS longitudinal instability
Longitudinal feedback based on broad-band Finemet cavity as kicker installed and deployed over Run 2 (2015 – 2018)  Heiko’s talk
New power converters for 40/80 MHz and broadband cavities + multi-harmonic feedbacks and 40 MHz as Landau system + transverse optimisation
Commissioning of coupled bunch feedback with broadband cavity and operational optimization

## Slide 15: Mitigation of the PS longitudinal instability
Longitudinal feedback based on broad-band Finemet cavity as kicker installed and deployed over Run 2 (2015 – 2018)  Heiko’s talk
Goal in terms of intensity out of the PS reached!
  However, we may need to seek further stabilization in order to decrease the longitudinal emittance into the SPS (requirement to minimize capture losses)
  In this case, the option of installing a Landau cavity in the PS with the right tuning range to cover ramp + flat top remains viable as a post-LIU action

## Slide 16: Lifting the SPS intensity limitation
Beam loading in the present 200 MHz TW RF system – intensity limited to about 1.3e11 p/b
Longitudinal instabilities during ramp with very low threshold cured by
  800 MHz RF system in bunch shortening mode
  Controlled emittance blow-up (with constraint of 1.7 ns bunch length at extraction) – not needed in Q20
Bunch length spread
Only RF power upgrade
Still lagging 20% below target …
Notes: (2x4 & 2x5 section cavities)
Bunch length variation due to controlled emittance blow-up in presence of beam loading
More 800 MHz voltage is available but it is kept at 10% level of 200 MHz voltage to avoid region with ω’(J)=0 during ramp

## Slide 17: Mitigation of the SPS longitudinal instability
Impedance reduction needed in addition
  Shielding of a subset of vacuum flanges
  Enhanced damping of HOMs of 200 MHz (factor 3 desired)  baseline for LIU
  Serigraphy on the injection kickers MKP
new HOM coupler

## Slide 18: Mitigation of the SPS transverse instability
Transverse Mode Coupling Instability (TMCI) threshold was raised from 1.6e11 p/b to 4e11 p/b when switching to a low gamma transition (gt) optics  See Yannis’ talk
original SPS optics
1.6e11
low gt SPS optics
x2.5
measurements confirm 2.5 times higher threshold!
4.0e11

## Slide 19: Mitigation of the SPS transverse instability
Electron cloud responsible for instabilities, can be mitigated by
  Beam induced scrubbing (it worked, it still works!)
  Coating with a-C the chambers of the focusing quadrupoles and adjacent drift chambers

## Slide 20: Mitigation of the SPS transverse instability
Horizontal coupled bunch instability
  Observed in 2017-18 for intensities above 1.8 x 1011 p/b
  Driven by resistive wall and narrow band horizontal impedances, but also destabilizing effect of impedance reduction  Carlo’s talk
  Needs to be operationally stabilized for future operation – tradeoff with beam lifetime
ξH~0.1–0.2
ξH~0.3–0.5

## Slide 21: A possible weapon for the unexpected …
Prototype of vertical (V) wideband feedback system deployed at SPS
  Using stripline pick-ups + two stripline kickers and a slotline kicker, bandwidth up to 1 GHz, power > 1 kW
Damping of Transverse Mode Coupling Instability (TMCI) with single bunch demonstrated in machine experiments in 2017-18

## Slide 22: Summary: Future LIU performance
PSB injection: from Linac4
PS injection: 2 GeV, larger longitudinal emittance
PS cycle: Longitudinal coupled bunch feedback system, impedance reduction
SPS cycle: RF power upgrade, longitudinal impedance reduction, beam scrubbing & partial a-C coating, low gt optics
 | Nb (x 1011 p/b) | ex,y, (mm)
HL-LHC target | 2.3 | 2.1
Present | 1.3 | 2.7
LIU matches HL-LHC

## Slide 23
Why upgrades and what are the upgrades for LHC and its injector chain?
Present intensity limitations and future performance of the LHC injectors
  Where do we need mitigation of coherent beam instabilities?
  How far we can go with the upgrades
Mitigation of beam instabilities in the LHC

## Slide 24: LHC beam stability
LHC transverse beam instabilities observed with different types of beams and at different stages of the LHC cycle (see Xavier’s talk)
2010, single bunch
during the ramp
2011-12, 50 ns beam
during b* squeeze or while adjusting the beams to collide
2015-18, 25 ns beam
at injection

## Slide 25: LHC beam stability
LHC transverse beam instabilities observed with different types of beams and at different stages of the LHC cycle (see Xavier’s talk)
Sources are mainly
  Transverse impedance (dominated by collimators, especially when closed at top energy) through loss of Landau damping due to beam-beam, electron cloud, linear coupling, cut tails, noise induced modifications of distribution
  Electron cloud, at least with 25 ns beams
Controlled through “extreme” machine settings, e.g. at 6.5 TeV Q’=+15-20, octupole strength close to maximum, maximum damper gain and bandwidth
Need to gain some margin with stabilisation knobs for operation with HL-HLC beam parameters (double intensity, double brightness)  Impedance reduction, electron cloud understanding and partial mitigation

## Slide 26: LHC beam stability
Due to the small gaps, at 6.5 TeV the most critical impedance contributor (80%) is collimators
Within HL-LHC primary and secondary collimators replaced by new ones with Mo-Gr jaws having same robustness and higher conductivity (with Mo coating on secondaries)  Alessio’s talk
Secondary collimators in IR-7
Primary collimators
Everything else
Geometric
Resistive wall
Present
Upgrade
Impedance reduction
secondary collimators

## Slide 27: LHC beam stability
Example: Effect of impedance reduction on TMCI threshold
Present LHC impedance model
Instability
HL-LHC impedance
(after collimator impedance reduction)
Instability

## Slide 28: LHC beam stability
Strong instabilities observed at 450 GeV with 25 ns beams, in both x and y
  Stabilized with high chroma (Q’=20), high octupole strength (DQ=1.5e-3)
  Caused mainly by electron cloud in quadrupoles
Simulations predict more stability for HL-LHC (thanks to lower electron cloud)
Instability simulations (450 GeV)
(e-cloud in the arc quadrupoles - SEY 1.3)
arc quadrupoles
e-cloud buildup simulations

## Slide 29: LHC beam stability
Strong instabilities observed at 450 GeV with 25 ns beams, in both x and y
  Stabilized with high chroma (Q’=20), high octupole strength (DQ=1.5e-3)
  Caused mainly by electron cloud in quadrupoles
Simulations predict more stability for HL-LHC (thanks to lower electron cloud)
More electron cloud instabilities have been observed e.g. at flat top induced by decaying intensity and onset of central stripe in dipoles

## Slide 30: Electron cloud mitigation
In general, low SEY after scrubbing is crucial to cure e-cloud instabilities
Heat load measurements show that SEY may remain as high as 1.35 (in average) in some cells
  Reason for high remaining SEY under close scrutiny to improve opening procedures in the future
Critical sections like the new triplets will be a-C coated
S12
S81
S23
S78
S34
S67
S45
S56
ATLAS
LHCb
ALICE
SEY = 1.15 – 1.25
SEY = 1.30 – 1.35

## Slide 31: Electron cloud mitigation
If electron cloud remains a problem with HL-LHC operation, a last resort safety net is the filling scheme …
25 ns (2760b)
25 ns slot
72b
25 ns slot
8b
4e
8b
4e
8b
4e
8b
8b+4e (1972b)
 Pure 25 ns and 8b+4e can be combined to reach the maximum heat load

## Slide 32: LHC beam stability: longitudinal
Instabilities at injection  Theodoros’ talk
  Persistent oscillation, and even instability, from injection errors
  Improved injection matching (voltage, energy)
Controlled longitudinal emittance blow up during the ramp (target bunch length 1.1-1.2 ns) to avoid onset of instabilities  Helga’s talk
Possible instabilities at flat top if bunch length decreases below 0.9 ns

## Slide 33: To wrap up and conclude
LHC and its injectors set to major upgrades: LIU, HL-LHC
  Injectors upgraded in 2019-2020, LIU beam commissioning in 2021-2024
  LHC upgraded in 2024-2025 and HL-LHC era >2026
Mitigation of beam instabilities is key to goal performance in the LHC injectors
  PSB, PS  Mainly rely on active feedback systems
  SPS  Impedance reduction, electron cloud suppression, longitudinal emittance blow up, enhanced Landau damping, optics change
Preservation of beam stability in LHC  Avoid loss of Landau damping, operational scenarios, impedance reduction, electron cloud build up & instability scaling, low electron cloud filling pattern

## Slide 34
THANK YOU FOR YOUR ATTENTION

## Slide 35: Mitigation of the PS longitudinal instability
Longitudinal feedback based on broad-band Finemet cavity as kicker installed and deployed over Run 2 (2015 – 2018)
Feedback off (Nb = 1.8 · 1011 ppb)
Feedback on (Nb = 1.8 · 1011 ppb)

## Slide 36: Mitigation of the PS longitudinal instability
Longitudinal feedback based on broad-band Finemet cavity as kicker installed and deployed over the last three years
With transverse optimisation, beam is now stable up to 2.6e11 p/b
Nb = 2.6 ∙ 1011 ppb, DN/N < 5%

## Slide 37: Timeline of the projects
Proton Runs
Technical Stops
Long Shutdowns
Beam Commissioning
Run 2
LS2
Mainly LIU work
LS3
Mainly HL-LHC work
Run 3
Run 4
Run 3: LIU beam commissioning through the injector chain
Run 4: HL-LHC run with a period of ‘luminosity learning’
We are here

## Slide 38: Lifting the PS intensity limitation
Longitudinal feedback based on broad-band Finemet cavity as kicker installed and deployed over the last three years
With transverse optimisation, beam is now stable up to 2.6e11 p/b
Goal in terms of intensity out of the PS reached!
Brightness still pending Linac4 and space charge mitigation in PS
2.6e11 p/b, 5 mm

## Slide 39: HL-LHC single particle dynamics
Strong effect of linear and nonlinear errors in IRs due to large b  Low Dynamic Aperture in absence of correction
Pre-computed corrections from magnetic measurements needed even for basic optics measurements
b∗ levelling will require commissioning of a large number of optical configurations  Challenge for efficiency of the optics measurement and correction tools
Simulated evolution of an HL-LHC physics fill with baseline parameters
Notes: needed to fulfil the tight tolerances coming from DA or coherent stability constraints

## Slide 40: Luminosity projection

## Slide 41: LHC beam stability
Strong instabilities observed at 450 GeV with 25 ns beams, in both x and y
  Stabilized with high chroma (Q’=20), high octupole strength (DQ=1.5e-3)
  Caused mainly by electron cloud in quadrupoles
Simulations predict more stability for HL-LHC (thanks to lower electron cloud)
Instability simulations (450 GeV)
(e-cloud in the arc quadrupoles - SEY 1.3)
arc quadrupoles
e-cloud buildup simulations

## Slide 42: Beam induced heat load in LHC
High heat load on beam screen in cold regions (cryo limit 160 W/hc in the arcs)
  With 25 ns beams
  Much higher than calculation from impedance + synchrotron radiation
  Different among arcs
Most observations compatible with electron cloud, probably localised in some magnets (or even some parts of magnets)
  Coating with a-C for triplet quadrupoles to decrease SEY
Heat load
per half cell
8 Aug 2017
Notes: Only 25 ns, scaling with bunch intensity (linear, threshold at just below 4e10 p/b), power loss localised in last bunches of trains from RF measurements of stable phase, at least partly scrubbable, behaviour in dipoles and quadrupoles

## Slide 43: E-cloud build up with intensity
Underlying mechanism:
When the SEY decreases the energy window for multipacting becomes narrower
For high bunch intensity the e- spectrum drifts to higher energies and can move outside the most efficient region

## Slide 44: Inferring the average SEY
6.5 TeV
Simulations
450 GeV
6.5 TeV
Measurements
High-load
Low-load

## Slide 45: Inferring the average SEY
450 GeV
Simulations
450 GeV
6.5 TeV
Measurements
High-load
Low-load

## Slide 46: Beam induced heat load in LHC
Two fold issue for HL-LHC
  Less margin for cryostat with HL-LHC parameters (three-fold contribution from impedance and synchrotron radiation)
  How does the additional load scale with bunch intensity?  We can make a prediction only if we assume it is caused by electron cloud
Maximum allowed by cryogenics
Margin
~7 kW
e-cloud S12
(2017)
~6 kW
Margin
~4 kW
2556b
1.15e11 p/bunch
6.5 TeV
2760b
2.2e11 p/bunch
7 TeV
e-cloud S34
(2017)
~2kW

## Slide 47: Some other challenges in LHC
Beam-beam interaction
  Head-on beam-beam tune shift limit (based on past experience) currently surpassed
  Effect of the long-range  6s DA comfortably achieved during the whole levelling process, even including the chromaticity and octupole settings necessary for beam stability
Incoherent emittance growth along the cycle
  Larger than expected from Intra Beam Scattering (with margin), but impact de-facto mitigated by b* levelling
  Influence of noise  minimise sources by careful design of power converters, crab cavity controls, transverse damper upgrade (it might also benefit coherent instabilities)
Beam halo active control for machine protection
  Potentially large halo generation with HL-LHC beams, especially during commissioning
  Cleaning techniques under study, option for Hollow Electron Lens
Notes:  adjust crossing angle during levelling process to reduce the pile-up density and the radiation on the inner triplets

## Slide 48: Some other challenges in LHC
Beam-beam interaction
  Head-on and long range (dynamic aperture during leveling), compensation techniques
Incoherent emittance growth along the cycle
  Sources to be understood, influence of noise
Large beam halo generation with future beams
  Halo active control for machine protection, cleaning techniques under consideration
RF power and longitudinal stability
  Power consumption for future injection voltage, transient beam loading, instabilities at flat bottom, longitudinal emittance blow up
Notes:  adjust crossing angle during levelling process to reduce the pile-up density and the radiation on the inner triplets