## Slide 1: Dosimetry of light-ion beams
Hugo Palmans
MedAustron, Wiener Neustadt, Austria
and National Physical Laboratory, Teddington, UK

## Slide 2: Overview
  Dosimetry defined
  Why absorbed dose to water
  Mechanisms for dosimetry
  Detectors for dosimetry of light-ion beams:
  calorimeters, ionization chambers, solid state detectors, chemical dosimeters, microdosimeters, nanodosimeters

## Slide 3: Dosimetry defined
Measurement of dose (in radiation measurement dose = absorbed dose)
Measurement of dosimetric quantities
  energy imparted (absorbed dose)
  kinetic energy released (kerma)
  number of particles (fluence)
  a function of number and energy (e.g. product of dose and a quality factor)

## Slide 4: Absorbed Dose
Absorbed dose D
Where is the mean energy imparted to matter of mass dm.
Energy imparted is the energy incident minus the energy leaving plus any reduction in rest mass energy.
The medium should always be specified.
Unit: J kg-1 = Gy (gray)

## Slide 5: Why absorbed dose to water?
  Tradition, for high-energy photon and electron beams:
  biological effect ~ f(nionizations ) ~ absorbed dose
  Water is close to tissue + ionizations mainly in water
  -> RT prescription is generally in terms of Dw
  Easy and reproducible material

## Slide 6: Ionising radiation mechanisms for dosimetry
Ionisation
Energy cascade
Free radicals creation resulting in a chemical reaction chain
Physical effects

## Slide 7: Calorimetry

## Slide 8: Calorimetry: principle
 | C (J.kg-1.K-1) | T/D (mK.Gy-1) |  (m2.s-1)
water | 4182 | 0.24 | 1.44x10-7
graphite | 704 | 1.42 | 0.80x10-4

## Slide 9: Water calorimeter
Cooling fluid
Air
4ºC
Beam

## Slide 10: Water calorimeter – chemical heat defect
H2O+ e- H2O*
H3O+ e-aq H• OH•
+ (10-7s)
H2 H2O2 OH-
(10-12 s)

## Slide 11: Water calorimetry / chemical heat defect protons
0,0
1,0
2,0
3,0
LET (keV.mm-1)
G (100 eV-1)
10-1
100
101
102
H+
OH•
e¯aq
H•
OH¯
H2
HO2
H2O2
60Co
(100 MeV)
(1MeV)
protons
0,00
1,00
2,00
3,00
4,00
0,0
0,2
0,4
0,6
0,8
1,0
t (s)
G (100eV-1)
(-) H2O
H2
H•
H2O2
H+
OH•
e-aq
OH-

## Slide 12: Water calorimetry / chemical heat defect ions
Brede et al. 2006 Phys. Med. Biol. 51:3667-82

## Slide 13: Graphite calorimetry
Beam
DC
Dw

## Slide 14: Graphite calorimetry
Palmans et al (2004)
Phys Med Biol 49:3737
NPL primary standard level proton calorimeter under development:
Core
Inner jacket
Outer jacket
Annular PCB
Graphite vacuum body
Notes: With graphite calorimetry the thermal diffusivity is such that any temperature distribution in a small single block is levelled out within less than a second. For this reason a sample (core) is normally separated by one or more vacuum gaps from the graphite phantom as is illustrated here in a new calorimeter dedicated for proton dosimetry which is under development at NPL. The main concern with graphite calorimetry is, however, the conversion from dose to graphite to dose to water, the quantity of interest.

## Slide 15: Dose conversion graphite calorimetry
?
kfl

## Slide 16: Ionization chambers

## Slide 17: Dose determination with ion chamber
Q: charge produced in the air of the chamber
W: mean energy required to produce an ion-pair in air
Unfortunately, for commercially available chambers, the volume V is not known with the necessary accuracy (would otherwise be a primary standard!).
We have to rely on methods other than “first principles”, which involve the use of ion chamber calibration factors
p
s
D
D
×
×
=
air
w,
air
w
Wair
m
Q
D
×
=
air
air
Wair
V
Q
×
×
=
air
r

## Slide 18: Simple absorbed dose protocol
But we have with →
This is formalism of IAEA TRS-398 and ICRU Report 78

## Slide 19: Experimental determination of
from calorimetry:

## Slide 20: Calculation of

## Slide 21: (Wair)p
33,0
34,0
35,0
36,0
37,0
0
100
200
300
400
E (MeV)
wair (J/C)
ICRU 59
ECHED
AAPM-16
IAEA TRS398

## Slide 22: (Wair)p
33,0
34,0
35,0
36,0
37,0
0
100
200
300
400
E (MeV)
wair (J/C)
ICRU 59
ECHED
AAPM-16
IAEA TRS398
Jones 2006 RPC 75:541

## Slide 23: Water/air stopping power ratio
r
o,p
= 1mm
r
o,e
= 1mm
100
101
102
103
10-6
10-4
10-2
100
102
t
= E
k
/E
rest
S
coll
/
r
(MeV cm
2
g
-1
)
proton water
protons air
electrons water
electrons air
0.90
1.00
1.10
1.20
1.30
s
w,air
sw,air protons
sw,air electrons
ICRU 49
ICRU 37

## Slide 24: Perturbation correction factors
0.0
10.0
20.0
30.0
40.0
50.0
60.0
70.0
0.0
10.0
20.0
30.0
Depth (mm)
D
air
per proton per cm
2
(Gy)
-5.0
0.0
5.0
Difference pdd and
reconstruction
Palmans 2006 Phys Med Biol 51:3483
z
sleeve
wall
air
c.e.
z0
water
x
Rcel
Rcav
Rwall
Rsleeve
Proton
p
Palmans 2011 Proc IDOS
IAEA-CN182-230

## Slide 25: Initial recombination
E

## Slide 26: Volume recombination

## Slide 27: Track structure
Electron:
Alpha:
Heavy ion:

## Slide 28: Initial recombination
E

## Slide 29: Initial recombination
E

## Slide 30: Quenching in chemical and solid dosimeters
Ionisation density
Radical formation
Termination reactions
Transport phenomena

## Slide 31: Protons
Kempe et al. (2007) Med. Phys. 34:183-92
0.0
5.0
10.0
15.0
20.0
0
5
10
15
20
25
30
depth in water / g cm
-2
energy loss per unit depth / MeV cm
2
g
-1
total
1
H
primary
1
H
secondary
1
H
secondary
1
H <10 eV/nm
> 2 eV/nm
> 6 eV/nm
> 10
eV/nm
> 20
eV/nm
< 2 eV/nm

## Slide 32: Carbon ions
Kempe et al. (2007) Med. Phys. 34:183-92
0
50
100
150
200
250
300
0
5
10
15
20
25
30
35
40
depth in water / g cm
-2
energy loss per unit depth / MeV cm
2
g
-1
total
12
C
primary
12
C
1
H
> 60 eV/nm
> 40 eV/nm
> 20 eV/nm
4
He
10+11
C
10+11
B

## Slide 33: Ferrous sulphate dosimeter

## Slide 34: EPR or ESR - Alanine

## Slide 35: Alanine/EPR
0.0
1.0
2.0
3.0
4.0
0.0
0.5
1.0
1.5
2.0
2.5
3.0
depth in alanine (cm)
dose per m.u. (Gy)
ion chamber measmnt
Dw,γ(alanine)
Palmans 2006
NPL report DQL-RD003

## Slide 36: Alanine/EPR dosimetry
Bassler et al, NIMB 266 929-936, 2008
CERN anti-proton beam
Birmingham 15 MeV beam
GSI 12C ion beam
Herrmann et al 2011 Med Phys 38:1859

## Slide 37: Radiochromic film
Protons
Vatnitsky 1997 Appl Rad Isot 48:643
Carbon ions
Martisikova 2010 PMB 55:5557

## Slide 38: Radiochromic film – energy dependence
Kirby et al. 2010 Phys Med Biol 55:417

## Slide 39: Polymer gel dosimetry
BANG3-Pro2:
BANG:
Heufelder et al. 2003.
Zeidan et al. 2010 Med Phys 37:2145

## Slide 40: Natural diamond detector
Fidanzio et al 2002 Med Phys 29:669

## Slide 41: CVD diamond
HE protons: Mandapaka, Med Phys 40:121702
HE carbon ions: Marinelli, Med Phys 42:2085
LE carbon ions: Rossomme et al. (BHPA 2016)
/ submitted Med Phys
LE protons: Rossomme et al. (BHPA 2016)

## Slide 42: Silicon-based detectors
Kohno et al 2006 Phys Med Biol 51:6077

## Slide 43: TLD - protons
Besserer 2001 Phys Med Biol 46:473

## Slide 44: TLD - protons
Eliyahu 2014 Radiat Meas 71:226

## Slide 45: Scintillators
Safai et al. 2004 Phys. Med. Biol. 49:4637

## Slide 46: Scintillators
Safai et al. 2004 Phys. Med. Biol. 49:4637

## Slide 47: Scintillators
Safai et al. 2004 Phys. Med. Biol. 49:4637

## Slide 48: Microdosimetry…
Andrea Pola, Politecnico di Milano
Cathode (A-150 plastic)
Rexolite®
Sensitive Volume: 0.9x0.9 mm2
Gas Out
Gas In
Aluminium
Rollet et al 2010, Rad Prot Dosim 143:445

## Slide 49: Microdosimetry
Colautti et al 2017 ESTRO Physics workshop Glasgow

## Slide 50: Nanodosimetry…
Ion counter / PTB Startrack / INFN

## Slide 51
Schulte et al 2011 AIP Conf Proc 1345:249

## Slide 52: Conclusions
No ideal detectors for proton and carbon ions
Calorimeters can serve as primary standards
Ionization chambers remain workhorse for light-ion reference dosimetry
Most chemical and solid state dosimeters exhibit signal quenching in the Bragg peak
Micro- and nano-dosimetry

## Slide 53: Reading
H. Palmans, A. Kacperek and O. Jäkel, “Hadron dosimetry” In: Clinical Dosimetry Measurements in Radiotherapy (AAPM 2009 Summer School), Ed. D. W. O. Rogers and J. Cygler, (Medical Physics Publishing), 2009
C. P. Karger, O. Jäkel, H. Palmans and T. Kanai, “Dosimetry for Ion Beam Radiotherapy,” Phys. Med. Biol. 55(21) R193-R234, 2010
Proton Therapy Physics, Ed. H. Paganetti (Taylor & Francis), 2011, second edition 2018
M. F. Moyers and S. Vatnitsky, Practical Implementation of Light Ion Beam Treatments, (Medical Physics Publishing), 2012
Principles and practice of proton beam therapy (AAPM 2015 Summer School), Ed. I. J. Das and H. Paganetti, (Medical Physics Publishing), 2015
H. Palmans, “Light-ion beam dosimetry” In: Clinical 3D Dosimetry in Modern Radiation Therapy, Ed. B. Mijnheer, (Taylor & Francis), 2017