## Slide 1: Hollow Electron Lens Quench Protection Design and Analysis status update
TE-MPE (HEL Quench Protection):
M. Maciejewski, M. Mentink, D. Wollmann, A. Verweij
EN-MME (HEL Design):
G. Gobbi, D. Perini + G. Kirby (TE-MSC)

## Slide 2: Superconducting Accelerator Circuits – Numerical Challenges
PI
Iref
-
+
Network model of a circuit
Differential-algebraic equations
Varying time constants ~1 ms (switch) - ~10 min (circuit discharge)
Varying geometric scales ~10 cm (diode) - ~10 km (circuit)
~10 k elements
Non-linear behaviour
Field/network model of a magnet
Controller Model
Differential-algebraic equations
Fixed frequency of operation
10-100 elements
Non-linear behaviour
Partial differential equations
Varying time constants ~10us (quench) - ~10ms (losses)
Varying geometric scales ~10 um (filaments) - ~10 m (magnet)
~10 k degrees of freedom
Highly non-linear material properties and equations
R
U
A
M2
M154
Multi-Domain, Multi-Physics, Multi-Rate and Multi-Scale Problem
Busbar Model
Partial differential equations
Varying time constants
Adaptive mesh refinement
~1k elements
Non-linear behaviour
LHC 27 km

## Slide 3: Simulation of Transient Effects in Accelerator Magnets - Our Solution
Multi-domain – dedicated, domain-specific numerical tools
Multi-physics – strong coupling in single model, weak coupling of independent models
Multi-rate – interaction, coupling of two or more models
Multi-scale – interaction, coupling of two or more models
No free lunch theorem – One tool can not simulate it all!
LHC
We use our models for performance evaluation of SC magnets and circuits for

## Slide 4: STEAM Overview
STEAM is a simulation framework to study transient effects in SC magnets.
STEAM consists of five pillars:
Numerical tools  standalone, co-simulation
Model generation API
Tool adapter API
Meta-Methods co-simulation, optimization
Front-end to interact with APIs
4. Meta-Methods (Co-simulation, optimization)
2. Model-Generator
APIs
5. Frontends (Jupyter, Matlab)
3. Tool Adapter APIs
1. Tools
(BBQ, ProteCCT, LEDET, ANSYS, COMSOL, PSIM, PSpice, LTSpice, QLASA)
https://cern.ch/steam

## Slide 5: Beam Cleaning – Collimation system
LHC 27 km
S. Redaelli, Beam Cleaning and Collimation Systems

## Slide 6
The HEL System – SC Magnets
The Hollow Electron Lens system consists of multiple superconducting magnets for
Guiding the hollow beam of electrons:
  (main solenoid, bending solenoid, solenoid after valve, e-gun, CCT)
Correcting the field imperfections and fine tune the beam position:
  (4 for the main solenoid, 4 for the main bending, 2 for the e-gun)
HL-MCF Meeting # 46: Conceptual Design of IFS, CLIQ and K-MOD Feeders+ Quench Study for MCBXF Magnets + Status on HEL Circuits, https://indico.cern.ch/event/794680/ D. Perini: Status Report on HEL Circuits
*A. Bertarelli, et al. Hollow Electron Lens Update, Collimation Upgrade Specification Meeting #56
-
Operating Principle (Collimator)*
Electron Trajectory
Magnetic Flux Lines
Force Directed Radially Inward
+
-
-
-
-
-
-
-
The aim of this work is to study the protectability of the superconducting circuits.

## Slide 7: Outline
System Overview + Methodology
Quench Protection Design
  E-gun cathode
  Solenoid After Valve + e-gun
  Main Bending Solenoids
  Main Solenoids
Summary
direction of electrons

## Slide 8
direction of electrons
1. System Overview*
- Bx
- By
- Bz
- Btot
* Bcathode
* Bvalve
*G. Gobbi, D, Perini: Main parameters of HEL electrical circuits, EDMS 2036694

## Slide 9
2. Solenoids – Powering Scheme
MainSol2_tot
MainSol1_tot
PC+EE
330 A
PC+EE
330 A
GunSol
PC+EE
257 A
BendSolGunSol_tot
PC+EE
320 A
BendSolGunSol_tot = SolAftValve1…4 + GunSol1 + GunSol1a; GunSol = GunSol2
MainSol1_tot = Main1 + Main1A + Main1B; MainSol2_tot = Main2+Main2A + Main2B
BendSol_tot = BendSolIN + BendSolINA + BendSolIN + BendSolINA
 | GunSol | BendSolGunSol_tot | BendSol_tot | MainSol1_tot | MainSol2_tot
GunSol | 834.18 | 100.79 | 1.63 | 1.92 | 0.19
BendSolGunSol_tot | 100.79 | 806.74 | 13.24 | 7.29 | 0.34
BendSol_tot | 1.63 | 13.24 | 2146.47 | 130.35 | 130.35
MainSol1_tot | 1.92 | 7.29 | 130.35 | 8877.46 | 49.91
MainSol2_tot | 0.19 | 0.34 | 130.35 | 49.91 | 8877.46
Differential Inductance [mH]
Stored Energy [kJ]
GunSol | 32
BendSolGunSol_tot | 47
BendSol_tot | 135
MainSol1_tot | 494
MainSol2_tot | 493
BendSol_tot
PC+EE
335 A

## Slide 10
2. Strategy for Quench Protection Analysis
We study the protection of busbars, magnets, and circuits.
We assume that if one of the main circuits quenches, all circuits are discharged.
For coils, we consider 100 mV threshold for quench detection and 10 ms validation.
In order to explore the parameter space, the following strategy was applied:
Quench propagation to calculate the quench detection time – 1D STEAM-BBQ model
Calculation of the maximum hot-spot temperature
  Quench integral curves with 1D STEAM-BBQ model
Calculation of minimum quench integral for a given maximum voltage to ground – Excel
  Neglecting internal magnet resistance growth and assuming constant inductance
  Constant energy extraction resistance
Iterate 3. varying energy extraction resistance until to conditions (can be adjusted) are met Thot-spot < 200 K - to limit the thermal load on the conductor as well as the cryogenic system Vground,max < 500 V - to limit the power converter common mode voltage and the insulation testing voltage
1
2
3
Design
iterations

## Slide 11
STEAM-BBQ [1]: FEM-based COMSOL model (inspiration: [2])
Calculation of quench-related conductor properties:
  Quench propagation velocity vQ
  Development of voltage after quench origination for quench detection
  Hotspot temperature as a function of quench integral
For circuit with known discharge quench integral:
  Time-dependent current (Exponential decay after quench detected)
  Time-dependent hotspot temperature
Compatible with STEAM co-simulation framework
Circuit current discharge
[1] M. Mentink and M. Maciejewski, “STEAM-BBQ User manual”, EDMS nr. 2159478, (2019)
[2] D. Paudel, CERN thesis 2015-090, June 30th (2015)
vQ
Temperature [K]
x [m]
Time [s]
Circuit current [A]
2. STEAM-BBQ - Overview
Temperature-development along length of conductor
Courtesy: M. Mentink

## Slide 12: STEAM-BBQ - Thermal Aspects
BBQ dimensionality: 1+1D
  Longitudinal heat transfer
  Transverse heat transfer (one node for core, six for insulation layers)
  Optional heat transfer to helium bath
BBQ simultaneously calculates the busbar hotspot temperature in two ways:
  ‘Adiabatic hotspot temperature’: No longitudinal heat propagation perfect transverse heat propagation without cooling to bath
  Regular hotspot temperature, with longitudinal heat propagation and transverse heat propagation
Uses STEAM material library for user-selected material properties (with cross-checked temperature and magnetic-field dependence)
Thermal layout: 1+1D dimensionality
Courtesy: M. Mentink
[1] M. Mentink and M. Maciejewski, “STEAM-BBQ User manual”, EDMS nr. 2159478, (2019)
[2] D. Paudel, CERN thesis 2015-090, June 30th (2015)

## Slide 13
Computation methodology
tq
td
td+v
i(t)
t
MIITs =

The goal is to calculate the peak voltage to ground and hot-spot temperature.

Energy extraction resistance
Voltage to ground
Hot-spot temperature
100 mV detection threshold
Vmax
Tmax


## Slide 14
2.A. E-gun Cathode - Parameters
Parameter | Value
Cu/Nb-Ti | 4:1
Ic(5 T, 4.2 K) | >= 750 A
RRR | >=100*
Inom | 257 A
Jnom | 149 A/mm2
Lnom | 0.83 H
Bnom,max | 3.7 T
VRleads @ Inom | 1 V
39.6 mm
76 mm
109 mm
HEL circuits follow LHC powering cycle
I [A]
t [s]
Inom = 257 A
1500
Inductive voltage during ramp-up
IRB = 11850 A
t = tdetect+validate
Inom
REE
Lnom
Rleads
1.65 mm
1.05 mm
Cable with polymide insulation
15-20 um
Same conductor for all coils
Magnet geometry
Circuit topology

## Slide 15
2.A. E-gun – Energy Extraction Resistance Sweep
RRR | 80 | 100 | 150 | 300
tdetect+validate [ms] | 160 | 190 | 220 | 270
Quench detection and validation time
Voltage to ground and hot-spot temperature as a function of energy extraction resistance.
Energy extraction grounded at the input terminal.
With the maximum temperature (200 K) and voltage to ground (500 V)
the permissible energy extraction resistance values span from 0.12 to 1.9 Ω.
Chart: Energy extraction resistance [ohm]
| 1.945525291828793 | 1.5 | 1.0 | 0.5 | 0.25 | 0.175 | 0.12
V_gnd [V] | 500 | 385.5 | 257 | 128.5 | 64.25 | 44.975 | 30.84
T_HS_max [K] | 200 | 200 | 200 | 200 | 200 | 200 | 200
T_HS_80 [K] | 39 | 41 | 46 | 58 | 88 | 126 | 214
T_HS_100 [K] | 39 | 41 | 45 | 57 | 86 | 122 | 207
T_HS_150 [K] | 39 | 40 | 44 | 55 | 82 | 115 | 194
T_HS_300 [K] | 38 | 40 | 43 | 53 | 77 | 108 | 182
Notes: Results are available at \\cern.ch\dfs\Projects\STEAM\HL-LHC\Hollow Electron Lens\Th\COMSOL\9
Results are available at \\cern.ch\dfs\Projects\STEAM\HL-LHC\Hollow Electron Lens\El\Excel\2

## Slide 16
2.B. Solenoids After Valve + e-gun - Parameters
Parameter | Value
Inom | 320 A
Jnom | 185 A/mm2
Lnom | 0.81 H
Bnom,max | 3.1 T
Same conductor as in the e-gun solenoid
Inductive voltage during ramp-up
39.6 mm
76 mm
109 mm
Magnet geometry
t = tdetect+validate
Inom
REE
Lnom
Rleads
Circuit topology

## Slide 17
2.B. Solenoid after Valve + e-gun – Energy Extraction Resistance Sweep
RRR | 80 | 100 | 150 | 300
tdetect+validate [ms] | 105 | 115 | 125 | 165
With the maximum temperature (200 K) and voltage to ground (500 V)
the permissible energy extraction resistance values span from 0.2 to 1.56 Ω.
Chart: Energy extraction resistance [ohm]
| 1.5625 | 1.0 | 0.5 | 0.25 | 0.175
V_gnd [V] | 500 | 320 | 160 | 80 | 56
T_HS_max [K] | 200 | 200 | 200 | 200 | 200
T_HS_80 [K] | 46 | 52 | 73 | 140 | 246
T_HS_100 [K] | 45 | 51 | 71 | 132 | 234
T_HS_150 [K] | 44 | 49 | 67 | 122 | 218
T_HS_300 [K] | 42 | 47 | 64 | 117 | 202
Quench detection and validation time
Voltage to ground and hot-spot temperature as a function of energy extraction resistance.
Energy extraction grounded at the input terminal.
Notes: Results are available at \\cern.ch\dfs\Projects\STEAM\HL-LHC\Hollow Electron Lens\Th\COMSOL\8
Results are available at \\cern.ch\dfs\Projects\STEAM\HL-LHC\Hollow Electron Lens\El\Excel\2

## Slide 18
2.C. Bending Solenoids - Parameters
150 mm
321 mm
258 mm
Parameter | Value
Inom | 335 A
Jnom | 193 A/mm2
Lnom | 2.147 H
Bnom,max | 3.5 T
CCT temporarily removed from the circuit.
Same conductor as in the e-gun solenoid
Inductive voltage during ramp-up
Magnet geometry
t = tdetect+validate
Inom
REE
Lnom
Rleads
Circuit topology

## Slide 19
2.C. Bending Solenoids - Energy Extraction Resistance Sweep
RRR | 80 | 100 | 150 | 300
tdetect+validate [ms] | 105 | 115 | 125 | 165
With the maximum temperature (200 K) and voltage to ground (500 V)
the permissible energy extraction resistance values span from 0.65 to 1.5 Ω.
To stay below the limits, the maximum allowed inductance for the CCT is 8 H.
Chart: Energy extraction resistance [ohm]
| 1.492537313432836 | 1.25 | 1.0 | 0.75 | 0.5
V_gnd [V] | 500 | 418.75 | 335 | 251.25 | 167.5
T_HS_max [K] | 200 | 200 | 200 | 200 | 200
T_HS_80 [K] | 73 | 83 | 100 | 138 | 269
T_HS_100 [K] | 70 | 80 | 96 | 135 | 257
T_HS_150 [K] | 67 | 75 | 91 | 125 | 239
T_HS_300 [K] | 64 | 72 | 86 | 117 | 224
Quench detection and validation time
Voltage to ground and hot-spot temperature as a function of energy extraction resistance.
Energy extraction grounded at the input terminal.
Notes: Results are available at \\cern.ch\dfs\Projects\STEAM\HL-LHC\Hollow Electron Lens\Th\COMSOL\7
Results are available at \\cern.ch\dfs\Projects\STEAM\HL-LHC\Hollow Electron Lens\El\Excel\2

## Slide 20
2.D. Main Solenoid - Parameters
1599 mm
249.3 mm
180 mm
Parameter | Value
Inom | 330 A
Jnom | 191 A/mm2
Lnom | 8.877 H
Bnom,max | 5 T
Inom
REE
Lnom
Rleads
t = tdetect+validate
20
Inductive voltage during ramp-up
Magnet geometry
Circuit topology
Same conductor as in the e-gun solenoid
Feasibility of application of 600 A LHC power converter with EE grounded in the middle
for this circuit (maximum voltage, stored energy, inductance) has to be studied by TE-EPC.

## Slide 21
2.D. Main Solenoid - Energy Extraction Resistance Sweep
With the maximum temperature (200 K) and voltage to ground (500 V)
the permissible energy extraction resistance values span from 2.46 to 3 Ω.
RRR | 80 | 100 | 150 | 300
tdetect+validate [ms] | 65 | 75 | 85 | 95
Chart: Energy extraction resistance [ohm]
| 3.030303030303028 | 2.75 | 2.5 | 2.25 | 2.0 | 1.75
V_gnd [V] | 500 | 453.75 | 412.5 | 371.25 | 330 | 288.75
T_HS_max [K] | 200 | 200 | 200 | 200 | 200 | 200
T_HS_80 [K] | 143 | 166 | 191 | 228 | 285 | 380
T_HS_100 [K] | 139 | 160 | 184 | 222 | 275 | 366
T_HS_150 [K] | 132 | 151 | 174 | 208 | 259 | 345
T_HS_300 [K] | 124 | 141 | 162 | 195 | 241 | 322
Quench detection and validation time
Voltage to ground and hot-spot temperature as a function of energy extraction resistance.
Energy extraction grounded in the middle.
500 V during standard operation, up to 1 kV under earth fault on current lead.
Notes: Results are available at \\cern.ch\dfs\Projects\STEAM\HL-LHC\Hollow Electron Lens\Th\COMSOL\6
Results are available at \\cern.ch\dfs\Projects\STEAMHL-LHC\Hollow Electron Lens\El\Excel\2

## Slide 22
3. Conclusion
    STEAM-BBQ allowed to carry out an end-to-end analysis
    All circuits except the main solenoid are protectable with a regular EE system.
    To limit the voltage to ground in the main solenoid circuit, for the main solenoid we assume that the energy extractor is grounded in the middle.
    The choice of the final EE resistance is a trade-off between the peak voltage and temperature (the peak values might need to be adjusted).
    Further studies involve analysis of protectability of corrector magnets.