## Slide 2: CERN Networks Automation
IT-CS Marwan Khelif

## Slide 5: LANDB
20+ years old Oracle database
Covers many aspects of Communication Systems:
  IPAM / DNS / DHCP
  Network Topology
  Network devices
  Firewall
  Structured cabling
  Telephony
  Security

## Slide 6: LANDB
Multiple applications:
  CSDBweb (Web) – Network administrators
  LanDB Portal / WebReq (Web) – End-users
  SOAP API (Web) – Specific services and users (experiments)
  CFMGR (CLI) – Configuration management
Large variety of languages:
  Java
  PL/SQL
  Perl
  Python

## Slide 7: IPAM

## Slide 8: IPAM – IP Blocks
Assigned to Network Domains (GPN, TN, ITS, LCG, …) interconnected by Gates (router interfaces with ACLs)
Provide same configuration for all IP services – Gateway / DNS / NTS

## Slide 9: IPAM – IP Services
IP Services = Subnets
Type of service defines configuration properties (MTU, IP 4/6 stack, MPLS, OSPF, …)
Support both dynamic/static addressing (campus)

## Slide 10: DHCP
Dynamic addressing by default (Campus)
  Static addressing on users’ request
  Public/internal IP address assignment (IP service)
Static addressing required for TN
Pool of IP addresses for unregistered devices

## Slide 11: DNS
Static configuration for main .CERN.CH zone
  Generated every 5min from LANDB
Dynamic zones delegated to users
  Eg: nodes load-balancing service, experiments
  Specific zone .DYNDNS.CERN.CH for “dynamic” devices (updated from DHCP)

## Slide 13: Plans
DNS
  Decrease time required to generate configuration (go to dynamic?)
DHCP
  Allow user to choose public/internal dynamic addressing
Standardise applications
  Standard protocol: NETCONF
  Languages: Java + Python
  OpenSource?