## Slide 1: Electrical Test Baseline
Tiago Catalao da Rosa, Fernando Menendez Camara, Felix Rodriguez Mateos
11th January 2019, Review on the Quench Protection Heaters and Electrical Tests of the 11T Dipole

## Slide 2: Content
Introduction
Electrical Test Strategy
11 T Dipole Failure Scenarios & Worst-case Voltages
Electrical Test Values
ElQA Tests Sequence
Proposed Intermediate Temperature Test

## Slide 3: Introduction
Maximum expected voltages during operation are calculated through simulation of worst conditions during a quench, including failure of protection elements.
Calculations are conducted at nominal current. Conditions at ultimate current should be covered by the margin in the components design without applying safety factors. Some exceptional conservative cases must follow the same rule, as they are realistic but with very low likelihood of happening (HL-LHC Project policy).
Electrical test levels are obtained by applying factors regarding the different environments and temperature-pressure conditions under which the magnet will be tested.

## Slide 4
Test voltages diagram
Electrical Test Strategy
Vsim: maximum expected coil voltage at quench (to ground and quench heaters)
Tests performed on a single magnet from the final test after assembly, through magnet reception at a test facility up to acceptance in test stations at cold.
Tests performed on a magnet or circuit (once the magnet is connected) during installation in the machine and further commissioning and operation.
Nominal Operating Conditions (NOC): superfluid helium in the cold mass, with all the ancillary components (e.g. instrumentation capillary tube and feedthrough) at the corresponding local conditions;
Warm (RT): room temperature in dry air.
Reference document EDMS 1995595

## Slide 5
Failure case analysis for a 11 T cryo-assembly during quench [1]:
The failure of 2 heater power supplies or circuits at nominal current
gives the worst-case voltage to calculate Vsim :
 | Nominal |  | 1 QH circuit failure |  | 2 QH circuits failure | 
 | Inom | Iult | Inom | Iult | Inom | Iult
Current [kA] | 11.85 | 12.80 | 11.85 | 12.80 | 11.85 | 12.80
Quench integral [MA2s] | 15.8 | 16.2 | 16.1 | 16.4 | 16.2 | 16.5
Hot-spot temperature [K] | 320 | 342 | 327 | 349 | 333 | 356
Peak voltage to ground [V] | 245 | 340 | 570 | 680 | 950 | 1070
Peak turn to turn voltage [V] | 75 | 80 | 80 | 90 | 90 | 95
Maximum expected coil voltage at quench (V) | To ground | 1400 (950+450)
 | To quench heater | 1350 (900+450)
[1] See Susana I. Bermudez’s presentation
11 T Dipole Worst-case Conditions
Energy Extraction voltage to ground
Assuming fuse failure in the heater power supply

## Slide 6
Test values at ‘Manufacturing Facilities and Test Stations’ stage:
Test values at ‘Tunnel’ stage:
Test name |  | Test voltage | Value
Test voltage at NOC at ‘Manufacturing Facilities and Test Stations’ stage (V) | To ground |  | 3300
 | To quench heater |  | 3200
Test voltage at warm before first helium bath (V) | To ground |  | 5000
 | To quench heater |  | 3200
Test voltage at warm after helium bath (V) | To ground |  | 660
 | To quench heater |  | 640
Maximum leakage current (µA) for a cryo-assembly – not including leakage of the test station |  |  | 30
Test voltage duration (s) |  |  | 120
Test name |  | Test voltage | Value
Test voltage at NOC at ‘Manufacturing Facilities and Test Stations’ stage (V) | To ground |  | 3300
 | To quench heater |  | 3200
Test voltage at warm before first helium bath (V) | To ground |  | 5000
 | To quench heater |  | 3200
Test voltage at warm after helium bath (V) | To ground |  | 660
 | To quench heater |  | 640
Maximum leakage current (µA) for a cryo-assembly – not including leakage of the test station |  |  | 30
Test voltage duration (s) |  |  | 120
Test name |  | Test voltage | Value
Test voltage at NOC at ‘Tunnel’ stage (V) | To ground |  | 2100
 | To quench heater |  | 1620
Test voltage at warm after helium bath (V) | To ground |  | 660
 | To quench heater |  | 640
Maximum leakage current (µA) for a cryo-assembly – not including leakage of the test station |  |  | 30
Test voltage duration (s) |  |  | 120
Test name |  | Test voltage | Value
Test voltage at NOC at ‘Tunnel’ stage (V) | To ground |  | 2100
 | To quench heater |  | 1620
Test voltage at warm after helium bath (V) | To ground |  | 660
 | To quench heater |  | 640
Maximum leakage current (µA) for a cryo-assembly – not including leakage of the test station |  |  | 30
Test voltage duration (s) |  |  | 120
11 T Dipole Electrical Test Values
ELQA test value in LHC at cold
Expecting feedback from tests
Expecting feedback from tests
Limits set by magnet designers

## Slide 7: Tests Sequence and Possible Scenarios
Test levels to apply at each ELQA step

## Slide 8: Proposed Intermediate Temperature Test
Tests at an intermediate temperature at 1 bar allow to qualify the magnet in a well-known environment, close to the conditions in which the worst voltages are expected at quench;
Reasons for such a test:
  Verification of the effects of helium pockets after cold tests which might degrade an already weak insulation;
  Test level at warm for refurbished magnets is still not clear (to be addressed after proper studies are conducted);
  High dielectric strength of liquid helium and air might hide defects due to the less stringent test voltage at warm after helium bath, Vtest3 (660 and 640 V);
Feasibility of this intermediate temperature test strongly depends on the test station capability in terms of voltage withstand and possible stable cooling conditions (temperature and pressure).
Test voltage | Temperature [K] | Maximum detectable defect length [mm]
3200 V, 3300 V | 80 | ~5
 | 150 | ~10
 | 200 | ~13
Test voltage | Temperature [K] | Maximum detectable defect length [mm]
 | 80 | ~5
 | 150 | ~10
 | 200 | ~13

## Slide 9: Thank you for your attention

## Slide 10: Backup Slide – Paschen Curves
Test voltage | Temperature [K] | Maximum detectable defect length [mm]
 | 80 | ~5
 | 150 | ~10
 | 200 | ~13
Test voltage | Temperature [K] | Maximum detectable defect length [mm]
 | 80 | ~5
 | 150 | ~10
 | 200 | ~13