## Slide 1: Week 1 (49/2018) LHC experimental areas
On behalf of BVO Josef Sestak
2nd VSC LS2 Overview of activities

## Slide 2: Performed activities during last week

## Slide 3: Performed activities during last week

## Slide 4: Planned activities for next 2 weeks

## Slide 5: Venting interventions
Venting gas N2 (60) – O2 (55) 80-20;
ALICE & CMS injected bypassing the NEG filter;

## Slide 6: Venting interventions challenges
ALICE
  VVGSW.A1R2.X interlocked by IT2L – solved by ICM;
CMS
  PLC and GIS table status due to the power-cut;
  PLC restarted but without respond of primary pump;
  GIS primary pump state reset on site;
LHCb
  VELO beam volume & detector volume opened to the atmospheric pressure;
  Bypass valve connecting both volumes removed (no balancing mode);
Detailed intervention reports will be published in EDMS

## Slide 7: Mechanical interventions

## Slide 8: Mechanical interventions

## Slide 9: Technical problems – CMS opening conflict

## Slide 10: Technical problems – CMS opening conflict
Cable tray broken during the HF opening – cabling & connectors damaged.
Leak detection of the CT2 chamber to be performed (on the surface)

## Slide 11: Technical problems – CMS opening conflict
Conflict occurred during the opening phase of HF detector
HF small movement by 10mm out of IP;
HF radial opening to increase the clearance around the beam-pipe;
HF movement out of IP (tens of centimetres);

## Slide 12: Thank you !

## Slide 13: Cabling routing in RB24
Cabling for vacuum equipment (1x VVGMT; 2x VGRB; 2x VPI; 1x VGI) to be re-routed (ALICE request – Mini-frame removal);
14m up to UX25 wall
Cabling from Run1 layout still in place (additional VGPB cabling).
EN – EL intervention on Thursday

## Slide 14: LHCb VELO – venting to atm pressure