## Slide 1: WP6 S-band based linac option status and linac modelling for FELs
S. Di Mitri,
Elettra Sincrotrone Trieste
Contributors:
A. Aksoy – Ankara Uni
A. Giribono, C. Vaccarezza – INFN LNF
Latina, X. Liu – CERN
E. Marin, R. Munoz Horta – ALBA CELLS
A. Faus Golfe, Y. Han – LAL

## Slide 2: Codes
PIC codes allow tracking with real number of electrons, e.g. from 0.4 to 5 billion or so.
Semi-analytical models of beam collective dynamics provide guidance to a first step-machine design.
I. Zagorodnov, M. Dohuls (2011)
S. Di Mitri (2013)
IMPACT
J. Qiang (2012)
ASTRA
ASTRA
ASTRA
CSRTrack
CSRTrack
CSRTrack
Elegant
Genesis
Chains of specialized codes allow to balance accuracy vs. CPU time in S2E simulations.
M. Dohuls et al. (2008)
GPT + Elegant

## Slide 3: Geometric (RF) Wakefields
Strong wake potential + magnetic compression = multi-kA current spikes at bunch edges.
P. Emma for LCLS (2009)
Model vs. Measurement @ FERMI
M. Cornacchia et al. (2006)
G. Penco et al. @ FERMI (2014)
Geometric and RW wakefields can be computed accurately, and imported into tracking codes.
  Spikes drive CSR & microbunching instability, and RW wake in low-gap pipe.
  Spikes magnitude depends on details of Injector Laser and Linac long. wakefield.
Wakefields data (to be made available):
S-band Injector
X-band Linac
Resistive Wall wake in Undulator ?

## Slide 4: CSR – 1D vs. 3D
S. Bettoni et al., PRAB (2016)
Projected emittance control is favoured by uniform slice Twiss parameters  injector optimization.
Slice norm. emittance is typically perturbed at < 0.05 m level. Can be much worse at full compression.
3-D codes needed to predict slice emittance growth. 1-D runs typically over-estimate the final projected emittance.
CSRtrack 3D
Exp. vs. Codes
200 pC
@ 200 MeV
P 2.84 µm
S 1.43 µm
P 4.95 µm
S 1.85 µm
CSRtrack 3D
CSRtrack Projected
Elegant Projected
H. Owen et al. for NLS (2008)
200 pC
@ 735 MeV
Codes

## Slide 5: Work Plan, 2.A option
A. Giribono
C. Vaccarezza
E. Marin
R. Munoz Horta
A. Faus-Golfe
Y. Han
A. Latina
X. Liu
S. Di Mitri
A. Latina
X. Liu
S. Di Mitri
Benchmarking injector beam dynamics
Optimized injector beam
Specifications of the linearizer and compressor
S2E simulation
1-D tentative run with 2 compressors, to the linac end
S2E simulation
PRESENT
NEXT STEP

## Slide 6: Codes – Our Choice
A. Giribono
C. Vaccarezza
E. Marin
R. Munoz Horta
A. Faus-Golfe
Y. Han
A. Latina
X. Liu
S. Di Mitri
A. Latina
X. Liu
S. Di Mitri
TStep
LiTrack
3-D Space-charge
// and  geometric wakefields
// and  wakefields
CSR (3-D)
Microbunching instability
Astra
GPT
Placet
GPT
RFTrack
Elegant

## Slide 7: Charge
for parabolic charge distribution
for S-band NC Gun, w/o RF bunching, long bunches
(FEL specs)
(assumption from preliminary FEL scaling laws)
(diffraction limit,
)
+
=
Spec on #ph/pulse suggests: Q > 50 pC anyhow, and If > 2 kA
3-D simulation: minimize at the expense of
(FEL specs)
Q = 75 pC
t  1 ps
n  0.2 m rad
Ii  15 A
&
CF  150
RF bunching  5
Chicane 1  30
Chicane 1  15
Chicane 2  10

## Slide 8: Injector ( 100 MeV)
3-D codes (space charge) benchmarking: TStep vs. GPT vs. Astra
75 pC, w/o VB
75 pC, w VB
Nominal beam parameters: optimization w & w/o VB
This slide by:
A. Giribono (INFN)
DONE
ONGOING
0.2 m
0.2 m

## Slide 9: Main Linac ( GeVs)
Q = 50 pC
Ii  30 A
CF = 20  5
One injector beam for both SX and HX
One linac setting for both SX and HX
SX-beam extracted at intermediate energy
EXERCISE

## Slide 10: Lessons Learned & Status
Q = 75 pC is a starting point. S2E runs will tell us if x  0.2 m rad & I  3 kA are good enough for SX FEL.
HX FEL specs are critical (75 pC, 0.1 m rad, 9 kA !!!).
X-band longitudinal wakefields impose off-crest acceleration for energy chirp compensation (manageable).
CF  150 most likely. CSR-induced projected emittance growth might become an issue (reduction of FEL gain) for CF > 100.
S-band injector file with optimized emittance/current @ 75 pC soon available (INFN)
GPT vs. Astra vs. TStep benchmarking soon finalized (ALBA, INFN)
S2E run with GPT ongoing (ALBA)
1-D run (Elettra) and S2E run (ALBA, CERN) follow

## Slide 11: SX FEL – F. Nguyen 18 Oct.’18

## Slide 12: HX FEL – F. Nguyen 18 Oct.’18