## Slide 1
Daniel González-Iglesias1, Daniel Esperante1, Marçá Boronat1, César Blanch1, Benito Gimeno1, Juan Fuster1, Avni Aksoy2
1Group of accelerator physics, Instituto de Física Corpuscular (IFIC), Valencia, Spain
2Institute of Accelerator Technologies, University of Ankara, Ankara, Turkey
11rd December 2018
XLS-WP3 Gun and Injector Meeting
X-band Gun RF design

## Slide 2: Summary
It is worth to mention, our group has no previous experience in the design of RF components. Due to this, the work carried out during the past months is focused on the understanding of the RF gun structures.
The tasks performed can be split in two categories:
  Bibliographic review of the technical literature. The objective is become familiar with the theoretical basis that supports photoinjector design and get an insight of how they operate.
  Learning to use the computational tools employed for the design of RF guns. Until now, we have focused on those related with the RF design, namely, SUPERFISH (2D) and HFSS (3D).
Some of the bibliography revisited:
T. P. Wangler, “RF Linear Accelerators”, ed. Wiley-VCH, 2nd edition, 2008.
T. Rao, D. H. Dowell, “An Engineering guide to photoinjectors”, 2013.
M. Reiser, “Theory and design of Charged Particle Beams”, ed. Wiley-VCH, 2nd edition, 2008.
L. Faillace, “Innovative Radio-Frequency Linear Accelerating Structures”, PhD Thesis, University La Sapienza, 2008.
F. B. Kiewiet, “Generation of ultra-short, high brightness relativistic electron bunches”, PhD Thesis, University of Eindhoven, 2003.
2

## Slide 3: 5.6 cell X-band RF gun
3
Firstly, we have been aimed on the analysis of a 5.6 cell X-band RF gun design provided to us by the Prof. Avni Aksoy from the University of Ankara
This design has been a very useful starting point and it has allowed us to learn about how to use the SUPERFISH software.
In fact, now we are able to build new geometries, obtain and plot the RF fields, estimate ohmic losses, change the mesh size, adjust precision parameters of the RF solver, etc.
Scheme of the 5.6 RF gun in SUPERFISH
Example: Convergence analysis performed for the Avni RF gun. It is plotted the RF electric field along the gun axis, for different values of the mesh spacing.
dx(mm) | 0.2 | 0.1 | 0.07 | 0.05 | 0.04
fπ (MHz) | 11991.47 | 11990.76 | 11990.080 | 11990.04 | 11989.96
dx, dy are the mesh increments along the z and r directions, respectively

## Slide 4: 5.6 cell X-band RF gun
3-D view in HFSS of the 5.6 cell X-band gun
4
In addition, the same structure was analysed using the HFSS software.
At present, we are able to use efficiently HFSS:
build and analyse RF gun structures (obtain and
export RF fields, adjust precision of the solutions,
etc.)
Comparison between the results provided by SUPERFISH and HFSS for the 5.6 cell X-band gun
In order to check that we are employing correctly both electromagnetic solvers, it was performed a comparison between the results provided with HFSS and SUPERFISH.
As it is observed in the left figure, there is a very good concordance between them, thus it is demonstrated the accuracy of our analysis.

## Slide 5: RF coupler
Once understood the basic structure of a RF gun, the next step we performed is to acquire some knowledge about the RF coupler that feeds the gun.
To reach this aim, the following structure extracted from the literature(1) has been considered for the analysis of a coaxial coupler scheme.
The main concern is the calculus of the coupling factor, β
(1) F. B. Kiewiet, “Generation of ultra-short, high brightness relativistic electron bunches”, PhD Thesis, University of Eindhoven, 2003.
5
Scheme of the 2.6 cell RF gun photoinjector
At resonant frequency, it can be shown that
C

## Slide 6: RF coupler
If the dielectric length is enough to ensure all the RF power is absorbed, then the coupling factor can be calculated in the following way:
Firstly, the analysis is performed using HFSS. Obtaining β is straightforward:
Secondly, the analysis is carried out with SUPERFISH. For obtaining β, it must be defined a fictitious dielectric lossy material with properties:
6
Dielectric
Scheme of the 2.6 cell RF gun with coupler in SUPERFISH
RF electric field along the coupler
Dielectric interface
is the power absorbed by the dielectric

## Slide 7: RF coupler
Finally, we compare the axial electric field and the resonant RF frequency for the sake of completeness:
Again, good concordance is obtained between HFSS and SUPERFISH
7

## Slide 8: Design of a RF gun with coupler
In order to learn a bit more about photoinjectors and couplers, we tried to design a 5.6 cell RF gun with a coaxial coupler using the Avni gun as the reference model.
To do this, SUPERFISH software (which is much faster than HFSS) was employed
The final objective was to design a gun with the following optimized magnitudes:
After some attempts we reached a prototype that presents the following characteristics:
8
Scheme of the 5.6 cell RF gun with coaxial coupler
RF electric field maximum flatness is better than 99%

## Slide 9: Design of a RF gun with coupler
9
  Finally, it is checked the convergence of the solution by essaying different mesh size increments
DX, DY are the mesh increments along the z and r directions, respectively
DX(cm), DY(cm) | f (MHz) | β
0.009, 0.008 | 11800.05 | 1.014
0.008, 0.007 | 11799.91 | 1.015
0.007, 0.006 | 11799.80 | 1.013
These are the mesh values employed in the design process

## Slide 10: Future work
For the previous designed 5.6 cell RF gun with coupler, it is expected to optimize other parameters such as the mode separation and the RF electric field intensity at cavity surfaces
We plan to learn the General Particle Tracer1 (GPT) software, which is a commercial code able to simulate the electron beam dynamics along the RF photoinjector. To reach this aim, the following steps will be given*:
    Read carefully the GPT manual (currently in progress)
    Run the examples included with the GPT manual
    Try to build some basic scenarios which might be checked with analytical expressions (e.g., one single electron in a pillbox)
    Simulations of an electron beam through a realistic RF gun, exploring all the GPT capabilities
10
Some GPT screenshots
*A physics degree student will be helping us with GPT simulations
1 http://www.pulsar.nl/gpt/