## Slide 1: Summary of 10 MHz cavity impedance measurements
G. Favia, A. Lasheen
Acknowledgments: H. Damerau, V. Desquiens
LIU-PS Beam Dynamics Working Group MEETING
12/12/2018

## Slide 2
Single-bunch beam measurements
Multi-bunch beam measurements
PSC10 impedance with closed gaps
PSC10 impedance contribution at higher frequencies
Conclusions
Overview

## Slide 3
TOF Single bunch beam to neglect the multi bunch effect
The impedance is computed from the beam induced voltage:
Single bunch beam
Measurements of the beam induced voltage (no RF on the gap )

## Slide 4
Recent observations
Beam intensity variations cause marginal impedance variations

## Slide 5
Multi bunch beam
Beam induced voltage measured just before the gap closure
Beam induced voltage
Closed gaps
Closure of gap relay
Measurements done using LHC type beam

## Slide 6
Measurement results
The voltage does not decay to zero as in the single bunch case
FFT computed over a 100 us period
Impedance calculated by dividing the induced voltage in frequency domain by the beam spectrum
The deconvolution is applied only on the revolution frequency peaks

## Slide 7
Measurement results
Average value comparable with 2016 results
C36 and C11 missing due to gap relay and amplifier issues

## Slide 8
The impedance source(s) responsible of the instability can be identified by checking the peak of resistive impedance vs. the frequency for each mode (vertical lines, up to mode )
The impedance of the 10 MHz cavities with the gaps short-circuited is not exactly on but close enough to raise suspicion…
Impedance and coupled-bunch modes *
( -> dipole, -> quadrupole)
Impedance gap relay closed *
* G. Favia, based on C10-11 measurements, https://cds.cern.ch/record/2286835/
Kicker resonance to be checked…
* A. Lasheen, LIU-PS Beam Dynamics Working Group 23/11/2018

## Slide 9
Closed gaps
The impedance of the 10 MHz cavities with the gaps short-circuited is not negligible
Single bunch measurements
h=8

## Slide 10
Above 30 MHz impedance results may be affected by :
Noise level comparable with signal one
Limited oscilloscope dynamics
Unknown gap probe attenuation
The impedance of the 10 MHz cavities with the gaps short-circuited is not negligible
Closed gaps
Single bunch measurements
h=8

## Slide 11
The peak of impedance moves by few kHz with frequency tuning
Measurements at different harmonics available just for cavity 11
C11, closed gaps
Closed gaps
Single bunch measurements

## Slide 12
The peak of impedance moves by few MHz with frequency tuning
The impedance is large, but in a frequency region far from the one expected for quadrupolar instability (~20 MHz)
C11, left gap closed
Closed gaps
Single bunch measurements

## Slide 13
C10 impedance at higher frequencies
The cavity coupling line has a very dangerous parallel resonance with the anode capacity of the final tube at about 32MHz
Final stage transfer function
Amplifier transfer function
Multi-bunch measurements h=21

## Slide 14
The peak of impedance at ~32 MHz seems moving with frequency tuning
C10 impedance at higher frequencies
Single bunch measurements

## Slide 15
Above 30 MHz impedance results may be affected by :
Noise level comparable with signal one
Limited oscilloscope dynamics
Unknown gap probe attenuation
Impedance measured using spectrum analyzer
C10 impedance at higher frequencies
Single bunch measurements

## Slide 16
Measurements of PSC10 impedance at h=21 using multi-bunch beam were performed
The PSC10 impedance when gap relays are closed is not negligible and may be responsible of quadrupolar oscillations
The PSC10 system may contribute to the total PS impedance above operational frequency, due to a parallel resonance at 32 MHz
The validity of impedance results at frequencies above operational one has to be further investigated
Worth investigating deeper the problem for eventual improvements?
Conclusions

## Slide 17
Thank you
for you attention